## Slide 1
César Domingo-Pardo, IGFAE Workshop Proton-Therapy, Santiago de Compostela, May 2023
Hybrid Compton-PET imaging for ion-range monitoring in hadron-therapy
J. Balibrea-Correa, C. Domingo-Pardo, I. Ladarescu, J. Lerendegui-Marco, I. Ladarescu, A. Tarifeño-Saldivia
IFIC (CSIC-UV)
V. Babiano-Suarez, F. Calviño, M. Pallás
UPC-Barcelona
C. Guerrero, M.C. Jimenez, J.M. Quesada, T. Rodriguez-González
University of Seville / Centro Nacional de Aceleradores
Thanks to the

## Slide 2
PET monitoring, pros & cons
Delayed (biological washout, organ motion…)
Not directly coinciding with the Bragg peak
Low counting statistics (10 Bq/ml)  Low efficiency
Sensitive to tissue stoichiometry and mass density
Functional character: physiological processes and tumour RF
Excellent sensitivity (1.3 mm, 50ms, 108p) and tomographic functionality (KVI-Group, Siemens PET heads, 12N, 13O, b+ 10ms Ozoemelam 2020)
Range verification via PET (Llacer, 1979)
GSI, Enghardt (2020)
p-beam
511 keV
511 keV
Prompt-Gamma Imaging, pros &cons
g
g
t
Range verification via Prompt Gamma Imaging (Stichelbault&Jongen, 2003)
Most advanced electronic (Compton) imagers: Kabuki, 2009; Richard, 2012; Peterson, 2010; Kormoll, 2011; Llosa, 2013; etc
High g-ray yield at the Bragg peakreliable signature of the ion-range
Limited intrinsic imaging resolution vs. PET  Still few mm range-shift feasible
Low efficiency (particularly for more than two detection planes)
Large neutron-induced backgrounds (in-beam)
g
g
Dresden, Enghardt (2020)
Prev. Talks by: Laura Moliner (I3M), Antoni Rucinski (CCB), A. Espinosa, C. Guerrero (USe)
Prev. Talks by G. Llosà (IFIC), P. Crespo (LIP)
Notes: PET: limited by delayed signature and spatial distribution of beta+ emitters, but it has a very high intrinsic image resolution
PGI: limited by image resolution, detection efficiency and neutron-induced backgrounds, but it is sensitive directly to the Bragg peak itself

## Slide 3
Prev. Talks by: Laura Moliner (I3M), Antoni Rucinski (CCB), A. Espinosa, C. Guerrero (USe)
PET monitoring, pros & cons
Delayed (biological washout, organ motion…)
Not directly coinciding with the Bragg peak
Low counting statistics (10 Bq/ml)  Low efficiency
Sensitive to tissue stoichiometry and mass density
Functional character: physiological processes and tumour RF
Excellent sensitivity (1.3 mm, 50ms, 108p) and tomographic functionality (KVI-Group, Siemens PET heads, 12N, 13º, b+ 10ms Ozoemelam 2020)
Range verification via PET (Llacer, 1979)
GSI, Enghardt (2020)
p-beam
511 keV
511 keV
g
g
t
Range verification via Prompt Gamma Imaging (Stichelbault&Jongen, 2003)
Most advanced electronic (Compton) imagers: Kabuki, 2009; Richard, 2012; Peterson, 2010; Kormoll, 2011; Llosa, 2013; etc
High g-ray yield at the Bragg peakreliable signature of the ion-range
Limited intrinsic imaging resolution vs. PET  Still few mm range-shift feasible
Low efficiency (particularly for more than two detection planes)
Large neutron-induced backgrounds (in-beam)
g
g
Dresden, Enghardt (2020)
Prev. Talks by G. Llosà (IFIC), P. Crespo (LIP)
GSI, Enghardt (2020)
p-beam
511 keV
511 keV
t
PET:
Compton-PGI:
Efficiency
Efficiency
Image Resolution
Signal/Background
Neutron backgrounds
Delayed / Indirect
Prompt / Pristine
g
Compton PGI & PET together?
g
g
Prompt-Gamma Imaging, pros &cons
Notes: Question whether one can combine both techniques in order to exploit the best aspect of each of them?

## Slide 4
Hadron therapy: concept of hybrid Compton-PET imaging for ion-range verification
(…) propose an original combination of different techniques in a hybrid detection scheme, aiming to make the most of complementary imaging methods and open new perspectives of image guidance for improved precision of ion beam therapy.
…novel concepts of complementary PET and prompt gamma imaging in a so called hybrid detection scheme. As already observed in [58], a possible solution would be a combination of multiple Compton camera arms offering sufﬁcient solid angle over- age and using opposite single detector layers to serve as Compton camera scatterers or PET coincidence identiﬁers, complemented by additional absorbers for Compton imaging or total energy check in PET operation (Fig. 3). …
K. Parodi, Nucl. Instr. Meth. A (2016)
High detection efficiency (500 cm2 PSDs)  Online real-time range verification
Low sensitivity to n-induced backgrounds (LaCl3, 6LiPE)  Improved S/B-ratio
Good performance in the g-ray energy range up to 5-6 MeV (thick crystals)
Compact & lightweight (TOFPET-ASICs)  Compatible with clinical environment
HYMNS ERC-CoG https://cordis.europa.eu/project/id/681740
Notes: Idea raised by K. Parodi in 2016, hybrid concept, Compton imgagers in front-to-front cross-configuration to achieve highe efficiency in both PET and PGI
In parallel a similar system was developed by ourselves for nuclear astrophysics experimnets at CERN, thereby aiming at:
  Maximizing efficiency (

## Slide 5
Applicable to ion-range monitoring in proton-therapy?
High detection efficiency (500 cm2 PSDs)  Online real-time range verification
Low sensitivity to n-induced backgrounds (LaCl3, 6LiPE)  Improved S/B-ratio
Good performance in the g-ray energy range up to 5-6 MeV (thick crystals)
Compact & lightweight (TOFPET-ASICs)  Compatible with clinical environment
(…) propose an original combination of different techniques in a hybrid detection scheme, aiming to make the most of complementary imaging methods and open new perspectives of image guidance for improved precision of ion beam therapy.
…novel concepts of complementary PET and prompt gamma imaging in a so called hybrid detection scheme. As already observed in [58], a possible solution would be a combination of multiple Compton camera arms offering sufﬁcient solid angle over- age and using opposite single detector layers to serve as Compton camera scatterers or PET coincidence identiﬁers, complemented by additional absorbers for Compton imaging or total energy check in PET operation (Fig. 3). …
K. Parodi, Nucl. Instr. Meth. A (2016)
HYMNS ERC-CoG https://cordis.europa.eu/project/id/681740
Hadron therapy: concept of hybrid Compton-PET imaging for ion-range verification
Notes: -Review work by James Krimmer: most important aspects in the CC design are 1) high efficiency and 2) low sensitivity to backgrounds

## Slide 6
J.Krimmer’ Review on PGI, 2018:
High detection efficiency (500 cm2 PSDs)  Online real-time range verification
Low sensitivity to n-induced backgrounds (LaCl3, 6LiPE)  Improved S/B-ratio
Good performance in the g-ray energy range up to 5-6 MeV (thick crystals)
Compact & lightweight (TOFPET-ASICs)  Compatible with clinical environment
Hadron therapy: concept of hybrid Compton-PET imaging for ion-range verification
HYMNS ERC-CoG https://cordis.europa.eu/project/id/681740
Applicable to ion-range monitoring in proton-therapy?
Notes: -Review work by James Krimmer: most important aspects in the CC design are 1) high efficiency and 2) low sensitivity to backgrounds

## Slide 7
i-TED Comtpon imagers applied to ion-range monitoring: A MC study
BP
SOE
AA
AA
J. Lerendegui-Marco, J. Balibrea-Correa, et al. (CDP), Scientific Reports (2022)
MC
14N
12C
15O
16O
SOE: A. Andreyev et al., Phys. Med. Biol. 43 (2016)
AA: T. Tomitani et al. Phys. Med. Biol. 47 (2002)
120 MeV
2x1010 p
Table: Efficiencies per incident proton at 10 cm from beam axis. E.g. x108 for total statistics/spot in realistic case.
Notes: - Study/summarize nature paper

## Slide 8
Hybrid Compton-PET imaging: first Proof-of-Concept measurements at CNA-Seville
J. Balibrea-Correa et al., Eur. Phys. Jour. Plus 137 (2022).
Beam off
1 graphite layer (2mm)
5 layers of PMMA (100 mm)
Beam off (PET of PMMAs)
Beam on (CC Graphite)
Beam on
PET
Beam-off
PMMA layers
(100 mm)
p-beam
18 MeV
i-TED.B
i-TED.A
511keV
511keV
4.4 MeV
Compton
Eg = 4.4 MeV
Beam-on
C-disk (2mm)
Graphite downstream (- 6cm)
Graphite centred (0 cm)
Proton beam
Proton beam
 First experimental demonstration of in-room hybrid Compton-PET concept with proton beams
Dx(CC) = 1.2(9) mm
24.71(9) mm FWHM
Dx(PET) = 1 mm
6.4(6) mm FWHM
Notes: -POC measurements at CNA 18MeV only two CCs

## Slide 9
First hybrid Compton-PET imaging with i-TED in clinical conditions at HIT Heidelberg
Clinical proton-beam energy (50-200 MeV)
Clinical proton-intensity (2x109 p/point)
Notes: - Clinical conditions study at HIT, four CCs in sequential configuration

## Slide 10
First hybrid Compton-PET imaging with i-TED in clinical conditions at HIT Heidelberg
J. Balibrea-Correa, J. Lerendegui-Marco, et al. (HIT, USe) (publication in preparation)
Compton
PET
Hybrid Compton-PET
Notes: - Promising results, analysis ongoing

## Slide 11
Next steps: Hybrid Compton-PET and “multimessenger” approach: combining gamma-rays and neutrons MCIN-PDC2021-12536-C21
Next measurements planned at Quironsalud, Madrid in july 2023,
Future access to an experimental proton-therapy room, like the one foreseen at Santiago dC, would be an excellent opportunity!
ICPO
Collimator: Brass collimator 65mm thickness and 55 mm circular aperture
Phantom: 34×40×35 cm³ water phantom
Clinical dose: 3.5 Gy at the entrance of the phantom
Energies: 100, 150 and 200 MeV
Time structure: spots 10 ms width, 10 ms beam-off (approx)
Prev. Talk by A. Tarifeño “Neutron dosimetry in particle therapy facilities: status of the LINrem project”
4x i-TED CCs in cross-config:
DACQ synchro LINrem & CC:
LINrem
1xi-TED CC
Notes: - Combine PGI-PET with time-resolved neutron dosimetry, aim is to explore relationship and gather more information about the relationship between primary (proton) and secondary (neutron) dose

## Slide 12
Summary & Outlook
We have developed an array of four Compton cameras optimized for high detection sensitivity and low neutron-induced backgrounds, whith potential applications in ion-range monitoring for proton-therapy treatments
MC Simulations [Lerendegui22], as well as previous review studies (Krimmer’18) show the relevance of large efficiency and low neutron backgrounds to aim for real-time ion-range monitoring
First proof-of-concept measurements for the hybrid Compton-PET approach [Parodi2016] have been carried out with two CCs in front-to-front configuration at the CNA cyclotron using 18 MeV proton beam, delivering excellent results for both PET and Compton imaging [Balibrea23]
Measurements have been made with four CCs in front-to-front configuration at HIT Heidelberg, using p-, He- and C-beams at clinical energies and intensities. Data analysis is in progress and preliminary results are quite satisfactory.
Next steps involve new measurements (in plan at Quironsalud in july 2023 at Madrid), thereby aiming at four CCs in cross-configuration and time-synchronization with 3He-based neutron dosimeters (LINrem) for exploring the interplay between primary and secondary dose
A dedicated experimental proton-therapy room at Santiago de Compostela would be highly beneficial for future R+D+I works and developments!!!
Notes: -Highlight the need for a dedicated experimental room for proton-therapy experimentation, developments and innovation

## Slide 13: Backup slides

## Slide 14: The concept of Total-Energy Detector with g-imaging
DE/E = 3.5%
Dr=1mm
DE/E = 6.5%
Dr=3mm
V.Babiano et al., NIM-A (2019)
i-TED requirements for (n,g) experiments with enhanced S/B-ratio

## Slide 15
SiPM
(sensL ArrayJ-30065-P-PCB)
LaCl3(Ce)
[White reflector]
P. Olleros et al., JINST 13-P03014 (2018)
P.Olleros, TFM@HYMNS, Avail. https://hymnserc.ific.uv.es
<DE/E> = 4.5% @ 662keV
Technical implementation of Compton imaging for (n,g) experiments
J. Balibrea-Correa et al. (CDP), NIM-A 1001 (2021) 165249
Support Vector Machine (linear kernel) Python sklearn-learn
Size: 50x50 mm2
Crystal Thickness (mm)

## Slide 16
i-TED requirements for (n,g) experiments with enhanced S/B-ratio
J. Balibrea-Correa et al. (CDP), NIM-A 1001 (2021) 165249

## Slide 17: Improved Compton imaging algorithms
Back-projection [1]
Very Fast
Poor resolution
Poor peak to background
Analytical algorithm[2]
Computational costly
Improved resolution
Huge improvement in peak/background
Na-22 source, 1274 keV peak, i-TED @ 100 mm
SOLUTION: GPU-BOOSTING
Back to computation times similar to BP
[1] Wilderman, S. J., et al. DOI:10.1109/NSSMIC.1998.773871 (1998)
[2] Tomitani et al., DOI: 10.1088/0031-9155/47/12/309 (2002)
ARM(BP) = 11º  ARM(AA) = 5º

## Slide 18
DoI
reconstructed DoI coordinates for the central scan position
reconstructed DoI coordinates for a peripheral scan position
The measured values for Aw at half maximum
(already calibrated)
are compared against MC calculated DoIs and
true or ideal simulated DoI values.
i-TED: intrinsic position resolution Dr FWHM / DOI
V.Babiano et al, NIM-A 931 (2019)
Notes: Examples of reconstructed DoI coordinates for the central scan
position (a-c) and for a peripheral scan position (d-f). In each case the 2D
(x; y) positions as reconstructed using a NN-algorithm are shown (a,d) and the
corresponding calibrated DoI distributions are shown in panels (b,e). The distribution of 3D-coordinates is shown in (c,f).
DoI-calibrated from the measured area (Aw) of the scintillationlight distribubion at half maximum (red-line histogram). MC simulation of
DoI values without broadening (dashed-line histogram) and with 5 mm fwhm
broadening (blue-line histogram).
The prominent peak in the
experimental distribution arises from γ-ray hits near the optical window (large DoIs), where most of the charge above hw is
concentrated in just one single pixel of the Si-PM. This leads
to a slight overestimation of events with large DoI-values.

## Slide 19
i-TED: intrinsic position resolution Dr FWHM / SUMMARY & COMPARISON
V.Babiano et al, NIM-A 931 (2019)
Notes: Examples of reconstructed DoI coordinates for the central scan
position (a-c) and for a peripheral scan position (d-f). In each case the 2D
(x; y) positions as reconstructed using a NN-algorithm are shown (a,d) and the
corresponding calibrated DoI distributions are shown in panels (b,e). The distribution of 3D-coordinates is shown in (c,f).
DoI-calibrated from the measured area (Aw) of the scintillationlight distribubion at half maximum (red-line histogram). MC simulation of
DoI values without broadening (dashed-line histogram) and with 5 mm fwhm
broadening (blue-line histogram).
The prominent peak in the
experimental distribution arises from γ-ray hits near the optical window (large DoIs), where most of the charge above hw is
concentrated in just one single pixel of the Si-PM. This leads
to a slight overestimation of events with large DoI-values.

## Slide 20: HYMNS: High sensitivitY Measurements of key stellar Nucleo-Synthesis reactions
Full i-TED = 4S+4A= 500 cm2
Readout: 1280 channels (!)
PETsys Electronics S.A. (Customized)
i-TED Demonstrator
R.Bugalho et al., JINST_079P_0918
 # pixels= 8x8y = 64 ch
 pixel size = 6x6 mm2
 area = 5x5 cm2 = 25 cm2
LaCl3
SiPM
PSDs: 10 mm (S) and 25 mm (A)
g EFFICIENCY
f RESOLUTION
distance
distance
variable
Sample
Patent PCT/ES2016/070916 “Focusable Compton Camera”, 21/12/2016 - WO 2017/109256 Al (CDP et al.)
YMNS

## Slide 21
i-TED Total Energy Detector with g-ray imaging capability
Efficiency at 662 keV
q-resolution at 662 keV
Back-projection Compton test:
FoV: 2/3x2p sr
V.Babiano et al., NIM-A (in review, 2019)

## Slide 22
i-TED applied to Hadron Therapy: A MC viewpoint
J. Lerendegui, J. Balibrea, et al. (CDP), Nat. Scientific Reports (2022)
MC
14N
12C
15O
16O
120 MeV
2x1010 p
14N
12C
15O
16O
J.M. Verburg, J.Seco, Phys. Med. Biol (2014)

## Slide 23
High detection efficiency, high CR-capability  Real time
Low sensitivity to n-induced backgrounds  Improved S/B-ratio
Good E- and spatial resolution  Few mm accuracy
Suitable performance in the gamma-ray energy range up to 5-6 MeV
Compact & lightweight  Compatible with clinical environment
i-TED applied to Hadron Therapy: A MC viewpoint
Best ML algorithms Boosted Decision Trees (XGBoost) and ANN (Tensorflow), out of kNN, Logistic Regression, SVM, Gaussian Naive Bayes, RandomForest, AdaBoost and Quadratic Discriminant Analysis
Trained with 5x1010 g-rays in 200keV-7MeV Energy range, using r1(x1,y1,z1), r2(x2,y2,z2), E1, E2, Compton angle, KN-formula
Classifier Output: 0 (Non FEE) or 1 (FEE)
Accuracy between 65% (6MeV) and 73% (1MeV), Confussion: 35-40% of Non FEE predicted as FEE.
S/N ratio enhanced between 1.5 and 2.1
Capable of rejecting 50% of neutron events (neutron sensitivity)
J. Lerendegui, J. Balibrea, et al. (CDP), Nat. Scientific Reports, 2021

## Slide 24
Neutrons in HT: the role of a CC optimized for low neutron sensitivity
J. Krimmer et al. NIM-A (2018)

## Slide 25
i-TED applied to HT: A MC constrasted with neutron measurements at CNA-Seville
High detection efficiency, high CR-capability  Real time
Low sensitivity to n-induced backgrounds  Improved S/B-ratio
Good E- and spatial resolution  Few mm accuracy
Suitable performance in the gamma-ray energy range up to 5-6 MeV
Compact & lightweight  Compatible with clinical environment
J. Lerendegui, et al. (CDP), NIM-A (in prep.)
7Li(p,n)
Neutron events
Background
J. Lerendegui, J. Balibrea, et al. (CDP), Nat. Scientific Reports 2022

## Slide 26
Key aspects of CC for PGI in HT:
Efficiency ( i-TED array 4 CCs of large S.A.)
Background rejection ( i-TED low Neutron Sensitivity)
Precision for the falloff determination in 1D profile
C = contrast
FW = Falloff width
B = Background level
Falloff Retrieval Precision:
FRP = B1/2/C = 1/N1/2
[ Falloff width has no impact  (non Bragg-peak PGs and broad e+ distributions (PET) are ok)]
Neutrons in HT: the role of a CC optimized for low neutron sensitivity

## Slide 27
Compton 4x i-TED
Compton & PET 4x i-TED
12C(p,*)12N (11ms)
100 MeV
95 MeV
Sub-mm range verification!
Beam
Beam
Beam
Simultaneous Compton and PET imaging with i-TED in-situ in clinical conditions at HIT Heidelberg

## Slide 28
Latest upgrades: portability (wheels), adjustability (slider arms), new CPU