## Slide 1: Higher Order Modes Based Beam Phase Study: Simulations and Measurements
The work is supported partly by EuCARD2 with Grant No. GA 312453
Presenter: L. Shi (U. Manchester / CI / DESY)
Members: N. Baboi (DESY), R.M. Jones (U. Manchester), T. Wamsat (DESY),
U. Mavric (WUT)
ICFA Mini Workshop on High Order Modes in Superconducting Cavities 2016

## Slide 2: Outline
  A brief introduction to the European XFEL and Higher Order Modes
  Principle of beam phase determination
  Simulations with circuit model
  Measurements with a broadband setup
  Summary and Outlook

## Slide 3: Introduction to the European XFEL
Commissioning of the European XFEL Injector, Frank Brinker, IPAC2016, PP1044
Notes: No additional space.

## Slide 4: Introduction to Higher Order Modes (HOM)
When beam transverses a cavity, wakefields
are excited. These fields are classified into monopole, dipole, quadrupole modes etc.
Monopole modes dominate the longitudinal wakefield:
Dipole modes dominate the transverse wakefield:
R. Wanzenberg, TESLA 2001-33, 2001.
Measured Quantity 
Measured Quantity 
Bunch charge
Bunch offset

## Slide 5: TESLA Cavity and HOM spectrum
TESLA Cavity (1.3 GHz)
HOM Spectrum
B. Anue, Phys. Rev. ST Accel. Beams 3, 092001.
Monopole band occupies ~ 2.4 GHz with 70 MHz (2.38-2.45 GHz) bandwidth. The last two modes are with higher R/Q
(~ 70 Ω).
Monopole modes

## Slide 6
  Introduction
  Principle of beam phase determination
  Simulation with circuit model
  Measurements with a broadband setup
  Summary and Outlook

## Slide 7: Field Control inside a cavity
FEL operation requires high stability of RF amplitude and phase. Requirements are derived from beam properties:
  Energy spread
  Emittance
  Bunch length
  Arrival time
 | Amp | Phase
FLASH | 0.01% | 0.01 degree
E-XFEL | 0.01% | 0.01 degree
C. Schmidt, IPAC 2013, WEPME009
Phase 0 is defined as on crest.

## Slide 8: How to determine the beam phase?
signal
signal
Flat top of RF field inside cavity
from HOMs can be used to define beam
arrival time and the phase relative to this
time for 1.3 GHz signal can be calculated.

## Slide 9: Signal strength estimation
Assume the gradient is 20 MV/m and 0.5 nC bunch charge
  Beam induced fundamental mode: 2*0.5nC*2.08V/pC = 2080 V;
  Beam induced high order monopole mode 2*0.5nC*0.6V/pC = 600 V;
  Direct measurement of the fundamental mode (induced from klystron and beam) needs a large dynamic range.
  The fundamental mode signals from HOM couplers are comparable to that of damped higher order modes.
TESLA cavity simulation
Mode | Loss factor
Pi (1.3 GHz) | 2.08 V/pC
TM011 (2.4499GHz) | 0.08 V/pC
TM011 (2.4419GHz) | 0.60 V/pC
TM011 (2.4539GHz) | 0.57 V/pC

## Slide 10
  Introduction
  Principle of beam phase determination
  Simulation with circuit model
  Measurements with a broadband setup
  Summary and Outlook

## Slide 11: A single chain coupled circuit model
A single chain of coupled parallel LC circuit is used to facilitate the beam phase monitor development.
1
|CM – MAFIA|
(1)

## Slide 12: Beam driven circuit model
Mode 8
Mode 9
Circuit is truncated to nine cells.
It is then driven with delayed Gaussian pulses.
The last two modes are excited strongly, and are used for beam phase calculation.
Notes: Add beam Gaussian pulse

## Slide 13: Resolution study - Circuit model
Vary the sampling frequency, while keeping other parameters constant
Vary the noise level, while keeping other parameters constant
By comparing phases calculated from two HOM couplers, resolution can be estimated.
The resolution clearly depends exponentially on the noise present in the system.
The resolution also depends on the sampling frequency.
In order to meet the 0.01 degree requirement, the SNR is at least 35 dB
0.01°

## Slide 14
  Introduction
  Principle of beam phase determination
  Simulation with circuit model
  Measurements with a broadband setup
  Summary and Outlook

## Slide 15: Experimental Setup
  HOM signals are available from HOM Patch panel.
  A fast scope (TDS6604B) with 20 GS/s, 6 GHz bandwidth is connected for two channels for HOM signals.
  A 10 Hz external clock is used to synchronize the measurement.
  The data from DOOCS and from scope are combined at TCP/IP Client
  Each triggered event takes
  ~ 20s

## Slide 16: Estimation of Noise based on SVD
S contains the singular values associated with the signal
Top 24 singular values are used to reconstruct the signal. The rest is regarded as noise.
The noise level is approximately 8 mV in RMS. SNR is ~20 dB for HOM1 and ~10 dB for HOM2.

## Slide 17: Resolution over charge
Experiment（20 GS/s）@22MV/m, 0.5 nC
Beam phase is varied at 0, -5, and 5 degree from DOOCS.
The beam charge was varied from 0.1 to
1 nC with a step of 0.1 nC
The simulation data was scaled with real measurements.

## Slide 18: HOM Phase vs LLRF result
RMS error is 0.4 degree
RMS error is 0.3 degree
Phase was changed from -10 to 10 degree with a step of 1 degree.
Up to a calibration offset, the probe phase agrees with the phase from HOM.
Note the measurement system is not fully synchronized.

## Slide 19: Resolution limit estimation
Minimal detectable thermal noise:
Energy deposited in a monopole mode: with 0.5 nC
By assuming 0.5 power coupling, the SNR is approximately 136 dB, which suggests ~ degree resolution.
By scaling the power of simulation signal based on measurements, the difference between simulation and measurement is 0.05 degree.
Simulation data with 0.5 nC and 20 GS/s

## Slide 20: Electronics of HOM based Beam Phase Monitor
1290-1310 MHz
1690-1710 MHz
2400- 2460MHz
The electronics are compact and can be used for beam phase and beam position
measurements.
It fully complies with MicroTCA.4 standard.
Notes: A

## Slide 21: Possible topologies of final system
Process at the front end and transmit the results over long distance.
Transmit the signal over long distance and process in the middle
Accelerator Module
Process unit
BKR
Longer cable
to different site
Vicinity of the module
Process unit
BKR
+ Less influence from the intermediate units
- Radiation protection
+ No need for radiation protection.
- Signal integrity issue
Accelerator Module

## Slide 22: Summary and Outlook
Circuit model aided the development of beam phase monitor.
At least 35 dB SNR is required to achieve 0.01 degree resolution.
SVD method is used to estimate noise level. Simulation and measurements agree well with each other.
Beam phase based on HOM is consistent with the phase from LLRF.
Signal power optimization is required to further improve the resolution.
The hardware development for the beam phase monitor is ongoing.
It is promising to integrate the monitor into LLRF system.

## Slide 23
Thank you for your attention!