## Slide 1: Development of Ultra-sensitive, Low Background Detector Technology for 10meV to GeV Dark Matter
Matt Pyle
Nobel Symposium on Dark Matter
8/25/23

## Slide 2: Don’t Put All Your Eggs in One Basket: Broaden the Search
10-22 eV
keV
1019 GeV
10 GeV
WIMPS
Dark Sectors: DM w/ New Mediators
This Talk
We’re still searching for high
mass WIMPs with noble gas
TPCs
Well motivated theoretical
models at other mass scales
US Cosmic Visions: New Ideas in Dark Matter: 1707.04591

## Slide 3: Light Mass DM Direct Detection Design Drivers

## Slide 4: Light Mass DM: Nuclear Recoil Direct Detection Constraints
?
There are basically no Direct Detection constraints. Why?
2203.08297
Typical Neutrino cross section

## Slide 5: Light Mass DM Design Drivers: Exposure
Interaction Rate scales with 1/MDM
Light Mass Dark Matter Search experiments are tabletop and have small project cost scales: <10M
?

## Slide 6: Kinematics: 2 Body Elastic Nuclear Scattering
Transfer of DM kinetic energy to nucleus is really inefficient for elastic 2 Body Scatters when Mn >> MDM
DM
When Mn>> MDM

## Slide 7: Light Mass Dark Matter: Elastic Nuclear Scattering
Design Driver #1: Energy Sensitivity
1 meV
<v> -
Vesc --

## Slide 8: It’s not quite this daunting …

## Slide 9: Inelastic e- Recoils in Semiconductors
Band Diagram for Si
Energy [eV]
Momentum
4.5x10-10 m
Crystal e- Momentum and Energy Scales Match MeV DM perfectly
DM
3 keV/c

## Slide 10: DM- Coherent Vibrational Interactions
For DM interactions with small momentum and energy transfers, we need to start thinking about DM interactions producing coherent crystal excitations!
<v> -
Vesc --
Single Phonon Regime
Multiphonon
Regime
2205.02250
Coherent Vibrational Excitations in Si
1712.06598

## Slide 11: Light Mass DM: Detector Design Driver #1: Energy Sensitivity
2203.08297
Typical Neutrino cross section
1. Energy Sensitivity

## Slide 12: Athermal Phonon Detectors
TES (W or IrPt)
Athermal Phonon Collection Fins (Al)
Crystal (Si,Ge,GaAs,SiO2,Al2O3)
1 cm
1 cm
To increase TES sensitivity, lower Tc and volume
1 cm

## Slide 13: The Challenge: Environmental Noise
Lowering Tc and decreasing Vtes, doesn’t just increase sensitivity to DM, it drastically increases sensitivity to all environmental power sources
To increase your sensitivity by x10, you need to decrease your susceptibility to environmental DC backgrounds by x100!

## Slide 14: Environmental Upgrades: IR
TES bias power decreased as we heated the still … we had an IR leak
x20 improvement with the addition of a 2nd IR tight can
Future: redesigning both cans for further IR tightness
Bias Power vs Still temperature
Bias Power [fW]
Still Temperature [mK]

## Slide 15: Environmental Upgrades: EMI Mitigation
Steal copper powder filter from Martinis, Devoret, Clarke (PRB 35.4682 1987) for the 4K and still stages. Currently in Fabrication. Test performance improvements in a few months.
By 2024, we’ll be largely finished with EMI upgrades
Measure EMI shielding effectiveness with 200Hz modulation of 800MHz EMI leakage seen
~x20 decrease in external GHz scale radiation susceptibility by tightening 300K faraday cage (just 2 weeks ago)
200Hz amplitude modulation of 800MHz EMI

## Slide 16: Current Detector Performance
1% of surface covered with TES based athermal phonon detectors
Wirebond support structure
  Mechanical vibration decoupler
  No frictional rubbing at interface between clamp and detector
  Minimal stress structural support
Tc ~50mK (not the lowest Tc device)
Prototype 1cm2x1mm Si pixel athermal phonon detector for HeRALD Superfluid He dark matter search

## Slide 17: Single Optical Photon Calibration
SPICE/HeRALD Preliminary
Calibrate detector with 405nm and 450nm
Photon bunches delivered by fiber
First time to see optical photon quantization in macroscopic phonon detectors without Luke-Neganov Gain
2212.12513

## Slide 18: 1) Achieved Energy Sensitivity
Measured Energy Sensitivity: phonon = 273 meV
CRESST Si Performance (2212.12513)
  phonon = 1360meV

## Slide 19: Significant Sensitivity Improvement Possible
Completely dominated in signal band by an unknown broadband power noise source
x5 Excess Noise

## Slide 20: Light Mass DM: Detector Design Drivers
2203.08297
Typical Neutrino cross section
1. Energy Sensitivity
2. Backgrounds
& Discrimination

## Slide 21: Mysterious Low Energy Excess
2207.09375
CRESST Background Studies
Expected Radiogenic Backgrounds
Seen in all calorimeter experiments to varying degree
?
SiO2 0.35g
LiAlO2 11g
Al2O3 16g
Al2O3 16g
CaWO4 24g
CaWO4 24g

## Slide 22: 1. Doesn’t vary with crystal mass or type
2207.09375
CRESST Background Studies
What does it scale with? Surface area? Sensor Volume?
SiO2 0.35g
LiAlO2 11g
Al2O3 16g
Al2O3 16g
CaWO4 24g
CaWO4 24g

## Slide 23: 2. Variation with time since cooldown
Warm up to 11K and 19K due to fridge issues
E. Queguiner
Thesis

## Slide 24: 3) Low Energy Excess is Non-Ionizing
From J. Gascon /EDELWEISS
EDELWEISS interleaved detectors measure both phonons (NTD) and ionization production
Large no ionization background of unknown origin out to pretty high energies

## Slide 25: Low Energy Excess Fact Summary
 | SPICE/CDMS | EDELWEISS | CRESST
1) Doesn’t vary with crystal volume/ type |  |  | Yes
2) Variation with time since cooldown (and/or time since fabrication) | Yes | Yes | Yes
3) Non-Ionizing | Yes | Yes | 
4) Same above /below ground | mostly | mostly | 
These facts are incredibly restrictive

## Slide 26: Stress Induced Microfractures?
Detector
Detector
Detector under stress due to thermal contraction,manufacturing, etc.
Detector relaxes releasing phonon energy
arXiv:physics/0504151

## Slide 27: Stress Related Microfractures: High Energy Evidence
CRESST had a sapphire ball support structure that tightened due to thermal contraction
Not an exact match to low energy excess:
  Events 100keV –MeV scale
  Non-poissonian rate distribution
Change in support structure mitigated events
arXiv:physics/0504151

## Slide 28: Stress Related Microfractures: 1st Low Energy Evidence
Glued Down with GE varnish
(High Stress)
Hanging (low stress)
2 orders of magnitude difference in rate between high stress (glued) and low stress (hanging) device
2208.02790

## Slide 29: Mitigation for Stress Induced Microfracture Events: GET RID OF ALL STRESS
Support Structure
Sensor Films
Stress on “Bare” Crystal Surface

## Slide 30: Understanding Source of Relaxation Events: 2 Channel Devices
Energy in Channel 1 [eV]
Energy in Channel 2 [eV]
0.25% 2 Channel Device
Microfractures in metal films should have assymmetric energy collection
Microfractures from bare surface/bulk should have symmetric energy collection
We see both symmetric and assymmetric relaxation events

## Slide 31: Noise in 2 Channel Device
We have both correlated and uncorrelated noise between the 2 channels

## Slide 32: Correlated Noise: Phonon Origin
Excess correlated noise has phonon collection pole
Peaks:EMI, microphonics…

## Slide 33: Uncorrelated Noise: Sensor Fluctuations
Noise event in TES/QET

## Slide 34: Excess Noise decreases with time
Excess noise is just shot noise from below threshold relaxation events!

## Slide 35: Low Energy Excess Summary
We see 2 classes of relaxation event excess both above and below threshold (shot noise)
Noise event in TES/QET
Next Step: understand the precise source of each background and mitigate

## Slide 36
Quantum Computing: Quasiparticle Poisoning
Superconducting quantum circuits (qubits) see anomalously short decoherence times partially due to high density of quasiparticles (QP, broken Cooper pairs)
  Lots of sources of excess QPs: radioactivity, muons, IR…
  In 2102.00484, excess quasiparticle density decreased as a function of time
This behaves identically to the low energy excess
Solve excess QP problem, allow quantum computers to make big step forward
arXiv: 2102.00484
Mannila et. al.

## Slide 37: Can one discriminate between relaxation backgrounds and Dark Matter Interactions? Julien’s talk

## Slide 38: Conclusions
Light Mass Dark Matter Design Drivers
  Energy sensitivity
  Relaxation Backgrounds
Below threshold relaxation backgrounds dominate our noise
Future:
  We are really close to precisely understanding the source of relaxation backgrounds
  Significant filtering upgrades will be implemented this coming year

## Slide 39: Backup

## Slide 40: TESSERACT Discrimination: Superfluid Helium
Superfluid Helium: it’s a liquid … no stress microfractures
Multiple Pixel Coincidence for He DM events discriminates DM from pixel microfractures
Pulse Shape Discrimination: Helium is slow!
Design Driver #2:
Mitigation plan
Discrimination plan
Surface
Underground
Stretch
Goal
Goal
Required
Al2O3
He

## Slide 41: Observational Evidence for Dark Matter
Notes: Main Idea: 1 slide showing all the observational evidence for dark matter

## Slide 42: Dark Matter & Particle Physics
US Cosmic Visions: New Ideas in Dark Matter: 1707.04591
Quarks
Bosons
Leptons
?
?
?
?
?
?
?
?
Dark Sector
Visible Sector
Portal
What are its properties?
  mass
  Is it charged under a new force(s)?
  How was it generated?
Can this knowledge help us understand the laws of physics at high energies?

## Slide 43: Midgal and Ionization

## Slide 44: Ionization Production in eV Scale Nuclear Recoils
<v> -
Vesc --
𝛳=180
Xenon
Si
No Ionization expected from elastic nuclear recoils for
MDM < O(200MeV) in Si
MDM < O(GeV) in Xe
NR Ionization << ER ionization
?
?

## Slide 45: Midgal Ionization
Knapen
Search for DM using NR interactions that share momentum and energy between nucleus and e-
Xe
Si

## Slide 46: Midgal Ionization: Signal Suppression
Knapen
Midgal, like all processes with off-shell particles, will have significantly suppressed signal rates
x106 greater exposure needed if exposure limited
x106 less backgrounds needed if background limited
x106 Penalty in Signal

## Slide 47: Developing Ultra-Sensitive Detector Technology

## Slide 48: 100meV Excitation Sensitivity -> Low Temperature Detectors
300K = 26meV
To sense 100meV excitations we’ll need to cool the detector down to near absolute zero
Use superconducting detector technology
  Transition Edge sensors
  MKIDs
  SNSPD (only for photon applications)
  Quantum Capacitors / QUBIT (THIS IS YOU GUYS)

## Slide 49: The Simplest Thermal Calorimeter
R
T
Transition Edge Sensor (TES): A superconducting metal film (W) that is externally biased so as to be within its superconducting/normal transition

## Slide 50: TES Sensitivity
~ Intrinsic Thermal Noise of Calorimeters

## Slide 51: TES Scaling Laws & Optimization
Minimize Temperature
  Dilution Refrigerators can cool detectors to 5mK
  Tc -> 1.5x Tbath
Minimize Heat Capacity
  Small Volume

## Slide 52: 100meV Threshold TES are really small!
𝜎theory ~ 20meV
Tc = 20mK
V = 275umx275umx40nm
= 3 x10-9 cm3
= 60ng
1 gram of active target mass -> 15M channels
TES can only be used by themselves when photon collecting over a very small area (true for MKIDs and most other sensor technology too)

## Slide 53: 2nd most simple thermal calorimeter
Couple the sensor to a large volume insulator -> low heat capacity

## Slide 54: Problem: Decoupling between the Sensor and Absorber
As T is decreased, it’s harder and harder to keep the sensor thermally coupled to the absorber
Energy leaks out of the absorber through Gab before its measured
TES sensitive to power fluctuations through Gtb
Physical clamps that support the absorber
Kapitza boundary conductance scale as as T3
e-/phonon thermal conductance scales as T4

## Slide 55: Athermal Phonon Sensor Technology
Collect and Concentrate Athermal Phonon Energy into Sensor
R
T

## Slide 56: Excitation Detectors & Volume Scaling
PMT
Scintillator
Reflector
Will these detectors have the same energy sensitivity?
Yes, if:
Lifetime of the athermal excitation (photon) is really long
Excitation absorption dominated by sensor
PMT
Scintillator

## Slide 57: Optimizing the Athermal Phonon Excitation Detectors
TES
Absorber
TES
Absorber
Minimize the number/volume of the TES sensors instrumented on the surface to the point that you begin to see the bare surface thermalization rate

## Slide 58: Athermal Phonon Sensor Sensitivity Scaling
Power Noise for various G
Phonon Power Noise [W/rtHz]
G
Lower 𝑣sensor (lower Tc) if 𝑣signal < 𝑣sensor
Lower 𝑣signal (decrease Al coverage) if 𝑣signal > 𝑣sensor
You can always say on VTc3 scaling (in principle)
45mK-> 10mK: 2eV -> 20meV

## Slide 59: Athermal Phonon Thermalization at Surfaces
Athermal phonon surface thermalization probability found to depend upon
  Crystal
  Surface roughness
  Surface cleanliness
(W. Knaak et al, Phonon Scattering in Condensed Matter V,1986)
0.1%-1% of the crystal surface covered with athermal phonon sensors … 1/1000-1/100 thermalization probability needed
Si, Ge -> ok

## Slide 60: Quantum Sensor?
The basic concepts of the athermal phonon detector are sensor agnostic
  ballistic bouncing of athermal phonons for long times
  Concentration and collection of QP
Just replace the TES
Quantum Sensor

## Slide 61: TESSERACT Discrimination: GaAs
To discriminate zero charge phonon only events in GaAs ER DM detector, one can require photon+phonon coincidence
Design Driver #2 (Backgrounds)
  Mitigation Plan
  Discrimination Plan
Scattering via Light Dark Photon

## Slide 62: TESSERACT Discrimination: Polar Crystal
Energy Channel 2
Film 0QLEE
DM
Dark Matter
Film OQLEE
DM
If stress is occurring in phonon sensor films, energy will preferentially deposited in a single channel
Design Driver 2 (Backgrounds)
  Plan to mitigate
  Plan to discriminate
Energy Channel 1
1
2

## Slide 63: NRDM Search Sensitivity @ Surface
Surface
Underground
Stretch
Goal
Goal
Required
Al2O3
He
Achieving pre-project energy threshold goals leads to world leading science @ surface

## Slide 64: Nearly everything the same
Having multiple targets with complementary DM science (NRDM, ERDM, Absorption) and orthogonal risks doesn’t increase cost (time & money) significantly since almost everything is identical (phonon sensor development, wiring, electronics, DAQ, data handling, processing, and analysis software) except the substrate.

## Slide 65: 1) HeRALD:Helium Roton Apparatus for Light Dark matter
 | Required Threshold | Goal Threshold | Stretch Goal Threshold
Si 4cmx4cm | 6.7eV | 900 meV | 12 meV
He | 21 eV | 570 meV | 24meV
Stretch
Goal
Required
Surface
Underground
#1 Design Driver for Light Mass Dark Matter Searches: Energy Sensitivity

## Slide 66: 2) SPICE: GaAs ERDM
Scattering via Light Dark Photon
“CRESST for ERDM”
1kgyr
No Backgrounds
1607.01009
 | Required (5 ) | Goal (5 ) | Stretch Goal (5 )
Ge | 2.3 eV (3 ) | 300 meV () | 12 meV
GaAs | 4.6 eV | 600 meV | 24meV
Ge |  |  | 12 meV
GaAs | 4.6 eV | 600 meV | 24meV
Ge
1meV 10meV 100meV 1eV 10eV
NR
Optical
ERDM
900meV
~600meV
GaAs
~35meV

## Slide 67: 3) SPICE: Sub-ev Polar Interactions Cryogenic Experiment
Scattering via Light Dark Photon
1kgyr
No Backgrounds
1910.10716
/SiO2
In ionic crystals, optical phonons are oscillating electric dipoles! Couple strongly to dark photons!
SiO2
10meV 100meV 1eV 10eV 100eV
NR
Optical
Phonon/ER
60meV
149meV
60meV
90meV
Al2O3
 | Required Threshold (5 ) | Goal Threshold (5 ) | Stretch Goal Threshold (5 )
SiO2 | 3.5eV | 350 meV | 20meV
Al2O3 | 3.5eV | 350 meV | 20meV
SiO2 | 3.5eV | 350 meV | 20meV
Al2O3 | 3.5eV | 350 meV | 20meV
Required
Stretch
Goal