## Slide 1: New Results from HAYSTAC's Search for Dark Matter Axions
Michael Jewell
Yale University
UCLA Dark Matter, March 2025

## Slide 2: Talk Outline
Introduction to HAYSTAC Experiment
Recent Results from Phase II Operations
Plans for HAYSTAC Phase III and Beyond

## Slide 3: Axion Dark Matter
Axions solve CP Problem + Dark Matter
https://cajohare.github.io/AxionLimits/docs/ap.html

## Slide 4: Axion Dark Matter
Axions solve CP Problem + Dark Matter
Post inflation models >10 μeV
https://cajohare.github.io/AxionLimits/docs/ap.html

## Slide 5: High Frequency Challenge
Fridge
Cavity
AMP
Rod
Solenoid
B-Field
Axion

## Slide 6: High Frequency Challenge
Fridge
Cavity
AMP
Rod
Solenoid
B-Field
Axion

## Slide 7: HAloscope at Yale Sensitive To Axion CDM
Located at Yale’s Wright Lab
Copper Microwave Cavity
  V: 1.5L
  : 3.6-5.8GHz
  Q: ~45k
8T Superconducting Solenoid
Dilution Fridge ~60mK
Josephson Parametric Amplifier (JPA)
Cavity
Tuning Rod

## Slide 8: Josephson Parametric Amplifier (JPA)
Tunable LC Resonator
Phase sensitive amplifiers
Allow for manipulation of squeezed states
Pump tone:

## Slide 9: Squeezed State Receiver (SSR)
Pump
SQ
AMP
Vacuum
Squeezed Vacuum
+ Cavity Noise
(+Axion Signal)
Amplify SQ Quad

## Slide 10: Bandwidth Enhancement
SQ off, overcoupled
cavity noise
reflected noise

## Slide 11: Bandwidth Enhancement
SQ off, overcoupled
cavity noise
cavity noise
reflected noise
reflected noise
SQ on, overcoupled

## Slide 12: Bandwidth Enhancement
SQ off, overcoupled
cavity noise
cavity noise
reflected noise
reflected noise
SQ on, overcoupled
S =
~2x Speed
M. Malnou et al., Phys.Rev.X 9 (2019)
K.M. Backes et al Nature 590 (2021)

## Slide 13
2015
2016
2017
2018
2019
2020
2021
2022
2023
2012
2013
2014
2024
2025
Phase I (Single JPA)
Phase II (SSR)
Design/Construction

## Slide 14
2015
2016
2017
2018
2019
2020
2021
2022
2023
2012
2013
2014
2024
2025
Phase I (Single JPA)
Phase II (SSR)
Design/Construction
PRL 118 (2017)
PRD 97 (2018)

## Slide 15
2015
2016
2017
2018
2019
2020
2021
2022
2023
2012
2013
2014
2024
2025
Phase I (Single JPA)
Phase II (SSR)
Design/Construction
Nature 590 (2021)
PRD 107 (2023)
arXiv:2409.08998 (2024) – Accepted to PRL
PRL 118 (2017)
PRD 97 (2018)

## Slide 16: Talk Outline
Introduction to HAYSTAC Experiment
Recent Results from Phase II Operations
Plans for HAYSTAC Phase III and Beyond

## Slide 17: New HAYSTAC Data
Roughly 3x previous Phase II coverage
New Data
Name |  | Initial Scan [days] | Int. Time [min] | Freq. Range [GHz] | Coverage [MHz] | Sensitivity | Publication
Phase II | a | 106 | 60 | 4.100-4.178 | 73 | 1.95 | Nature 590 (2021)
 | b | 53 | 60 | 4.459–4.523 | 64 | 2.06 | PRD 107 (2023)
 | c | 72 | 20 | 4.523–4.707 | 184 | 3.04 | arXiv:2409.08998 (2024) Accepted to PRL
 | d | 111 | 20 | 4.178–4.459 | 229 | 3.06 | 
Name |  | Initial Scan [days] | Int. Time [min] | Freq. Range [GHz] | Coverage [MHz] | Sensitivity | Publication
Phase II | a | 106 | 60 | 4.100-4.178 | 73 |  | Nature 590 (2021)
 | b | 53 | 60 | 4.459–4.523 | 64 |  | PRD 107 (2023)
 | c | 72 | 20 | 4.523–4.707 | 184 |  | arXiv:2409.08998 (2024) Accepted to PRL
 | d | 111 | 20 | 4.178–4.459 | 229 |  | 

## Slide 18: Mock Axion Signal Injection
Axion expected to have Maxwell Boltzman lineshape
Frequency hopping used to mimic this shape
6 injections during Phase IIc/d
All signals recovered
Observed power follows expected SNR
Axion Model
Data (CS)
Data (GS)
Antenna/rfl port
Cavity
Weak/tx port
Y. Zhu, et. al, RSI, 10.1063/5.0137870 (2023)

## Slide 19: Environmental RFI
12 RF large signals detected
  Large (> 5sigma)
  Filtered by Cavity Profile
  Some persisted upon rescan
  Very narrow (<1kHz)
  Many exhibited transient behavior
~80kHz

## Slide 20: Identification of RFI
RF “veto” receiver deployed in lab
All 12 had corresponding signal
Likely man made RFI
  4-5GHz is popular communication band
RF
IF
LO

## Slide 21: Results from Phase II
Phase II covered 550MHz of unexplored parameter space
  With 413MHz covered in new data
  Remaining gaps are inaccessible due to mode crossings
No evidence of an axion signal
90% Aggregate exclusion over all Phase II
Joint
Aggregate
PIIa/b
PIIc/d (new data)

## Slide 22: Final Exclusion
Combined with Phase I we have covered ~750 MHz in the 4-6GHz mass range
Accepted to PRL
arXiv:2409.08998 (2024)

## Slide 23: Squeezing Performance
SSR maintained enhancement over wide range
Scan Rate Enhancement:
Expected SRE ~2.0x given losses
  Average Enhancement of 1.7x
  Some regions with ~1.3x

## Slide 24: Vibrational Noise
Pump
SQ
AMP
Vacuum
Squeezed Vacuum
+ Cavity Noise
(+Axion Signal)
Amplify SQ Quad
Cavity vibrations can cause “dephasing” of squeezed state
Can reduce squeezing if effect is large enough

## Slide 25: Mitigating Vibrations & Phase II Details
Xiran Bai: Recent Results and Status of HAYSTAC Phase III Upgrades

## Slide 26: Talk Outline
Introduction to HAYSTAC Experiment
Recent Results from Phase II Operations
Plans for HAYSTAC Phase III and Beyond

## Slide 27: Beyond Phase II
P-IIIa
Rev.Sci.Instrum. 92 (2021)
P-IIIb
arXiv:2411.18914 (2024)

## Slide 28: Beyond Phase II
P-IV
P-IIIa
Rev.Sci.Instrum. 92 (2021)
P-IIIb
arXiv:2411.18914 (2024)
Lehnert Group:
Y. Jiang et al., PRX Quantum 4 (2024)

## Slide 29: Beyond Phase II
P-IV
P-V
P-IIIa
Rev.Sci.Instrum. 92 (2021)
P-IIIb
arXiv:2411.18914 (2024)
Lehnert Group:
Y. Jiang et al., PRX Quantum 4 (2024)
van Bibber Group

## Slide 30: ALPHA Experiment
Claire Laffan: Current Status of ALPHA's Search for Dark Matter Axions Between 10-20GHz

## Slide 31: Conclusion
HAYSTAC has continued to search for axions with > 10 μeV
Recently concluded Phase II operation
  Covered 550 MHz between 4.10GHz and 4.71GHz
  Excluding axions
Exploring new cavity and receiver designs to push to higher frequencies
Planning new run with a multi-rod cavity this year between 6-7GHz

## Slide 32: Thanks

## Slide 33: Backups

## Slide 34: RFI Veto

## Slide 35: Rescan Candidate Summary

## Slide 36: RF Deficits
A handful of “deficits” are observed
Power Excess > 5.1 sigma but negative
Unknown source but none have persisted upon rescan
f. [KHz]
f. [KHz]

## Slide 37: PIIIa: Multi-Rod Cavities
7-Rod Cavity gives higher TM010 frequency in same volume
Maintains high figure of merit
M. Simanovskaia, et al., Rev. Sci. Instrum. 92 (2021)

## Slide 38: PIIIb: Photonic Band Gap (PBG)
Intruder TE modes removed
TM010 mode confined still
D. Goulart et al. , arXiv:2411.18914 (2024)
With PBG
Without PBG

## Slide 39: Limiting Factor
SSR is limited by loss between two JPAs
  Loss is dominated by triple junction circulator
  4dB of Squeezing is roughly best we can do currently
SQ
AMP
Vacuum
Squeezed Vacuum
+ Cavity Noise
+ Vacuum
Amplify SQ Quad
M. Malnou et al., Phys. Rev. X 9, 021023 (2019)

## Slide 40: PIV: New Receiver Designs
Cavity Entanglement And Swapping Experiment For Improved Readout Efficiency (CEASEFIRE)
Solves the problem of loss between JPAs
Scan Rate Enhancement >8x quantum limited searches
SQ
AMP
Y. Jiang et al., PRX Quantum 4 (2024)

## Slide 41: PV: Meta-Material Cavities
Use Wire Array Meta-Materials to decouple resonant frequency from physical size

## Slide 42: Quantum Limit for Haloscopes
AMP
Cavity Hamiltonian:
Vacuum Fluctuations:
C. M. Caves. Phys. Rev. D, 26 1817-1839, (1982)
H. A. Haus and J. A. Mullen. Phys. Rev., 128 2407-2413, Dec 1962.
Linear Amplifier:
Total SQL:

## Slide 43: Josephson Parametric Amplifier (JPA)
Phase Sensitive Amplifier
Can operate in Phase Insensitive Mode
  Near Quantum limited amplifiers
Phase sensitive mode can produce “Squeezed” States
Pump tone:
AMP

## Slide 44: Axion Classifications
Ciaran O'Hare, Axion Limits, https://cajohare.github.io/AxionLimits/
Post-inflation axion: theoretically calculable from string production mechanisms.
Mass: 1 μeV – 1 meV
Typical Measurement: Cavity haloscopes
Pre-inflation axion – wide range of viable masses. “GUT-scale” axion.
Mass: 20 peV – 1 μeV
Typical Measurement: Lumped element detectors

## Slide 45: JPAs in HAYSTAC
JPA Shield
JPA Coils
JPA

## Slide 46: JPAs in HAYSTAC
JPA Shield
coil current [mA]
Frequency [GHz]

## Slide 47: HAYSTAC Timeline
Name |  | Amplifier | Dates | Freq. Range | Sensitivity | Publication
Phase I |  | Phase Insensitive | Jan. 2016 – Jan. 2017 | 5.6–5.8 GHz | 2.70 | Phys. Rev. D 97 (2018)
Phase II | a | Phase Sensitive | Sept. 2019 – April 2020 | 4.100-4.178 GHz | 1.95 | Nature 590 (2021)
 | b |  | July 2021 – Nov. 2021 | 4.459–4.523 GHz | 2.06 | PRD 107 (2023)
 | c |  | Sept 2022 – May 2023 | 4.523–4.707 GHz | 3.04 | arXiv:2409.08998 (2024)
 | d |  | June 2023 – Aug. 2024 | 4.178–4.459 GHz | 3.06 | 
Name |  | Amplifier | Dates | Freq. Range | Sensitivity | Publication
Phase I |  | Phase Insensitive | Jan. 2016 – Jan. 2017 | 5.6–5.8 GHz |  | Phys. Rev. D 97 (2018)
Phase II | a | Phase Sensitive | Sept. 2019 – April 2020 | 4.100-4.178 GHz |  | Nature 590 (2021)
 | b |  | July 2021 – Nov. 2021 | 4.459–4.523 GHz |  | PRD 107 (2023)
 | c |  | Sept 2022 – May 2023 | 4.523–4.707 GHz |  | arXiv:2409.08998 (2024)
 | d |  | June 2023 – Aug. 2024 | 4.178–4.459 GHz |  | 
Two Phases
  Phase I: Single JPA, Phase-Insensitive Measurement
  Phase II: Two JPAs, Phase-Sensitive Measurement

## Slide 48: Tuning with SSR
Five parameter optimization
JPAs tuned to match Cavity Resonance
  : Squeezer Flux Bias
  : Amplifier Flux Bias
Amplifiers share same Pump Source
  : Amplifier Gain
  A: Squeezer Gain
  : Phase difference
AMP
SQ
A
Pump 2

## Slide 49: Tuning with SSR
Five parameter optimization
AMP
SQ
A
Pump 2

## Slide 50: Improvements for Phase IIb
Higher Frequency JPAs
New pair of JPAs to extend frequency above 4.2GHz
Reduced DAQ Deadtime
Improved DAQ routine to reduce deadtime from in-situ processing (1.6x speed up)
 | Fractional Time [%] | 
 | Phase IIa | Phase IIb
DAQ | 40 | 10
Tuning | 12 | 8
Livetime | 48 | 82
SQZ JPA
AMP JPA

## Slide 51: Detector Calibration

## Slide 52: System Diagram

## Slide 53: First Demonstration
Demonstration by Colorado Group
SSR speed up for “Fake” Axion signal
M. Malnou et al., Phys. Rev. X 9, 021023 (2019)
S =
2.1x Speed