## Slide 1: MicroTCA Development and Status
Kay Rehlich
DESY
Real Time Conference 2016
June 9 2016
Notes: How to edit the title slide
Upper area: Title of your talk, max. 2 rows of the defined size (55 pt)
Lower area (subtitle): Conference/meeting/workshop, location, date, your name and affiliation, max. 4 rows of the defined size (32 pt)
Change the partner logos or add others in the last row.

## Slide 2: Motivation and Outline
1.6 km cold accelerator
XFEL start
The used standard
Architecture
  Hardware
  Software
1993
2016
FLASH
+ FLASH 2

## Slide 3: From VME to MicroTCA
Most cables from rear
Interne Clock & Trigger distribution
Redundant fans
Redundant power supply optional
Modern, high-speed data transfer
Excellent signal quality
Since 1993

## Slide 4: PICMG Standards “Telecom Computing Architecture”
Single
Double
AMC.0
MTCA.0
> 150 Mitglieder
MTCA.4

## Slide 5: MicroTCA.4: Compact and Modular Design
Cables from rear side
Space for ….
See MTCA.4.1
Redundant:
Power
Fan
© Elma

## Slide 6: MTCA.4: Clocks, Triggers und Interlocks
MTCA.4 Backplane
Ethernet
MCH
Trigger
Clock
Timing
From central timing
CPU
Trigger
Interlock
Clock
Clock
Interlock
Machine
Protection
System
ADC
Digi. IO
Controller
….
Common modules
Application modules
LLRF
Diagnostics
Cpl. Interlocks
Laser
…

## Slide 7: Timing System: Synchronization of all Subsystems
RJ45
LVDS
x2timer /
NAMC-psTimer
receiver / transmitter / repeater
Transmitter Piggyback with 3 channels of link drift compensation
Fiber IO

## Slide 8: Timing System: Versatile IO
RJ45
LVDS
Optional RTM
backplane
AMC
9 Lemo outputs (50 Ohm):
Triggers, Clocks, Data
3 channels with 5ps resolution
9 SFP outputs:
with length compensated fiber links
9 Fiber outputs (ST):
Triggers, Clocks, Data
used for modulators
> 100 m
x2timer /
NAMC-psTimer
receiver / transmitter

## Slide 9: Timing System: Principle of Operation
Distributes:
  Triggers, gates, clocks (10ns … 5ps resolution)
  Bunch information (charge, destination,…), unique ID
Link drift compensation: Jitter ~10ps RMS
∿∿∿∿
1.3 GHz
∿
50 Hz
Clock
Trigger
Data
Generation
Delay
Delay
Controller
Fiber Cable
4 km
Clock
& Data
Recovery
Clock
Trigger
Data
Trigger
Transmitter
Receiver

## Slide 10: XFEL Injector Operation
In operation since Dec. 2015
Implements most of the XFEL subsystems:
  Klystron, Modulator, LLRF, BPM, Toroid, Magnet, Laser, Undulator, Vacuum, Water, Camera, Motor, Cryo, Timing, Protection, Dump, …
  DAQ system, middle layer servers, GUI programs and tools, …
> 3.3・106 control system properties online now (270 000 channels with history)
Photo Gun 2 superconducting acceleration modules (1.3 and 3.9 GHz) length: 45m

## Slide 11: XFEL Injector: 1. Diagnostics Crate
Rack Cooling
Gun

## Slide 12: XFEL Injector: Regelung der Hochfrequenz
Front
Rear

## Slide 13: MicroTCA Crate Inside the XFEL Tunnel
1 Klystron drives 4 Modules
MicroTCA Crates:
2 LLRF
2 Coupler Interlocks
1 Diagnostics
1 von 100
Superconducting
Accelerator Modules
LLRF MicroTCA Crate

## Slide 14: MicroTCA Remote Management
14
Display by standard controls tool jddd
Management
View
DOOCS
Control System
View

## Slide 15: MicroTCA Crate Management View
Shows all Crates in XFEL
Shows all Modules in
selected Crate

## Slide 16: DOOCS Control System Data Flow

## Slide 17: DOOCS Data Acquisition System
      Front-end
Toroid Server
Toroid 1
Toroid 2
DAQ
Ethernet
Fast Collector
Slow Collector
Buffer Manager
Shared Memory
Orbit
Server
Energy
Server
Other
Server
Writer
Feedback
Server
Disk
Tape
  Multicast to several
  DAQ instances
Configuration
Controller

## Slide 18: Analyze all Shots with Bunch Resolution
Fast Collector
Slow
Collector
Buffer Manager Shared Memory
Orbit
Server
Energy
Server
Other
Server
Writer
DAQ GUI
Jddd: GUI editor
MATLAB

## Slide 19: DAQ Maintenance Panel (Example: FLASH)
Storage
Streams
Attached
Processes
Data
Collectors
Distributed
Front-ends

## Slide 20: Summary
PICMG Standard
  Started 2009  MTCA.4 published 2011
    Q2 2016: MTCA.4.1 extensions
  Other projects can benefit from the standard
XFEL fast Diagnostics and Controls platform is
  Final installation > 200 MicroTCA.4 Crates
  Injector is fully operational since Dec. 2015
  Linac cool-down will start Oct. 2016
Critical Hardware and Software is successful in operation

## Slide 21: Thank you!
More info: doocs.desy.de