## Slide 1: System Demonstration of a Tracking Trigger using an Associative Memory Approach
Zhen Hu on behalf of Fermilab/LPC
Tracking Trigger R&D group, in collaboration with
21st IEEE Real Time Conference
Colonial Williamsburg, Virginia - USA

## Slide 2: Contents
Motivation
System overview
  Multiplex in space and time
  Associative Memory (AM) introduction
System demonstration
  Hardware introduction
  Demonstrator at Fermilab
  Performance
Summary

## Slide 3: History
Over the past few years, Fermilab in close collaboration with CMS institutions has established a generic R&D program
  Silicon-based Tracking Trigger based on Associative Memory approach
  The initial R&D concept was presented at Real Time 2012
  The initial hardware development was presented at Real Time 2014
Real Time 2018： excellent prototype results
  Allowed us to demonstrate at system level towards a working solution for the L1 tracking system in HL-LHC environment
  The techniques developed are rather generic and could have other applications far beyond tracking trigger, both within and outside HEP

## Slide 4: Physics Motivation: HL-LHC Trigger Upgrade
High Luminosity LHC in 2026
  40 MHz bunch crossing
  Up to 200 pileup (high occupancy)
  Tons of data
Current Level-1 Trigger will not work
  Current maximum bandwidth
    only 100 kHz (L1 output rate)
  For HL-LHC, current trigger system would give
    EG rate @25 GeV → 100 kHz
    Overall Trigger Rate → > > 1000 kHz (unsustainable) to reach physics goals
  Increasing trigger threshold → lose the opportunity of new physics with low threshold
Upgrade trigger system
  Must increase total bandwidth
  Must increase trigger capabilities
  Level-1 Tracking is a completely NEW handle
Notes: Competition between accelerator and detector

## Slide 5: Track trigger advantage and challenge
Silicon based tracking trigger is crucial for CMS Phase2 upgrade
  Sharp turn-on efficiency curve
  Background rate reduction → allows for low object threshold
Huge challenges
  How to handle readout of the entire tracker?
    260 M channel, 40 MHz, 100 Tbps data (after on-detector suppression using pT-modules), 2e4 hits
  4 μs latency:
    Data distribution, track reconstruction, track fitting …
  Silicon-based L1 tracking trigger has never been realized under these conditions
TP for Phase-II Upgrade
Red： without L1 tracking
Black: with L1 tracking
Notes: Competition between accelerator and detector

## Slide 6: Solution : divide and conquer
Data Formatting
/Delivery
Pattern Recognition
Track
Fitting
CMS Tracker
Data
Space parallel
  6*8 trigger tower
  100 Tbps → ~2 Tbps per tower

## Slide 7: Solution : divide and conquer
Space parallel
  6*8 trigger tower
  100 Tbps → ~2 Tbps per tower
Time parallel
  8x time multiplexing
  25 ns → 200 ns
Data Formatting
/Delivery
Pattern Recognition
Track
Fitting
CMS Tracker
Data
Huge amount of cabling work without ATCA
ATCA full mesh
Conventional
Associative Memory,
Hough Transform,
Tracklet,
… …

## Slide 8: Solution : Associative Memory
Associative Memory
  Based on CAM cells to match and majority logic to associate hits with a set of pre-determined hit patterns that represent allowed track trajectories (massively parallel, finishes right after all hits arrive)
Data Formatting
/Delivery
Pattern Recognition
Track
Fitting
Data
Layer 1
Address 4
Match
Layer 1
Address 4
Match
Match
Layer 3
Address 7
Match
Match
Layer 3
Address 7
Match
Match
Match
Match
Layer 3
Address 9
Match
Match
Match
Match
Layer 3
Address 9
Match
Match
Match
Match
Match
Match
Match
Match
Layer 2
Address 1
Match
Match
Match
Match
Layer 2
Address 1
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Layer 4
Address 4
Match
Match
Match
Match
Match
Match
Layer 4
Address 4
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Layer 2
Address 4
Match
Match
Match
Match
Match
Match
Match
Match
Match
Layer 2
Address 4
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Road!
A pattern
Implementation of a High-Performance Pattern Recognition Associative Memory in an FPGA
Jun 12, 2018, 09:30
Jamieson Olsen (Fermilab)

## Slide 9: Solution : Associative Memory
Associative Memory (AM)
  Based on CAM cells to match and majority logic to associate hits with a set of pre-determined hit patterns that represent allowed track trajectories (massively parallel, finishes right after all hits arrive)
Perfect tool to mediate the high pileup effect
  Avoiding the typical power law dependence of execution time on occupancy
Data Formatting
/Delivery
Pattern Recognition
Track
Fitting
Data
Before AM
After AM
Roads found
With AM
Without AM
occupancy
time
Layer 1
Address 4
Match
Layer 1
Address 4
Match
Match
Layer 3
Address 7
Match
Match
Layer 3
Address 7
Match
Match
Match
Match
Layer 3
Address 9
Match
Match
Match
Match
Layer 3
Address 9
Match
Match
Match
Match
Match
Match
Match
Match
Layer 2
Address 1
Match
Match
Match
Match
Layer 2
Address 1
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Layer 4
Address 4
Match
Match
Match
Match
Match
Match
Layer 4
Address 4
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Layer 2
Address 4
Match
Match
Match
Match
Match
Match
Match
Match
Match
Layer 2
Address 4
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Road!
A pattern

## Slide 10: FNAL based hardware R&D
ATCA shelf
The full mesh backplane interconnections effectively blur the distinction between FPGAs, and allow data sharing in both space and time

## Slide 11: FNAL based hardware R&D
ATCA shelf
Pulsar2b
Pulsar2b RTM (Rear Transition Module)
We tested the data transfer performance for the full mesh back plan, Pulsar2b and RTM (10 Gbps)
A custom ATCA full mesh enabled FPGA-based processor board
Designed with the goal of creating a scalable architecture abundant in flexible, non-blocking, high bandwidth interconnections
Pulsar3a: Next Generation ATCA Full Mesh General Purpose FPGA Based Processing Board
Jun 12, 2018, 10:10
Jamieson Olsen (Fermilab)

## Slide 12: FNAL based hardware R&D
ATCA shelf
ATCA Processing Blade: Pulsar2b
Pulsar2b RTM (Rear Transition Module)
PRM (Pattern Recognition Mezzanine Card)
IPMC (Intelligent platform management controller)
We tested the data transfer performance between PRM and Pulsar2b (10 Gbps) and the interconnection between two FPGAs in PRM (16 Gbps)

## Slide 13: FNAL based hardware R&D
ATCA shelf
ATCA Processing Blade: Pulsar2b
Pulsar2b RTM (Rear Transition Module)
IPMC (Intelligent platform management controller)
VIPRAM ASIC
(Vertically Integrated Pattern Recognition Associative Memory)
PRM (Pattern Recognition Mezzanine Card)
Currently we emulate AM with FPGA

## Slide 14: Full system demonstration at Fermilab
Using the technology today to demonstrate tracking trigger feasibility
For one Trigger Tower: two shelves fully loaded with Pulsar2b boards
Front view
Back view
Pattern Recognition Board (PRB) shelf
12 Pulsar2b with PRM Mezzanines
Bandwidth between any pair of Pulsars is 20Gbps
Data Source Board (DSB) shelf
12 Pulsar2b to Emulates the detector output of ~400 modules
120 QSFP+ fibers
Each with 4 bidirectional lanes each running at 10Gbps
Capable of sourcing up to 4.8 Tbps data with full shelf

## Slide 15: Full system demonstration at Fermilab
All Pulsar2b boards in the system are synchronized to a common master clock optical link
  Provided by a CERN TTCcx board that encodes a simulated LHC 40MHz bunch crossing clock and various control signals
  This optical link is received by one Pulsar2b board in each shelf
  From this Pulsar2b board the master clock and other control bits are distributed to other Pulsar2b boards in the shelf over dedicated clocks on the ATCA backplane

## Slide 16: Full system demonstration at Fermilab
Simulated event data is first loaded into the DSB FPGAs
When triggered by bunch crossing signal, data is transmitted over the 120 QSFP+ optical links at full speed to the PRBs in the upper shelf
The 12 PRBs receive the incoming data, perform sophisticated time multiplexed data transfers over the full mesh ATCA backplane
Finally the event data sent to the FMC Pattern Recognition Mezzanine (PRM) cards
(DSB)
(PRB)

## Slide 17: PRM firmware design
Slave FPGA is used to emulate associative memory
  Enables us to quickly evaluate and optimize the performance of the AM-FPGA interface and internal AM logic features
Implementation of a High-Performance Pattern Recognition Associative Memory in an FPGA
Jun 12, 2018, 09:30
Jamieson Olsen (Fermilab)
(hits)

## Slide 18: Demonstrator validation
Hardware and emulator perfectly matched
  Output from each stage validated bit-by-bit
With the full chain demonstrator, we have measured
  Latency, FGPA resource usage, efficiency, resolution
Data Formatting
/Delivery
Pattern Recognition
(PR)
Track
Fitting
(TF)
Data
Sourcing
(DS)
Full simulation & emulation software
PRB Firmware
PRM Firmware
TF Firmware
DS Firmware
Firmware in hardware demonstrator
PRBF2.txt
DS.txt
FiredRoads.txt
DS.txt

## Slide 19: Latency well within specs
Data Formatting
/Delivery
Pattern Recognition
Track
Fitting
Data
Sourcing
950ns
250ns
642ns
25ns
175ns
Data delivered to PRM starts/ends: @1.20 – 1.70 μs
Pattern Recognition output starts/ends: @1.84 – 2.34 μs
Track Fitting output starts/ends: @2.04 – 3.04 μs
PR
500 ns
642 ns
950 ns
DD
175 ns
TF
3042 ns
250 ns
500 ns
1000 ns
2542 ns (PU250)

## Slide 20: An example event in Vivado
4xTF, 7191.666 ns to 7716.666ns = 525ns, 126 clk @240MHz
A) Input Stubs
B) DO Stubs Input
C) PRM SSID Input
D) PRAM Road Output
E) DO SSID Input
F) Global Stubs
G) Track Candidate
Confirmed on Hardware
This is with a selected ttbar + PU200 event with high tail of combinations

## Slide 21: FPGA Resource Utilization (KU060)
Data Organizer only
Data Organizer and 8 Tracker Fitters
Very light weighted design
BlockRAM mainly used for DO
  TF does not increase BlockRAM usage, leaving enough room for TF
TF: modest increase in registers and DSP blocks
  Plenty of room for parallel copies of the fitter

## Slide 22: High efficiency up to PU250
System is robust against higher luminosity or increase in stub occupancy
  We demonstrate that the system reconstructs all tracks for events with PU250 within 2.5 μs (no truncation needed)
  Only for very high pT jet, truncation needed to meet the pipeline window
Tracking efficiency in ttbar+PU jets

## Slide 23: Resolution
Excellent performance for L1 trigger application
pT resolution
z0 resolution

## Slide 24: Summary
Demonstrated with a vertical slice
  Achieved excellent performance in terms of tracking efficiency and momentum resolution
  Very low total latency (2.5 μs): data dispatch to the trigger towers, pattern recognition, track fitting
The success of the demonstration system
  An existence proof of fast data delivery, fast pattern recognition and track fitting implemented using the full mesh ATCA and associative memory approach
  Technology advancements could lead to reduced size of the system in the future

## Slide 25
Backup

## Slide 28: Excellent hardware performance
ATCA shelf
  10 blades for parallel processing
  Full mesh backplane is a natural solution for time multiplexing
    All of the 56 bidirectional links among 8 Pulsar2b boards were tested at 10Gbps
Rear Transition Module
  10 QSFP bidirectional links
    10 Gbps per link achieved
PRM performance
  Communication between Pulsar2b and PRM FPGAs
    10 Gbps achieved
  Two latest generation of Xilinx FPGAs
    Interconnection achieved 16.3 Gbps
Notes: What is time multiplexing scheme

## Slide 29: AM Pattern and Bank
A pattern is a low resolution track
  Made of 1 superstrip (SS) per layer
    A SS is a group of adjacent strips
Fountain SS
More powerful AM => less demand on the FPGA
More powerful FPGA => less demand on the AM

## Slide 30: AM in FPGA: Overview
AM in FPGA: very closely follows the AM ASIC (chip) design
  Match two silicon tiers in ASIC with two modules in FPGA firmware
    CAM Tier -> a 2D array of Pattern Modules
    I/O Tier -> fired roads serialization and output
  Pipelined operation
    CAM tier: processes pattern matching with stubs for current event N
    I/O tier: outputs road addresses for event N-1 at the same time
CAM tier logic is optimized for 7-Series/UltraScale FPGA architecture

## Slide 31: Latency well within specs
Data Formatting
/Delivery
Pattern Recognition
Track
Fitting
Data
Sourcing
950ns
250ns
642ns
25ns
175ns
Data delivered to PRM starts/ends: @1.20 – 1.70 μs
Pattern Recognition output starts/ends: @1.84 – 2.34 μs
Track Fitting output starts/ends: @2.04 – 3.04 μs
PR
500 ns
642 ns
950 ns
DD
175 ns
TF
3042 ns
250 ns
500 ns
1000 ns
2542 ns (PU250)

## Slide 32: Demo with FPGA
Pattern 1
Pattern 2
Pattern 3
Pattern 4
Full pattern bank in ASIC (for a trigger tower)
Pattern 5
… …
… …
Pattern 1M
Pattern 6
Pattern 7
Event 1
fire
Event 2
Partial pattern bank demo in FPGA
Pattern 6
Pattern 7
Event 2
… …
… …
~ 100 patterns fired per event
… …
Test ~10-20 events at a time
  more than 1-2 bunch train worth, the rest is repeating
  only need ~1K patterns loaded at a time