## Slide 1: Introduction to EasyPET Exercise
Martin Grossmann :: Center for Proton Therapy :: Paul Scherrer Institute

## Slide 2: What is PET

## Slide 3
PET – Positron Emission Tomography
Back-to-back 511KeV photons are detected
Radionuclide decays, emitting +.
+ annihilates with e– from tissue, forming back-to-back 511 keV photon pair.
511 keV photon pairs detected via time coincidence.
Positron lies on line defined by detector pair (known as a line of response or a LOR).
Ring of Photon
Detectors
From Martin Purschke!

## Slide 4
Why PET is so cool
PET can be tailored to show metabolic processes in tissue
Remember, the chemical properties of a radioactive isotope are the same as the stable isotope – it will be used by the body indiscriminately
So you take a molecule that is used in your body for some process – sugar, dopamine, what have you, swap out an atom for a radioactive one
You get “hot spots” where lots of said molecules are used by the body
For example, a tumor that grows uses a lot of energy (sugar), so radioactively tagged sugar will accumulate a lot of activity there
Or tag molecules that the brain burns when it “thinks” – active areas show up as hot spots
Frequently used radiotracers are 11C and 18F (all beta+ = positrons)
From Martin Purschke!

## Slide 5
An Example - 18F
18F-FDG - Fludeoxyglucose is one of the commonly used radiotracers
It is a sugar, so it accumulates where the body burns a lot of energy (“uptake”)
Unusual “hot spots” can point to cancer
Whole-body PET scan using 18F-FDG to show liver metastases of a colorectal tumor
From Martin Purschke!

## Slide 6: PET image of the brain
Dopamine = chemical messenger in our body
Parkinson’s disease: dopamine production in the central brain not properly working
PET image using dopamine with F18 isotope

## Slide 7: Coincidence detection

## Slide 8: 2D PET image
LOR (lines of response) arranged into sets of 1-dimensional parallel projections

## Slide 9: 2D PET image
Back-Projection allows to reconstruct original source distribution

## Slide 10: Commercial PET scanner

## Slide 11: Commercial PET scanner

## Slide 12: EasyPET
2 detectors moving around the target

## Slide 13: LySO Crystals
Lutetium-yttrium oxyorthosilicate Lu2(1-x)Y2xSiO5
Scintillator crystal

## Slide 14: Silicon Photo Multiplier - SiPM
Solid state photon detectors
High gain, low voltage («bias»)
Very compact
Compatible with magnetic resonance imaging MRI

## Slide 15: Silicon Photo Multiplier - SiPM
Many institutes/companies are involved in SiPM production
  CPTA, Russia
  Amplification Technologies , USA
  Novel Device Laboratory (NDL), China
  Excelitas tech. (formerly Perkin-Elmer)
  National Nano Fab Center, Korea
  MePhi/Pulsar Enterprise, Russia
  Zecotek, Canada
  Hamamatsu HPK,, Japan
  FBK-AdvanSiD, Italy
  ST Microelectronics, Italy
  MPI-HLL, Germany
  Philips, Germany
  KETEK, Germany
  SensL, Ireland
  RMD, USA
Chart: Year
| 2001 | 2003 | 2005 | 2007 | 2009 | 2011 | 2013 | 2015
 | 11 | 42 | 124 | 335 | 701 | 1355 | 2545 | 3285
Papers on Google Scholar about «SiPM»

## Slide 16: Silicon Photo Multiplier - SiPM
SiPM is a High density (up to 104/mm2 ) matrix of diodes with a common output, working in Geiger-Müller regime
Common bias is applied to all cells (few % over breakdown voltage)
Each cell has its own quenching resistor (from 100kΩto several MΩ)
When a cell is fired an avalanche starts with a multiplicative factor of about 105-106
The output is a fast signal (trise~ ns; tfall ~ 50 ns) sum of signals produced by individual cells
SiPM works as an analog photon detector

## Slide 17: Silicon Photo Multiplier - SiPM
SiPM can be seen as a collection of binary cells, fired when a photon is absorbed
Counting cells provides information about the intensity of the incoming light
Dark Count Rate (DCR)
  Avalanche induced by thermal effects
  Depends on
    Temperature
    Sensor technology
    Bias voltage
Detector counts even without radioactive source

## Slide 18: EasyPET PCB
Channel 1
Channel 2
Analog output
Comparator signal
Coincidence signal

## Slide 19: DT5770 Multi Channel Analyzer (MCA)
Analyze pulses
Accept signal and trigger input
Readout with PC

## Slide 20: Multi Channel Analyzer (MCA)
Look at individual pulses
Acquire spectrum

## Slide 21: EasyPET GUI

## Slide 22: EasyPET GUI

## Slide 23: Handling radioactive sources

## Slide 24: Handling radioactive sources

## Slide 25: Handling radioactive sources

## Slide 26: Handling radioactive sources
Let your instructor do most of the source handling!
Minimize the time you are handling the sources directly
Maximize your distance from the sources during the experiment
When not needed store the sources in the lead castle (small desk in the corner)

## Slide 27: Na22
Sealed sources of Na22
β+ emitter
12 µCi activity
Emission of 511 keV from positron annihilation
Emission of 1274 keV from Ne22 in excited state

## Slide 28: EXERCISE

## Slide 29: Single Pulses

## Slide 30: Multi Photon Spectrum

## Slide 31: Gamma Spectrum

## Slide 32: PET image

## Slide 33: Two sources resolution

## Slide 34: Seminar Room PG 57