## Slide 1: Development and Test of a 48-optical Ports High Precision Clock Distributor Board
D. Calvet, E. Molina,
Irfu, CEA Paris-Saclay, France
denis.calvet@cea.fr
emmanuel.molina-gonzalez@cea.fr

## Slide 2: High Precision Clock Distribution, Hyper-K case
  Some physics experiment require larger and larger detection volumes and increasing channel counts
  Synchronizing electronics spread across large space with high precision (e.g. few 10’s ps) is required
  Example: next generation neutrino observatory Hyper-Kamiokande
  Constructed 1996; in operation
  50,000 ton water target
  39 m diameter x 42 m height
  ~12.000 phototubes
  Data taking from 2027
  260,000 ton water target
  68 m diameter x 71 m height
  ~20.000 phototubes
October 2023: completion of the excavation of the dome of the cavern (69 m diameter)

## Slide 3: Requirements for Hyper-K, System Architecture
  Distinct path for synchronization and DAQ
  Synchro. path: 125 MHz clock + 125 Mbps data min.
  Stable phase offset after system reconfiguration
  ≤100 ps rms clock jitter at all end-points
  Up to 1000-2000 end-points
  Two stage clock distribution tree
  48-port distributors to scale up to 2308 end-points
  Based on modern FPGAs and optical technology
Main requirements
Proposed architecture

## Slide 4: Beyond Common Clock Distribution Solutions
  Many designs rely on FPGA high-speed SerDes for clock and synchronous data distribution
  Clock and Data Recovery circuit (CDR) within SerDes block produces a copy of the transmitter clock
  WhiteRabbit, started at CERN, combines the idea with Ethernet. It’s standard, commercially available.
Present landscape
  Based on Super-K experience, Hyper-K, will have distinct clock and DAQ paths. Using a White Rabbit network solely for synchronization + a regular Ethernet network for DAQ does not seem judicious
  Available WR switch (v.3) is an aging product (Virtex 6); v.4 in development following its own planning
  → R&D on synchronization for Hyper K moved towards custom solutions developped internally
Why search for alternatives?
https://www.white-rabbit.tech/

## Slide 5: 48-Port Clock Distributor Board
Standard 1U x 19’’ enclosure
OLED
Display
Dual Gigabit Ethernet (GTR)
QSFP
(4 x GTH)
Dual
fan
Redundant 24 V input
RS485
Versatile Clock Mezzanine Card
Commercial
System-on-Module
(Trenz – Zynq UltraScale+)
Up to 48-SFP transceivers
  Small available number of high speed SerDes (4 GTH) assigned to high troughput interface while more numerous ordinary I/O’s drive up to 48 SFPs: 48 TX in 6 groups via 1:8 fanout chips + 48 individual RX
  Proprietary serial protocol implemented on UltraScale+ ISERDESE3/OSERDESE3 primitives
1:8 fanout chip

## Slide 6: Transmit Operation – Jitter Performance
  Depending on serializer inputs (8-bit x 125 MHz) various operating modes: clock up to 500 MHz, serial data up to 1 Gbps and sub-multiples rates
  6 TX groups of 8 SFPs can be set to a different mode independently
FPGA
500 MHz DDR
D0
D1
…
D7
Q
Data(7..0)
OSERDESE3
125 MHz
6
125 MHz
osc.
1→8
fanout
chip
×6
8
SFP
TXin
8
  TX mode: 125 MHz clock fanout
  SFP port #8: Rj < 10 ps Dj < 1 ps
  TX mode: 1 Gbps PRBS data
  SFP port #8: Rj < 15 ps Dj = 21.4 ps
  TX mode: 125 MHz clock duty cycle modulated by 125 Mbps PRBS data
  SFP port #8: Rj < 10 ps Dj = 1 ps

## Slide 7: Test Setup for Longer Term Measurements
  Logic based on ”Digital Dual Mixer Time Difference (DDMTD)” (used in WhiteRabbit) is implemented in FPGA to track phase shifts between local clock and echo clocks returned by TX to RX loop-back fibers
P. Moreira, P. Alvarez, J. Serrano, I. Darwezeh and T. Wlostowski, "Digital dual mixer time difference for sub-nanosecond time synchronization in Ethernet", in Proc. IEEE International Frequency Control Symposium, Newport Beach, CA, USA, 2010, pp. 449-453

## Slide 8: Distributed Clock Phase Variations Over 1 Week
  Group of 8 ports in 125 MHz clock distribution mode
  TX to RX loopback on 8 ports by 150 m MMF fibers
  200 ps p.p. drift measured; 6 °C p.p. temperature var.
  Histogram of reference clock to echo clock phase differences on one port (125 kHz measurement rate)
  Spurious peak, 4 orders magnitude smaller than main, probably caused by imperfections in DDMTD logic, but no other deviant points

## Slide 9: Adding a Programmable Delay on TX Path
  ODELAYE3 set to perform 12 delay steps of 100 ps
  Expected delay jumps verified with an oscilloscope
  Phase steps also correctly measured by DDMTD logic
FPGA
500 MHz
DDR
D0
D1
…
D7
Q
Data(7..0)
OSERDESE3
125 MHz
6
1→8
fanout
chip
8
SFP
TXin
×6
8
125 MHz
osc.
Oscilloscope
Differential probe
O/E converter
125 MHz
clock
ODELAYE3
Fixed or
modulated
1 ns
  UltraScale+ OSERDESE3 can be followed by a 512-tap calibrated delay line, ODELAYE3, cascadable up to 3. Delay tap resolution: 2.1-12 ps
Results obtained with DDMTD logic
1 ns

## Slide 10: Clock Fanout Phase Regulation with ODELAYE3
  Demonstrator set for 125 MHz clock fanout
  1 TX port drives 150 m SM fiber + 1:8 optical splitter looped-back to 8 RX ports
  All hardware placed in a climatic chamber set at 0°C to 30°C in 4 steps of 10°C
Measured clock distributor board temperature
Phase 125 MHz reference to 8 clocks looped backed (DDMTD method)
Phase regulation OFF
Phase regulation ON
  Designed a corrector on embedded processor tuning ODELAYE3 to stabilize distributed clock phase drift
  For 30°C variations: delay variations ~1.2 ns without regulation and ~6 ps with regulation

## Slide 11: Simultaneous Serial Data Reception and Clock Round-trip Monitoring on FPGA Ordinary Inputs
  Previous tests use loop-back clock on RX port to measure phase difference with the reference. But recovered clock not provided by serial data receiver made from ordinary FPGA input pins.
  How an ordinary FPGA input pair can simultaneously receive serial data and monitor echo clock phase?
  Proposed solution: use specific encoding to introduce a fixed periodic pattern, e.g. ”01” in the serial stream
  Send user data bits followed by their complement at the next cycle
Receiver
input
Clock at
(F-DF)
Resulting
signal
Magnified periodic pattern – keep to trigger DDMTD block
Oscillating pattern – remove with a digital filter

## Slide 12: Dual Function Receiver on a Differential Input
Digital filter removes oscillating part of serial stream sampled at (F-∆F)
Deserializer oversamples received serial input at x2 rate.
For 3 adjacent positions, logic calculates how close are received groups of bits from the plausible pattern
Decision logic selects the optimal set of samples and adjusts the sampling offset if necessary
  PRBS pattern sent is verified at receiver using an Integrated Logic Analyzer (ILA) in FPGA fabric
  Measured 500 MBd serial stream embedding 125 MHz periodic pattern and 125 Mbps user data (coding efficiency: 25%)
FPGA diff. IN
diff. OUT buffer

## Slide 13: GTP Transceiver Reception from OSERDESE3
  Typically, FPGA ordinary I/O’s and high speed SerDes overlap in the 500-1500 Mbps region
  Example shown uses 250 Mbps user data with Manchester encoding leading to 500 Mbd on media
  Instead of comma insertion, user data are XOR’ed with a framing pattern to align received data
GTP
SerDes
31.25 MHz
Pattern
Comparator
Logic
16
RESET
31.25 MHz
PLL
125 MHz
Manchester
Decoder
16
8
Word
Converter
4 Phase
Identifier
2
125 MHz
De-serializer
This blocks checks if the framing pattern is found, and resets the GTP until success
When synchronization has been gained, this clock has a fixed offset with that of the framing pattern on the sender side
This block labels each of the four 125 MHz cycles that come when multiplying by 4 the 31.25 MHz recovered clock
This block converts incoming 8-bit words @31.25 MHz to outgoing 2-bit words @125 MHz preserving the original word boundaries and phase alignment
This block converts the 2-bit words @125 MHz stream into the original data frame and extracts its different field content
OSERDESE3
Manchester
Encoder
4
XOR
2
250 MHz
DDR
SFP
SFP
User Data
Framing
pattern
“11110000”
2
2
250 Mbps
serial data
500 Mbd
Sender OSERDESE3
Receiver GTP
125 MHz
This blocks XOR’s user data with a constant framing pattern used by the receiver to delineate parallel data words

## Slide 14: GTP Transceiver Reception from OSERDESE3
  At 500 MBd, a GTP in 16-bit parallel interface mode produces a 31.25 MHz recovered clock
  Recovered clock can have 16 possible phase offsets, 2 ns apart, compared to the 500 MHz serial clock
  For deterministic latency, select the only recovered clock that makes the framing pattern appear at output
  At link startup, GTP is reset until the recovered clock has the desired phase offset (probability p = 1/16)
  Probability of correct synchronization after exactly N trials: p * (1 – p)(N-1)
Number of trials to reach proper alignment
User data reception checked with Integrated Logic Analyzer
Artix 7 GTP receiver used for interoperability tests with OSERDESE3 sender

## Slide 15: 8B/10B Serial Transmission with OSERDESE3
  For precise clock distribution applications, logic and clock domain crossings must have fixed latency
  How can this be implemented?
  8B/10B is a popular method for serial communication. Supported in FPGA high-speed transceivers
  FPGA I/O SerDes in most recent devices, e.g. Xilinx UltraScale+, only support serialization factor 2:1, 4:1 and 8:1 but no longer 5:1 or 10:1 (Xilinx 7 family). User has to build the equivalent function in fabric
10:1
PISO
PLL
1250 MHz
1.25 GBd
8B/10B
encoder
10
8
125 MHz
GTx Transceiver
FPGA fabric
User
data
8:1
PISO
PLL
1250 MHz
1.25 GBd
8
8B/10B
encoder
8
125 MHz
OSERDESE3
FPGA fabric
Gear
box
10
156.25 MHz
User
data
FPGA high speed transceiver scheme
FPGA ordinary I/O scheme

## Slide 16: Deterministic Latency 10B-8B Gear Box
  Clocks are edged aligned every 4 periods of clock A (125 MHz) and 5 periods of clock B (156.25 MHz)
  40 bits parallel data transferred from Register A to B when both clock edges are aligned (31.25 MHz)
8B-10B Encoder
10
8
40
125 MHz
User data
8
8:1 PISO
156.25 MHz
625 MHz DDR
40-bit Register A
Shifts by 10 bits every 8 ns
40-bit Register B
Shifts by 8 bits every 6.4 ns
1.25 GBd
CLK_125
CLK_156_25
Data 0
-1
-1
Encoded data 0
Data 1
0
0
Encoded data 1
Data 2
Encoded data 0
1
1
Encoded data 0
Encoded data 2
Data 3
Encoded data 1
3
2
2
Encoded data 1
Encoded data 3
Data 4
Encoded data 2
Encoded data 0
4
3
4
5
Encoded data 2
Encoded data 4
Data 5
Encoded data 3
Encoded data 1
Byte 4
Byte 3
Byte 2
Byte 1
Byte 0
Encoded data 3
Encoded data 5
Data 6
Encoded data 4
Encoded data 2
Byte 4
Byte 3
Byte 2
Byte 1
5
6
Encoded data 4
Encoded data 6
Data 7
Encoded data 5
Encoded data 3
Byte 4
Byte 3
8
6
7
Encoded data 5
Encoded data 7
Data 8
Encoded data 6
Encoded data 4
Byte 4
7
9
Encoded data 6
Encoded data 8
Data 9
Encoded data 7
Encoded data 5
Byte 8
Byte 7
Byte 6
Byte 5
Byte 9
8
10

## Slide 17: Clock Cycle Numbering Logic for Gear Box
  PLL generates clock at frequency of greatest common divisor of two other clocks. Divide it by 2 in logic
  Detect rising edges of this toggling signal to send SET signals to the counters numbering clock cycles
PLL
125 MHz
156.25 MHz
31.25 MHz
125 MHz
D
Q
31.25 MHz
toggle
D
Q
D
Q
AND
125 MHz
Mod 4 Counter
SET
toggle
D
Q
D
Q
AND
156.25 MHz
Mod 5 Counter
SET
toggle
(15.625 MHz)
Input clocks
Numbered clock cycles

## Slide 18: Fixed Latency 8B/10B Encoder on OSERDESE3
  Deterministic latency upon board power cycling verified using a debug pin of the sender FPGA
  Demonstrates capability of UltraScale+ HP I/O for deterministic latency 8B-10B encoding @1.25 Gbd
  Pathway to implement synchronous Gigabit Ethernet on plain FPGA I/O’s (only TX part shown here)
  Serial line rate: 1 Gbps user data; 1.25 Gbd on fiber
  Optical probe with bandwidth limited to 2.5 GHz
  TX stream: idle commas (K28.1); Messages: start comma (K28.0) + 32-bit counter (4 Data symbols)
  Correct data reception and decoding in oscilloscope

## Slide 19: Sending 250 Mbps Data on top a 125 MHz Clock
  Advantage of clock duty cycle modulation for data transport: clock extraction by ordinary PLL (no CDR)
  D. Calvet, “Clock-Centric Serial Links for the Synchronization of Distributed Readout Systems”, IEEE Trans. Nucl. Sci., Vol. 67, N°8, pp. 1912-1919, Aug. 2020
8:1
PISO
PLL
625 MHz SDR
625 MBd
4
Encoder
125 MHz
OSERDESE3
FPGA fabric
Gear
box
5
156.25 MHz
User
data
“01”
D0
D1
Fixed
header
2
3
Data
Symbol
00
01
Data
Symbol
10
11
Timing content
Data content
  650 MBd stream is 125 MHz clock with modulated duty cycle: 20%, 40%, 60%, 80%
  2 bits of user data per 8 ns period, i.e. 250 Mbps
  A scrambler shall be used to keep DC balance

## Slide 20: Summary and Perspectives
  Successful contruction of a 48-port clock distributor demonstrator
  Using FPGA I/O primitives for serial communication with deterministic latency are a viable option
  After review, the Hyper-K collaboration opted for a synchronization system composed of custom-made distributors arranged in a 2-stage tree
  The 2nd stage distributors (Lpnhe) and end-points (INFN) will use the traditional and more established approach based on high speed FPGA SerDes (1 Gbps net bandwidth + 8B-10B encoding)
  The 1st stage distributor (Irfu) will re-use some of the concepts and techniques developed in this R&D
    Same overall architecture
    Number of optical port reduced to 32
    Serial communication using FPGA I/O’s
    Additional low speed I/O’s at rear panel
Hyper-K First Stage Clock Distributor board (in design)