## Slide 1: Machine Learning for Sub-Microsecond Edge Data Processing
Audrey Corbeil Therrien
Berthié Gouin-Ferland, Mohammad Mehdi Rahimifar, Quentin Wingering, Ryan Coffee
24th IEEE Real Time Conference – Quy Nhon, Vietnam

## Slide 2: Sensor Challenges in Physics
Channel density
Size
Rate
Infrastructure
Storage
Therrien, Applied Optics 61 (8), 2022

## Slide 3: Sensor Challenges in Physics
Detector
Online analysis nodes
Disks
Detector
EdgeML
Online analysis nodes
Disks
Source
DAQ
(ASIC/FPGA)
Therrien, Applied Optics 61 (8), 2022

## Slide 4: CookieBox
Ne
Energy Levels (0-127)
Channel
Photoelectron count
Event from the CookieBox
Hartmann, Nature Photonics 12, 2018
Li, Optics Express,26, 2018

## Slide 5: CookieBox
experimental hutch
4 Sub-spikes
2 Sub-spikes
3 Sub-spikes
Linac Coherent Light Source II (LCLS-II)
1 MHz X-ray pulses
TB/s generated by experiments
The CookieBox
Buffers
TB/s
< 1µs analysis
<TB/s

## Slide 6: Required Analysis
Energy Levels (0-127)
Channel
Photoelectron count
Event from the CookieBox
time
Number of sub-spikes
Energy spectrum per channel
Analog output from MCP
<1 µs
Gouin-Ferland, Frontiers in Physics 10, 2022

## Slide 7: Input Processing for Neural Network
7 bits
5 bits
Photoelectron count
Minimizes the quantization error
Reduces image size
Energy (eV)
Photoelectron count
Raw
Uniform
Optimized
Reduce input bit depth
Reduce input image size
Reduce model size
Lower latency!
Gouin-Ferland, Frontiers in Physics 10, 2022

## Slide 8: Neural Network
NN model | FCNN 5 bit | CNN 5 bit
Parameters | 3,433 | 3,665
Accuracy | 84% | 86%
Loss | SCC | SCC
Optimizer | Adam | Adam
Learning rate | 0.001 | 0.001
Batch size | 256 | 256
Gouin-Ferland, Frontiers in Physics 10, 2022
Input
32x16
Flatten
5
Softmax
Output
1x5
32
RELU
32
RELU
4
RELU
Rahimifar, Mach. Learn.: Sci. Technol., under review
FCNN 5 bit Prediction

## Slide 9: FPGA Synthesis
Aarrestad, T. et al, 2021
DOI: 10.1088/2632-2153/ac0ea1
Synthesis
Keras NN Model
HLS
Model
Data preprocessing
algorithms
HLS
Modules
HLS4ML Configuration
HDL optimization
Monitoring/
Communication
Rahimifar, Mach. Learn.: Sci. Technol., under review

## Slide 10: Validation experiment
The CookieBox
The AWG
ADC
FPGA
FPGA
FPGA
FPGA
FPGA
ADC
8b
6.4 GSps
FPGA
Data
processing
Other channels
(Memory)
NN model
x2
Data pre-processing
Inference engine
ADC
ADC
ADC
ADC
ADC
ADC
ADC
Wingering, NSS 2023
Keysight M8195
VCU128
ADC08DJ3200EVM

## Slide 11: Validation experiment
Serial mode
Memory mode
NN
Memory
Channel 1
Channels 2-16
NN
Channels 1-16
Full speed acquisition
Measure: Latency
1/16th throughput acquisition
Measure: Hardware impact on precision
Wingering, NSS 2023

## Slide 12: Validation experiment
Wingering, NSS 2023

## Slide 13: Results : Footprint and Power
(200 MHz Clock) | Peak finder | Histogram
Latency (µs) | 0.05 | 0.1
DSP | 0 | 0
LUT | 1985 | 580
BRAM | 0 | 0
FF | 2252 | 760
Peak finder
Histogram
ML model
FCNN | CNN
2.8 | 50
141 | 350
14k | 85k
4 | 76
7k | 31k
✔
DSP | FF | LUT | BRAM | Power (W)
141 (2%) | 18k (0,7%) | 20k (1.6%) | 22 (1%) | 5.28
Total utilisation for initial implementation
Rahimifar, Wingering, NSS 2023
VCU128

## Slide 14: Reaults : Neural Network Optimisation
Chart: NN Latency (200 MHz clock)
| HLS4ML | Optimized
Block latency | 0.5 | 0.08
Data fetching | 2.3 | 0.11
2.8
0.2
Rahimifar, Wingering, NSS 2023
Rahimifar, Mach. Learn.: Sci. Technol., under review

## Slide 15: Results : Footprint and Power
Peak finder
Histogram
ML model
DSP | FF | LUT | BRAM | Power (W)
141 (2%) | 18k (0.7%) | 20k (1.6%) | 22 (1%) | 5.28
Total utilization for optimized serial mode implementation
(200 MHz Clock) | Peak finder | Histogram | FCNN 5 bits Optimized
Latency (µs) | 0.05 | 0.1 | 0.2
DSP | 0 | 0 | 141
LUT | 1985 | 580 | 14k
BRAM | 0 | 0 | 2
FF | 2252 | 760 | 7.1k
Rahimifar, Wingering, NSS 2023
Rahimifar, Mach. Learn.: Sci. Technol., under review
VCU128

## Slide 16: Results : Neural Network
Acquired from test bench
Ground truth
Energy bins
Both
Experimental setup
Serial mode
Neural Network Precision:
Expected on subset = 89 %
Measured on subset = 90 %
Rahimifar, Wingering, NSS 2023

## Slide 17: Results : Latency
1.4 µs
AWG Markers
(calibration pulse)
ML block output (valid pin)
AWG to ML: 1.4 μs
Pulse width : 1 μs
0.4 µs
latency
Rahimifar, Wingering, NSS 2023

## Slide 18: Summary of results
 | Target | Result
Full single channel validation testbench | End-to-end emulation | End-to-end emulation (except FPGA-FPGA link)
Neural Network Accuracy | ≥ 80 % | 90 % *
FPGA Power | < 10 W | 5.28 W
Total Latency | < 1 µs | 0.4 µs
* On data subset, full validation with noise upcoming

## Slide 19: Other projects
120 TB/s (14x14 po2)
Time-of-flight CT
Billion pixel camera
~10 TB/s
Dark matter search
ARGO
200 m2
>20 Mcps
Network intrusion
100 Gbps

## Slide 20: Conclusion
Very efficient Machine Learning modules can be integrated for low latency real-time analysis
To achieve high throughput:
Minimize neural network
Maximize pre-processing
Maximize data throughput
Pipeline and parallelize operations
Validate individual steps and system integration
Axe Imagerie Médicale

## Slide 21: Backup slides

## Slide 23: FPGA resources
JESD204B interface
Timestamper (calibration)
Pre-processing
ML block
Microblaze
Ethernet
Serial Mode (Xilinx VCU128)

## Slide 24: AWG

## Slide 25: Analog signals
Chart: time (ns)
| 0 | 1.5625E-2 | 3.125E-2 | 4.6875E-2 | 6.25E-2 | 7.8125E-2 | 9.375E-2 | 0.109375 | 0.125 | 0.140625 | 0.15625 | 0.171875 | 0.1875 | 0.203125 | 0.21875 | 0.234375 | 0.25 | 0.265625 | 0.28125 | 0.296875 | 0.3125 | 0.328125 | 0.34375 | 0.359375 | 0.375 | 0.390625 | 0.40625 | 0.421875 | 0.4375 | 0.453125 | 0.46875 | 0.484375 | 0.5 | 0.515625 | 0.53125 | 0.546875 | 0.5625 | 0.578125 | 0.59375 | 0.609375 | 0.625 | 0.640625 | 0.65625 | 0.671875 | 0.6875 | 0.703125 | 0.71875 | 0.734375 | 0.75 | 0.765625 | 0.78125 | 0.796875 | 0.8125 | 0.828125 | 0.84375 | 0.859375 | 0.875 | 0.890625 | 0.90625 | 0.921875
 | 0 | 0.3784 | 0.64231 | 0.81772 | 0.92539 | 0.9818 | 1 | 0.99027 | 0.96064 | 0.91735 | 0.86522 | 0.8079 | 0.74817 | 0.68805 | 0.62903 | 0.57215 | 0.51811 | 0.46736 | 0.42012 | 0.3765 | 0.33648 | 0.29997 | 0.26682 | 0.23685 | 0.20985 | 0.18561 | 0.16391 | 0.14454 | 0.12728 | 0.11195 | 0.098343 | 0.086298 | 0.075651 | 0.066254 | 0.057973 | 0.050683 | 0.044275 | 0.038648 | 0.033712 | 0.029387 | 0.0256 | 0.022288 | 0.019393 | 0.016865 | 0.014659 | 0.012735 | 0.011059 | 0.0095983 | 0.0083273 | 0.0072215 | 0.0062602 | 0.0054247 | 0.004699 | 0.004069 | 0.0035223 | 0.003048 | 0.0026368 | 0.0022803 | 0.0019715 | 0.0017041