## Slide 1: A new methodology of clock phase adjustment in a large-scale clock distribution system for HL-LHC ATLAS TGC front-end electronics
Ren Nagasaka (ICEPP, University of Tokyo) on behalf of the ATLAS Collaboration
IEEE real time conference, 23 April 2024
Key topic
Methodology of clock phase adjustment for large-scale electronics system.
  ATLAS Thin Gap Chamber system:
    1,434 front-end electronics.
    1,434 fibers to distribute clock signals for synchronization.
  Requirement on clock phase adjustment:
    Well better than 1 ns precision to guarantee good performance of hit-bunch crossing assignment (BCID), regarding 25 ns bunch spacing of LHC.
      Note: 1 ns also corresponds to precision of signal arrival timing alignment.
      Aim to O(100) ps.
Thin Gap Chamber
25 m

## Slide 2
IEEE real time conference, 23 April 2024
We conclude that phase adjustment of 1.434 front-end electronics can be done with an accuracy of ~ 50 ps (sufficient accuracy for our purpose).
50 ps
Actual implementation of clock phase adjustment functionality in firmware and software.
  Taking advantage of SoC devices, measurement, and adjustment of clock phase can be done remotely in a semi-automated manner.
Validation of the system and estimation of the precision of the system.
  Reproducibility validation
  Estimation of uncertainty with measurement-driven method.