## Slide 1: Synchronization between Detector anD Motion in A Neutron Instrument
Hot single crystal neutron diffractometer HEiDi
  Operated by RWTH Aachen and Forschungszentrum Jülich at fission reactor FRM II
  Motion electronics: Siemens S7-1500 PLC + ET200S decentral periphery
  Detector: 3He detector tube
GOAL: movement during measurement
Detector
Mono-chromator
Eulerian
Cradle
H. Kleines, F. Suxdorf, M. Meven, W. Luberstetter, G. Brandl; JCNS-2, Forschungszentrum Jülich, Germany

## Slide 2: ToolBOX in the Siemens S7-1500 Environment
Electronic Gearing
S7-1500 isochronous mode
Time-based IO
Profinet IRT
CAM Track and Measurement Input

## Slide 3: System Architecture
CAM Tracks
  Position-based histogramming
Diagnostics: Measurement input
First measurements at linear table test system
  Position resolution at 10 mm/s: 3,6 µm
  Potential for improvement
4 Motors
4 SSI Encoders
Feedback of CAM track to measurement input
Detector Electronics
(Time resolved counter)
CAM track pulse
24 V to TTL
HE-3 Tube
Profinet IRT
FTPS Server
Diagnostic data from measurement input
S7-1500 CPU
1517TF-3 PN/DP
DI 32 x 24V DC HF
TM PTO 4
TM PosInput 2
IM 155-5 PN HF
TM PosInput 2
TM Timer DIDQ