## Slide 1
Design of a 11-bit column-parallel ADC for Monolithic Active Pixel Sensor
Weijia Han2, Yongsheng Wang1, Chengyou Xia1, Weijia Han2,, Yuhao Wen1, Boxuan Li1, Jiarui Wang1, Fangfa Fu1, Jinxiang Wang1, Chengxin Zhao*,2,3
1Department of Electronic Science and Technology, Harbin Institute of Technology, Harbin, China
2Institute of Modern Physics, Chinese Academy of Sciences, Lanzhou, China
3School of Nuclear Science and Technology, University of Chinese Academy of Sciences, Beijing, China
E-mail: chengxin.zhao@impcas.ac.cn
Introduction
The various physics and applications at the Heavy Ion Research Facility in Lanzhou (HIRFL) and the High-Intensity Heavy-ion Accelerator Facility (HIAF) require MAPS to measure particle hit's position, energy deposition, and arrival time.
An 11-bit column-parallel ADC has been designed to serve the pixels in every two adjacent columns.
This ADC uses cyclic architecture to meet the strict requirements of the area.
This ADC uses SHA-less architecture to reduce the power consumption.
A novel MDAC architecture with two residue generators is proposed to reduce the power consumption without additional area.
Overall architecture
Amplifier implementation
MDAC implementation
Fig. 1. Architecture of proposed Cyclic ADC
The simplified cyclic ADC architecture is shown in Figure 1, mainly consisting of a multiplying digital-to-analog converter (MDAC), a sub-ADC, and a digital correction circuit.
Fig. 2. Schematic of the MDAC
As seen in Figure 2, two RG are used in the MDAC.
Allowing the amplification and sampling process to operate in the same time.
The area remains unchanged by reusing the Sampling cap as load cap.
The core amplifier of the MDAC is shown in Figure 3.
This amplifier uses a two-stage structure to meet the requirements of high gain, high speed, and high output swing.
This amplifier uses two kinds of cascode compensation.
A PMOS input pair and an NMOS input pair are placed parallelly to achieve a wide input common mode range close to rail-to-rail.
Fig. 3. Schematic of the core amplifier
Measurement Results
Fig. 5. Spectrum for 113 kHz input sampled at 1 MS/s
The measured performance of the ADC is shown in Figure 5 and the Layout of the ADC is shown in Figure 6. The signal-to-noise and distortion ratio (SINAD) is 57.71 dB, and the effective number of bits (ENOB) is 9.3 bits. The area of the ADC is 60×670 μm2.
Fig. 6. Layout of this column-parallel ADC
Weijia Han