## Slide 1
24th IEEE Real Time Conference ICISE, 22-26 April 2024, Quy Nhon, Vietnam
N.T. Anh1, L.X. Chung2, L.T. Anh2, T.T. Anh3, M. La Cognata4, M.V. Dien2, B.T. Hoa3, P.D. Khue,
D.T.K. Linh2, N.T. Nghia3, G.G. Rapisarda5, M. Sferrazza6, and D.T. Tran7
1Hanoi Irradiation Center, Minh Khai, Bac Tu Liem, Hanoi, Vietnam;
2Institute for Nuclear Science and Technology, VINATOM, 179 Hoang Quoc Viet, Hanoi, Vietnam;
3Faculty of Physics, VNU-University of Science, 334 Nguyen Trai, Ha Noi 100000, Vietnam;
4Istituto Nazionale di Fisica Nucleare, Laboratori Nazionali del Sud, Catania, Italy;
5University of Catania, Catania, Italy;
6Université Libre de Bruxelles, Belgium;
7Institute of Physics, VAST, 18 Hoang Quoc Viet, Hanoi, Vietnam
Faraday Cup Development for Beam Monitoring in nA Scale and Its Application in the Cross section Measurement of p+12C Scatterings with Ep=1-3.2 MeV
Notes: 1

## Slide 2
Introduction
2
A Faraday cup (FC) suitable for nA intensive beam has been developed to serve nuclear reaction study using the pelletron at the VNU-University of Science (HUS).
The FC operation was tested with a proton beam by varying the high voltage (-HV) applied in the repeller ring;
comparing with CST Studio Suite simulation.
The FC was used in an experiment to measure the cross sections of p+12C scattering with Ep=1-3.2 MeV at the laboratory angles of 50, 106, 120, 130, and 160o.
Notes: 2

## Slide 3
3
The Faraday cup is designed in tradditional way. The testing experimental setup is presented in Figure 1.b. The experiments were carried out with proton energy of 0.8, 2.63 MeV, and varying HV from 0-500 (V).
CST simulation with the following assumptions:
Uniform source disk of 8 mm diameter at the botom of the FC
Electron polar angle took the average value of the cosin distribution.
Their energy obeys to the Maxwell distribuiton.
Good agreement between CST simulation and experimental results was obtained.
The plateau region is observered from about -50 V.
The current loss measured by the the FC dependent on HV
FARADAY CUP DESIGN, SIMULATION MODELS
AND TESTING EXPERIMENT
Figure 1: FC design (a) and test setup (b)
Figure3: The distribution of electrostatic field with -350 V applied in the repeller
Notes: In some cases where potential has a bound state of particular angular momentum, the scattering of particles with that angular momentum will be especially enhanced. In such cases, the total scattering cross section will show a peak, and the angular distribution will be characteristic of the appropriate Pl(cos θ). This very strong scattering is known as resonance and is a powerful method for studying bound states
3

## Slide 4
A FC for nA scale intensive beam has been successfully developed. From test results, the suppressing voltage should be greater than 100 V to avoid the secondary electrron loss.
Excitation functions of p+12C elastic scattering were measured from 1-3.2 MeV at five center-of-mass angles. The obtained results are in good agreement with published data.
The experimental setup placed in a 10-6 torr vacuum chamber is shown in Figure 5.
Five silicon PIN didodes were located at different angles. Their bias voltage was +100 V.
The target was made of formva (C3H6O2).
Proton energy was scanned from 1-3.2 MeV with 60 keV step.
The FC repeller ring was applied by -350 V.
CONCLUSION
Figure 5: Experimental setup
Figure 6: Excitation function of p+12C scattering
THE CROSS SECTION MEASUREMENT OF p+12C
SCATTERINGS WITH Ep=1-3.2 MeV

## Slide 5
Pelletron Maintenance in 02/2023

## Slide 6
COLLABORATION

## Slide 7
THANK YOU FOR YOUR ATTENTION!