## Slide 1: Mastering Picosecond Precision: Lessons learned from Large-Scale Timing Systems
Stefan Ritt :: Head of Muon Physics Group :: Paul Scherrer Institute
IEEE NPSS Real Time Conference, Qui Nhon, Vietnam, April 25, 2024

## Slide 2: Measuring precision timing
Electronics
Detector
Detector

## Slide 3: Measuring precision timing
Two particle decay
Different Time

## Slide 4: Measuring precision timing
Electronics
Time-of-Flight
x [mm]
1 mm ≅ 7 ps

## Slide 5: Large systems
N Detectors
N Detectors
N2 Clocks
N=1000  1,000,000 Clocks

## Slide 6: Large systems with reference clock
N Detectors
N Detectors
2N Clocks
Reference Clock

## Slide 7: Time inaccuracy
Reference Clock
“Skew”
Repeater
“Jitter”
Timing inaccuracy occurs both on the detector side
and the clock distribution side: Skew & Jitter

## Slide 8: MEG II Experiment at PSI
108 m+ / s
detection in liquid
Xenon Calorimeter: 4760 channels
e+ detection in
Timing Counter: 1024 channels
Normal m decay
(Standard Model):
m+  e+ ne nm
Lepton-Flavor Violating Decay
(New Physics):
m+  e+ g
MEG II Experiment requires
~10 ps at electronics level

## Slide 9: How to achieve timing at the Pico second level?
Sources of timing jitter: Single ended lines, PLL jitter
Clock stability
Noise reduction strategies
Timing calibration
Lessons learned from the MEG II system

## Slide 10: Jitter caused by voltage noise
voltage noise Du
timing uncertainty Dt
signal height U
rise time tr
Typical values
Du = 10 mV
U = 3.3 V
tr = 1 ns
Dt = 3 ps
receiver threshold

## Slide 11: Differential Signals e.g. LVDS
+
-
+
-
+
-
+
-
+
-
+
-
FPGA
Do not send low-jitter clocks through FPGAs!

## Slide 12: Optical Signals
+
-
+
-
Careful with optical clock distribution!
+
-
Optical fiber

## Slide 13: Clock stability
T2K, Japan
MEG II, PSI
GPS clock for measurements far apart
Atomic clock for long term measurements
Particle physics: Measurement periods O(100 ns)  Frequency stability of 10-5 is enough 100 ns * 10-5 = 1 ps  Excellent low-jitter clock distribution to all detector channels needed

## Slide 14: WaveDAQ system for MEG II @ PSI
9000+ channels 5 GSPS / 12 bit
DRS4 chip
WaveDREAM Board
WaveDAQ Crate

## Slide 15: Low-jitter quartz

## Slide 16: LVDS clock distribution
fully
differential

## Slide 17: DRS4 Phase Locked Loop
T
Q
Phase
Comparator
External
Reference
Clock
Inverter Chain 1024x
loop
filter
down
F1
F2
sampling speed control
PLL
up
R
C
t = RC

## Slide 18: PLL Jitter
Perfect
Clock
PLL
Clock
Period
Jitter
Phase
Jitter

## Slide 19: PLL Jitter
Slow PLL
Fast PLL
Low period jitter
High period jitter
Low phase jitter
High phase jitter

## Slide 20: Jitter between two PLLs
Detector 1
PLL1
Detector 2
PLL2
Timing jitter from PLL jitter
To achieve minimal timing jitter, PLL phase jitter must be minimized

## Slide 21: PLL jitter from power supply noise
Power Noise
Jitter
Switching Regulator
24 V
3.3 V
R
ESR
C
0.1 mV
ESR = 1 Ohm
8 mV
ESR = 0.01 Ohm
Use low-ESR capacitors for power supply filtering
DRS4 chip: 1 mV noise  10 ps jitter
Inoise
VDD
ESR: Equivalent Series Resistance
SPICE simulation

## Slide 22: Used filter components
LC combines EMI Suppressor Filter NFE31PT222Z1E9
560 mF / 9 mW
R = 100 mW

## Slide 23: Power section WaveDREAM board

## Slide 24: Electromagnetic Interference (EMI)
EMI pulse from switching converter
Slew rate limiter
Shielding

## Slide 25: Use of DRS4 clock channel
1024 cells, 200 ns @ 5 GSPS
DRS4
Deviation
~ 50 ps
100 MHz, 10 ns
Sampling the clock channel reduces uncertainty from ~25 ps to <2 ps

## Slide 26
The WaveDAQ system

## Slide 27: Custom Design “WaveDAQ”
Standard 19” crate + custom backplane (no VME, no xTCA)
Idea: Not only a solution for MEG II, but more general “crate standard”
Features:
  Serial bus (SPI) for configuration
  Trigger / Busy signals in backplane
  “Dual Star“ Serial gigabit links
  Hot-swap functionality
  Low jitter (<5 ps) clock
  Shelf management with Ethernet and power
Data Concentrator Board (DCB)
Trigger Concentrator Board (TCB)

## Slide 28: WaveDAQ Backplane
master clock
DCB
FCI Densishield Cable
WD
WD
WD
WD
Crate
LMK03000 Jitter Cleaner

## Slide 29: Half Height Backplane

## Slide 30: MEG II System
Scaling up to 16000 channels Synchronous System (single clock)
Clock and Trigger distribution

## Slide 31: Synchronization
Master
Clock
Trigger
PLL
Fanout
PLL
PLL
Trigger
Busy
Trigger
Bus
Clock
Sync
Lesson learned: Make all PLL frequencies
integer multiples of each other
DRS4
DRS4
80 MHz
80 MHz
PLL1
PLL2

## Slide 32: Jitter measurements courtesy E. Schmidt, PSI
sjitter = 1.9 ps
Tektronix MSO64B
8 GHz, 50 GSPS
soldered diff. probes!
Slot - Slot
Crate - Crate

## Slide 33: Global calibration
Clock distribution is never perfect to the ps level
Global sync injection at ADC does not calibrate different cable lengths
Signal injection at detector can be difficult
Det.
Det.
Det.
ADC
ADC
ADC
Det.
ADC
Clock

## Slide 34: Global calibration
Solution: Use a physics event which is seen by all detectors:
  LED flash in calorimeter
  Cosmic traversing many channels
  Correct for different light path
Det.
Det.
Det.
ADC
ADC
ADC
Det.
ADC

## Slide 35: MEG II Timing Counter
8 x 108 m/s
256 scintillating tiles 4x6 cm, 512 WDB channels (2 crates)
Resolution scales with sqrt(N)
35 ps reached with 8 hits

## Slide 36: Lessons learned (so far...)
Designing a crate standard is easier than anticipated (if no committee is involved 😉)
Distributing a 5 ps jitter clock is not so hard
Doing everything from scratch can simplify things
  shelf manager with 8-bit uC with few 100 lines of code
  crate costs ~ 2k$ including power supply
Mixed signal board with 40 mV of noise (gain=100 !) is tough
  whole project took 6 years from first idea with ~2 FTE
  analog front-end took 1.5 years, FW ~2 years
  careful selecting and shielding DC-DC converter, needed 4 revisions
  the more noise you fix, the more new sources you find
  Lots of experience obtained often missing in textbooks
DALL-E

## Slide 37: Conclusions for precision timing in large systems
Use end-to-end differential clock distribution
Careful filter power for all PLLs with low-ESR capacitors
Identify and remove EMI sources
Large systems with <5 ps timing can be built
This talk: IEEE NPSS Educational Video at https://ieee-npss.org/videos/
5.4 ps