## Slide 1: 50 years of Trigger/DAQ evolution
Patrick Le Dû,
PhD
patrickledu@me.com

## Slide 2: RT24 Award
For achievement and contributions to nuclear instrumentation for High Energy Physics and its application to medical imaging and radiotherapy"

## Slide 3
I Dedicace this talk and Award to my MENTORS
Aldo Michelini
Omega Spark chamber testing
NA3 experiment Head
OPAL experoment Head
MWPC development
1930-2020
1924-2010
Gearges Charpak

## Slide 4: Who I am ? -
NA3 @ CERN (Di-Muon Drell Yan) : 1974-1980
  Large MWPC (4x4 m2)
  Trigger & DAQ
LEP - OPAL @ CERN (1980-1990)
  TOF system
  Trigger & DAQ  First Z0
SSC- SDC @ Dallas/LBL Berkeley (1990-1994)
  Trigger L2
  Shower Max Detector electronics (APD & SCA)
LHC- ATLAS @ CERN (1994-2000)
  L2 trigger & LARG calorimeter Read Out electronics (SCA)
D0 @ FNAL (1996-2005)
  L1 Calormeter trigger and L2 trigger.
ILC study group (1996-2008)
  Trigger & DAQ convener  Software trigeer
2000Technology transfer advisor for medical application (PET & Particle therapy)
Ultra fast (picosecond) timing and TOF
Experimental Physicist
  CEA Saclay (1969-2008)
  IN2P3-IPN Lyon (2009 ..)

## Slide 5: Goals of this lecture
The evolution during the last 50 yerars
of Electronics, Trigger and DAQ applied to HEP and medical domains
A short survey and light overview along my long career as experimental Physicist.
Give my own lessons and experiences of this period
Notes: This overview interdisciplinary talk has the main purpose to present how HEP developments and evolution of front end deadtimeless low noise electronics, parallel read-out , real time selection of events (trigger), terabit data networking (DAQ) and on-line processing farms can be use to improve drastically the performances and efficiency of medical imaging devices like the Positron Emission Tomograph (PET) of next genration. The first part of the presentation will introduce the generic architectural model of future large colliding experiments like the future Colliders (ILC/CLIC) and its main features like the software trigger concept. An example of possible implementation will be shown using the new Advance Telecom Computing Architecture (ATCA) standard. Then, it will be discussed how these innovative ideas, tools and techniques of modern architectural concept in data acquisition can be applied in two particular applications of the future: the whole body Time Of Flight Positron Emission Tomography (TOF-TEP) for tumour diagnostic and the Hadrontherapy In-Beam PET for cancer treatment.

## Slide 6: My CERN PS time ( 1969-1973)
Polarized target charge exchange with Neutral Pi zero and antiproton (Regge pole ) my diploma (71) and PHD thesis (73)
First coincidence unit with IC
Spark chambers with camera ,scaning and IBM card
12 bit computer (SDS 920 ?) that just register beam parameters with the First 12 wires MWPC from G. Charpak
Few Hz trigger with 1 crate NIM electronics (discri ,scalers and coincidence units)
Spark
Chamber
Fast Camera
Scanning table
IBM punched card
Notes: This overview interdisciplinary talk has the main purpose to present how HEP developments and evolution of front end deadtimeless low noise electronics, parallel read-out , real time selection of events (trigger), terabit data networking (DAQ) and on-line processing farms can be use to improve drastically the performances and efficiency of medical imaging devices like the Positron Emission Tomograph (PET) of next genration. The first part of the presentation will introduce the generic architectural model of future large colliding experiments like the future Colliders (ILC/CLIC) and its main features like the software trigger concept. An example of possible implementation will be shown using the new Advance Telecom Computing Architecture (ATCA) standard. Then, it will be discussed how these innovative ideas, tools and techniques of modern architectural concept in data acquisition can be applied in two particular applications of the future: the whole body Time Of Flight Positron Emission Tomography (TOF-TEP) for tumour diagnostic and the Hadrontherapy In-Beam PET for cancer treatment.

## Slide 7: My MWPC time (1972-76)
Working with the Gearges Charpak team to develop small (20x20 cm2 up to 4 m2 (NA3) MWPC) mechanics (mylar cathodes and read out)
Test the first IC read out using the Filas LETI
8 channels discriminator

## Slide 8
Deacreasing the dose
with HEP Gazeous detector
A pioner !
Georges Charpak idea!

## Slide 9: The 1970’s dream : Digital radiography with MWPC A tribute to George Charpak
With 10 time less dose
Georges Charpak
1924 - 2012
Multiwire Proportional Chamber
1992
1968

## Slide 10
MWPC
Drift Chamber
MGPD
From MWPC’s to MGPD’s
1970 - 1990
PS- ISR- SPS- LEP
1975 - 1995
UA2-LEP
1990 -
Multiwire Proportional Chamber
Georges Charpak 1968
GEM F.Sauli)
Micromegas Y. Giomataris

## Slide 11
GEM for 2D Imaging:
Using the lower GEM signal, the readout can be self-triggered with energy discrimination:
9 keV absorption radiography of a
small mammal
(image size ~ 60 x 30 mm2)
Position resolution ~ 100 m
(limited by photoelectron range in the gas)
And 25 years later

## Slide 12: My CERN SPS time ( NA3 1973-1980)
Physics : Drell Yan Dimuon Spectrometer PSI to UPSILON production by Hadron (quark composition)
Very Large MWPC (4 m2) with ASIC Read out
Trigger hodoscope
Hardired processor box with filter storage principle (Morpion)
Notes: This overview interdisciplinary talk has the main purpose to present how HEP developments and evolution of front end deadtimeless low noise electronics, parallel read-out , real time selection of events (trigger), terabit data networking (DAQ) and on-line processing farms can be use to improve drastically the performances and efficiency of medical imaging devices like the Positron Emission Tomograph (PET) of next genration. The first part of the presentation will introduce the generic architectural model of future large colliding experiments like the future Colliders (ILC/CLIC) and its main features like the software trigger concept. An example of possible implementation will be shown using the new Advance Telecom Computing Architecture (ATCA) standard. Then, it will be discussed how these innovative ideas, tools and techniques of modern architectural concept in data acquisition can be applied in two particular applications of the future: the whole body Time Of Flight Positron Emission Tomography (TOF-TEP) for tumour diagnostic and the Hadrontherapy In-Beam PET for cancer treatment.

## Slide 13: NA3 Physics
Harwired processor
For real time calculation of dimuon mass and separate stream of data

## Slide 14: NA3 Trigger
NIM and CAMAC electronics,PDP 11/45
Harwired Trigger BOX to select Dimuon mass
Storage and filter between burst

## Slide 15: My CERN –LEP OPAL time (1980-1990)
One level Simple hardware Trigger
160 Time of flight (TOF) counters hodoscope with 300 psec resolution. (development of cheap XP20 PMT (XP32 Philips) and CFD integrated to the PM base)
VME Motorola 68020 series processors to read in parallel each detector crate (30) OS9 SW
CAMAC, VME and NO Fastbus
Display and slow control using Apple Macintosh
Filter processor using RISC machine (Appolo)
Digital Vax to collect data upstair

## Slide 16: OPAL Trigger basic
Matrix
  24 Phi
  6 Eta
  Total =144 trigger cells
64 ‘Phi’ single input signals
80% of Trigger
TOF
EM
HAD
MUON
TRACK

## Slide 17: Simple:The LEP-OPAL TRIGGER
15 mSec
22 mSec

## Slide 18: The LEP Z0 first event
The First Z0  e+e- at LEP
OPAL-13 August 1989
TOF + EM Lead glass Calorimeter only
TOF
EM
A.Michelini, H. VonDerSmitt, R.Heuer, P.Le Dû

## Slide 19: LEP-OPAL Z mm
Z mm
First LEP event
Zee

## Slide 20: My SSC Berkeley Time ( 1991-1994)
SSC_SDC project in Dallas : FNAL,Chicago,LBNL
L2 trigger with Univ of Chicago (CDF)
Read out of the EM shower max detector (160 K Channels)
APD’s Read Out development
Kleidelder SCA (Switch Capacitor Array) electronics
Notes: This overview interdisciplinary talk has the main purpose to present how HEP developments and evolution of front end deadtimeless low noise electronics, parallel read-out , real time selection of events (trigger), terabit data networking (DAQ) and on-line processing farms can be use to improve drastically the performances and efficiency of medical imaging devices like the Positron Emission Tomograph (PET) of next genration. The first part of the presentation will introduce the generic architectural model of future large colliding experiments like the future Colliders (ILC/CLIC) and its main features like the software trigger concept. An example of possible implementation will be shown using the new Advance Telecom Computing Architecture (ATCA) standard. Then, it will be discussed how these innovative ideas, tools and techniques of modern architectural concept in data acquisition can be applied in two particular applications of the future: the whole body Time Of Flight Positron Emission Tomography (TOF-TEP) for tumour diagnostic and the Hadrontherapy In-Beam PET for cancer treatment.

## Slide 21: My CERN –ATLAS & FNAL D0 Time ( 1994-2000)
ATLAS LVL2 Trigger (ROB : Read Out Buffer)
FNAL Tevatron RUN 2 DO LVL1 upgrade
ATM study as posssible ‘event building’ network ???
ILC trigger study  Software trigger concept (1996)
Notes: This overview interdisciplinary talk has the main purpose to present how HEP developments and evolution of front end deadtimeless low noise electronics, parallel read-out , real time selection of events (trigger), terabit data networking (DAQ) and on-line processing farms can be use to improve drastically the performances and efficiency of medical imaging devices like the Positron Emission Tomograph (PET) of next genration. The first part of the presentation will introduce the generic architectural model of future large colliding experiments like the future Colliders (ILC/CLIC) and its main features like the software trigger concept. An example of possible implementation will be shown using the new Advance Telecom Computing Architecture (ATCA) standard. Then, it will be discussed how these innovative ideas, tools and techniques of modern architectural concept in data acquisition can be applied in two particular applications of the future: the whole body Time Of Flight Positron Emission Tomography (TOF-TEP) for tumour diagnostic and the Hadrontherapy In-Beam PET for cancer treatment.

## Slide 22: Tevatron RUN 2 TRIGGER architecture
L2
4.2 µs
<50 Hz
D0
Detector
L1 Buffer
Pipeline)
L1 Trigger
L3 Farm
Mass
Storage
10 KHz
Accept
Acce/rej
< 1KHz
100 µs latency
7.6 MHz Xing rate
48 Input nodes
1 s latency
L2 Global
Preprocessing
Farm
L2 Buffer
&
digitization

## Slide 23: LHC Logical structure
Level 1
Level 2
ROI
Level 3
ATLAS
CMS
Level 1
High
Levels
Front end buffers
( ~107 channels)
Region Of Interest
Read Out Buffers
1000-1500 units
256 x 256
40 MHz
100 KHz
1KHz
100 Hz
Switching Network
(Event builder)
Processor farm
(~2 to 5 x 10 MIPS)
6
Sub- Detectors
10KHz
“Virtual”
level 2
Synchronous
Asynchronous
1-10 s
variable
2.5 ms
fixed
Custom made
Hardware pipelined
rigger processor
Commercial DSPs,
RISCs, etc.
Farms of RISCs,
workstations, etc.
1000 - 1500Gbit/s
20 Gbit/s
10 Gbit/s
1 Gbit/sec
1000 x1000
100 Mbit/sec
250-500 Gbit/s
few m s
variable
Permanent storage
100 MBytes/sec --> TBytes/day

## Slide 24: Software Trigger concept  No hardware trigger !
Sub-Detectors FE Read-out
Signal processing – digitization, no trigger interrupt
Sparcification,cluster finding and/or data compression
Buffering
Data Collection is triggered by every train crossing
Trigger :Software Event Selection using partial information of a complete train (equivalent to L1)
Select ‘Bunches Of Interest’
Event classification according to physics, calibration & machine needs (HLT)
Monitoring & on-line processing
S1
S2
S3
S4
Sn
1 ms
200 ms
Few sec
Data streams
Read-Out
Buffer
Network
Detector
Front End
Processor
Farm(s)
Storage
3000 Hz
Few Hz
1 MBytes
Average
event size
Data Flow
up to 1 ms
active pipeline
(full train)
Dead
time
free

## Slide 25: ILC DAQ conceptual (ILD) Architecture 2005)
VFD
VTX
ECAL
TPC
HCAL
MUON
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
Data Steams Logger and Mass Storage
Event building
Network
10-20 Gbit/sec
Processor farm (one bunch train per processor)
Event
manager
& Control
Detector Buffering (per bunch train in Mbytes/BT = 140 MB/s)
Links
Select Bunch Of Interest (200 Hz)
SiT
Machine
1 G
2.6 M
5 M
5K
4568 K
12K
9215K
10k
5MB
1MB
110 MB
20 MB
3 MB
1 MB
1GB/s = 100 PB/year

## Slide 26
Summary of my Trigger/DAQ time in HEP
1970 -2000

## Slide 27
1970
Historical Evolution of
data collection
VME (FIC) micro processor card
1980
2010
Digital PDP 11/45 mini computer
1990
LHC PC farm
IBM card

## Slide 28: Signal processing first step  THE discriminator
The single threshold is the least precise time extraction measurement. It has the advantage of simplicity
Single threshold
Multiple threshold
Constant fraction
Waveform sampling
The multiple threshold method take into account the finite slope of the signal. It is still easy to implement
The constant fraction algorithm is very often used due to its relatively good performance and its simplicity for Timing measurement
The waveform sampling above the Niquist frequency is the best algorithm since its preserve the signal integrity (time and amplitude)

## Slide 29
CAMAC
FASTBUS
VME
ATCA
Evolution of Standards
1970 - 1990
PS- ISR- SPS- LEP
1980 - 1995
UA2-LEP
1980 - 2007
UA1-LEP -LHC
2010 - ?
AGATA-PANDA
LHC/ ILC
From HEP
(ESONE)
From Computer INDUSTRY
BCNAF
From Telecom
INDUSTRY

## Slide 30: The Long Term issue challenge  15 years of design-20 years of life
The ‘More law’
LHC example
Tevatron
CDF/DO
1980-2012

## Slide 31: Evolution of DAQ technologies and architectures
1970-80
CERN PS/SPS
Minicomputers
Readout custom design
First standard: CAMAC
kByte/s
1980-90
LEP
Microprocessors
HEP standards (Fastbus)
Embedded CPU,
Industry standards (VME)
MByte/s
2007 …
LHC (CMS)
Networks/Grids
IT commodities, PC, Clusters
Internet, Web, etc.
GByte/s
Event building
Detector Readout
On-line processing
Off-line data store
From S. Cittolin

## Slide 32
TIPP09
32
L1
L1
L2
L3
HLT
Analysis
Pass1
On-line
farm
hardware
On-line
Off-line
Analysis
Pass2
Analysis
Pass2
Software
trigger
Multipurpose
farm
Analysis
Pass2
ILC/CLIC
Tevatron
LHC
GRID
GRID
Summary of T/DAQ architecture evolution

## Slide 33: Technology forecast summary (2015)
End of traditional parallel backplane bus paradigm
  Announced every year since ~1989
  VME-PCI still there
    watch PCI Express, RapidIO, ATCA
Commercial networking products for T/DAQ
  Conferences:
    ATM, DS-Link, Fibre Channel, SCI
  Today: Gigabit Ethernet ( 1  10  30 GB/s)
The ideal processing / memory / IO BW device
  The past:
    Emulators (370E),Transputers, DSP’s, RISC processors
  Today: FPGA’s 
    Integrates receiver links, PPC, DSP’s and memory

## Slide 34: Technology forecast (Con’t)
Point-to-point link technology
  The old style: Parallel Copper – Serial Optical
  The modern style: Serial Copper – Parallel Optics
    Today 10Gb/s  30Gb/s
Processors  Moore’s law still true until 2015 ..at least!
  Continuous increasing of the computing power (Clock)
Memory size  quasi illimited !
    Today : > 100 GBytes
    2015: > Tera Bytes …
Modern wisdom (about technology)
  “People tend to overestimate what can be done in one year, and underestimate what can be done in 10 years.”

## Slide 35: Timing & synchronization issues
From microseconds  to picoseconds
How to synchronize 106-108 channels ?
msec
Picosec

## Slide 36
My medical time
1997- …as technology transfert advisor
In-beam PET scanner at GSI
12C-therapy unit
CPET Hopital Tenon

## Slide 37
.. how the development of radiation instrumentation has been crucial for fundamental scientific discoveries
and for the improvement of human life...
Some history

## Slide 38: A survey of common area between HEP and medical
Front end electronics & signal treatment
    Fast shaping, integrated, low noise, low power, self trigger
    Digital filtering and signal analysis
      --> Waveform Digitizer :SCA
Read Out, Trigger & DAQ
    Pipeline and parallel read-out  FPGA
    Feature extraction techniques like Time Of Flight (TOF)
    Real Time selection  GPU’s image processing
    High bandwidth networks  new telecom standard (xTCA)
Computing & software : handling high quantity of data
    Reconstruction, simulation & modelling --> GATE
Global design
    Compact integration of large number of channels
DRS4 (PSI)
Giga sampling chip
LAL-Saclay)
NECTAR

## Slide 39: Survey of common area with HEP (2)
Energy
    From Kev to Tev with very good resolution
Scintillator & crystal
Photodetector
  compact, high QE, high gain and stability
  Standard : PMT ---> SiPM/MPPC,DSiPM
Fast Electronics devices
  We are speaking today to achieve the PICOSECOND
# Channels
  Billions due to ‘pixellated & high granularity’ detectors

## Slide 40: My medical Time ( 1997 - ….)
Hopital Tenon collaboration (Prof. J.N. Talbot) to improve PET electronics (1997)
Implementing TOF for PET ‘U. Chicago electronics brainsturming’ & dedicated workshops series.
Fast timing (Psec) workshops organizer
GSI –Rosendorf collaboration for Real Time PET with SiPM.
ETOILE ion therapy project (Lyon)
ORSAY CPO protontherapy ‘new machine’ advisor

## Slide 41: HEP & PET Similarities and differences
Similarities
Geometry and granularity
Detector (Crystals & scintillator)
Sensor (PMT,APD)
Digitizers: ADC,TDC,
Data volume (Gbytes)
Differences
Energy range
(10GeV  -511keV)
Event Rate 40  10 MHz
CMS
PET
Camera
Biomedical
Imaging
Calorimeter
HEP
No synchronization
Self triggered elrctronics
Multiple vertices

## Slide 42
1977
Historical Evolution of PET
First Steps
Townsend & Jeavons
C-PET Philips
Biograph PET + X ray-CT
1997
2007
First mouse imaging with 18F

## Slide 43: From Today ---> Tomorrow Challenge
Sucima PET-MRI EU project
TDM/PET-TOF (250 psec)
2017
2022
no TOF
~600 ps TOF
~200-ps TOF PET Siemens Biograph Vision 600

## Slide 44: From Today ---> Tomorrow Challenge
2022
Explorer total body project
2024
CEA Iseult 11.7T Whole-Body MRI
CRT = Laboratory 30ps
 10 to 1 psec 3 min scan
SNR, Direct imaging Multi-photon imaging, Positronium imaging
Scintillation, Cerenkov, Metascintillators, Photonics
AI vs TOF, Cost?

## Slide 45: The Physician Dream (2005)
Combined whole-body PET/CT or PET/MR…..
Minute PET/CT
PET
CT
PET
MDCT
PET
PET/MRI
PET
MR
(S.R. Cherry, 2006)
Magnet
Magnet
PET
PET
PET Insert with
Semiconductor photodetectors
Less dose
Less movment correction
Screaning capability
Courtesy of D.Townsend
Image In Real Time !

## Slide 46
Particle Therapy

## Slide 47
In beam Time-of-Flight PET for treatment planning and dosimetry monitoring
  Carbon ion beam will induce 11C after collision with cell DNA
  11C is a β+ emitter which can be used for online PET imaging
  11C activity profile correlated with dose profile: measure β+ profile to reconstruct “true” dose profile and check against planning
47
Carbon beam
PET camera
Courtesy K.Parodi
Positron emitters are produced in situ by the carbon beam

## Slide 48: What are the critical issues & challenges?
This is NOT a ‘simple target’ but a human body
  Treatment and quality assurance techniques of conventional radiotherapy not adequat for particle therapy
    A complex procedure for the ‘treatment planning’
How to be sure that the dose is delivered at the right place (tumour) ?
  Particle beam are error sensitive
    Displaced organ & overdose
    Moving organ in some case
What is the dose deposited ?
How to verify the treatment?

## Slide 49: The two ‘simultaneous’ challenges
Reducing error means  Real Time imaging
  3D in vivo dosimetry and tomography
    Use fragments of beam projectile reactions in the biological matter emerging from the tumor target volume
Verification using Computed Tomography/Radiography:
  CT imaging in charged Particle therapy is needed for:
    Target volume definition (anatomical boundaries with additional information from multimodality imaging (CT/MRI/PET studies)
    Dose and range calculation
    Patient alignment verification
But today these process are made at different moment and place

## Slide 50: Particle therapy workflow
Step 1  Treatment planning after CT scan
  Dose to be distributed
  MC simulation
  Give information to the machine
Step 2  Treatment
  10-20 fractions (tumour irradiation)
Step 3  verification using CT scan
Overdosage in normal tissue

## Slide 51: In-beam nuclear method principle for ‘in vivo’ dosimetry
Balance of promptly emitted
particles outside the target:
Incident protons: 1.0 (~1010)
-rays: 0.3 (3·109)
Neutrons: 0.09 (9·108)
Protons: 0.001 (1·107)
a-particles: 2 · 10-5 (2·105)
Time (s)
after collision
10-21 10-18 10-15 10-12 10-9 10-6 10-3 100 103
Particles
Prompt -rays
+ - emitter decay
Relation between dose and + activities
However the photon energy different from standard medical (Anger) SPECT camera
Projectile
Target
Nucleons
& projectile/target fragments

## Slide 52
Another dream The Proton CT
Radiograph of a phantom
Uwe Schneider PhD thesis (1978,PSI)
A tribute to G.Charpak

## Slide 53: Schematic block diagram of an integrated concept of radiography / therapy system
Photon detector
Photon detector
CT
CT
Treatment
Beam hodoscope
Sampling calorimeter
In beam SPECT-PET
Tumour
CT
Plastic
scintillator
Tracking
detector
Tracking
detector
Identify tracks and energy deposition of individual protons
Scintillators for trigger to read-out detectors
Tracking detectors for 3D tracks
Sampling Calorimeter for energy determination
High rate integrated DAQ

## Slide 54
Simulation & Sofware

## Slide 55: GATE : Geant4 Application for Tomographic Emission (2005)
Monte-Carlo simulation allowing to :
define geometries
(size, materials,…)
define sources
(geometry, nature, activity)
choice of physical process
(low energy package of G4)
follow track point by point
GATE specificities:
CERN GEANT4 libraries
Time modellign
(sources , movement,random…)
Script language(avoid C++)
Code interactivity
Sharing development

## Slide 56: GATE ‘early ’Collaboration 2004)
Uni Lausanne (IPHE)
Uni Clermont-Ferrand (LPC)
Uni Ghent (ELIS)
CHU Pitié-Salpêtrière (U494 INSERM) Paris
Vrije Uni Brussel (IIHE)
CERMEP, Lyon
CEA (SHFJ) Orsay
CHU Nantes (U463 INSERM)
Sungkyunkwan Uni. Seoul
Uni Claude Bernard (IPNL) Lyon
Uni Louis Pasteur (IRES) Strasbourg
Uni Joseph Fourier (LPSC) Grenoble
Forschungszentrum-Jülich (IME)
Uni. Massachusetts, Worcester
CHU Morvan (LATIM) Brest
Uni California (CRUMP) Los Angeles
Uni Toronto (CAMH)
CEA (DAPNIA) Saclay
MSKCC New York
Uni Athens (IASA)
Irène Buvat CEA SHFJF – Orsay-F)
Technical Coordinator: S. Jan (CEA - Orsay, F)

## Slide 57: Summary lessons & Conclusions
It take sometime between the discovery and initial ideas.
But when the technology is mature, it can make a gigantic breakthrough in the development of a technical device or system
Collaboration between various scientists and experts is fundamental and the key factor for success.
Building a community (network) about a specific subjects is the way to integrate students and experts

## Slide 58: Final Conclusion

## Slide 59
Questions?
Or send me an email
patrickledu@me.com
Thank you for your attention

## Slide 60: Thanks to ALL my colleagues
CEA DPHPE –DAPNIA-IRFU & SHFJ Orsay
CNRS IN2P3
Hopital Tenon & Institut Curie (Paris)
CERN & PSI.
DESY, Dresden Rosendorf & GSI.
FNAL & Chicago University.
Canada/Quebec Montreal Univ. & Sherbrook
Lawrence Berkeley National Laboratory
Japan KEK & Osaka University
UK Rutherford Lab. & Manchester University
… and many others ….
See you in Elba in 2026

## Slide 61
Special THANKS
Without
them
I was not able
to get this award
Since 1993
Vancouver RTC

## Slide 62: 1997 Beaune France
The Hotel Dieu
Chateau de Meursault diner
Wine tasting