## Slide 1: ERSAP: Towards Better HEP/NP Data-Stream Analytics With Flow-Based Programming
Environment for Real-time Streaming, Acquisition and Processing
V. Gyurjyan, D. Abbott, N. Brei, M. Goodrich, G. Heyes, E. Jastrzembski, D. Lawrence, B. Raydo, C. Timmer

## Slide 2
“Enable full offline analysis chains to be ported into real-time, and develop frameworks
that allow non-expert offline analysis to design and deploy physics data processing systems.”
A Roadmap for HEP Software and Computing R&D for the 2020s. HEP Software Foundation, Feb. 2018

## Slide 3: Outline
Looking forward to future experiments at the JLAB and EIC
  Reevaluate existing readout systems and their interface to the back-end
Reactive, actor-model based programming model
Results from ERSAP based pilot applications.

## Slide 4: Streaming system components: Tiered storage model
FE
Detector 1
FE
Detector 2
FE
Detector N
FE
Buffer
FE
Buffer
FE
Buffer
Aggregator
Processor
Processor
Online
Storage
Processors
Nearline
Storage
Processors
Permanent
Storage
Tier 1
Tier 2
Tier N
Final Tier
Storage capacity/ retention time >= . Processors latency
Components | Framework Support
A stream-oriented timing system | 
A standard stream data format | 
Front-end electronics that outputs time-based streams of data | 
Efficient streaming data transport | 
A stream oriented random-access data storage tier | 
A framework for data processing tasks (virtual triggers, calibration, reconstruction, monitoring, data storage, etc.) | 
A framework for data-flow orchestration and data-stream processing application design and deployment | 
Detector
DAQ
Online/nearline data processing
Processors
Offline data processing

## Slide 5: Flow-Based Programming Paradigm
Proposed in the late 60s by J. Paul Rodker Morrison
“Assembly line” data processing
Data flows through asynchronous, concurrent processors (“black box” actors)
Actors communicate via data chunks (called information packets or data-quanta)
Data-quanta are traveling across predefined connections (conveyor belts), where connections are specified externally to the processors.
Data is pushed through actors, while actors are reacting on passing data quantum.
Actors are performing independent, well-defined functions
Simple reconfigure
Minimizes side-effects

## Slide 6: ERSAP architecture
Reactive event driven actor, data-stream pipe, and orchestrator.
Stream of data quanta, flowing through directed graph of actors.
Application is a network of independent “black box” actors.
Data moves across actors not instructions
Actors communicate with each other by exchanging the data quanta across predefined connections by message passing, where connections are specified externally to actors.
User provided data processing single-threaded algorithms (engines) are presented as fully scalable actors in the framework.
S9
S6
S2
S8
Data–stream pipe
Data processing station
Workflow manager
Service engine
S1
S3
S4
S5
S7
S10

## Slide 7: ERSAP 3-layer structure
FE
Actor Layer
Orchestration Layer
Registration
DPE
SC
SC
DPE
SC
SC
DPE
SC
SC
DPE
SC
SC
gateway
security
Local Registration
Local Registration
Local Registration
Local Registration
Meta-Data
Data
ZeroMQ(xMsg)
in-Memory Data-Grid
POSIX Shared Memory (FIPC)

## Slide 8: Data processing station: actor
User engine run-time environment.
Engine follows data-in/data-out interface.
Engine gets JSON object for run-time configuration.
Data Processing Station
Data Processing Actor
Multi-threading
Configuration
Runtime Environment
Communication
User provided code
Engine

## Slide 9: Streaming data transport (conveyer belt)
Communication
Data-Stream Pipe
Meta-description
Serialization
0MQ/POSIX_SHM/Data-Grid
Publish/Subscribe
P2P
Transient Data
Data Processing Actor
Engine
Address
Topic
Envelop
Metta-Data
Version
Status
Data Location
Shared Memory address
Description
Author
Severity-ID
Sender
Sender State
Communication ID
Composition
Execution Time
Action
Control
Data Type
Data Description
Reply To
Byte Order
Data
Serialized Native
Serialized Custom

## Slide 10: Hall-D EIC prototype calorimeter setup

## Slide 11: Hall-D prototype calorimeter ERSAP SRO pipeline
Data
Lake
VTP
File
Writer
Calorimeter
ERSAP
F
ADC
VT
P
VXS Crate
VTP
Receiver
Format1
VTP
Frame Decoder
Beam Event
Identifier
Data
Lake
1 FADC250
Stream
(9 channels)
Zero
Suppression
4Gbyte
DDR3
Frame Builder
10Gbps Ethernet
(TCP) Stream
VXS Trigger Processor
Cosmic Event
Identifier
VTP payload

## Slide 12: VTP fADC data stream frames
65.5us VTP frame

## Slide 13: Event Identification. Sliding window technique
Beam Event
Only 1 hit/channel
Cut on min number of hits
Central channel energy deposition > than any other
Cosmic Event
Hits in only 3 modules on the path of muons
Sliding window - 32ms
Sliding step - 1ms
65.5us VTP frame
Sliding pointers
Find min/max time of hits within the frame

## Slide 14: 3x3 Calorimeter. Beam

## Slide 15: 3x3 Calorimeter. Beam sum
~2GeV
Based on cosmic muon deposition
(see next slide)

## Slide 16: 3x3 Calorimeter. Cosmic
~60MeV

## Slide 17: Hall-D prototype calorimeter ERSAP SRO pipeline
Data
Lake
VTP
File
Writer
Calorimeter
ERSAP
F
ADC
VT
P
VXS Crate
VTP
Receiver
Format1
VTP
Frame Decoder
Beam Event
Identifier
Data
Lake
1 FADC250
Stream
(9 channels)
Zero
Suppression
4Gbyte
DDR3
Frame Builder
10Gbps Ethernet
(TCP) Stream
VXS Trigger Processor
Cosmic Event
Identifier
VTP payload
ROC
Calorimeter
ERSAP
F
ADC
VT
P
VXS Crate
VTP
Receiver
Format2
VTP
Frame Decoder
Beam Event
Identifier
12FADC250
Stream
(32 channels)
Zero
Suppression
4Gbyte
DDR3
Frame Builder
10Gbps Ethernet
(TCP) Stream
VXS Trigger Processor
Cosmic Event
Identifier
DC
CODA
ET
VTP payload

## Slide 18: EIC prototype calorimeter SRO pipeline at DESY
ROC
Calorimeter
ERSAP
F
ADC
VT
P
VXS Crate
VTP
Receiver
Format2
VTP
Frame Decoder
Beam Event
Identifier
12FADC250
Stream
(32 channels)
Zero
Suppression
4Gbyte
DDR3
Frame Builder
10Gbps Ethernet
(TCP) Stream
VXS Trigger Processor
Cosmic Event
Identifier
DC
CODA
ET
VTP payload

## Slide 19: EIC prototype calorimeter SRO application design and configuration
--- io-services: reader: class: org.jlab.ersap.coda.engines.AggFileReaderEngine name: Source writer: class: org.jlab.ersap.coda.engines.AggStoreHistogramEngine name: Sync services: - class: org.jlab.ersap.coda.engines.FAdcIdEngine name: Beam - class: org.jlab.ersap.coda.engines.FAdcCosmicIdEngine name: Cosmic
# -class: KMeanEvtdentifier
# name: cppBeam
# lang: cpp
configuration: io-services: writer: frame_title: "ERSAP" frame_width: 1400 frame_height: 1200 #> hist_titles is a string containing the list of crate-slot-channel separated by , hist_titles: "1-17-0, 1-17-1, 1-17-2, 1-17-3, 1-17-4, 1-17-5, 1-17-6, 1-17-7, 1-17-8, 1-17-9, 1-17-10,
hist_bins: 100 hist_min: 0 hist_max: 8000 scatter_reset: true #> grid_size defines a layout for histogram visualization #> (e.g. 5 will plot 25 histograms in 5x5 matrix) grid_size: 5 services: Beam: s_window: 32 s_step: 1 s_hits: 5 # t_slot: 17 # t_channel: 14 b_thr: 20 bc_slot: 17 bc_channel: 12 bc_qmin: 0 bc_qmax: 8000 Cosmic: s_window: 32 s_step: 1 s_hits: 5 mime-types: - binary/data-evio - binary/data-jobj

## Slide 20
Time[ns]
fADC Channel
Time distribution of hits
32nsec

## Slide 24
Charge cut effect
2GeV, TET=50
DESY_stream_134.evt.0
Total frames – 1861687
Empty frames – 1807602
Total identified (soft trigger) – 18774
97% empty frames
34.71% identified as beam events
No energy/charge cut in the soft trigger
2GeV, TET=50
DESY_stream_134.evt.0
Total frames – 1861687
Empty frames – 1807602
Total identified (soft trigger) – 11487
97% empty frames
21.24% identified as beam events

## Slide 25
fADC threshold effects (2GeV)
Chart: Number of identified beam events
| 10 | 20 | 30 | 40 | 50
Trigger | 20415 | 20742 | 20081 | 23026 | 20516
Stream | 24965 | 25275 | 23318 | 25686 | 22032
Chart: SRO event identification efficiency % of events identified more by the software trigger
| 10 | 20 | 30 | 40 | 50
 | 18.2 | 18 | 13.9 | 10.4 | 6.8
Chart: Empty frames
| 10 | 20 | 30 | 40 | 50
 | 68.9 | 90.3 | 95.1 | 96.5 | 96.5

## Slide 26
Chart: Energy Deposition
| 2 | 3 | 4 | 5
 | 5673.2 | 6971 | 7990 | 8901.6
Calorimeter response linearity

## Slide 27: Summary
ERSAP is a software LEGO system
  Encourages application design based on software artifacts (LEGO bricks)
    Easier to understand and develop
    Reduced develop-deploy-debug cycle
    Easy to migrate to data
    Scales independently
    Independent optimizations
Improves fault isolation
Easy to embrace hardware as well as software heterogeneity.
Eliminates long term commitment to a single technology stack.
Agile framework that makes easy software evolution over time!

## Slide 28: Current status and future plans
ERSAP is a reactive actor/micro-service based data-stream processing framework. https://wiki.jlab.org/epsciwiki/index.php/ERSAP
Combines decade-long experience: CODA, AFECS and CLARA
  ERSAP Java binding, betta release: https://github.com/JeffersonLab/ersap-java.git
  ERSAP C++ binding development in progress: https://github.com/JeffersonLab/ersap-cpp.git
  ERSAP Python binding in the design stage
  Plans to design ERSAP Julia binding
Many ERSAP engine development projects are in progress
  CODA engines: https://github.com/JeffersonLab/ersap-coda.git
  JANA2 based engines: https://github.com/JeffersonLab/ersap-jana.git
  TriDAS engines: https://github.com/JeffersonLab/ersap-tridas.git
  CLAS12 AI reconstruction engines https://github.com/JeffersonLab/ersap-vtp.git
  INDRA ASTRA project ML engines
Collaborative effort between JLAB Physics and CST divisions.

## Slide 29
Thank You

## Slide 30: Streaming CODA and ERSAP to achieve data stream acquisition and processing
Detector reconstruction services (DRS)
Cluster, segment finder
Road finder
Detector 1
Sector 1
SIS
SIS
SIS
SIS
VTP/FPGA
Stream interface services (SIS)
Runs on FPGA
0 suppression
Electronic noise removal
Flash ADCs/TDCs
VXI Crate
Detector N
Sector N
ERS 1
EP
DRS X
DSTP
ERS N
ANAS 1
ANAS 2
ANAS N
Detector reconstruction services (DRS)
Full detector reconstruction
Calibration, alignment
Kalman filter
Note: some DRS services might run on GPGPU/TPU
Event persistency
Raw data
Some detectors might need
other detector’s data to
complete their reconstruction.
Event reconstruction services
DST persistency
Reconstructed data
Analysis services
Note: FPGA based ERSAP service’s code base (C++) will be deployed in CPU first for
verification and quality control, and only after will be deployed into FPGAs.
To use existing hardware in a streaming mode data must be reduced while streaming.
DRS
DRS
SRS
EB service
Geometry matching
Partial software trigger
FPGA/EJFAT
EBS
VXS

## Slide 31: Hardware vs. software event identification
TS
L1
L2
L3
FE
Modules
L1 accept
L2 accept
L3 accept
clear
busy
ROCs
trigger type
strob
ack
DL
ER
FE
Modules
EB
EH
ER
user
TS | Trigger supervisor
ROC | Readout controller
EB | Event Builder
EH | Event Hub
ER | Event Recorder
DL | Data Lake/tiered storage
Challenging to deal with event-pileups
Not ideal to read general purpose detectors
Cary bias to low-energy particles
Data is digitized at fixed rate
Data is read out continuous parallel streams
Data is cooled down at the tiered storages
CODA
CODA Streaming
DL
Processor N
Event Builder
Processor N

## Slide 32
2GeV, TET=10
DESY_stream_138.evt.0
Total frames – 1832550
Empty frames – 1262899
Total identified (soft trigger) – 15409
68.9% empty frames
2.7% identified as beam events
2GeV, TET=50
DESY_stream_134.evt.0
Total frames – 1861687
Empty frames – 1807602
Total identified (soft trigger) – 11487
97% empty frames
21.24% identified as beam events
fADC threshold effect

## Slide 33
2GeV, TET=50
DESY_stream_134.evt.0
Total frames – 1861687
Empty frames – 1807602
Total identified (soft trigger) – 18774
97% empty frames
34.71% identified as beam events
No energy/charge cut in the soft trigger
2GeV, TET=10
DESY_stream_138.evt.0
Total frames – 1832550
Empty frames – 1262899
Total identified (soft trigger) – 24965
68.9% empty frames
4.4% identified as beam events
No charge cut in the soft trigger

## Slide 34
2GeV, TET=10
DESY_stream_138.evt.0
Total frames – 1832550
Empty frames – 1262899
Total identified (soft trigger) – 15409
68.9% empty frames
2.7% identified as beam events

## Slide 35
3GeV, TET=10
DESY_stream_129.evt.0
Total frames – 1832550
Empty frames – 1262899
Total identified (soft trigger) – 15409
68.9% empty frames
2.7% identified as beam events

## Slide 36
4GeV, TET=10
DESY_stream_128.evt.0
Total frames – 2336701
Empty frames – 1633961
Total identified (soft trigger) – 17086
69.9% empty frames
2.43% identified as beam events

## Slide 37
5GeV, TET=10
DESY_stream_120.evt.0
Total frames – 5390065
Empty frames – 3702572
Total identified (soft trigger) – 17257
68.7% empty frames
1.02% identified as beam events

## Slide 38
2GeV, TET=50
DESY_stream_134.evt.0
Total frames – 1861687
Empty frames – 1807602
Total identified (soft trigger) – 11487
97% empty frames
21.24% identified as beam events

## Slide 39
2GeV, TET=10
DESY_stream_138.evt.0
Total frames – 1832550
Empty frames – 1262899
Total identified (soft trigger) – 24965
68.9% empty frames
4.4% identified as beam events
2GeV, TET=10
DESY_stream_138.evt.0
Total frames – 1832550
Empty frames – 1262899
Total identified (soft trigger) – 15409
68.9% empty frames
2.7% identified as beam events

## Slide 40: PbWO4 Christal based 3x3 Calorimeter