## Slide 1: Nuclear Security and Safeguards NPSS School Dakar, Senegal November 15, 2022
Some of this work was sponsored by the U.S. Department of Energy and the U.S. Department of Homeland Security
Richard Kouzes
Laboratory Fellow Emeritus
Pacific Northwest National Laboratory
Notes: Nuclear Security and Safeguards
The detection of ionizing radiation is a little over 100 years old, dating from the first observation of natural radioactivity. Today, radiation detection plays a key role in diverse fields from medicine to defense to basic science. For homeland security, countries around the world are deploying passive radiation detection instrumentation to interdict the illegal shipment of radioactive material crossing international borders at ports of entry. These efforts include deployments in the United States and several European and Asian countries by governments and international agencies. Safeguards are activities carried out by national and international agencies to assure that nuclear material is secure and not diverted for clandestine use. Administered by the International Atomic Energy Agency, international safeguards serve to monitor nuclear activities under the Non-Proliferation Treaty and are the primary vehicle for verifying compliance with peaceful use and nuclear nonproliferation undertakings. For safeguards, radiation detection is used to assure accountancy for nuclear materials in order to protect us from the illicit production and use of nuclear weapons. This talk will discuss some of the aspects of radiation detection applied to safeguards and our experience with radiation detection interdiction for national security.

## Slide 2: Talk Outline
International Safeguards
  Ensuring that nuclear material remains under a nation’s control and complies with international agreements
Border Security
  Protecting from external nuclear threats crossing a country’s border

## Slide 3: Safeguards

## Slide 4: International Safeguards
Nuclear safeguards include “an extensive set of technical measures by which the International Atomic Energy Agency (IAEA) Secretariat independently verifies the correctness and the completeness of the declarations made by States about their nuclear material and activities”
IAEA monitors declared facilities and quantities of fissile material at:
  Enrichment plants
  Fuel fabrication plants
  Power reactors and storage facilities
  Spent fuel reprocessing plants
4

## Slide 5: Safeguard Methods
IAEA methods:
  Containment and Surveillance
  Remote monitoring
  Non-destructive analysis
  Destructive analysis
  Environmental samples
Measurements of plutonium (Pu) and highly enriched uranium (HEU)
Gamma ray detectors to determine isotopics
Large variety of neutron detectors to observe fission
5

## Slide 6: Gamma Ray Detection for Safeguards

## Slide 7: Gamma Ray Detectors
Gas counters
  Ionization chambers
  Proportional counters
  Geiger counters
Scintillators
  NaI(Tl)
  Plastic: polyvinyl toluene (PVT)
Solid state detectors
  Si
  High purity Ge (HPGe)
Scintillator
PVT
HPGe
Gas
Notes: Gamma and neutron detection are complementary.

## Slide 8: Isotopic Identification
Characteristic gamma rays can be used to identify what radionuclides are present in what quantities
Non-destructive analysis
Can be shielded from view
V. Bottau, Study of gamma-­‐‑ray background noise for radioactive waste drum characterization with plastic scintillators, EPJ Web of Conferences 225, 05004 (2020)

## Slide 9: Neutron Detection for Safeguards

## Slide 10: Fission
Fission of a heavy nucleus such as plutonium and uranium can be spontaneous or induced
Fission produces two daughter nuclei and one to several neutrons
Kouzes, NIM 584 (2008)
Neutron
Spectra

## Slide 11: Neutron Detectors
Neutrons observed from fission sources
Energy not unique to special nuclear material (SNM) – Pu and U
Background
  From cosmic rays
  ~1/1000 of gamma-ray background
  Few commercial sources
Many scatterings prior to capture
Difficult to shield
Detectors: 3He, 6Li, 10B
3He Tube
Moderator
Bonner Sphere
Notes: Gamma and neutron detection are complementary.

## Slide 12: Safeguards Neutron Detection
Gross neutron counters
Coincidence neutron counters: measure “singles” and “doubles” neutrons from fission in plutonium and uranium
Multiplicity neutron counters: measure “singles,” “doubles” and “triples” neutrons
From these measurements, can determine:
  Mass – the amount of fissile material present
  Multiplication – the geometry of the material allows for limited chain reactions to amplify the number of neutrons
  Alpha-n – alpha particles from decays impacting on matrix materials generate additional neutrons from reactions
These three values define the material being measured
12

## Slide 13: Fork Detector
3He Neutron detector housed in a submersible “fork” assembly that is lowered into a spent fuel storage pool
Spent fuel assemblies raised and placed between the forks
Analysis is performed to assay/verify spent fuel burn-up.
13

## Slide 14: UNCL
3He based Uranium Neutron Coincidence Collar
Measurement of Pu in MOX fuel – passive mode
Verification of 235U in low enriched U fuel assemblies – active mode
Measure to an accuracy of less than 1% in a time of ~15 minutes
UNCL in active mode configuration
14

## Slide 15: The 3He Problem

## Slide 16: The 3He Supply
By-product of nuclear weapons program
  Tritium decays with 12.4-year half-life to 3He
  U.S. accumulated 200,000 liters of 3He by the end of 1990s
  Tritium was produced for nuclear weapons in reactors
  U.S. tritium production ended in 1988 - weapons needs met through recycling and reductions in the weapons stockpile
  Tritium production restarted in U.S. at Watts Bar reactor in 2007 only to support a smaller weapons stockpile
  U.S. 3He now made available through DOE Office of Science / Office of Nuclear Physics Isotope Program
  Decay now produces ~8,000 liters/year of 3He in U.S.
  Russia is only other supplier of 3He besides the US
16

## Slide 17: The 3He Problem (~2008)
National security and science applications drove up demand for 3He for neutron detection
Currently, 3He comes solely from the processing of tritium
No significant production of new tritium
Production of tritium solely for 3He need is cost prohibitive
Reserves of 3He have been consumed
Projected 3He Supply ~10-20 kL/y (U.S. & Russia)
Demand for 3He in 2007 was ~65 kL/y
Nothing matches all of the capabilities of 3He
Alternatives are needed
3He Tubes

## Slide 18: Supply and Demand (2009)
18
Data from Steve Fetter, OSTP
U.S. 3He inventory ~40,000 liters (Bentz 2011)
Projected demand ~65 kL/y - Projected Supply ~10-20 kL/y

## Slide 19: 3He Supply Projection (2016)
Plots From Jehanne Gillo, DOE Office of Nuclear Physics
19
Chart: Fiscal Year
| 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040
Demand | 2699 | 4528 | 2481 | 2446 | 2436 | 2300 | 2178 | 2178 | 2178 | 2178 | 2178 | 2178 | 2178 | 2178 | 2178 | 2178 | 2178 | 2178 | 2178 | 2178 | 2178 | 2178 | 2178 | 2178 | 2178 | 2178
supply | 62890 | 74098.2427 | 79444.3081 | 84527.9451 | 93135.4558 | 97803.7132 | 102329.1768 | 106599.9087 | 110625.5889 | 116315.5292 | 119878.6877 | 123223.6823 | 126358.803 | 129292.0252 | 132031.0209 | 134583.1708 | 142655.5749 | 144855.0638 | 146888.208 | 148761.3288 | 150480.507 | 152051.5924 | 155380.2125 | 156671.7811 | 157831.5061 | 164564.3976
Demand decreases to 2,178 L/y in FY21.
Several increases of 1,900-7,600 L occur between FY15 & FY40
~8,500 L added to sales inventory each year at SRS.
This projects availability of gas to the end of this century.
Notes: May not be accurate to list top plot as ³constant². It is more like previous projections over past couple of years ­ it is a hypothetical situation and assumes a 4000l a year auction (which we do not approach) and a 10,000l/yr federal use, which we don¹t come close to. It does assume two new increases in supply of about 8000 liters in both 2014 and 2024.
- The bottom plot is what our actual projections are now, based on federal agency input, and assuming the two supply additions in 2014 and 20124. It assumes no auction.
- So if you will, the two plots were intended to show a range ­ the possible maximum utilization for fed use and the minimum use (assuming no auction). (we also typically do better than the conservative 9,700 liters/year extraction. We have already done better than plot one. so range is maybe enough he-3 for 20-100 years?

## Slide 20: Alternative Neutron Detectors
Proportional Counter Alternatives
  BF3 filled proportional counters
  Boron-lined proportional counters
Scintillator-based Alternatives
  Coated wavelength shifting fibers/paddles
  Scintillating glass fibers loaded with 6Li
  Crystalline: LiI(Eu), LiF(W), Li3La2(BO3)3(Cr), CLYC
  Liquid scintillator (fast neutrons)
Semiconductor Neutron Detectors
  High intrinsic efficiency, but limited in size
  Gallium arsenide, perforated semiconductor, boron carbide, boron nitride, pillar-structured detectors
20

## Slide 21: Alternatives Neutron Detectors for Safeguards

## Slide 22: Alternative UNCL
Uranium Neutron Coincidence Collar (UNCL)
Measurement of Pu in MOX fuel in passive mode
Verification of 235U in low enriched U fuel assemblies in active mode
Want accuracy of less than 1% in ~15 minutes
UNCL active mode configuration
ABUNCL models

## Slide 23: Modeling
MCNP modeling plays a central role in development of safeguards instruments
Modeling of Active and Passive UNCL
Passive 3He-based UNCL
Active 3He-based UNCL
PWR
BWR
23

## Slide 24: Validation Testing of Models
Models compared to measurements
Model of B-10 Tube Array
Testing of B-10 Tube Array
Testing Bare B-10 Tube
Testing Moderated B-10 Tube
Testing of B-10 Tube Array
24

## Slide 25: GE Reuter Stokes ABUNCL
GE Reuter Stokes constructed a passive ABUNCL and provided it for testing
ABUNCL in Passive Configuration

## Slide 26: Muons for Safeguards

## Slide 27: Rad Waste Monitoring with Muons
Muons can be used for diversion monitoring in spent fuel in casks
  Casks shield gamma rays and neutrons
  Measure muon scattering over periods of weeks
  Muon flux is ~160 s-1m-2 at sea level

## Slide 28: Antineutrinos for Safeguards

## Slide 29: Antineutrino Reactor Monitoring
Antineutrinos first observed at reactor in 1956
Remote monitoring antineutrinos from reactors
  Safeguards approach to monitor diversion of fuel
  Provides independent monitor of power output
Watchman Experiment (cancelled?)
  Boulby potash mine in England
  Cherenkov detector with 35 metric tonnes of water
  25 km from reactor
29

## Slide 30: New Safeguards for New Reactors?
Despite the climate change threat, nuclear power is declining
Will small modular reactor (SMRs) become widespread?
  Up to 300 MW electric
  Factory-fabricated and transported to a location for on-site assembly
  Light water, gas-cooled, molten salt, or liquid metal
  2-10 years of fuel
  Modular, inherently safe, scalable, small land use, siting flexibility, process heat
  Independence from the grid
Will new safeguards methods be needed?
Westinghouse

## Slide 31: Conclusions on Safeguards
Radiation detection (gamma ray and neutron) for safeguards is routinely used by the IAEA
Alternative neutron detectors being tested for safeguards applications
Muons may play a role in future safeguards
Antineutrino detection is being investigated for use in safeguards
New small modular reactors will pose new problems for safeguards
  Number of reactors
  More countries with nuclear power
  New types of fuel
  New reactor cycles
31

## Slide 32: Nuclear Security

## Slide 33: The Problem And The Threat
Weapons of Mass Destruction (WMD)
Improvised Nuclear Devices (IND)
Special Nuclear Material (SNM)
Radiation Dispersal Devices (RDD)
DOE: 4 kg 239Pu or 25 kg HEU are sufficient for a nuclear explosive device
IAEA Significant Quantity: 8 kg 239Pu or 25 kg HEU
    NRC & IAEA Cat I: 2 kg 239Pu and 5 kg HEU with >20% 235U

## Slide 34: Orphaned Well Logging Sources
Notes: Gamma backscatter and neutron induced gamma emission are both used to look for hydrogenous material.

## Slide 35: Soviet Sr-90 (~40 kCi) RTG Recovered in Georgia
December 2001: three woodsmen in former Soviet republic of Georgia suffered severe radiation burns after handling the strontium-90 core from an abandoned radiothermal generator.
Notes: RTGs exist in the thousands

## Slide 36: 1987 Incident in Goiania, Brazil
Container of 137Cs scavenged from defunct medical clinic
Children played with the glowing powder (1400 Ci)
11 days before discovered (up to 100 miles away)
Four people died (450-600 rem)
28 suffered radiation burns, 249 contaminated
More than 112,000 requested medical monitoring!
Clean-up effort cost ~$20M (275 truckloads of waste).
36
Notes: 5000 m^3 of stored waste
3800 200 liter drums
1400 1.2 m^3 boxes
10 32 m^3 ship containers
6 waste containers
7 houses demolished
Cheap labor
50% drop in agriculture, housing prices fell, cars were stoned, tourism dropped
Goiania ~800,000 people
CsCl in 2” x 2” source 1375 Ci, 456 rad/hr @ 1m
Sept 13 - salvagers took home and opened source
Sept 15 - 1 sought medical help - sent home as allergic reaction to bad food
Sept 14-15 - disassembled, punctured source, scooped out material, sold to salvage yard
Sept 28 - wife of junk yard dealer sought medical care - carried source to clinic; diagnosed as tropical disease
Doctor got 100 rad dose
Suspected radiation
4 deaths at 1 month: wife, 2 junk yard employees, 6 yr old niece
Oct 3 - situation fully appreciated

## Slide 37: International Incidents
37
IAEA reported 18 incidents involving the smuggling of weapons grade nuclear materials between 1993 and 2004.
1994: police at the Munich airport intercepted a suitcase from Moscow with half a kilogram of nuclear-reactor fuel (363 grams weapons grade Pu).
1994: Prague police seized 2.7 kilograms of HEU from a former worker at a Russian nuclear institute.
1995: Chechen rebels buried a small amount of 137Cs in a Moscow park and notified Russian television crew.
2004: Russian Customs uncovered some 200 attempts to smuggle nuclear or radiological materials.
37

## Slide 38: Radiation Detection Effectiveness
Source activity (A)
  Strength, type, and energy
Detection geometric efficiency (eg ~ 1/r2)
  Source and detector size and distance
Detector intrinsic efficiency (ei)
  Material, geometry, collection
Shielding (S ~ e-x)
  Amount, type, and geometry
Background (B)
  Type, energy distribution, and intensity
  Naturally occurring radioactive material (NORM)
Time for detection (t)
  Statistics for signal to noise
  Operational limitation
Expert/Automated analysis of information
Time
Distance
Shielding
r
38

## Slide 39: Border Security

## Slide 40: The Global View of Commerce
20 foot Shipping Container Traffic Per Year

## Slide 41: Layered Lines of Defense: Interdiction Opportunities
Secure [MPC&A]
Outbound Borders [SLD]
Loading [Megaports, CSI]
Transit [DoD]
In-Bound Borders [CBP]
Transit [TSA]
Delivery [UNWD]
Transit
Target
U.S.
Europe
1
2
3
4
6
7
5
Graphic From Rich Tighe, BNV

## Slide 42
Mail/ECCF
Land Border
Maritime
Air Cargo
307 Ports of Entry representing:
621 border sites to protect
332,622 vehicles per day
The Challenge: U.S. Ports of Entry
57,006 trucks/containers per day
2,459 aircraft per day
580 vessels per day
100% of containerized cargo is screened for radiation
42
Notes:   The dots represent each of the ports of entry. Each has unique challenges to be addressed: quantity of traffic, natural radiation background, seasonal variation in cargo, environmental/weather

## Slide 43: Radiation Portal Monitors
Used for decades in the scrap steel industry.
Sensitive to small quantities of SNM & RDD materials.
Large area, high-efficiency gamma-ray detectors & 3He neutron detectors.
Best cost/performance ratio of any detection technology.
Provide the capability to rapidly screen cargo.

## Slide 44: Homeland Security Systems
Second Line of Defense / Megaports (1997)
  RPMs deployed overseas
Radiation Portal Monitor Project (2002)
  Over 1600 systems deployed in US
Guardian Program (2003)
  Screening at DoD bases
44

## Slide 45: Border Security Examples
Notes: US Customs (CBP) is deploying COTS at POEs

## Slide 46: RPM Concept of Operations
Primary Detection
Confirm
Secondary Detection
Isolate
Isolation
Identify
Identification of Isotope
Neutron Scan
Respond
Seize/Arrest
or Release
Detect
Gamma Detectors – Poly-Vinyl Toluene (PVT) Plastic Scintillators
Neutron Detectors – Moderated Helium-3 Gas Tubes

## Slide 47: Layered Approach: Imaging
X-ray and gamma-ray transmission or backscatter imaging
Aracor Eagle
AS&E

## Slide 48: Challenges & Solutions
48

## Slide 49: Naturally Occurring Radioactive Material and Man-Made Sources
NORM is the dominant source of alarms for cargo, but not passenger cars
NORM, and technologically enhanced NORM, contain:
  uranium series (238U; 4.5 billion years)
  thorium series (232Th; 14 billion years)
  potassium (40K; 1.3 billion years)
Commercial isotope examples
  241Am, 133Ba, 137Cs, 57Co, 60Co, 192Ir, 226Ra, 252Cf, nuclear fuel, depleted uranium
Medical radioisotopes
  92% of procedures are 99mTc for stress tests
  18F, 14C, 111In, 57Co, 201Tl, 153Sm, 89Sr, 131I, 67Ga, 51Cr
  One in 2600 Americans carries a radioactive burden large enough to be seen in an RPM
Skyshine from radiography
49

## Slide 50: Decay Chain Example
238U 4.5 Gy
234Th 24 d
234Pa 1.2 m
234U 250 ky
230Th 7.5x104 y
226Ra 1502 y
222Rn 3.8 d
218Po 27 m
218At 1.8x10-4 s
…
206Pb
a
a
a
a
a
b
b
b

## Slide 51: “Nuisance” or “Innocent” Alarms
Neutron Alarms - Few sources
  Troxler gauges, nuclear fuel, yellowcake, well logging sources
  Ship effect
Gamma Ray Nuisance Alarms
  Naturally Occurring Radioactive Material
  agricultural products like fertilizer
  kitty litter
  ceramic glazed materials
  aircraft parts and counter weights
  polishing compounds and abrasives
  propane tanks
  road salt
  welding rods
  ore and rock
  smoke detectors
  medical radioisotopes
  skyshine
Troxler Gauge
51

## Slide 52: Baseline Depression
Fraction of
Normal
Background
Normal
“No-Vehicle”
Background
Potential
Medical
Signal
Potential
Threshold
Above NORM
Potential NORM Profile
Depressed Baseline
SNM Calibration
Source Signal
w/o Vehicle
Potential
SNM Source
in NORM
Potential
SNM Source
w/o NORM
Extra Baseline Dip
52

## Slide 53: Skyshine
Radiation scattered from the air above a source
Radiography (192Ir, 60Co) or “x-ray” imaging sources
Very large sources (~100 Ci)
Can produce interference with radiation detection systems at very large distances (1% strength at 200 m)
Impacts all detector types (gross-counting or spectral)
Requires mitigation through distance, shielding, and operations
192Ir Radiography Skyshine Source
53

## Slide 54
Neutron Ship Effect Event Example
54
3 neutrons in 30 microseconds in an IAT detector

## Slide 55: Observations of Plastic Aging
Polyvinyl toluene (PVT) and polystyrene (PS) are widely used plastic scintillators
Most new and old PVT & PS shows no significant change in response to gamma radiation with temperature
Various forms of damage are observed in PVT and PS
Internal temporary and permanent fogging are two forms of damage that may be seen even at room temperature
Severe fogging sometimes observed at low temperature
The effect, first observed in 2009, was not reproduced in the lab for new PVT samples until 2013
55
Surface Crazing
Surface Clouding
Internal Fogging

## Slide 56: Active Interrogation
From Morse

## Slide 57: Active Interrogation (AI)
AI initiated by energetic photons, neutrons or muons
Detected signal is photons, neutrons or muons
Large source required giving large dose
Our study includes only:
  High-Z: presence of high atomic number (Z) material
  Photofission: presence of fissionable material
  Differential die-away: presence of fissile material
  Nuclear resonance fluorescence: presence of HEU or Pu
57
Notes: CAARS: SAIC – L3 – AS&E
Raytheon - Passport

## Slide 58: Modeling With MCNP & GEANT4
58
Analytical calculations performed to establish order of magnitude requirements
MCNP models of differential die-away (DDA): comparison made to published information provided model validation
MCNP models of PF for SNM and surrogates
Neutron die-away times observed for bare tungsten, DU, HEU and Pu.
9 MeV Bremsstrahlung beam GEANT4 simulation

## Slide 59: Is Active Interrogation Feasible?
Passport
Rapiscan
Can we do 100% imaging?
Is active interrogation operationally possible?
  AI cannot be used in primary screening, so limited to targeted containers
  Large dose
  Large footprint (on private land)
  Large cost
  If looking for a weapon, it is too late!

## Slide 60: Conclusions on Security
Radiation detection (gamma ray and neutron) for security is routinely used around the world
Radiation portal monitors are the main detector technology for border security
Many portable, handheld, and personal radiation detectors are used in diverse applications
Radiation detection technology for security is undergoing continuous improvements
People, not technology, are the key to successful security systems
60

## Slide 61: Pacific Northwest National Laboratory
Questions

## Slide 62: Backup Slides

## Slide 63: Traffic Monitoring Example
Traffic flow over 7 hours - each dip or rise is a passing vehicle
63
Notes: Example of RPM traffic monitoring.

## Slide 64: High-Z & Photofission Detection
Interrogate with x-rays and look for gamma-rays or neutrons
DU is a good surrogate material for High-Z detection and Photofission
Surrogate for high-Z detection can be 2 kg DU
Surrogate for Photofission detection can be 2 kg
  Consider prompt neutrons, delayed neutrons and delayed gamma rays
  Too many combinations of possible surrogate masses: Pb attenuators used to reduce signal to correct value
64

## Slide 65: Differential Die-Away
Interrogate with neutron pulse
LEU is a usable surrogate for DDA
Surrogate mass for DDA is 2 kg LEU
Surrogate provides similar response as HEU & Pu
65
Comparison of PNNL validation model results with measured data (Jordan et al. 2007)

## Slide 66: Nuclear Resonance Fluorescence
Interrogate with gamma-rays and observe gamma-ray signal
DU is good surrogate material for NRF
NRF signal size depends on mode (transmission or scattering) and HEU or Pu
Surrogate for NRF is 2 kg DU
  2 kg DU provides more signal than SNM
  Pb attenuators used to reduce signal to correct value and depends on transmission or scattering modes
66

## Slide 67: Muon Scattering Detection
Cosmic ray muons used
Muon scattering is highly dependent on density
Measure the muon path through a vehicle
Demonstrated to show presence of high-density material like HEU and Pu
Takes minutes to make a measurement because of small muon flux of ~160 m-1s-1
Decision Sciences
67

## Slide 68: Energy-Based Algorithms for Enhanced Portal Sensitivity
Energy-based algorithms can preferentially alarm on low-energy gamma-ray signals
  HEU, WGPu & Medical Radionuclides
Energy discrimination avoids many NORM alarms
  NORM spectra contain a significant high-energy component from thorium and potassium
Energy ratio modeling also handles baseline depression
  Background spectral ratios nearly constant with and without a vehicle in the portal
68

## Slide 69: Energy-Window Ratio Algorithm
Use PVT spectral shape for discrimination
Low
Window
High
Window
Using ratios of energy regions enhances discrimination significantly and minimizes effect of intensity variations
Notional
Threshold
Create the ratio:
69

## Slide 70: PVT Degradation Mitigation
Keep the plastic in an environmentally controlled space
Heat the plastic so it never gets cold
Dehumidify so water is not available to permeate the plastic
Encapsulate the plastic in a water impermeable membrane
  Requires material with MVTR ~ 10-5 g·m-2·d-1
  Requires sealants for edges
  Might require electrical feedthroughs
New formulations of plastic scintillator
70

## Slide 71: Spectroscopic Portal Monitors
Pros and cons of NaI(Tl) versus plastic scintillator
  Pros:
    Higher energy resolution
    Allows for identification
    Improved NORM rejection
    Improved identification rate
  Cons:
    Higher cost
    Physical limitations of NaI(Tl)
Efficiency requirement for SPMs
  Equivalent efficiency to plastic based RPMs
  For example, Five 4”x2”x16” crystals per panel
Automated secondary isotopic identification

## Slide 72: Standards
72
72
20 cm
20 cm
20 cm
ANSI N42.41: Minimum Performance Criteria for Active Interrogation Systems used for Homeland Security
  Non-intrusive inspection of closed containers, vehicles, and packages, but not imaging
  Inspection times of 90-900 s depending on size
  Test masses: explosives (200 kg), chemicals (200 kg), fissionable material (25 kg), weapon shells (16 kg)
Standards establish test methods based on threat-informed unclassified source materials and configurations
Standards establish performance requirements for automated active systems that detect shielded SNM