## Slide 1: Particle Camera Experiment guidelines
Michael Holik, Vladimir Vicha, Stanislav Pospisil, et al.
Institute of Experimental and Applied Physics
Czech Technical University in Prague
2022/11/02

## Slide 2: CERN Medipix Collaboration
Development of pixel detectors
Technology transfer initiative
Application of pixel detectors in the field of education

## Slide 3: Geiger-Muller counter vs Timepix based Particle camera Particle Camera = Modern Instrument for Teaching of Physics
Notes: 2022 Corvette Stingray 3LT - Chevrolet

## Slide 4: Timepix
Single photon counting readout provides low noise, high contrast images with very high dynamic range
55 x 55 um pixel pitch Matrix 256 by 256 Si, CdTe, GaAs sensors
Different sensor thickness 300um, 500um, 1mm, 2mm, 5mm
Timepix - Hybrid Pixel Detector with Single Particle Detecting Capability

## Slide 5: Timepix - Hybrid Pixel Detector with Single Particle Detection Capability
Sensor part and readout electronics part are optimized separately (sensor materials – Si, CdTe, GaAS)

## Slide 6: Pixel detector as “Active emulsion”
Some particles can be identified from shape of their tracks as in formerly used nuclear emulsions.
Example: Cosmic rays and natural background
Are particles photogenic?
Yes of course, they are when observing them with Timepix detector.

## Slide 7: Particle Camera Working Principle
….Different kind of radiation produces tracks of different shape

## Slide 8
Muons
Alphas
Particle Tracking
and Recognition
Type of interacting particle can be recognized by its specific track left in the pixel matrix
Track shape depends on interacting particle energy, mass, sensor material, bias voltage, angle,…
Gammas/X-Rays
Electrons

## Slide 9
Principle of semiconductor single particle counting pixel detector
N+
P+
Si
Counter: Particle count
+
Amplifier
Compa
rator
000
001
Threshold level above
electronic noise
No false counting.
Digital integration (counting)
No dark current.
Unlimited dynamic range and exposure time.
Detected count obeys poissonian distribution
Bias Voltage
Common
back-side
electrode
Pixelated
front-side
electrode
Pixel electronics
Threshold
level
Notes: 9

## Slide 10: Timepix read-out chip Single pixel schematics
Independent signal processing is performed in each individual pixel
Very high level of miniaturization and functionality implementation
All 65 536 detector channels (pixels) are running in parallel

## Slide 11: Timepix readout chip layout
256x256 55µm square pixels
36M Transistors Serial readout (@100MHz) -> 9.17 ms (~100 frames per second) Parallel readout (@100MHz) -> 287 µs (~3000 frames per second)
Single pixel floor plan

## Slide 12: Pixel Operation Modes
Each pixel can be configured to operate in different mode independently to other pixels
Medipix mode Counter is incremented if incoming particle is registered
Time of Arival mode Counter is continuously incremented from the time when first particle is registered
Time Over Threshold mode Counter is incremented as long as a signal is over threshold
Masked mode pixel is disabled

## Slide 13: Medipix / Event Counting Mode
Each event registered is counted as 1
Counter value equals to a number of interacted particles
Event rate is limited by run up time and time of integration
Threshold
Pixel Counter

## Slide 14
High contrast imaging: Unlimited dynamic range
Single photon counting device can count unlimited number of photons, noise in images is given just by poissonian statistics:
  => Unlimited number of gray levels in images depending just on the beam intensity and exposure time.
  => Almost unlimited contrast
Mouse head – different scaling of same data
Hard structures: skull
Softer structures: muscles
Even softer structures
Surrounding soft tissue
Very light parts: hairs
Example 1:
X-ray transmission
Image of mouse head
(dose 0.9 mGy)

## Slide 15: Timepix / Time Of Arrival Mode
Threshold
Counts from passing threshold to closing shutter
Allows accurate timing of hits in individual pixels
Pixel Counter

## Slide 16
Measured events: 8He decays (TOA Mode)
Alpha decay
2ndbeta decay
1st beta decay
Primary ion
8He
β
β
α
n
120 ms
810 ms
< ns

## Slide 17: Time Over Threshold Mode Energy measurement
E.g. 20ke- ~1us = 40 x 25ns (i.e. base clock 40 MHz)
Residual errors come from non linearity with small charge signals and a slow return to baseline
Preamp has fast rise (90ns) but slow (500ns -2500ns) constant current return to zero
Threshold
Linearity of one pixel measured at three different threshold values
Counter Clock
Counter is incremented as long as a signal is over threshold

## Slide 18
per pixel energy measurement: Time Over Threshold mode
If the pulse shape is triangular then Time over Threshold is proportional to collected charge i.e. to energy.
Due to limited bandwidth the pulse can be NEVER perfectly triangular.
Non-linear TOT to energy dependence
Threshold
Time
Energy
Calibration
curve
Counter in each pixel can be used as
Wilkinson type ADC to measure energy of each particle detected.
Energy
TOT

## Slide 19
distance
+1 cm
distance
0 cm
And when per-pixel calibration is applied on measured TOT values…
Exemplar 241Am spectra
Exemplar 241Am alpha spectrum measured in air at two different distances between the radiation source and the Timepix detector

## Slide 20
Charge Sharing Effect
creation of clusters
Ionizing particle creates a charge in the sensor.
The charge is collected by external electric field => the process takes some time
Due to charge diffusion the charge cloud expands
The charge cloud can overlap several adjacent pixels => CLUSTER
Pixels in a cluster will detect the charge if it is higher than certain threshold
The Cluster size depends on:
Particle energy and range
Depth of interaction
Detector Bias Voltage
Local CCE (e.g. due to a material inhomogeneities and radiation damage)
Energy threshold
TimePix can measure charge in each pixel

## Slide 21: 4.93 MeV proton tracks in silicon pixel detector recorded by Timepix device. Exposition under different angles and different applied detector biases.
What is the spatial resolution? X- and Y-coordinates are determined with a precision of about 500nm. Determination of angle is with a precision of about 1o. It needs additional experiments.

## Slide 22: Flock of 11 MeV protons entering the silicon sensor under 85o
ΔE/Δx Bragg profile nicely pronounced, proton range about 960 μm
Fit by model

## Slide 23: Readout interface and its role in data the acquisition process
Detector supporting electronics
Acquisition control
Detector powering
Data transfer (USB, Ethernet, …)
Never ending need for a development of application specific variants of readout interfaces (vacuum operation, space environment, multi-detector arrays,…)

## Slide 24: Timepix based devices developed and tested in IEAP CTU

## Slide 25: Data Acquisition Control Software
PIXELMAN – IEAP CTU
Acquisition and control tool for Medipix & Timepix Detectors
Finally, it makes Timepix detector a powerful tool. Otherwise it is useful as a car without the steering wheel.

## Slide 26
SESTRA - School Education Set with Timepix for Radiation Analysis

## Slide 27: SESTRA Kit Components
Particle Camera MiniPixEDU (Timepix detector, calibrated)
Control Software Pixelman Simple preview & Pixet basic (acquisition, online visualisation, etc.,)
SZZ Alfa (241Am, 𝛼 and 𝛾 source, 9.5 kBq)
DZZ Gamma (241Am, 𝛾 source, 300 kBq, optional)
Potassium Salt (𝛽 and 𝛾 source)
Thoriated Tungsten Electrode (𝛼, 𝛽 and 𝛾 source)
Uranium Glass (𝛼, 𝛽 and 𝛾 source)
Mounting Rails
Source Holder
Camera Holder
Aluminium, Stainless, Copper, Brass and Lead Shielding Plates
Radiography Adapter Head +Samples with Hidden Patterns
Vacuum Cleaner Grate Adapter
USB Cable
Book of detailed guidelines “Experiments Using Pixel Detector in Teaching Nuclear and Particle Physics”
Set of kit accessories was designed according to practical experiences gained while using the Timepix for teaching of students...

## Slide 28: Detailed guidelines to experiments practicable with Timepix based particle camera
Wide set of 50 experiments ...involving detection and recognition of different kinds of ionising radiation in pixel detector, observation of natural background radiation, space originating radiation, basics of radiography….
Focused on high school students and university students by means of practical exercises to help them to understand physics and motivate them in further learning

## Slide 29: Mechanics of the SESTRA educational kit
Fast (re)arrangement of various experimental set-up(s)
Prepared for performing of real time demonstrations within a time span of the standard classes

## Slide 30: Set of Radiation Sources in the SESTRA kit
Thoriated Tungsten Electrode (𝛼, 𝛽 and 𝛾 source)
Uranium Glass (𝛼, 𝛽 and 𝛾 source)
Potassium Salt (𝛽 and 𝛾 source)
241Am 𝛼 and 𝛾 source 9.5 kBq (optional)
241Am 𝛾 source 300 kBq (optional)

## Slide 31: URANIUM Glass Radioactivity
Sample included in the kit
Uranium
235U, 0.72%, T1/2 = 7,0.108 years
238U, 99.274%, T1/2 = 4,5.109 years
Uranium serving as a yellowish-green glass colorant
Freely available on the market in the form of various decorative items

## Slide 32: Pixelman - Simple Preview
Measurement control, data acquisition and visualisation software
The main control window appears after starting application “Pixelman.exe”
One window instance for the real Particle camera and one instance for a virtual (file reader) device will appear on the screen.

## Slide 33
Experiment set-up:
Particle camera and computer, mounting rails, uranium glass sample placed in the source holder close to the detector
Settings:
Exp. count: 60 Continuous measurement: No
Mode: Spectrometer Exp. time: 1 s
Analysis type: Basic Min. level: 0
Bias voltage: 20V Max. level: 20
Integral mode: No Colormap: Hot
Uranium Glass
preparation of measurement

## Slide 34: URANIUM Glass Radioactivity Observation
Uranium glass as a weak source of mixed radiation field
Evidence of alpha, beta, gamma particle detection

## Slide 35: Review of the characteristic patterns
1) Dot
2) Small blob
3) Curly track
4) Heavy blob
5) Heavy track
6) Straight track
Photons and electrons (10keV)
Photons and electrons
Electrons (MeV range)
Heavy ionizing particles with low range (alpha particles,…)
Heavy ionizing particles (protons,…)
Energetic light charged particles (MIP, Muons,…)

## Slide 36
https://en.wikipedia.org/wiki/Alpha_particle
Exemplar alpha decay
Radiation Origin Overview
Alpha Particles

## Slide 37
https://en.wikipedia.org/wiki/Beta_particle
Exemplar beta- decay
Radiation Origin Overview
Beta Particles

## Slide 38
Radiation Origin Overview
Gamma Photons
*The nucleus in an excited state returns to the ground state by emitting a photon.
Exemplar gamma photon emission
https://en.wikipedia.org/wiki/Gamma_ray

## Slide 39: Uranium Glass Radioactivity Close Look Observation
Evidence of alpha, beta, gamma particle detection

## Slide 40: Uranium Glass Radioactivity Close look on a single particle
When zoomed-in, properties of single particle track can be obtained (deposited energy in keV, cluster area, track type classification)

## Slide 41: Uranium Glass Radioactivity as seen by the Timepix pixel detector
Several useful hints on software functionality
Getting a snapshot (Menu: Tools -> Snapshot) Displaying of integral frame composed of separate frames (Menu: Tools -> Integral frame)

## Slide 42
Kinetic Energy Absorbed in the Sensor,
How to find-out speed of hitting particle
The Einstein relation
E = E0 + Ek
Rest mass energy:
Alpha: E0 =3,735,000 keV ,
Beta: E0 = 511 keV
Speed of alphas?
Speed of betas?
Hint:
Use the excel table “Speeds of particles i lambda.xlsx” to compute speed of observed particles

## Slide 43
Kinetic Energy Absorbed in the Sensor,
How to find-out speed of hitting particle
What are the highest energies of detected alphas, bettas and gammas?
Speed of alphas
VS
speed of bettas?
Can speeds of alphas or betas be comparable to speed of light?
Emax ?

## Slide 44
Tungsten Welding Electrode with THORIUM
WTh-40
WTh-20
Thorium 232Th, T1/2 = 1,4.1010 years
Age of the Earth: 4,5.109 years

## Slide 45
Thoriated Welding Rod
preparation of measurement
WTh-40
WTh-20
Experiment set-up:
Particle camera, computer, mounting rails, thorium welding rod in a holder.
Settings:
Exp. count: 60 Continuous measurement: No
Mode: Spectrometer Exposition time: 1 s
Analysis type: Basic Min. level: 0
Bias voltage: 20V Max. level: 20
Integral mode: No Colormap: Hot

## Slide 46: Thoriated Welding Rod Radioactivity Observation
Thoriated electrode as a weak source of mixed radiation field
again, evidence of alpha, beta, gamma detection
Higher portion of alpha radiation is apparent

## Slide 47: Thorium Radioactivity as seen by Timepix pixel detector
Are there more energetic alpha and beta tracks in comparison to uranium glass observation?

## Slide 48: POTASSIUM Chloride Salt
89.28 %, emission of β- with energy 1.311 MeV
20.72 %, emission of gamma with energy 1.5049 MeV
KCl - Potassium Chloride
Natural abundance 0.0117% of radioactive isotope 40K with half life 1.277*109 years
Decay modes

## Slide 49
Potassium Chloride Salt
preparation of measurement
Experiment set-up:
Particle camera and computer, container with potassium salt inserted into the holder at close position to the detecto.
Settings:
Exp. count: 60 Continuous measurement: No
Mode: Spectrometer Exp. time: 1 s
Analysis type: Basic Min. level: 0
Bias voltage: 20V Max. level: 20
Integral mode: No Colormap: Hot

## Slide 50: …Few facts about potassium
How much potassium does a human body contain?
A human body of 70 kg weigh contains about 140 g of potassium while just (0.0117%) a small portion of 0.0164 g is the radioactive isotope 40K
Aren’t we living radiation sources??? Corresponding activity of such amount is 4300 Bq (decays/sec)
Are bananas save to eat???
1kg of banana contains 0.390 g of potassium …where 0.00004563 g is a portion of the radioactive isotope 40K
…with activity of 12 Bq (decays/sec)

## Slide 51: Potassium radioactivity observation
Container filled with the potassium chloride (KCl) salt
Weak source of gamma and beta radiation

## Slide 52: Potassium Radioactivity as seen by Timepix pixel detector
Obvious difference to Uranium glass and Thoriated electrode experiment - no alpha particle tracks present

## Slide 53
SZZ Alfa
241Am isotope radiation source
E(α) = 5 500 keV
Half-life of 241Am is 432 years.
E(γ) = 59.5keV
Activity 9.5 kBq
Adapted for educational purposes
Source of alpha and gamma radiation

## Slide 54
1 - Closed
3 –“Short collimated“
2 - „Sieve“
(multihole)
4 –“Long Collimated“
SZZ Alfa Radiation Source
4 selectable output configurations
Note: Radiation in other directions is shielded out by a brass body

## Slide 55
9. ENERGY OF ALPHA PARTICLES EMITTED FROM SZZ Alfa 241Am radiation source
Experiment set-up:
Particle camera, computer, mounting rails, SZZ Alfa placed in a holder.
Settings:
Exp. count: 60 Integral mode: No
Mode: Spectrometer Exposition time: 0.05 s
Analysis type: Basic Min. level: 0
Bias voltage: 20V Max. level: 20
Continuous measurement: Yes Colormap: Hot
Visual Tools: Histograms of particle properties - Energy all frames (tab Alpha)

## Slide 56: SZZ Alpha Radiation Source Americium 241 source observation
Source of alpha and gamma radiation low activity, 9.6 kBq
Suitable for demonstration of properties of heavy charged particles
Collimated vs Non-collimated Beam

## Slide 57
Beam Collimation
241Am
241Am
Brass body
shielding
Short collimated output Long collimated output

## Slide 58
Loss of Alpha Particle Energy in the air
distance
1 cm
distance
0 cm
LET=1590 keV/cm
for 3.5 MeV alpha
a~1015 m/s2
Experiment set-up:
Particle camera and computer, SZZ alfa placed in the holder, distance in between the detector and radiation source is changed
Settings:
Exp. count: 60 Continuous measurement: YES
Mode: Spectrometer Exp. time: 0.05 s
Analysis type: Basic Min. level: 0
Bias voltage: 20V Max. level: 20
Integral mode: No Colormap: Hot
Visual Tools: Histograms of particle properties - Energy all frames (tab Alpha)

## Slide 59
Americium 241 represents a source of monoenergetic alpha particles but there are displayed several peaks in the spectrum
Energy of higher peaks exceeds energy of americium alphas
What happens if frame exposition time is significantly prolonged???
Effect of particle track overlapping

## Slide 60
Loss of Alpha Particle Energy in other materials
What happens if some material is placed in between the alpha source and the detector???
…Sheet of paper, aluminium wrapping foil, thin plastic foil, …..
Experiment set-up:
Particle camera and computer, SZZ alfa placed in the holder, various materials are placed in between the detector and radiation source
Visual Tools:
Histograms of particle properties - Energy all frames (tab Alpha)
Histograms of particle properties - Histogram of rate (tab Alpha and Gamma)
the edge of paper
The entire chip area is covered
Is the covered area really empty without any tracks?

## Slide 61
Statistical Nature of Radioactivity
Decay n - Random Variable
Alpha particle flux in time Flux histogram
Gama particle flux in time Flux histogram
Experiment set-up:
Particle camera and computer, SZZ alfa placed in the holder, multihole output is selected, radiation source close to the detector
Settings:
Exp. count: 200 Continuous m.: YES
Mode: Spectrometer Exp. time: 0.05 s
Analysis type: Basic Min. level: 0
Bias voltage: 20V Max. level: 20
Integral mode: No Colormap: Hot
Visual Tools: Histograms of particle properties - Energy all frames (tab Alpha or tab Gamma)
Poisson Distribution

## Slide 62
Background Radiation with Origin in Space
Exemplar frames measured at different conditions: one frame represents response acquired at the vertically oriented sensor at the airport. The next one was acquired on board of the airplane on the standard flight level at the vertical sensor orientation and the last one at the horizontal sensor orientation.
Detection of cosmic muons and their contribution to background radiation on the ground.

## Slide 63
Linear Tracks of Interacting Particles at the Polar Angle
Significantly different results of muon observation are obtained in dependence on the detector orientation
Note the typical dimensions of Timepix sensor 14 x 14 x 0.3 mm (w x l x h)

## Slide 64
WHY MUONS OF LOW INCLINATION DO NOT REACH TO GROUND?
Half-life of muons is: 2,2 μs.
How long distance can be reached until it decays?
Presumption, muon was created at altitude of 10 km, its velocity is 0,999c.
Can it reach the ground?
Classical physics: It can not reach the ground
STR: It can reach the ground
(in dependence inclination on angle)

## Slide 65
Working with Pre-measured Data Using the Virtual (filedevice 3000) Paraticle Camera
Select Folder: Location of the measured data
The virtual particle camera allows to replay experimental data measured in the past
same visualisation and processing functionalities are available as if a real particle camera would be connected to a computer

## Slide 66: Radiation field observation on board of the airplane as seen by the particle camera
Recording from the flight from London to Prague
Significant difference in field composition and intensity when flying or when landed…

## Slide 67
Close look on airplane flight observation recorded by the particle camera
Typical composition of radiation field at flight level (high count of muons)
Occasional detection of heavy energetic ions

## Slide 68
Particle flux Φ in dependence on time (with 10 s step)
On Earth 1
On Earth 2
On board of the airplane
Radiation intensity observed on Earth vs on board of the airplane

## Slide 69: Dosimetry in space: SATRAM – ESA Proba-V satellite
Characterization of mixed radiation field on low orbit of PROBA-V satellite
Altitude ~ 800 km
Timepix for the first time outside in the space
Launched in May 2013

## Slide 70
SATRAM
(Space Application of Timepix Radiation Monitor)
The same kind of pixel detector Timepix as one embedded in the particle camera MiniPixEDU of the SESTRA educational kit
on board of Proba-V ESA satellite
Radiation field recordings available for research and also for educational purposes
mission on LEO - altitude 820 km
Timepix for the first time outside in the space
Launched in May 2013

## Slide 71: SATRAM Radiation Observation on the Earth Orbit
Radiation field as seen by Timepix detector
Mission data available online at the web portal:
https://satram.utef.cvut.cz/
Variation of radiation field composition in depence on the earth orbit position
Notable difference in field composition when compared to observations performed with natural radiation sources in the SESTRA educational kit

## Slide 72: Timepix/ESA Proba-V: LEO space radiation @ 820 km
HETPs: Highly energetic heavy charged particles (ions) 🡪 HZE’s

## Slide 73: Timepix/ESA Proba-V: LEO space radiation @ 820 km
LETPs: Energetic light charged particles (I) + nuclear interactions

## Slide 74: Measured radiation map by Satram device in orbit around the Earth at an altitude of 820 km from the earth's surface obtained within 36 days from January 1, 2014 to February 7, 2014 logarithmic scale in μG/hr.

## Slide 75
Radon as a common source of background radioactivity
Noble gas originating from decay of radium
It further decay through the serie of daughter products

## Slide 76: Radon as a common source of background radioactivity
The histogram of alpha particles emitted from a paper tissue right after the air filtering was stopped.
Energy peaks correspond to the values presented in the scheme of the decay chain.

## Slide 77: Radon - Easy way how to prepare own radiation source
Preparation requires just usage of a vacuum cleaner + grate adapter + paper tissue (or head mask) (ideal location - non-ventilated basement of an old building)
After several minutes letting air pass through the filter, radon daughter products get captured in the filter
Then the paper tissue is placed on the top of the particle camera and radiation measurement is started

## Slide 78
Comparison of Radioactivity observed in the
Non-ventilated (left) and ventilated (right) room
Demonstration of the radioactivity of the paper tissue that was used as an air filter in one house in Pardubice – Czech Republic
The filtering took 5 minutes and exposure time was 10 minutes in both cases

## Slide 79
(Alpha) Radiography
What is
Hidden
Inside?
Settings of Filedevice: Radiation source other, analysis type OFF, continuous YES, integral YES, exposure count 60, exposure time 0.01 s, max. level 1, colormap GRAY.
Settings of Particle camera: Radiation source other, analysis type OFF, continuous YES, integral YES, exposure count 60, exposure time 1 s, max. level 1, colormap GRAY.
Samples with hidden patterns

## Slide 80: (Alfa) Radiography Demonstration
Impact of
Beam
collimation
Impact of
Sample
position
(magnification)
even µm material thickness matter

## Slide 81
ABSORPTION of gamma particles in metals
Settings of Simple preview: Radiation source americium, bias voltage 50 V, continuous NO, integral NO, exposure count 300, exposure time 0.5 s, max. level 1, colormap GRAY.
Metallic
plate

## Slide 82: Absorption of Gamma/X-Ray in shielding plates of various materials
Aluminum vs Brass vs Lead
vs OTHER materials vs Background?
SZZ Alpha Americium 241 source 9.5 kBq activity
DZZ Gamma Americium 241 source 300 kBq activity
Settings of Filedevice: Radiation source other, analysis type OFF, continuous YES, integral YES, exposure count 60, exposure time 0.1 s, max. level 1, colormap GRAY.
Settings of Filedevice: Radiation source other, analysis type OFF, continuous YES, integral YES, exposure count 60, exposure time 1 s, max. level 1, colormap GRAY.

## Slide 83
Radiography (Gamma)
What is hidden
inside?
Settings of Filedevice: Radiation source other, analysis type OFF, continuous YES, integral YES, exposure count 60, exposure time 0.01 s, max. level 1, colormap GRAY.
Samples with hidden patterns
Settings of Particle camera: Radiation source other, analysis type OFF, continuous YES, integral YES, exposure count 60, exposure time 1 s, max. level 1, colormap GRAY.

## Slide 84: (Xray) Radiography Demonstration
Prove of basic working principle
In contrary to more advanced imaging

## Slide 85: Hidden pattern examples….
Airgun pellet
Paper clip

## Slide 86
Thank you for your participation
Any initiative in a way to further cooperation is welcome!!!
outreach.and.education@utef.cvut.cz

## Slide 87: Course Outline
Part 1
Introduction into Timepix detector, particle camera working principle, content of SESTRA kit, Pixelman simple preview software and its functionality
Part 2
Uranium glass experiment, Potassium experiment, Thoriated electrode experiment, Study of particle properties, Using of online visualisation tools, americium isotope radiation source, beam collimation, study of alpha radiation properties, start of long term background measurement
Part 3
Evaluation of long term background measurement, Radiation at on Earth ground vs orbit, observation of radon decay, Cosmic radiation, utilization of virtual particle camera, utilization of advanced particle type analysis
Part 4
alpha radiography, absorption of gammas in metals, gamma radiography, Own radiation sample study
Discussion