## Slide 1
Nuclear Energy
Fusion Reactor Instrumentation and Approach
By Michael Walsh
ITER Organization, Provence, France
The views and opinions expressed herein do not necessarily reflect those of the ITER Organization.

## Slide 2
Nuclear Energy – Fusion
https://euro-fusion.org/fusion/fusion-on-the-sun/

## Slide 3
What fuel is used in the sun?
Hydrogen

## Slide 4
What fuel is practical on earth?
Deuterium
Tritium
In reality a mix of D/T us used as the practical way forward

## Slide 5
>100 Million degrees Kelvin needed, 1eV is 11605 K
D+T => n (14 MeV) + α (3.5 MeV)
Deuterium-Tritium Fusion
https://www.researchgate.net/figure/Reaction-rate-averaged-over-a-Maxwellian-energy-distribution-as-function-of-the_fig1_338596522

## Slide 6
What happens?
Deuterium
Tritium
High energy
Neutron
Helium
nucleus
Need high speed of D and T ions to force collisions
Results in Helium-nucleus and n and something else too……………..

## Slide 7: Magnetic Field
Circular Road leads to a clever scheme known as a Tokamak- other options also exist

## Slide 8
text
text
text
text
Many Different Options
I will explore the Tokamak now

## Slide 9
Example Magnetic Fusion Power Generators- TFTR, JET proved- ITER coming

## Slide 10
TF Coil – To contextualise
Mass of (1) TF Coil:
16 m Tall x 9 m Wide, ~360 t
Boeing 747-300
(Maximum Takeoff Weight) ~377 t

## Slide 11
text
text
text
text
11
TOROIDAL FIELD COILS
18 coils
41 gigajoules
11.8 Tesla
Each coil:
360 tonnes
9 x 17 metres
Status:
Manufacturing of all 19 coils completed. All coils have been delivered to the ITER site.

## Slide 13
The Site Recently [Provence, France]

## Slide 14
Who is working on this Project?
We are here

## Slide 15: An International, Integrated Team
Eoin Walsh
I
T
E
R
T
E
A
M
I
T
E
R
T
E
A
M

## Slide 16
Diagnostics/instrumentation is to provide the measurements necessary to control the plasma

## Slide 17
Spectral Areas Covered by the Diagnostics
In ITER- the plasma emits in all regions and diagnostics make good use of this
250 Million K
IOCT
RFDA
IOCT - CEA
JET
Radial Neutron Camera Schematic

## Slide 18
Q=10 scenario with (ELMy H-mode ):
Ip= 15MA, Paux= 50MW, H98(y,2) = 1
This allows us to control what is happening?
Some example uses of real-time measurements?

## Slide 19
Plasma shape and size
Neutrons
Light emitted
Hot surfaces
Gases
Safe operation
Around 50 diagnostics and >100 projects needed to realize the measurement systems
Things to Control

## Slide 20
To Observe – Systems are either
Passive
or
Active

## Slide 21
Passive Systems
Measure what is happening
Example- Heart monitor
In ITER- place detectors around the machine and measure what is happening

## Slide 22
Passive Systems Examples

## Slide 23
Plasma Current and magnetic Field?
Magnetic fields created by putting current in coil
ITER will have 15MA flowing in the “jelly” like plasma?
MagLab

## Slide 24
how to measure local magnetic field?
Faraday’s law of inductance
Inductive coil
3. Hall-effect sensor
I.Duran for WEST
2. Micro Electro-Mechanical System (MEMS)
VTT

## Slide 25
design procedures
Spatial allocation
Engineering Analysis
(Loading, structural, welding…)
VV
Blanket
Distribution
Functional
REQs.
Assembly
& Installation
Integration
design
components
specification,
prototyping,
lab testing…

## Slide 26: inductive coil design
N
A
dB/dt
A
equivalent circuit
: effective area
inductance
resistance
f-response

## Slide 27: step forward: sensor development
LTCC Sensor
(Low-Temperature Co-fired Ceramic)
metallic ink via filling on ceramic substrate
Substrates stacking, vias connected
sintering
Courtesy Consorzio RFX
small and thin (~few mm thickness)
easy to integrate and cool, excellent thermal performance
suitable for long-pulse, ideal for equilibrium sensors
ceramic brittle, need to keep temperature uniform
structural integrity after neutron radiation (initial test promising)

## Slide 28
Delivery of Integrated Sensor Housing [size for each is 15cmX15cmX10cm]
Site delivery of integrated Sensor Housing (just over 150 sensors out of 400 in total)
Items packaged in zip plastic bags and carton boxes
Carton boxes stacked and loaded into wooden crates

## Slide 29
Outer Vessel Diagnostic Coils fully installed on the Vacuum vessel Sector 6
OVC Diagnostic coils(EUDA)

## Slide 30
High Frequency (MHD)
Real Magnetic Coil Example
Distribution of Sensors on the Vessel and Divertor
Inboard
Outboard
Components delivered

## Slide 31: Status of 55.Ax FP magnetics by delivery milestone fraction (parts quantity in brackets)

## Slide 32
Plasma Shape measurements and Control

## Slide 33: What do we do with all the magnetic signals?
Reconstruction
Numerical Code
(EFIT)
Magnetic Flux Topology (reconstructed)
Magnetics densely distributed on VV surface inside and outside the vessel wall
Very importantly- these measurements can be used to grow the plasma and maintain it in real-time within centimeters of the walls of ITER and keep it there for very long periods
A very serious undertaking given the hostile environment!

## Slide 34
Plasma Start up
ITER Plasma using Magnetics
The magnetic field is also measured using an array of coils
With these - the plasma shape, position and many other parameters can be determined

## Slide 35
How about getting samples of dust from inside ITER

## Slide 36: Dust Collection Head design and prototype
Dust Collection Container
Biased grid assembly
Ceramic insulators
HV contact electrode
Direction of container removal
Dust tube guidance spring
First version of dust collection head prototype has been manufactured and tested
Dust collection efficiency has been tested
CAD – Design
Prototype
110 mm
Opening for the dust container
Latching tailpiece

## Slide 37
Tungsten Dust 1-100 µm
Aluminium Chips up to 1500 µm
Dust sample before collection | Dust sample after collection
Prototype demonstrated its ability to mobilize dust particles of different sizes and collect them with approximately 84% efficiency.

## Slide 38
Infrared Viewing systems

## Slide 39
Let’s take an example measurement
Infrared or also known as IR measurement
Can’t see with naked eye but we have detectors

## Slide 40
Infrared Viewing?
infrared map of sea surface temperatures
an infrared image of a cup holding a hot drink (degrees F)

## Slide 41
How about the walls of the machine?
What happens if they get hot?
When they get hot - they emit a characteristic signal
This is well measured using infrared

## Slide 42
Key areas are monitored – like Divertor
If this gets too hot –we have a big problem
The IR system will monitor this
And allow us to stop the operation if needed

## Slide 43
Now to Active Diagnostic Systems

## Slide 44
Active Systems
Externally influence to see effect
Example- Magnetic Resonance Imaging (or NMR)-
In ITER- launch laser, microwave or Particle beam and look at various physics effects

## Slide 45
Electron Density measurement

## Slide 46: TIP [Toroidal Interferometer/Polarimeter]
Principle
  IR interferometer
  2nd interferometer for vibration compensation
  Polarimeter for fringe skips
Design Features
  CO2 laser, 10.6μm;
  2nd laser - Quantum Cascade ~5μm
  Corner cube retroreflector (CCR) in blankets
Particular Challenges
  Retroreflector design
  Long beam path (>50m round trip)
  Alignment issues
  Large vibrations
interferometry
overview of TIP in vessel
USDA /PPPL/General Atomics/IO

## Slide 47
TIP System Overview

## Slide 48
I&C is a Critically important system for ITER

## Slide 49: Electronics and Cameras
  Need to be able to face up to some neutrons and gammas
  Need also to be able to take local magnetic fields (not DC-DC transformers!!))
  Radiation effects Data for components is important

## Slide 50
Electronic Components and Radiation
577 in the port-cells, 540 in galleries, 726 in the shielded corners and 1646 in Diag Building

## Slide 51
Use configurable code modules provided
Still works with CCS out of the box, all interfaces handled by infrastructure
Signal exchange fully transparent
Interface management drastically simplified
Highly flexible, easy to maintain, scalable
Synergy possible between diagnostics for similar functions (binning, averaging, calibrating, 2-out-of-3 voting, etc.)
Diagnostic under resp. of DA 1
Diagnostic under resp. of DA 2
Diagnostic under resp. of DA 3
IO resp.
Real-time signal exchange
Common use of the ITER
Real-time framework
I&C Infrastructure

## Slide 52: I&C for the Power distribution for the Diagnostics
The I&C subsystem of 55.NE.X0 controls and monitors the power supply to every diagnostic
A prototype has been installed in Corbières to verify operation and HMI

## Slide 53
The big Picture

## Slide 54
text
text
text
text
Who works for ITER?
The ITER Organization employs ~1250 staff from 35 countries, plus about 500 experts and subcontractors.
ITER Domestic Agencies (mostly Fusion for Energy, the EU-DA) has about 350 employees in France.
On the construction site, we also have about 2500 additional workers.
Globally, ITER partners also employ more than 3000 scientists, engineers, technicians, and support staff.

## Slide 55: Work to be done roughly?
Funding (getting enough!)
Hiring (the right people!)
Safety & Training (takes time in new industries!)
Managing budgets and projects and Administration
Mechanical and Electrical Engineering and Physics
System Engineering (essential for big projects!)
Managing people (everyone is different!)
Computer Aided Design (CAD) and Diagrams
Instrumentation & Control (I&C) and real-time programming
Conflict management
Leading and Team Building (developing a positive culture)
Overall Design and Ideas and Modelling (collaborative!)
You must work out what your strengths are, and what are your areas where you could develop
Notes: Check animation order for the new stuff

## Slide 56
See Video [on disk]
https://youtu.be/iHZjgPSfZNs?si=DnKo3JwsR7dr2DWb

## Slide 57: Conclusion – I issue a challenge to you all
  Work to high quality, making sure to balance time and cost
  Look for opportunities to innovate and simplify using modern methods, keep up with the times
  Integrate systems to simplify where possible
  Work hard and always believe in yourself

## Slide 58
Thank you!
ITER Open Doors Day
June 2023

## Slide 59
text
text
text
text
ASSEMBLING THE MACHINE: ITER Assembly Hall
September 2023
59

## Slide 60
a
text
text
text
text
60
CRYOGENIC PLANT
75kW @ 4 Kelvin
Equipment installation is complete, and has entered pre-commissioning phase.

## Slide 61
text
text
text
text
CHALLENGES OF
FIRST-OF-A-KIND COMPONENTS
… but the sector-to-sector welding of Vacuum Vessel sectors was reassessed to be too challenging to perform in situ, based on the previously identified geometric non-conformities in the field joints.
61

## Slide 62
a
text
text
text
text
CHALLENGES OF FIRST-OF-A-KIND COMPONENTS
Leakage was also identified in thermal shield cooling piping due to chloride stress corrosion.
62

## Slide 63: Power Creation
Picture courtesy of the SOHO/EIT collaboration
SunFusion
START Machine-CCFE
Our Approach to Fusion on earth
Magnetic Confinement Fusion- Tokamak
This leads to ITER

## Slide 64
55B4 D0 Neutron Flux Monitor EQ#7 – NFM-7
Lower cryostat cylinder LCC
NFM7

## Slide 65: Fusion Product - Fusion Power
Fusion power limit of 500 MW – for archiving for nuclear licensing
Redundancy through large number.
Neutron Flux Monitors NFM (fission chambers) Front end electronics in port-cell Radiation hard preamplifiers?
Calorimetry for diversity
Electronics in diagnostics building Details to be developed