## Slide 1: Radiation Detection at International Borders
Richard Kouzes, Ph.D.
Laboratory Fellow Emeritus
Pacific Northwest National Laboratory
IEEE Nuclear and Plasma Sciences Society School
Rabat, Morocco
July 2024
PNNL-SA-135051
Notes: Abstract: Radiation Detection at International Borders
The detection of ionizing radiation is a little over 100 years old, dating from the first observation of natural radioactivity. Today, radiation detection plays a key role in diverse fields from medicine to defense to basic science. For homeland security, countries around the world are deploying passive radiation detection instrumentation to interdict the illegal shipment of radioactive material crossing international borders at ports of entry. These efforts include deployments in the United States and several European and Asian countries by governments and international agencies. This talk discusses our experience with radiation detection interdiction at international borders and other applications to national security.

## Slide 2: IEEE is …
The Institute of Electrical and Electronics Engineers
  Largest technical/scientific organization – 38 Technical Societies.
  International with activities in all regions of the world.
  Organizes the most technical meetings with highest aggregate attendance.
Nuclear and Plasma Sciences Society
  Computer Applications in Nuclear and Plasma Sciences
  Fusion Technology
  Nuclear Medical and Imaging Sciences
  Particle Accelerator Science and Technology
  Plasma Sciences and Applications
  Pulsed Power Systems
  Radiation Effects
  Radiation Instrumentation

## Slide 3: Pacific Northwest National Laboratory
Physical Sciences Facility
  Ultra-trace Laboratory
  Radiation Detection Laboratory
  Materials Science & Technology Laboratory
  Underground Laboratory
  Large Detector Laboratory
U.S. DOE National Laboratory
Office of Science Lab
> 4500 staff
> $1B

## Slide 4: Talk Outline
The Threat at International Borders
Radiation Detection
Border Security
Challenges and Solutions

## Slide 5: The Threat

## Slide 6: The Problem And The Threat
Weapons of Mass Destruction (WMD)
Improvised Nuclear Devices (IND)
Special Nuclear Material (SNM)
Radiation Dispersal Devices (RDD)
US DOE: 4 kg 239Pu or 25 kg highly enriched uranium (HEU) are sufficient for a nuclear explosive device
IAEA Significant Quantity: 8 kg 239Pu or 25 kg HEU

## Slide 7: Orphaned Sources
Notes: Gamma backscatter and neutron induced gamma emission are both used to look for hydrogenous material.

## Slide 8: Soviet Sr-90 (~40 kCi) RTG Recovered in Georgia
Radioisotope thermoelectric generator (RTG)
December 2001: three woodsmen in former Soviet republic of Georgia suffered severe radiation burns after handling the strontium-90 core from an abandoned radiothermal generator.
Notes: RTGs exist in the thousands

## Slide 9: 1987 Incident in Goiania, Brazil
Container of 137Cs scavenged from defunct medical clinic
Children played with the glowing powder (1400 Ci)
11 days before discovered (up to 100 miles away)
Four people died (450-600 rem)
28 suffered radiation burns, 249 contaminated
More than 112,000 requested medical monitoring!
Clean-up effort cost ~$20M (275 truckloads of waste).
Notes: 5000 m^3 of stored waste
3800 200 liter drums
1400 1.2 m^3 boxes
10 32 m^3 ship containers
6 waste containers
7 houses demolished
Cheap labor
50% drop in agriculture, housing prices fell, cars were stoned, tourism dropped
Goiania ~800,000 people
CsCl in 2” x 2” source 1375 Ci, 456 rad/hr @ 1m
Sept 13 - salvagers took home and opened source
Sept 15 - 1 sought medical help - sent home as allergic reaction to bad food
Sept 14-15 - disassembled, punctured source, scooped out material, sold to salvage yard
Sept 28 - wife of junk yard dealer sought medical care - carried source to clinic; diagnosed as tropical disease
Doctor got 100 rad dose
Suspected radiation
4 deaths at 1 month: wife, 2 junk yard employees, 6 yr old niece
Oct 3 - situation fully appreciated

## Slide 10: Radiation Detection Basics
r

## Slide 11: History of Nuclear Physics
1895 – Roentgen discovers x-rays
1896 – Becquerel finds U salts fog film
1897 – Thompson discovers the electron
1903 – Curies get radiation burns
1903 – Rutherford & Soddy “radioactive change”
1905 – Einstein publishes E = mc2
1907 – Rutherford notes “scattering of α rays”
1911 – Rutherford announces nuclear atom from measuring α scattering
1914 – HG Wells publishes “A World Set Free”
1942 – Nuclear reactor

## Slide 12: Radioactivity – a, b, and g Decay
De-excitation photon hf = Ef - Ei
Excitation increase PE (Ei to Ef)
Chart: 
neutrons/protons
p
n
e+
ν
n
p
e-
ν
_
g decay
β- decay
β+ decay
a decay

## Slide 13: Radioactivity – Fission
Fission of a heavy nucleus such as plutonium and uranium can be spontaneous or induced
Fission produces two daughter nuclei and one to several neutrons
For example: 235U  90Rb + 143Cs + 2n
Kouzes, NIM 584 (2008)
Neutron
Spectra

## Slide 14: Detection of Radiation
Since there is radiation, how do you detect these gamma rays, beta rays, alpha particles and neutrons?
130 years since discovery of x-rays and natural radioactivity
Charged particles and photons interact with matter through the electromagnetic force, depositing energy
Neutral particles (neutrons) must scatter off protons that then deposit energy, or are absorbed, causing fission

## Slide 15: Radiation Interaction With Matter
Summary of α, β, γ, x-ray, muon radiation interaction with matter:
  All radiation releases energy in matter in the form of electrons and ionized atoms
  Biological effects come from chemical changes produced by freed electrons, destroyed molecules, and chemical radicals that attack cell components
Energy | α | β | γ | n
1 MeV | 0.0006 cm | 0.5 cm | ~10 cm | ~10 cm
10 MeV | 0.01 cm | 5 cm | ~36 cm | ~50 cm
Range Table in Tissue

## Slide 16: Radiation Detection Effectiveness
Source activity (A)
  Strength, type, and energy
Detection geometric efficiency (eg ~ 1/r2)
  Source and detector size and distance
Detector intrinsic efficiency (ei)
  Material, geometry, collection
Shielding (S ~ e-x)
  Amount, type, and geometry
Background (B)
  Type, energy distribution, and intensity
  Naturally occurring radioactive material (NORM)
Time for detection (t)
  Statistics for signal to noise
  Operational limitation
Expert/Automated analysis of information
Time
Distance
Shielding
r

## Slide 17: Gamma Ray Detectors
Gas counters
  Ionization chambers
  Proportional counters
  Geiger counters
Scintillators
  NaI(Tl)
  Plastic: polyvinyl toluene (PVT)
Solid state detectors
  Si
  High purity Ge (HPGe)
CsI
NaI(Tl)
PVT
HPGe
Notes: Gamma and neutron detection are complementary.

## Slide 18: Alpha and Beta Detectors
Gas detectors or scintillators
Ionization chambers, proportional counters and Geiger counters for alphas
Plastic scintillators for betas
Thin windows
Notes: Gamma and neutron detection are complementary.

## Slide 19: Neutron Detectors
Neutrons observed from fission sources
Energy not unique to special nuclear material (SNM) – Pu and U
Background
  From cosmic rays
  ~1/1000 of gamma-ray background
  Few commercial sources
Many scatterings prior to capture
Difficult to shield
Detectors: 3He, 6Li, 10B
3He Tube
Moderator
Bonner Sphere
Notes: Gamma and neutron detection are complementary.

## Slide 20: Border Security

## Slide 21: The Global View of Commerce
20 foot Shipping Container Traffic Per Year

## Slide 22
Mail/ECCF
Land Border
Maritime
Air Cargo
307 Ports of Entry representing:
621 border sites to protect
332,622 vehicles per day
The Challenge: U.S. Ports of Entry
57,006 trucks/containers per day
2,459 aircraft per day
580 vessels per day
100% of containerized cargo is screened for radiation
Notes:   The dots represent each of the ports of entry. Each has unique challenges to be addressed: quantity of traffic, natural radiation background, seasonal variation in cargo, environmental/weather

## Slide 23: Radiation Portal Monitors
Used for decades in the scrap steel industry.
Sensitive to small quantities of SNM & RDD materials.
Large area, high-efficiency gamma-ray detectors & 3He neutron detectors.
Best cost/performance ratio of any detection technology.
Provide the capability to rapidly screen cargo.

## Slide 24: Homeland Security Systems
Second Line of Defense / Megaports (1997)
  RPMs deployed overseas
Radiation Portal Monitor Project (2002)
  Over 1600 systems deployed in US
Guardian Program (2003)
  Screening at DoD bases

## Slide 25: Traffic Monitoring Example
Traffic flow over 7 hours - each dip or rise is a passing vehicle
Cars and trucks moving through a portal block background radiation
Notes: Example of RPM traffic monitoring.

## Slide 26: Border Security Examples
Notes: US Customs (CBP) is deploying COTS at POEs

## Slide 27: Layered Approach: Imaging
X-ray and gamma-ray transmission or backscatter imaging
Aracor Eagle
AS&E

## Slide 28: Challenges & Solutions

## Slide 29: Background Radioactivity Sources
Radiation comes from cosmic rays, the ground, the air we breath, surrounding buildings, medicine and the food we eat
Exposure to people depends on where you live (e.g., altitude, local geology) and how you live (e.g., medical exposure, work exposure, flying)
Chart: 
Radon
Cosmic
Rays
U, Th, K
Food
Medical Exposure
n
m
n

## Slide 30: Naturally Occurring Radioactive Material and Man-Made Sources
NORM is the dominant source of alarms for cargo, but not passenger cars
NORM, and technologically enhanced NORM, contain:
  uranium series (238U; 4.5 billion years)
  thorium series (232Th; 14 billion years)
  potassium (40K; 1.3 billion years)
Commercial isotope examples
  241Am, 133Ba, 137Cs, 57Co, 60Co, 192Ir, 226Ra, 252Cf, nuclear fuel, depleted uranium
Medical radioisotopes
  92% of procedures are 99mTc for stress tests
  18F, 14C, 111In, 57Co, 201Tl, 153Sm, 89Sr, 131I, 67Ga, 51Cr
  One in 2600 Americans carries a radioactive burden large enough to be seen in an RPM
Skyshine from radiography

## Slide 31: “Nuisance” or “Innocent” Alarms
Neutron Alarms - Few sources
  Troxler gauges, nuclear fuel, yellowcake, well logging sources
  Ship effect
Gamma Ray Nuisance Alarms
  Naturally Occurring Radioactive Material
  agricultural products like fertilizer
  kitty litter
  ceramic glazed materials
  aircraft parts and counter-weights
  polishing compounds and abrasives
  propane tanks
  road salt
  welding rods
  ore and rock
  smoke detectors
  medical radioisotopes
  skyshine
Troxler Gauge

## Slide 32: Skyshine
Radiation scattered from the air above a source
Radiography (192Ir, 60Co) or “x-ray” imaging sources
Very large sources (~100 Ci)
Can produce interference with radiation detection systems at very large distances (1% strength at 200 m)
Impacts all detector types (gross-counting or spectral)
Requires mitigation through distance, shielding, and operations
192Ir Radiography Skyshine Source

## Slide 33
Neutron Ship Effect Event Example
33
3 neutrons in 30 microseconds in an IAT detector

## Slide 34: Energy-Based Algorithms for Enhanced Portal Sensitivity
Energy-based algorithms can preferentially alarm on low-energy gamma-ray signals
  HEU, WGPu & Medical Radionuclides
Energy discrimination avoids many NORM alarms
  NORM spectra contain a significant high-energy component from thorium and potassium
Energy ratio modeling also handles baseline depression
  Background spectral ratios nearly constant with and without a vehicle in the portal

## Slide 35: Energy-Window Ratio Algorithm
Use PVT spectral shape for discrimination
Low
Window
High
Window
Using ratios of energy regions enhances discrimination significantly and minimizes effect of intensity variations
Notional
Threshold
Create the ratio:

## Slide 36: Observations of Plastic Aging
Polyvinyl toluene (PVT) and polystyrene (PS) are widely used plastic scintillators
Most new and old PVT & PS shows no significant change in response to gamma radiation with temperature
Various forms of damage are observed in PVT and PS
Internal temporary and permanent fogging are two forms of damage that may be seen even at room temperature
Severe fogging sometimes observed at low temperature
The effect, first observed in 2009, was not reproduced in the lab for new PVT samples until 2013
36
Surface Crazing
Surface Clouding
Internal Fogging

## Slide 37: PVT Degradation Mitigation
Keep the plastic in an environmentally controlled space
Heat the plastic so it never gets cold
Dehumidify so water is not available to permeate the plastic
Encapsulate the plastic in a water impermeable membrane
  Requires material with MVTR ~ 10-5 g·m-2·d-1
  Requires sealants for edges
  Might require electrical feedthroughs
New formulations of plastic scintillator
37

## Slide 38: Conclusions
Radiation detection is important for a wide range of applications
Radiation detection at borders is challenging
NORM and medical alarms can be operational limiting factors for border interdiction
Computer simulation is widely applied to development of radiation detector systems
Gamma ray and neutron detection are very active fields of research for developing new technologies
38

## Slide 39: Acknowledgements
Thanks to IEEE NPSS for supporting this lecture.
Support for this work came from:
  US Department of Energy
  The US Department of Defense
  The US Department of Homeland Security
  PNNL
39

## Slide 40: Pacific Northwest National Laboratory
Questions

## Slide 41: Backup Slides

## Slide 42: International Incidents
42
IAEA reported 18 incidents involving the smuggling of weapons grade nuclear materials between 1993 and 2004.
1994: police at the Munich airport intercepted a suitcase from Moscow with half a kilogram of nuclear-reactor fuel (363 grams weapons grade Pu).
1994: Prague police seized 2.7 kilograms of HEU from a former worker at a Russian nuclear institute.
1995: Chechen rebels buried a small amount of 137Cs in a Moscow park and notified Russian television crew.
2004: Russian Customs uncovered some 200 attempts to smuggle nuclear or radiological materials.
42

## Slide 43: Consumer & Therapy Sources
Brachytherapy
Radiation Therapy
43
Notes: Tritium and 241Am sources

## Slide 44: Industrial Radiography, Irradiators, DU
747 Airplane Counterweights
Photo Courtesy Boeing
Notes: 192Ir or 60Co, 25-200 Ci (new)

## Slide 45: Non-Traditional Vectors
Transportation Modes
Unpredictable Delivery
45

## Slide 46: Photon Interactions With Matter
X-rays and gamma rays – three interactions
  Photoelectric effect – low energy (~ 1 eV - 100 keV)
  Compton effect (scattering) – medium energy (~100 – 2000 keV)
  Pair production - higher energy (> 2000 keV)
Photons have an attenuation length, not a range
  For 1 MeV gamma rays in tissue, 66% are gone after 10 cm, and 98% are gone after 40 cm
Chart: 
e-
Photoelectric Effect
e+
e-
Chart: 
Pair Production
e-
e-
Compton Scattering
Chart: 

## Slide 47: Charged Particle Interactions With Matter
Alphas, betas, and other charged particles
  Interact with electrons through their electric charge
  Energy lost through multiple scattering events
  Relativity is important for betas
  Positrons annihilate with electrons after slowing down
  Protons/heavy ions lose most energy at end of range
e-
α, β, p …
e-
α, β, p …

## Slide 48: Neutron Interactions With Matter
Neutrons
  Uncharged, so no electromagnetic interaction
  Scattering and absorption through the strong force
  Attenuation length similar to photons
  Hard to shield
1 MeV neutrons penetrate 10 cm in tissue
10 MeV neutrons penetrate 50 cm in tissue
n
Absorption
n
n
Elastic Scattering

## Slide 49: Gamma Ray Spectra (HPGe)

## Slide 50
Alarms From 3 Border Crossings

## Slide 51: RPM Concept of Operations
Primary Detection
Confirm
Secondary Detection
Isolate
Isolation
Identify
Identification of Isotope
Neutron Scan
Respond
Seize/Arrest
or Release
Detect
Gamma Detectors – Poly-Vinyl Toluene (PVT) Plastic Scintillators
Neutron Detectors – Moderated Helium-3 Gas Tubes

## Slide 52: Baseline Depression
Fraction of
Normal
Background
Normal
“No-Vehicle”
Background
Potential
Medical
Signal
Potential
Threshold
Above NORM
Potential NORM Profile
Depressed Baseline
SNM Calibration
Source Signal
w/o Vehicle
Potential
SNM Source
in NORM
Potential
SNM Source
w/o NORM
Extra Baseline Dip
52

## Slide 53: Background Radiation
Background radiation: 360 mrem/y (3.6 mSv/y)
Source | Dose (mrem)
Medical x-rays | 103
Chicago | 80
Miami | 65
Denver | 125
Airline crew, 720 hours | 160
Airline passenger, 10 flights | 3
Tobacco, 1.5 pack/day | 8000
Bricks and masonry | 7
Smoke detectors | 1
Clocks | 9
Global fallout | 4
Gas ranges | 8
TV, males | 1
TV, females | 0.3
Nuclear power | 0.3

## Slide 54: Medical Radiation
Medical x-rays have become the dominant background radiation for many Americans
Chest x-ray ~20 mrem
Dental - full set of 16 films ~3 rem to head
Frequent x-rays should be avoided
A dose of 500 rem to the whole body is lethal 50% of the time in 60 days
  If a person lives 100 years, and there were no repair, 5 rem/y would be fatal in 100 years (50% of time)
  5 rem/y is the legal limit for radiation workers
  0.5 rem/y is the legal limit for general population

## Slide 55: Biological Effects
Radiation dose correlated with cancer rate, cell death, cancer deaths, cataracts, leukemia deaths
Is the linear or thresholds hypothesis true?
Cannot be experimentally tested since so small
Normal level of incidence
Thresholds
Linear
Demonstrated Effect

## Slide 56: Acute Whole Body Radiation
Much of what is known is from Hiroshima and Nagasaki
If you survive the blast effects:
  1 kton bomb gives 1000 rem at 0.3 mile
  1 Mton bomb gives 1000 rem at 1.5 mile
Prompt whole body dose effects
  25-100 rem: no illness
  100-200 rem: slight illness
  200-1000 rem: survival is possible
  >1000 rem: survival is improbable

## Slide 57: Medical Radiation Therapy
Diagnostics and therapeutics
  X-rays, CAT and PET
  Stress tests with 99mTc
Basis: killing cells through damage and repair
Susceptibility to damage depends on cell cycle
Rapidly dividing cells more subject to damage
Treatments over several weeks like chemotherapy
Cancer may be localized or dispersed
  External radiation, injected or implanted
  Shape beam and rotate to reduce damage to good tissue
  Oxygen enhancement

## Slide 58: Units, Exposure and Dose
Unit of radioactive decay
  Curie (Ci): 1 Ci = 3.7x1010 decay/s
  Becquerel (Bq): 1 Bq = 1 decay/s
Exposure – exposed to amount of radiation
  Roentgen (R): 1 R = 2.58x10-4 coulombs/kg
Absorbed energy deposited per unit mass
  Rad: 1 rad = 0.01 J/kg
  For x-rays and gamma rays: 1 R ≈ 1 rad
  Gray: 1 Gy = 1 J/kg = 100 rad
Biological effect of radiation depends on type
  Radiation equivalent man: 1 rem = 1 rad  QF
  Sievert: 1 Sv = 100 rem
  500 rem (5 Sv) whole body is fatal 50% in 60 days

## Slide 59: Decay Chain Example
238U 4.5 Gy
234Th 24 d
234Pa 1.2 m
234U 250 ky
230Th 7.5x104 y
226Ra 1502 y
222Rn 3.8 d
218Po 27 m
218At 1.8x10-4 s
…
206Pb
a
a
a
a
a
b
b
b

## Slide 60: Benefits of Energy-Window Ratio
Truck with NORM cargo
Truck with dense cargo
Reduce NORM alarms
Reduce effects of
background suppression
Notional
Thresholds
Gross Counts
Gross Counts
Simple EWR
Simple EWR

## Slide 61: Standards
61
61
20 cm
20 cm
20 cm
ANSI N42.41: Minimum Performance Criteria for Active Interrogation Systems used for Homeland Security
  Non-intrusive inspection of closed containers, vehicles, and packages, but not imaging
  Inspection times of 90-900 s depending on size
  Test masses: explosives (200 kg), chemicals (200 kg), fissionable material (25 kg), weapon shells (16 kg)
Standards establish test methods based on threat-informed unclassified source materials and configurations
Standards establish performance requirements for automated active systems that detect shielded SNM

## Slide 62: Active Interrogation
From Morse

## Slide 63: Active Interrogation (AI)
AI initiated by energetic photons, neutrons or muons
Detected signal is photons, neutrons or muons
Large source required giving large dose
Our study includes only:
  High-Z: presence of high atomic number (Z) material
  Photofission: presence of fissionable material
  Differential die-away: presence of fissile material
  Nuclear resonance fluorescence: presence of HEU or Pu
63
Notes: CAARS: SAIC – L3 – AS&E
Raytheon - Passport

## Slide 64: Modeling With MCNP & GEANT4
64
Analytical calculations performed to establish order of magnitude requirements
MCNP models of differential die-away (DDA): comparison made to published information provided model validation
MCNP models of PF for SNM and surrogates
Neutron die-away times observed for bare tungsten, DU, HEU and Pu.
9 MeV Bremsstrahlung beam GEANT4 simulation

## Slide 65: Muon Scattering Detection
Cosmic ray muons used
Muon scattering is highly dependent on density
Measure the muon path through a vehicle
Demonstrated to show presence of high density material like HEU and Pu
Takes minutes to make a measurement because of small muon flux of ~160 m-1s-1
Decision Sciences

## Slide 66: Is Active Interrogation Feasible?
Passport
Rapiscan
Can we do 100% imaging?
Is active interrogation operationally possible?
  AI cannot be used in primary screening, so limited to targeted containers
  Large dose
  Large footprint (on private land)
  Large cost
  If looking for a weapon, it is too late!

## Slide 67: High-Z & Photofission Detection
Interrogate with x-rays and look for gamma-rays or neutrons
DU is a good surrogate material for High-Z detection and Photofission
Surrogate for high-Z detection can be 2 kg DU
Surrogate for Photofission detection can be 2 kg
  Consider prompt neutrons, delayed neutrons and delayed gamma rays
  Too many combinations of possible surrogate masses: Pb attenuators used to reduce signal to correct value
67

## Slide 68: Differential Die-Away
Interrogate with neutron pulse
LEU is a usable surrogate for DDA
Surrogate mass for DDA is 2 kg LEU
Surrogate provides similar response as HEU & Pu
68
Comparison of PNNL validation model results with measured data (Jordan et al. 2007)

## Slide 69: Nuclear Resonance Fluorescence
Interrogate with gamma-rays and observe gamma-ray signal
DU is good surrogate material for NRF
NRF signal size depends on mode (transmission or scattering) and HEU or Pu
Surrogate for NRF is 2 kg DU
  2 kg DU provides more signal than SNM
  Pb attenuators used to reduce signal to correct value and depends on transmission or scattering modes
69