## Slide 1: Time-of-Flight Lab Introduction
Stefan Ritt, Paul Scherrer Institute, Switzerland IEEE NPSS Prague EduCom International Summer School
July 1st, 2025, Prague, Czech Republic

## Slide 2: Cosmic rays
Energetic particles (mainly protons and alpha particles) generated in solar eruptions and astrophysical processes even outside our Milky Way
Some particles have much higher energies than those possible with the biggest man-made accelerators.
Used as messengers to understand cosmic processes such as supernovae
Primary cosmic rays generate secondary rays in the upper earth atmosphere
Most showers are absorbed by atmosphere
Some muons (m) make it down to earth

## Slide 3: Fun fact: Time dilation
Muon lifetime: t1/2 = 2.2 x 10-6 s
Thickness of earth atmosphere: ~10 km
Average travel distance of a muon having speed of light: d = t1/2 * c = 2.2 x 10-6s * 3 x 108 m/s = 660 m
Special relativity predicts time dilation
Muon lifetime @99.9% of c: t’1/2 = 2.2 x 10-6 s / sqrt(1-0.9992) = 49 x 10-6 s
Modified travel distance: d = t’1/2 * 0.999 * c = 49 x 10-6s * 3 x 108 m/s = 14.7 km
Lorentz factor g = 22.4
10 km

## Slide 4: Direction of cosmic muons (CM)
CM are anisotropic
CM loose energy proportional to thickness d of atmosphere
At q=90 deg. rate goes to zero (flat earth approximation)
d0/d = cos(q)  d = d0 / cos(q) r(q) = r0 / d = r0 * cos(q)
Better approximation (earth curvature, inhomogeneous atmosphere, muon scattering, …) r(q) = r0 * cos2(q)
Empirical formula, not exactly derived
q
d0
d
~cos(q)
~cos2(q)

## Slide 5: Detection of Muons
Scintillator BC400
10x100x100 mm3
SiPM
MCX
Connector
WaveDREAM
with DRS4 Chip “Oscilloscope”
CH0
CH1
CH2
CH3

## Slide 6: Lab goals
Configure measurement
Measure speed of cosmic muons
Measure direction of cosmic muons

## Slide 7: Connect oscilloscope
WaveDREAM
with DRS4 Chip “Oscilloscope”
CH0
CH1
CH2
CH3

## Slide 8: Setting up the oscilloscope
Turn on channels 0-3
Set
trigger
Set
gain

## Slide 9: Setting high voltage for SiPM to 54 V

## Slide 10: Define time measurement
Measured value
Number

## Slide 11: Zoom to -5 ns to +5 ns

## Slide 12: Measure Speed of Cosmic Muons

## Slide 13: Measure speed of muons
Case A
Measure 300-500 events
write down mean
Case B
Measure 300-500 events
write down mean
Rotate

## Slide 14: Difference Measurement
Case A: DtA = (t0,A+tc0) – (t2,A+tc2) = d / v
Case B: DtB = (t0,B+tc0) – (t2,B+tc2) = d / (-v)
Difference:
DtA - DtB = (t0,A+-t0,B)-(t2,A+-t2,B) = 2d / v
v = 2d / (DtA – DtB)
Task: measure v in % of c (= 3x108 m/s)
t0
tC0
t2
tC2
d = 0.1m
v = ?
t0
tC0
t2
tC2

## Slide 15: Measure Direction of Cosmic Muons

## Slide 16: Measure direction of cosmic muons
Set angle = 0,10,20…90 deg.
Measure 5 minutes
Write down counts
Plot normalized counts vs. angle
https://docs.google.com/spreadsheets/d/17GKjGK5fU1BGCbbJZV7dLj1fum2MoU38QzSnF404W-o
~cos(q)
~cos2(q)
data

## Slide 17: JupyterLab https://jupyter.org
Document your measurement!

## Slide 18: Data Analysis
Write python code to plot your data
Get help from ChatGPT if necessary
Double check the code from ChatGPT!
More details in Lab Script

## Slide 19: Questions to ask yourself
Why does the rate do not go to zero at 90 deg.?
Why are the points not on a smooth line?
If I measure again, will I get exactly the same points?
How could the experiment be improved?

## Slide 20: Student Presentations
Next week, every student is supposed to give a ~5 min presentation about one of the four lab courses
Document your measurements, save results, take pictures