## Slide 1: Photo detection Statistical fluctuation
July/2025
NOMACHI, Masaharu
Notes: 業績リストや昔話にはしたくない。
その周辺のちょっと面白そうな話、これまでする機会のなかった話をしたい。
でも、ねたはどうしても昔の話、ご容赦願います。

## Slide 2
Masaharu Nomachi
Research Center for Nuclear Physics University of Osaka nomachi@rcnp.osaka-u.ac.jp
Nuclear physics / RCNP Osaka
Hadron physics / Anti proton experiments at LEAR CERN
Particle physics / Collider experiments at SSC, LHC
Astro physics / Gamma rays from SN1987A in Brazil
Neutrino physics / Double beta decay experiments
          in Kamioka and Europe (France,
Data acquisition system developments
    SSC/LHC, Data link on Satellites (ESTEC/ESA in the Netherlands)
    Underground experiments
School activities
    2009,10,11 JSPS school in Osaka
    2014,15,16,17,18,19 JST SAKURA school in Osaka
    2022 Remote, 2023 JST SAKURA school in Fukushima
    IEEE/NPSS school 2014 Osaka, 2016 Vietnam
      2018 South Africa, 2019 Malaysia, 2023 Senegal, 2024 Morocco

## Slide 4: Light detection
How do we measure weak light?
How much energy we need to measure?

## Slide 5: Quantized Energy flow

## Slide 6
Newton and Huygens
Is light a wave or a particle?
Behave as a wave
What is the medium of a light wave?
How light travel in vacuum?

## Slide 7: Quantized Energy flow
Energy flow is quantized.
Intensity is the number of photon
Max Planck
The Nobel Prize in Physics 1918
Prize motivation: "in recognition of the services he rendered to the advancement of Physics by his discovery of energy quanta"
Photon energy = wave length = color

## Slide 8
How can we detect light
We need ENERGY to excite the micro system
How can we detect weak light
Do we need accumulate the energy enough to excite?
No.
Energy is quantize as photon.
Intensity = the number of photon
Count the photon.
no excitation -> no change!

## Slide 9: photoelectric effect
Albert Einstein
The Nobel Prize in Physics 1921
Prize motivation: "for his services to Theoretical Physics, and especially for his discovery of the law of the photoelectric effect"
Photon energy must be larger than Binding energy

## Slide 10
＝
2 eV = 600 nm (Visible light)
1 keV = 1.2 nm （〜size of atom）
20MeV = 60 fm （〜size of atomic nuclei）
197 eV nm
197 MeV fm
＝
Energy
Wave length

## Slide 11: chemical energy
Battery voltage is related to the chemical interactions.
Ni-Cd
battery (1.2V)
Alkaline manganese battery (1.5V)
It is the same order of ionizing energy

## Slide 12: Thermal Energy
8.6171E-5 eV/K
at room temperature, it is about 25 meV = 0.025 eV
k is Boltzmann constant
Energy of gas molecular is proportional to the temperature.
It is much lower than the ionization energy
Thermal neutron energy

## Slide 13
https://www.researchgate.net/figure/Blackbody-radiation-curves-at-different-selected-temperatures-as-derived-from-equation_fig17_240856156

## Slide 14: Gravitation
Free fall of 1 kg from 1m high
mgh ＝ ~10 J = 6 x 1019 eV = 6 x 107 TeV
It is large energy but it cannot causes high energy radiation.
Because each nucleon may get small energy.
6 x 1019 eV / (1000 x 6 x 1023) = 1 x 10-7 eV = 100 neV
Compare to other Energy,
it is several order magnitude smaller.
On the surface of neutron stars, “g” is 1011 larger
100 neV -> 10 keV !

## Slide 15: Energy Scaleionizing radiation
Gravity
Heat
Chemical
ionizing radiation
https://www.env.go.jp/en/chemi/rhm/basic-info/1st/index.html

## Slide 16: Photo sensor

## Slide 17
Photon Counting
How many photon from scintillator?
LYSO scintillating crystal causes 16,000 photon for 511keV gamma rays.
32 eV gamma energy / one scintillation photon
While scintillation photon energy is 2 eV.
Why so different?
We see ~one direction out of 6 (L-R,U-D,F-B) direction.
So ~2,670 photon will come out.
LYSO is 2mm x 2mm but Sensor is 1mm x 1mm. It is 1/4
Consequently, only 670 photon will hits the sensor.
case of EasyPET

## Slide 18
The number of photon
How many photon are we seeing?
Visible light is ~2eV

## Slide 19
0.1s flush ~ 3x1017 photon
R
Into eye
of probability
The number of photon
How many photon are we seeing?
600 photon =１W flush 0.1s is seen in 22 km distance
Visible light is ~2eV
r

## Slide 20: photoelectric effect
Conversion from photon to electron
Charged particle is easy to handle.
However, efficiency is not 100%.
~ 20 %
600 photon -> 120 electron
120 electron is not easy to measure
Increase the number of electron !

## Slide 21: Electron multiplication
Accelerated electron hits metal.
Secondary electrons are emitted.

## Slide 22: Photomultiplier
Multi-stage
105~106 gain can be obtained.
120 photoelectron is multiplied to 108 electron

## Slide 23
https://www.hamamatsu.com/content/dam/hamamatsu-photonics/sites/documents/99_SALES_LIBRARY/etd/PMT_handbook_v4E.pdf

## Slide 24
Electron Counting
How many electron do we need to observe?
We can see→ 0.1s
6 x 1011electron is needed to “See”
10８ is not enough to “See”
Ammeter can measure about 1μA. How many electron?
e/s
e/s

## Slide 25
10８ electron pass in 10ns.
Current ＝ Charge/ Time
1.6x10-19 x 108 / (10 x 10-9) = 1.6 mA
Cannot see in Ammeter but can be detected by electronics.
Electronics can measure voltage.
Current to Voltage
1.6mA x 50Ω = 80mV
Why 50Ω？

## Slide 26
MPPC (SiPM)
Multi-Pixel Photon Counter (MPPC), also known as silicon photomultiplier (SiPM)
https://www.hamamatsu.com/content/dam/hamamatsu-photonics/sites/documents/99_SALES_LIBRARY/ssd/si-apd_kapd9007e.pdf
https://www.hamamatsu.com/content/dam/hamamatsu-photonics/sites/documents/99_SALES_LIBRARY/ssd/mppc_kapd9008e.pdf
https://goalp.com/qa-139

## Slide 27
overvoltage
Too high gain (huge avalanche) destroy the device

## Slide 28
Amount of water (Charge) is proportional to the number of hits

## Slide 29: Easy PET

## Slide 30
Photon Counting
LYSO scintillating crystal causes 16,000 photon for 511keV gamma rays.
We see ~one direction out of 6 (L-R,U-D,F-B) direction.
So ~2,670 photon will come out.
LYSO is 2mm x 2mm but Sensor is 1mm x 1mm. It is 1/4
Consequently, only 670 photon will hits the sensor.
case of EasyPET
40% of area is active in SiPM
= about 270 photons will hits active area
Max hits is 400. We don’t see bigger than that.
Non linear!

## Slide 31
SiPM in eazyPET has 400 pixel.
# of photon hits active area

## Slide 32: Intrinsic radio activity
LYSO crystal has intrinsic radioactivity.
gamma rays
gamma rays + beta rays
0.3 Bq/mm3
EasyPET 2x2x30 mm3 x 0.3 Bq/mm3 = 36 Bq

## Slide 33: Dark signal
Signal in Dark
Thermal excitations causes avalanche.
Event rate for SiPM in EasyPET is 110 kHz
110 k in sec ~ 1 in 9 μsec
Probability of overlap on 1 us signal is 1 x 1/9 = 11 %.
1 hit = 110 kHz
2 hit = 110 x 0.11 = 12.1 kHz
3 hit = 1.3 kHz
4 hit = 140 Hz
log Hits
Signal

## Slide 34: Hits and Signal
Signal is proportional to the number of hits.
Signal
0
1
2
3
4
5
Signal
Gain
Signal is proportional to the Gain.
Gain changes the size of signal but does not change the number of hits.

## Slide 35: Threshold
Signal
Gain
Signal is proportional to the Gain.
Threshold
Respond to the signal
4 hit = 140 Hz
3 hit = 1.3 kHz
2 hit =12 kHz
Intrinsic 35 Hz
~1k Hz
~200 Hz
~35 Hz
Small signals are not seen.

## Slide 36
Dark Hits
Intrinsic photons
higher over voltage = higher gain
Getting more than 100 Hz ~~ Getting dark hits (Noise events)
Vias voltage depends on temperature, device etc.

## Slide 38
400 Hits
Dark hits ~ Noise events
400 Hits
Dark hits ~ Noise events
Higher Gain

## Slide 39
SiPM in eazyPET has 400 pixel.

## Slide 40
External = No beta
Internal = gamma + beta

## Slide 41: Coincidence rate
10 μCi = 370 kBq
2mm x 2mm
50 mm
370 k x 2x2 / 4 π 50x50 = 370 k x 1.3/10000 = ~50
Coincidence rate should be an order of ~50.

## Slide 42: Statistical fluctuation

## Slide 43
Statistical behavior
Uniform distribution
Intensity decreases as 1/r2
Intensity = photon counts
Counts decrease
Photon counts cannot be fractional numbers.
Photon is observed statistically
Intensity = probability of photon existence
Uniform distribution = Uniform probability

## Slide 44
Counting rate μ is constant.
Measured counts cannot be constant.
It fluctuate statistically.
Probability to observe n counts in interval t
Pn(t)
Expected counts to ovserved counts

## Slide 45
Poisson distribution
Probability to observe n counts in interval t
Pn(t)
Pn(t+Δt) = (μΔt) Pn-1(t) + (1-μΔt) Pn(t)
Skip the calculation
Poisson distribution

## Slide 46
Mean value and variance
Average and variance is the same for Poisson distribution

## Slide 47
Normal distribution
When the average is large in Poisson distribution.
This is zero at n=μt.
Let’s expand this with Taylor series at n=μt
This is known as Normal distribution
(also known as the Gaussian distribution)
of average = μt and variance = μt.

## Slide 48
Normal distribution
As shown in the Poisson distribution, any kind of distribution approaching to Normal distribution with many samplings.
It is known as “The central limit theorem”

## Slide 49
Normal distribution
68%
95%
+σ
-σ
+2σ
-2σ
FWHM

## Slide 50
Measured counts and Counting rate
If we measure the 3 counts in 10 seconds, how about the counting rate?
0.3 count / second is probable.
0.5 counts / second is also possible.
How about 1.0 counts / second?
0.3 c/s
0.5 c/s
1.0 c/s

## Slide 51
+σ
-σ
If the true value is larger, the measured value is less probable
If the true value is smaller, the measured value is less probable
error bar
Measured value and true value

## Slide 52
Error propagation
z = z(x,y)
x and y fluctuate independently.

## Slide 53: Hamadohri Environmental Radiation School

## Slide 54
2011.3.11
2:46 PM
East Japan Earthquake

## Slide 55: East Japan Earthquake
https://www.pref.miyagi.jp/site/miyagifukkounotabi/overview/index.html

## Slide 56: Tsunami at Fukushima Dai Ichi

## Slide 57
H-explosion of #3
1F Before Tsunami
1F After Tsunami and explosion

## Slide 58
 | Chernobyl | Fukushima
Explosion | steam explosions at the core | Hydrogen explosion outside of the core
Ejection of RI | By explosion and fire. | Evapolation
Source: OECD NEA

## Slide 59: Major Radioactive material released from NP
Nuclide | boiling point | Half-life | 
133Xe | -108.1°C | 5 days | Short half-life, noble gas
131I | 184.3°C | 8 days | Short half-life
137Cs | 670.8°C | 30 years | Nuclide currently in issue
134Cs |  | 2 years | Short half-life
90Sr | 1,382°C | 29 yeard | No evaporation in 1F
7–20 PBq for 137Cs
Because of North-west wind, 40–80% was deposited in the ocean.
~300 PBq of 137Cs by Nuclear bomb test fallout still exist in the ocean.
~20,000,000 PBq of 40K , ~150,000 PBq of 87Rb

## Slide 60
https://www.rcnp.osaka-u.ac.jp/dojo/index_en.php
Survey of Fukushima Soil Radio activities
Osaka university and the Japan Atomic Energy Agency (JAEA) played a key of role in the collection of the soil samples in June - July, 2011.
409 scientists from 94 academic research institutions, and 3 private enterprises participated.

## Slide 62
Compared air dose rate of 7months after the accident (as of November 2011) with that of 91months after the accident (as of October 2018), the latter decreased by 74%. It was confirmed that the decrease was faster than natural attenuation as an overall tendency

## Slide 64
In Hamadohri school, lectures are given on the minimum knowledge, but, we place emphasis on seeing with own eyes.
We hope that students will develop the ability to think for themselves, identify the essence of a problem through discussions among students.
We value the diversity of students.
Students with diverse backgrounds can exchange ideas rooted in their own backgrounds and awaken to new ways of thinking
2016
Fukushima Hamadohri is unique education field.
We started Hamadohri school in 2016.

## Slide 65
Sampling in the mountain
Measurement of the soil.
137Cs peak can be seen.
Tsunami area near nuclear power plants

## Slide 66
Sampling
Measurements

## Slide 67
Communication with locals
Discussions

## Slide 68
Hamadohri Environmental Radiation School
Male: Female ≒ 3 : 2
Humanities: Science ≒ 1 : 1
2018
2019

## Slide 69
Hamadohri Environmental Radiation School
2021 2 group
2022 2 group + 2 group

## Slide 70
Science | 15
Engineering / Agriculture | 23
Literature | 4
Economics | 4
Law and Politics | 5
Human Science | 8
Medicine / Dentistry | 5
Foreign Studies | 11
Education | 2
Tourism | 4
Major of students (2021)
The students has wide variety of background. It causes multidisciplinary view point on the discussion.
Most of them are the 1st year in Osaka University.
Some of students come from other University.
We don’t require any knowledge to the participants.

## Slide 71
2023
141 students Including 16 foreign students + 43 staff members
2 group + 3 group
Hamadohri Environmental Radiation School

## Slide 72
2024 Hamadohri school
215 students! (32 from abroad)
3 group + 3 group + 1 group
1) 19-24 August
2) 9-14 September
14-17 September IEEE school
3) 23-27 September IAEA school
@ Osaka University Fukushima Center
    It was opened in August 2024.

## Slide 73
Osaka University students | 91
Other University students in Japan | 92
Foreign students | 32
Professores | 75
total | 290
3 groups in August
3 groups in September
1 IAEA group in September
Each group is about 40 people
Malaysia | 7
Indonesia | 5
Germany | 3
Philippines | 10
Netherlands | 1
Finland | 1
Taiwan | 1
Australia | 1
Saudi Arabia | 3
2024 Hamadohri school

## Slide 80
University of Groningen - Osaka University Student Symposium 2023,2024,2025

## Slide 81
Hamadohri Environmental Radiation Measurements international school 26-31 July 2025
EXPO2025 - Osaka University Symposium
4-5 August 2025
School in English
Symposium under the theme: Designing a Future Society for our Life 4-5 August 2025
Natural and Climate-Change Induced Disasters’ Effect on Women and Under-Represented Groups
Climate Change Effects on Women and Under-Represented Groups
Education Enhancement through Technology Nepal Solar Panels
WePower a case study to empower women in the energy sector
Introduction of ESTEK or Public Safety
Climate Change Activities from YP Perspective
Case Study - Women Resilience: Bare-Foot College
Case study - Natural and CC Disasters Preparedness
Effect of the Fukushima Disaster on Women
The Fukushima Disaster Case Study: the role of education
The Sociology and Psychology of the Natural and CC-Induced disasters on Women and UR Groups

## Slide 82: Osaka University Fukushima Center
Crowdfunding for OU Fukushima Center
Hamadohri is unique place to study Environment Radiation.
We would like to make “OU Fukushima Center” a leading international center for Environmental Radiation Measurements.