## Slide 1
Medical Imaging:
PET
July 2nd 2025
Andrea Gonzalez-Montoro, PhD
andrea.gm@i3m.upv.es

## Slide 2
Outline
PET History & Evolution
PET Detector  PET scanner
PET system technology requirements
  Pre-clinical PET
  Clinical PET
State-of-the-art
  Dedicated-, WB-, and TB-PET
Conclusion

## Slide 3
Andrea Gonzalez-Montoro, PhD in Physics Born in Valencia, Spain, on December 13th 1992
Medical and technological sciences
Decisions, doubts, fears…
Darmstadt, Germany
1st international experience
School:
C.P. José Sotó Micó
1996-2006
Highschool:
I.E.S. Juan de Garay
2006-2010
Degree in Physics
2010-2014
Master in Medical Physics
2014-2015
PhD in Physics
2015-2018
Qualification: Cum Laude
December 2018
Postdoctoral Fellow at
Stanford University 2018-2023
2023-Actualidad
i3M-CSIC-UPV
Ramón y Cajal, Postdoc
ERC Stg Grant
December 2024 – 2029
PHOENIX
2021Young Scientific Female Talent. aRac y MasterCard España
Permanent position at i3M
February 2025
About me

## Slide 4
Outline
PET History & Evolution
PET Detector  PET scanner
PET system technology requirements
  Pre-clinical PET
  Clinical PET
State-of-the-art
  Dedicated-, WB-, and TB-PET
Conclusion

## Slide 5
PET: History & Evolution
PET  uses radiotracers for the detection, diagnosis, monitoring and treatment of numerous medical conditions. It is the most widely used molecular imaging technique in the clinical field and also in preclinical research.
Historical facts contributing to the development of PET:
1929
Experimental discovery of the positron by
Anderson
Theoretical prediction of the positron by Dirac
1932
1934
Discovery of radioactive elements,
Curie y Joliot
Use of the cyclotron to generate artificial radionuclides. Univ, California Berkeley
1945
First use of radiotracers in humans
1948
Detector improvements, launch of the
PMT
1952
Brownell y Sweet (MGH), radiation
to visualize and
treat tumors
1953
Construction of the first PET, brain studies
Notes: Massachusetts General Hospital

## Slide 6
DEVELOPMENTS IN THE DETECTOR TECHNOLOGY
1953
1970
1990
2000
2010
Present
First completed PET scanner: Positome.
Robertson and Thompson
New scintillators: BGO y LSO.
Improved PET
1978
Synthesis of new radiotracers
18F-FDG
1993
pre-clinical PET,
research with animals
Solid-state detectors: SiPMs.
Image improvements: DOI & TOF
Introduction of AI in PET
State-of-the-art
PET: History & Evolution

## Slide 7
gkjdsh
Talk: PET Detector Developments
Positrons have very short lifetime, annihilate with electrons and produce two 511 keV photons that are detected.
Common isotopes for positron imaging: 18F(~H), 13N, 15O, 11C.
Positron-electron annihilation
Unstable parent nucleus
Two anti-parallel 511 keV
Photons produced
Proton decays to neutron in nucleus  positron and neutrino emitted
𝛾
𝛾
Positron-electron annihilation
PET: Basics

## Slide 8
t
DET 1
Pulse Processing
AND
DET 2
Pulse Processing
ev1
ev2
TC Window ~ few ns
+1
ev3
LOR (“line of response”)
From List-mode data or Sinograms, and “After complex software manipulation of the signal, a visual representation is reconstructed”.
Q.C. Black et al., “Radiotherapy target,” I.J. Rad. Oncol. Biol. Phys., 2004.
PET basics
8
Notes: Ventana de coincidencias < 5-10 ns
Sinograma: forma de alamcenaje más estandarizada.

## Slide 9
Pixellated
Monolithic
Photosensor
PMTs
Solid State
SiPMs
PET detector block
Readout
Scintillator block
Analog
ASIC
Properties:
Dense (g/cm3) and high Zeff
High Light Yield (32k ph/MeV)
Transparent to their own wavelength 420 nm
Gamma ray detectors
Notes: Propiedades de los cristales:
-Generar muchos gammas, de menos energía
-ser transparentes a su propia longitud de onda
-high LY
Freno los gamma de 511 leV  Genero una señal medible en el fotosensor transformande la luz visible en un impulse electrico. Ganacia appr. 1000000  acondiciono la señal (signal shaping)
PMT
GENERATING!!
MOST USED IN MEDICAL IMAGING

## Slide 10
-ray 511 keV
Detector level evaluation
Acquisition of coincidence data to study the Influence of bias voltages, threshold levels, temperature drifts and other factors are also evaluated
Detectors
22Na source
Spatial Resolution
DOI Resolution
Energy Resolution
CTR Resolution
Average FWHM and FWTM of the the light distribution profiles obtained using radioactive sources
Side irradiation experiments at known depths. Average FWHM of the profiles
Corrected LOR
Wrong LOR
∆E/E x 100% , ∆E is the FWHM and E the centroid of the 511 keV photopeak
The coincident photons arrival time to the detector is recorded and histogram.
PET: Parameters
10

## Slide 11
11
DOI
No DOI
!!
Corrected LOR
Wrong LOR
DOI
TOF
SNR gain
CTR (ps)
16
12
8
4
0
- 100. 300 500 700
FOV Diameter
PET: DOI & TOF
Non-DOI
DOI

## Slide 12
Outline
PET History & Evolution
PET Detector  PET scanner
PET system technology requirements
  Pre-clinical PET
  Clinical PET
State-of-the-art
  Dedicated-, WB-, and TB-PET
Conclusion

## Slide 13
From the detector level…
…to the system assembly
and validation
-ray 511 keV
Scaling-up process
Factors to consider for the scaling-up :
Scintillator material and surface treatment
Photodetector and arrangement
Number of elements (per module)
Number of modules
Their arrangement to minimize gaps
  High packing fraction and sensitivity
  Scintillator-photodetector coupling
Electronic readout
  Trade-off between performance, power consumption, and number of output signals

## Slide 14
Scaling-up process
System level evaluation
Once the PET scanner has been assembled, several parameters are evaluated usually following the NEMA Standards
Spatial Resolution
Sensitivity and NECR
Determined as the FWHM and FWTM of the reconstructed source profiles.
Different phantoms are used. These parameters determine the system ability to handle high rates
Image Quality
The IQ phantom is used to observe different spheres
TOF imaging
Implementation of TOF information to improve image SNR

## Slide 15
Outline
PET History & Evolution
PET Detector  PET scanner
PET system technology requirements
  Pre-clinical PET
  Clinical PET
State-of-the-art
  Dedicated-, WB-, and TB-PET
Conclusion
Outline

## Slide 16
WB-PET
Preclinical PET
Organ-dedicated PET
TB-PET
PET: Requirements

## Slide 17
1.5
1.2
1.0
0.9
0.8
0.7
Large FOV allows for simultaneous whole body mouse imaging
PET/MRI (FDG) Mouse - whole body. Courtesy of Dr W Gsell and Pr U Himmelreich, KU Leuven, Belgium
PET Dynamic Imaging
Quantitative Cardiac Imaging in Rats
17
Preclinical Dynamic PET

## Slide 18
Simultaneous PET/MR allows for MRI guided PET motion correction
Cardiology: IntraGate/PET.
Collaboration KU Leuven / Bruker:
Courtesy: Dr. W. Gsell, Prof. C. Deroose and Prof. U. Himmelreich
IntraGate / PET cardiac imaging:
  Works in diseased heart models
  Fast, simple and reliable animal preparation
  Multiple cardiac/respiration movie reconstruction
  No ECG electrodes, no trigger levels or timing synchronization
  Inherently avoids MRI induced noise in PET gating signal
  Outlook: this is the pathway for multi-mouse PET/MR cardiac studies
Healthy Rat Injected with FDG
18
Preclinical MR-gated PET
Notes: MRI guided mage correction could be static or dynamic
Cardiac is a dynamic example, it’s not correction but image reconstruction based on MRI navigators

## Slide 19
Oncology:
  Cancer Detection and Staging
  Treatment Response Monitoring
  Recurrence Detection
Cardiology:
  Coronary Artery Disease
  Myocardial Viability
  Inflammatory Myocardial Diseases
Neurology:
  Alzheimer's Disease and Cognitive Impairment
  Epilepsy
  Other Neurological Disorders: diagnosis and management of Parkinson's disease, stroke, and other neurological conditions.
Clinical PET/CT

## Slide 20
PET/CT  help pinpoint abnormal metabolic activity and may provide more accurate diagnoses than the two scans performed separately
Clinical PET/CT
CT  uses x-rays, and in some cases a contrast material, to produce images of the inside of the body. Provides excellent anatomic information
PET  based on the coincidence detection of annihilation photons. measures body functions, such as metabolism. Provides functional information

## Slide 21
Clinical PET/CT
Source: https://www.mic.ca/pet-ct-practitioner-applications/#/

## Slide 22
Clinical Brain PET
Sources:
https://www.everydayhealth.com/alzheimers-disease/
https://www.britannica.com/science/brain-scanning/

## Slide 23
Outline
PET History & Evolution
PET Detector  PET scanner
PET system technology requirements
  Pre-clinical PET
  Clinical PET
State-of-the-art
  Dedicated-, WB-, and TB-PET
Conclusion
Outline

## Slide 24
PET is the most sensitive (at the picomolar level) non-invasive molecular imaging system. However, PET studies are still limited by statistics (long scanning times), dose delivered to the patient (and clinicians), or both.
Clinical scanners only collect about 1% of the emitted signals. Every count counts.
Increase in sensitivity
PET
PET: State-of-the-art
Notes: Pixelated detectors:
Coincidence data is acquired, and positioning algorithms are applied to generate 2D Flood maps.
Pixel profiles are extracted, and Gaussian fitting is applied.
Monolithic detectors:
Same procedure but, a collimator is used to generate the flood maps and extract the sources profiles.
Pixelated detectors: discrete DOI information (usually)
Monolithic detectors: continuous DOI information

## Slide 25
Total-Body PET
Medical Imaging breakthroughs provided by an increased sensitivity
Dynamic and Simultaneous studies of several organs
Dose reduction
  Paediatric imaging/Follow up
Imaging Faster
Imaging Tumour Heterogeneity
Non-malignant diseases imaging
State-of-the-art
PET: State-of-the-art
Notes: Pixelated detectors:
Coincidence data is acquired, and positioning algorithms are applied to generate 2D Flood maps.
Pixel profiles are extracted, and Gaussian fitting is applied.
Monolithic detectors:
Same procedure but, a collimator is used to generate the flood maps and extract the sources profiles.
Pixelated detectors: discrete DOI information (usually)
Monolithic detectors: continuous DOI information

## Slide 26
PennPET EXPLORER
High TOF resolution (close to 200 ps)
70cm-1m40 long
Philips technology platform
PIXELS, no DOI
EXPLORER
Highest sensitivity,
2m long
United imaging Healthcare
PIXELS, no DOI
Siemens Quadra
High TOF resolution (214 ps)
1m06 long
Siemens Vision technology
PIXELS, no DOI
Recently announced  Biograph Vision.X
achieves a CTR of 178 ps
PET: State-of-the-art
Notes: Pixelated detectors:
Coincidence data is acquired, and positioning algorithms are applied to generate 2D Flood maps.
Pixel profiles are extracted, and Gaussian fitting is applied.
Monolithic detectors:
Same procedure but, a collimator is used to generate the flood maps and extract the sources profiles.
Pixelated detectors: discrete DOI information (usually)
Monolithic detectors: continuous DOI information

## Slide 27
PET: State-of-the-art

## Slide 28
*However, its high price and the requirement for large hospital footprints is a challenge for its clinical deployment as well as research use.
S. Vandenberghe, EJNMMI 7, 2020
SiPM
PET: State-of-the-art
Notes: Pixelated detectors:
Coincidence data is acquired, and positioning algorithms are applied to generate 2D Flood maps.
Pixel profiles are extracted, and Gaussian fitting is applied.
Monolithic detectors:
Same procedure but, a collimator is used to generate the flood maps and extract the sources profiles.
Pixelated detectors: discrete DOI information (usually)
Monolithic detectors: continuous DOI information

## Slide 29
PET limitations:
﻿Time-consuming
Low sensitivity and non-uniform spatial resolution
  Advancements in instrumentation
Lack of anatomical information
  Specially trained personnel required to interpret reports
﻿False positives
  ﻿﻿Can show up areas of high activity which may be mistake for cancers
  Reduces specificity
Radioactive substance has a very short
  Appointments must run on schedule
  Cyclotron is required for generating the radiotracers ﻿﻿
PET scans are expensive, and are not available all the time
PET: Limitations

## Slide 30
Challenges and limitation of Pediatric PET imaging
Positron Emission Tomography (PET): the imaging modality of excellence in nuclear medicine
  Key in the diagnose and follow up of severe medical conditions
  Used for both adult and pediatric studies
Pediatric PET unique challenges
Since Conventional WB-PET scanners:
Limited axial coverage
Low Spatial resolution > 3-5 mm
Low sensitivity:
  High radiotracer doses
  Long scan times
Expensive
!
15-32 cm
Diagnostic quality compromised!
54.5 cm
PHOENIX Keys:
Detector block
System implementation
cm
Potential Solution: PHOENIX
TB-PET for pediatric patients
High-performance < 3 mm
High sensitivity:
  Dose reduction
  Fast imaging
Affordable
Andrea Gonzalez-Montoro
Notes: radiation effects than adults and have a longer post-exposure life expectancy in which to exhibit adverse radiation effects
Developing the PHOENIX scanner constitutes major research and technological challenges. If successful, will promote PET imaging of children, improve its diagnostic capabilities, staging and response assessment.
Pediatric PET imaging research focusses on reducing patient dose whenever possible and on minimizing exam durations as well as sedation times  still requires several technological advancements.
-without becoming claustrophobic- and,
uniform spatial resolution in the range of 2-3 mm (current WB-PET scanners: 3-6 mm10; organ dedicated PET scanners: 1.5-3 mm19) in the entire FOV by enabling depth of interaction (DOI) resolution < 4 mm. The PHOENIX large FOV combined with the Signal to Noise (SNR) gain resulting from the inclusion of Time Of Flight (TOF) information will permit for a significantly increased in sensitivity of 30, when compared to conventional PET.
radiation effects than adults and have a longer post-exposure life expectancy in which to exhibit adverse radiation effects
Developing the PHOENIX scanner constitutes major research and technological challenges. If successful, will promote PET imaging of children, improve its diagnostic capabilities, staging and response assessment.
Pediatric PET imaging research focusses on reducing patient dose whenever possible and on minimizing exam durations as well as sedation times  still requires several technological advancements.
-without becoming claustrophobic- and,
uniform spatial resolution in the range of 2-3 mm (current WB-PET scanners: 3-6 mm10; organ dedicated PET scanners: 1.5-3 mm19) in the entire FOV by enabling depth of interaction (DOI) resolution < 4 mm. The PHOENIX large FOV combined with the Signal to Noise (SNR) gain resulting from the inclusion of Time Of Flight (TOF) information will permit for a significantly increased in sensitivity of ×30, when compared to conventional PET.

## Slide 31
PHOENIX: Technical objectives and breakthroughs
TOF
Effective sensitivity 30
BGO  Hybrid scintillator
Scintillation + Prompt (Cherenkov) Light
!
Compton Kinematics (BGO)
Photoelectric interaction ~30-40%
Compton scatter ~70-60%
Andrea Gonzalez-Montoro
(2/5) TOF exploiting BGO’s Cherenkov yield
<350 ps CTR. Boost in image SNR
(3/5) Reaching ultra-high sensitivity
Exploiting Compton kinematics
(1/5) 3D photon positioning using BGO slabs
Uniform 3D resolution < 2-3 mm
SNR gain
CTR (ps)
16
12
8
4
0
- 100. 300 500 700
FOV Diameter
Corrected LOR
Wrong LOR
DOI
Geomsensitivity gain 10
TOFsensitivity gain  3
Notes: , BGO is more suitable for boosting timing performance by properly exploiting the low Cherenkov yield24. Unfortunately,
Once the events are classified based on its nature, data will be post-processed to convolve the different contributions encountered in the coincidence time resolution (CTR) spectra: (i) each of the four categories will be fitted using a double Gaussian distribution29,30; (ii) the centroid of the distribution (μk) will be considered as the time bias for each category and will be used to correct each measured time-stamp (tik) as: tik= tik-μk; (iii) the corrected CTR profile, which is the convolution of all detected coincidences, will be fitted again providing an accurate CTR value that will be implemented as the TOF-kernel during reconstruction31, 32.
Based on previous evidence, properly exploiting the low Cherenkov yield may be the key to unlock precise estimation of the TOF kernel using BGO and thus, constructing affordable high-efficiency PET scanners such as PHOENIX which targets for a CTR value < 350 ps
Extending the axial length of the scanner (TB-PET28).
Placing the detectors closer to the area under study
iii) Enabling TOF information during the image reconstruction provided

## Slide 32
PHOENIX: Technical objectives and breakthroughs
Andrea Gonzalez-Montoro
(5/5) PET system calibration using NN
Fast and easy calibration procedure. Better image quality
(4/5) Robust readout electronics for BGO TOF-PET
First low-cost, scalable and robust electronics for BGO
Unique circuit. No scalable technology yet developed!
PHOENIX: The first scalable solution for BGO-PET
Fast pediatric TB-PET (avoid sedation)
Ensuring children comfort and safety
Enhanced SNR, better image quality
Reduced dose exposure
New clinical studies
Affordable  transference to industry
Notes: , BGO is more suitable for boosting timing performance by properly exploiting the low Cherenkov yield24. Unfortunately,
Once the events are classified based on its nature, data will be post-processed to convolve the different contributions encountered in the coincidence time resolution (CTR) spectra: (i) each of the four categories will be fitted using a double Gaussian distribution29,30; (ii) the centroid of the distribution (μk) will be considered as the time bias for each category and will be used to correct each measured time-stamp (tik) as: tik= tik-μk; (iii) the corrected CTR profile, which is the convolution of all detected coincidences, will be fitted again providing an accurate CTR value that will be implemented as the TOF-kernel during reconstruction31, 32.
Based on previous evidence, properly exploiting the low Cherenkov yield may be the key to unlock precise estimation of the TOF kernel using BGO and thus, constructing affordable high-efficiency PET scanners such as PHOENIX which targets for a CTR value < 350 ps
Extending the axial length of the scanner (TB-PET28).
Placing the detectors closer to the area under study
iii) Enabling TOF information during the image reconstruction provided
The most defiant goal  development of the required readout and frontend electronics in a scalable format

## Slide 33
Outline
PET History & Evolution
PET Detector  PET scanner
PET system technology requirements
  Pre-clinical PET
  Clinical PET
State-of-the-art
  Dedicated-, WB-, and TB-PET
Conclusion
Outline

## Slide 34
High performance PET systems 
  Novel Scintillators; Enhanced Photosensors; Fast Electronics; More Efficient Algorithms (AI)
  Higher sensitivity x 2-4  (Large coverage PET (TB) or/and TOF)
  Homogeneous spatial resolution < 2mm in the entire FOV  Accurate 3D positioning (DOI)
  Better SNR  Medical breakthroughs
Screening
Low dose
Lower statistics required  Shorter scan times / Dose reduction / A combination of both
Follow-up studies and better assessment of treatments
Dynamic studies
New categories of patients (pediatric-PET)
High dynamic range
3-5 times longer acquisitions than the half-life of the isotopes
11C
Take home message
   Improved diagnostic quality
WB- and TB-PET 
  Larger Axial Coverage; Simultaneous Multi-organ Studies; Intratumor Homogeneity Studies
Advancements in nuclear imaging:

## Slide 35
PET technology in Prague
Almost 26 years already

## Slide 36
Advice
Darmstadt, Germany
1st international experience  2015 (as a Master Student)
YOUR TASKS:
Take out the most of this experience
Enjoy the school
Interact with the lectures
Make new Friends
This is an unique experience!!
10 years ago…
Still have Good Friends from then!

## Slide 38
Medical Imaging:
PET
July 2nd 2025
Andrea Gonzalez-Montoro, PhD
andrea.gm@i3m.upv.es