## Slide 1: Present and future of nuclear power engineering
Jan Syblík, 10.7.2025

## Slide 2: Content
Introduction to the topic
Nowadays status of nuclear power engineering
Where are we heading? SMRs, Gen IV
Virtual tour at the nuclear power plant

## Slide 3
Jan Syblík
Faculty of Mechanical Engineering (CTU)
  Experimental thermalhydraulics
  Supercritical CO2 as a coolant for fusion projects
  Safety analysis (subchannel, thermohydraulics, severe accidents)
SÚRO: National radiation protection institute (est. 1995)
TSO: Technical Support Organization (est. 2017)
Notes: 50s

## Slide 4: Fission
One fission of 235U produces 192 MeV of usable energy (loss in gamma and neutrinos)
Neutrons are divided:
  Fast, Epithermal and Thermal
Microscopic effective cross section – σ
  expresses the probability of neutron interaction
σe , σi , σf, σr - cross-sections for elastic and inelastic scattering, fission and radiative capture
Fission cross section; resonance region

## Slide 5: Controlled fission
Chain reaction can be described by the multiplication factor
k>1 => critical reactor
Delayed neutrons (seconds to few minutes) – beta decays, half-life
Notes: https://nuclear-power.com/wp-content/uploads/2019/01/Neutron-Life-Cycle.png

## Slide 6
* 105

## Slide 7
VVER-1000
L = 3.65 m
d = 9.1 mm
pin pitch = 12.75 mm
312 x 163

## Slide 8
Simplified layout of NPP with PWR
Simplified layout of NPP with VVER

## Slide 9
Notes: Problem at Fukushima - BWR 3 and 4 .... They didn't have a concept for the restoration of the technical work

## Slide 10: Nowadays (2024) electricity generation

## Slide 11
PRIS - Reactor status reports - In Operation & Suspended Operation - By Type

## Slide 12: Under construction
Notes: Rosatom, China, IAEA graphs

## Slide 13: Where are we heading?
Spread of proven technologies – PWRs, BWRs
SMRs – challenging topics
  μMRs
Gen IV. reactors
Increasing of safety
Notes: Generace I:Do I. generace patří reaktory, které byly projektovány v letech 1950 - 1960. Do této generace se například řadila i první československá jaderná elektrárna A1 v Jaslovských Bohunicích na Slovensku. Posledním provozovaným reaktorem této generace byl 1. blok jaderné elektrárny Wylfa ve Velké Británii, který byl odstaven na konci roku 2015.
Generace II:Projektování a výstavba jaderných elektráren s reaktory II. generace byla zahájena v sedmdesátých letech minulého století. V současné době mají elektrárny s reaktory II. generace nejvýznamnější podíl na výrobě elektrické energie v jaderných elektrárnách. Více než polovinu těchto elektráren tvoří tlakovodní reaktory (PWR). Do této generace se řadí také reaktory VVER (ruské označení pro PWR), budované a provozované v bývalém Československu (a jeho následovníky ČR a SR). V porovnání s reaktory I. generace je úroveň elektráren s reaktory II. generace velmi výrazně vyšší, především v oblasti bezpečnostních systémů.
Generace III:Reaktory generace III představují další evoluční stupeň ve vývoji reaktorů. Hlavní technologické rysy jsou velmi podobné reaktorům druhé generace. Hlavními rozdíly oproti předchozí generaci je použití standardizovaných projektů, zkracujících dobu schvalování a také dobu výstavby. Dále zlepšení ekonomiky provozu prodloužením doby provozu mezi odstávkami, zvýšení hodnoty vyhoření jaderného paliva a v souvislosti se standardizovaným projektem i snížení investičních nákladů. Významné je také zlepšení celkové bezpečnosti elektrárny (zvládání vícenásobných poruch a těžkých havárií a také zlepšení odolnosti vůči vnějším vlivům).
Generace III+:Reaktory generace III+ představují další evoluční vylepšení III. generace reaktorů v souladu s novými bezpečnostními požadavky a s ohledem na zkušenosti z licencování a výstavby bloků III. generace. Nabízejí tak v současné době nejlepší dostupnou technologii v oblasti jaderných elektráren. Mimo jiné jsou v projektech zapracovány závěry z analýzy havárie jaderné elektrárny Fukušima (v EU ve formě závěrů ze tzv. stress testů a doporučení WENRA), jmenovitě vyšší odolnost vůči vnějším vlivům (např. zemětřesení, záplavy apod.), vyšší autonomie, zvýšená redundance a diverzita bezpečnostních systémů pro řešení základních projektových nehod, vícenásobných poruch i těžkých havárií a také možnost využití mobilních prostředků pro plnění bezpečnostních funkcí.
Generace IV:Projekty IV. generace jsou zatím předmětem vývoje v několika různých koncepčních směrech. Jde převážně o první demonstrační reaktory, pracující s rychlými neutrony a uzavřeným palivovým cyklem, které umožňují efektivnější využití jaderného paliva zároveň snížení množství radioaktivních odpadů. Patří sem však i některé technologie pracující s tepelnými neutrony a otevřeným palivovým cyklem. Zahájení provozu prvních pilotních jednotek této generace je podle stavu jejich vývoje odhadováno mezi lety 2030 až 2040, komerční nasazení potom po roce 2050.

## Slide 14: SMRs
Small (up to 300 MWe)
Modular (?)
Reactor √
Interesting for big investors: lower CAPEX, lower OPEX, higher LCOE
Variety of use:
  Desalination
  Heat production
  Remote places (Canada mining fields and remote towns)
  Cargoships

## Slide 15: Challenges for SMRs
Non-boric acid operation
  Used only for emergency purposes - unintentional dilution, loss of redundant system for reactivity control
Passive systems
Integral constructions
Common cause failure
Different water chemistry regimes
Speed up the constructions and maintain safety and security (!) at the same time
Harmonization of legislation (lowering the CAPEX by tens of percents)
Artificial Inteligence in the regulatory framework
  Low human capacities
  Risks

## Slide 16: Rolls-Royce SMR
UK company, ČEZ owns 20 % from 2025
PWR, three loops
450 MWe
GDA process, stage 3
Evolutionary in:
  Introducing few passive systems
  Modularity of the turbine island, constructions, etc.
  Construction site
  Non-boric acid regime
  Large load-following

## Slide 17: BWRX-300
GE Hitachi
Boiling water reactor, natural circulation
300 MWe
Evolutionary in:
  Reduction in building volume
  Without reactor coolant pumps
  Low LCOE

## Slide 18: and many more…
Asia: Russian Federation KLT-40S, HTR-PM
Under costruction: CAREM-25 (Argentina), ACP100 (China), BREST-OD-300 (Russian Federation), USA n Kairos Power’s Hermes Low-Power Demonstration Reactor - fluoride salt-cooled, high-temperature reactor
Canada – BWRX-300
France - EDF-NUWARD SMR (Newcleo, Jimmy Energy, Otrera, Calogena, Blue Capsule Technology, Hexana, Stellaria and Thorizon)
Japan – HTTR
Republic of Korea – SMART, i-SMR
UK – Rolls Royce
USA – NuSCALE VOYGR, AP300 SMR, SMR-300, GenIV: X-energy Xe-100 (HTGR), Oklo Aurora Powerhouse, Westinghouse eVinci
Floating power plants – China, Denmark, Republic of Korea, Russian Federation

## Slide 19
Notes: MH-1A (reactor Sturgis) 1968-1975
KLT-40S

## Slide 20: GenIV
Set in 2002
The main goal is increasing safety
NPPs have low efficiency against coal power plants – low thermodynamic parameters (Carnot)
Gen IV should reach 45-55 % efficiency
100x higher safety against Gen I
Waste reduction (closed loops)
Challenges:
  Mainly materials
  Fuel
Closed fuel cycle
  Fabrication of nuclear fuel
  Power production
  Power refabrication (recycling)

## Slide 21
Notes: Spent fuel storage at ETE is for 30 years - possibility of extension and doubling of capacity
Question: how to label a nuclear repository so that even 10,000 years from now it will be clear what is stored there?

## Slide 22: GenIV designs
SFR - Sodium Fast Reactor
GFR – Gas-cooled Fast Reactor
LFR - Lead cooled Fast Reactor
MSR - Molten Salt cooled Reactor
VHTR - Very High Temperature Reactor
SCWR - Supercritical Water Reactor

## Slide 23: SFR
Sodium-cooled fast breeder reactor
Core outlet temperature: 500-550 °C, atm., 50-1500 MWe
Coolant: Liquid sodium
Large power density– lower volume of the active zone
Past projects: EBR-1 (1950), Fermi 1 (1963), BOR-60 (1969), BN-350 (1972), Phénix (1973), Superphénix (1986), Monju (1995), …
Current developments: BN-600, BN-800, CFR-600, PFBR, …
Under development: BN-1200, ASTRID, 4S, …
Pros
  Formation of fissile material - 233U 239Pu
Cons
  Three loops due to sodium interaction with water, sodium reacts chemically with air and water and requires a sealed coolant system
  Sodium is not transparent, it requires a very different set of in-service monitoring and inspection tools and dedicated operating procedures that differ from conventional LWRs
Notes: Flux spectrum

## Slide 24: GFR
Core outlet temperature: 800-850 °C
Coolant: Helium
Primary pressure: 7 MPa
Power range: 2400 MWe
Main challenges:
  High thermomechanical resistance (temperature 850°C & pressure 7 MPa)
  Resilient tensile fatigue characteristics and long-term creep resistance
  Resistance to extreme environments – corrosion/oxidation in impure helium which may include hydrogen and helium gas that can cause embrittlement
Current developments: ALLEGRO, Kamado, EM2, HeFASTo

## Slide 25: LFR
Core outlet temperature: 480-540 °C, atm., 50-1200 MWe
Coolant: Lead (Pb) / Lead-Bismuth Eutectic Alloy (Pb-Bi)
Past projects: Project 645, Submarine K-27 (1963)*, Projects 705 and 705K, NATO designation Alfa class (1971)*, test loops in all Japan
Under construction: BREST-OD-300
Under development: ALFRED, ELFR, MYRRHA, SEALER-55, LFR-AS-30, LFR-AS-200
Pros:
  high boiling point (up to 1743°C), benign interaction with water and air
  favorable neutronic and radiation shielding properties - due to its large atomic mass, lead is an excellent reflector; this contributes to high neutron utilization and minimizes neutron leakage from the core. This results in a high conversion factor and a high potential for propagation or transmutation
Cons:
  high melting temperature of lead (327°C), opacity of lead
  corrosion when in contact with structural steels (accelerated with temperatures) - Lead leaches alloying elements from pipes, errosion of circulation coolant pumps
* The experience gained from the submarine nuclear reactors is valuable, but not completely transferrable to modern LFR concepts - different operating spectrum and conditions of operation (very compact reactors, highly enriched fuel, high-power density).

## Slide 26: MSR
Core outlet temperature: 700-800 °C, atm., 1000 MWe
Coolant: Fluoride salts
Molten fuel
FLiBe (7Li vs. 6Li), FLiNaK, ...
Previous projects: mainly ORNL, MSRE (1965)
Pros:
  High thermal efficiency
  Low pressure
  Passive safety
  Continual work without fuel outage
Cons:
  Materials: resist corrosion, endure high temperatures, and tolerate neutron fluxes over long periods
  Fuel Salt Processing
  Accidents at experiments
  High Toxicity of the salts

## Slide 27: VHTR
Core outlet temperature: 900-1000 °C, atm., 250-300 MWe
Coolant: Helium
TRISO fuel - millimeter in diameter
  Silicon carbide, pyrolytic graphite
HTR-PM since 2024
Pros:
  Inherent safety
  High temperature is valuable for the industrial heat (hydrogen, steel, …)
Cons:
  power peaking and temperature gradients in the core, as well as hot streaks in the coolant gas
  Helium – expensive, leakages

## Slide 29: SCWR
Core outlet temperature: 510-625 °C, 25 MPa, 300-1500 MWe
Coolant: Water
Critical point of water: 374°C, 22.1 MPa
Pros:
  Improved economics (high efficiency),
  S.Water is a mature approach, improving PWR concept
Cons:
  Cladding - structural materials that can withstand the SC conditions usually have a large neutron capture cross-section
  Unsolved water chemistry (radiolysis of water)
  Lack of validated computer codes (need of experimental verification)
  Reaching critical point during start-up
ECC-SMART

## Slide 30: INES
Notes: The International Nuclear Event Scale
7 – Chernobyl Fukushima
6 – Majak
5 – TMI, Windscale Pile (Sellafield)

## Slide 31: Industrial accidents
Banqiao Dam 1975
Bhopal 1984
Beirut 2020
Chernobyl 1986
Fukushima 2011
Notes: https://www.3pol.cz/cz/rubriky/fyzika-a-klasicka-energetika/1801-jak-smrtici-je-vase-kilowatthodina
Pan-čchiao – 26k directly, 145k for epidemics and famine, 11m people affected, 6m buildings destroyed
methylisokyanátu 25 k deaths, 520 k affected
200 deaths 6500 wounded
42 deaths from acute radiation. Impacted 500k people - mainly in clearance work. 23% increased number of abortions (Ukraine approx. 50 effects per foetus).
Lots of hoaxes

## Slide 32: Radioactive water release from Fukushima
150 tons daily
Limits for water of tritium:
Japan: 60 000 Bq/l (safety)
WHO: 10 000 Bq/l (drinkable)
Limits for drinking water sources:
EU (in general): 100 Bq/l
Finland (tritium): 30 000 Bq/l
Fukushima (tritium): 1500 Bq/l
Notes: https://www.osel.cz/11694-tritiova-voda-z-fukusimy-i-skonci-v-oceanu.html

## Slide 33: Blackout in Spain

## Slide 34: Power Outage in Prague
4.7.2025
Black out x Massive Power Outage
Renewables x Damaged cable

## Slide 35
Can the NPP react on fluctuations in the network?
How fast can it start-up?
What is an iodine pit, what effect does it have on operators?

## Slide 37
Lattice Codes:
SCALE
HELIOS
CEZ Data – From State Office for Nuclear Safety (SUJB)
Severe Accident Analyses: MELCOR
TH Analyses:
TRACE
Full Core Neutronics:
ANDREA
PARCS
Sub-channel:
SCF
P and P profile,
Decay Heat
Σ, β, λ, φ, ν
K-infinite
K-fision
Kg, Decay heat of FP, Pu, U and MA
P and P profile per assembly,
decay Heat
P and P profile,
Decay Heat based on the selected methodology
Cladding Temperature Profile
Inlet Temperature,
Inlet Flow,
Inlet Pressure
Source Term
Thermomechanical Analyses:
TRANSURANUS
Release of radioactive material:
JRODOS
Mechanical Analyses: FEM
CFD
Constitutive Analyses

## Slide 38: Cenelín
https://www.cenelin.org/about/
Virtual Nuclear Power Plant | Godot engine #4

## Slide 39
Thank you for your attention!
Jan.Syblik@suro.cz