## Slide 1: High-Power Switching using Super-Critical Fluids
TU/e
Bert van Heesch
Jin Zhang, Frank Beckers, Guus Pemen,
Tom Huiskamp, Wilfred Hoeben
CWI
Ute Ebert, Aram Markosyan
e.j.m.v.heesch@tue.nl

## Slide 2
High-voltage switch
For industrial applications
Challenges:
High hold-off voltage
Large current
Nanoseconds rise time
Fast recovery
High repetition rates
Very low on resistance
Accepting overload
Self healing
Environmentally safe
Long lifetime

## Slide 3: Breakdown in Super Critical Fluid
Fluid above critical
pressure + temperature
CO2: 74 bar 31C
N2: 34 bar -147C
Very high E-field
High heat conductivity
High heat capacity
Low viscosity
Liquid but no vapor bubbles
Self healing
liquid
gas
solid
Pressure 
Temperature 
Super
critical
Approach to meet the challenges
Phase diagram
Liquid
Unlike oil or water

## Slide 4
Discharge current and
CCD picture
Pulse Source
SC Switch

## Slide 5
Arc Voltage is High during first 150 ns current flow
E field and voltage, gap of 0.3 mm in 80 bar Nitrogen after breakdown from 25 kV open gap voltage
Arc voltage 
24 kV
0
6 kV

## Slide 6
120 kV super-critical
switch device
25 cm

## Slide 7
Comparison with existing CO2 and SF6 switching performance
 | Parameters at existing switch conditions |  | 
 | Breakdown | Arc Voltage | Switch condition
Supercritical N2 [4,10] | 180 kV/mm @80bar | 6 kV | Supercritical, pulsed V
CO2 [9] | 2 kV/mm @1 bar | 2 kV @14 bar | 14 bar, 50 Hz
SF6 [8] | 9 kV/mm @1 bar | 1 kV @14 bar | 14 bar, 50 Hz
Paschen’s curve: ratio SF6 to air is 2.5
but this only holds for (non-streamer-like) homogeneous discharge situations
At very high pressures the situation is always inhomogeneous since breakdown is streamer like
Very high pressure  Ratio between SF6 and air is 1 [11]
Indication: at SC pressures SF6 and N2 have similar BD strength

## Slide 8
Conclusions
Design and operation of reliable SCFs insulated switches
Two models for switching & recovery in SCFs
Experimental & theoretical analysis of plasmas in SC N2
Very high dielectric strength: ≤ 180 kV/mm, comparable with solid dielectrics
Fast dielectric recovery: ≤ 200 μs in both experiment and model
Successful current interruption for t > 2 ms, gap width ≈ 2 mm