## Slide 2: A Hybrid Bouncer System for Highly Repeatable and Precise Klystron Modulators
Xavier Bonnin and Davide Aguglia
CERN – European Organization for Nuclear Research, Technology department, Electrical Power Converter Group

## Slide 3: Context: Compact Linear Collider (CLIC)
Parameter | Value | Unit
Nb of klystrons | 1300 | 
Voltage | 180 | kV
Current | 160 | A
Pulse length | 140 | µs
Rep. Rate | 50 | Hz
Stability | 0.85 | %
Repeatability | 10 | ppm
Evaluation of a Hybrid Bouncer System for High Precision Klystron Modulators

## Slide 4: Context: Compact Linear Collider (CLIC)
Parameter | Value | Unit
Nb of klystrons | 1080 | 
Voltage | 180 | kV
Current | 160 | A
Pulse length | 148 | µs
Rep. Rate | 50 | Hz
Stability | 0.85 | %
Repeatability | 10 | ppm
Large number of modulators => Reliability
  Capacitor discharge based topology
High level of constraint on the precision
  Compensation techniques are needed (bouncer circuits)
Evaluation of a Hybrid Bouncer System for High Precision Klystron Modulators

## Slide 5: Capacitor discharge based modulator
Evaluation of a Hybrid Bouncer System for High Precision Klystron Modulators

## Slide 6: Capacitor discharge based modulator
Bouncer circuit:
  Goal: compensating the cap. bank voltage droop
  Variety of technical solutions
    Active switch(es)
      Linear mode / switching mode / both
    Passive resonant bouncer topologies
Evaluation of a Hybrid Bouncer System for High Precision Klystron Modulators

## Slide 7: Bouncer circuits examples
 | Corr | Ripple | Flex. | Robust | Eff
Linear | ++ | No | + | + | -
Evaluation of a Hybrid Bouncer System for High Precision Klystron Modulators

## Slide 8: Bouncer circuits examples
 | Corr | Ripple | Flex. | Robust | Eff
Linear | ++ | No | + | + | -
Switching | + | Yes | ++ | - | +
Evaluation of a Hybrid Bouncer System for High Precision Klystron Modulators

## Slide 9: Bouncer circuits examples
 | Corr | Ripple | Flex. | Robust | Eff
Linear | ++ | No | + | + | -
Switching | + | Yes | ++ | - | +
Hybrid | + | No | ++ | - | +
Evaluation of a Hybrid Bouncer System for High Precision Klystron Modulators

## Slide 10: Bouncer circuits examples
 | Corr | Ripple | Flex. | Robust | Eff
Linear | ++ | No | + | + | -
Switching | + | Yes | ++ | - | +
Hybrid | + | No | ++ | - | +
Passive | - | No | - | ++ | ++
 | Corr | Ripple | Flex. | Robust | Eff
Linear | ++ | No | + | + | -
Switching | + | Yes | ++ | - | +
Evaluation of a Hybrid Bouncer System for High Precision Klystron Modulators

## Slide 11: Passive bouncer with linear switches
Requirements:
Vb < 0 or >0
ic < 0 or >0
=> 4-Q topology is needed
Evaluation of a Hybrid Bouncer System for High Precision Klystron Modulators

## Slide 12: Passive bouncer with linear switches
Requirements:
Vb < 0 or >0
ic < 0 or >0
=> 4-Q topology is needed
4 switches
  2 in linear mode
  2 in switching mode
Additionnal insulated power supply
Possible solution
Evaluation of a Hybrid Bouncer System for High Precision Klystron Modulators

## Slide 13: Passive bouncer with linear switches
Requirements:
Vb1 > 0
ic < 0 or >0
=> 2-Q topology is needed
2 switches in linear mode
Additionnal grounded power supply
Other solution
Evaluation of a Hybrid Bouncer System for High Precision Klystron Modulators

## Slide 14: Passive bouncer with linear switches
Other solution
Evaluation of a Hybrid Bouncer System for High Precision Klystron Modulators

## Slide 15: Designing procedure
Real Time compensation by the linear circuit
« Feedforward » compensation by the passive bouncer
Linear analysis:
Evaluation of a Hybrid Bouncer System for High Precision Klystron Modulators

## Slide 16: Designing procedure
Real Time compensation by the linear circuit
« Feedforward » compensation by the passive bouncer
Linear analysis:
Optimize this term in order to minimize the pulse error
Evaluation of a Hybrid Bouncer System for High Precision Klystron Modulators

## Slide 17: Designing procedure
Real Time compensation by the linear circuit
« Feedforward » compensation by the passive bouncer
Linear analysis:
Optimize this term in order to minimize the pulse error
Evaluation of a Hybrid Bouncer System for High Precision Klystron Modulators

## Slide 18: Designing procedure
Real Time compensation by the linear circuit
« Feedforward » compensation by the passive bouncer
Linear analysis:
Optimize this term in order to minimize the pulse error
Evaluation of a Hybrid Bouncer System for High Precision Klystron Modulators

## Slide 19: Designing procedure
Real Time compensation by the linear circuit
« Feedforward » compensation by the passive bouncer
Linear analysis:
Optimize this term in order to minimize the pulse error
New set of components and initial values
Evaluation of a Hybrid Bouncer System for High Precision Klystron Modulators

## Slide 20: Designing procedure
Evaluation of a Hybrid Bouncer System for High Precision Klystron Modulators
Parameters:
Components: Cb, L, Ltransfo
Initial conditions: Vin0, iL0 and Vb0
Constraints (equality):
Energy conservation in the bouncer (=steady state)
Sensitivity analysis (normalized function):
1% of error 100% deviation
10% of error  60% deviation

## Slide 21: Designing procedure
Real Time compensation by the linear circuit
« Feedforward » compensation by the passive bouncer
Linear analysis:
Evaluation of a Hybrid Bouncer System for High Precision Klystron Modulators

## Slide 22: Designing procedure
Real Time compensation by the linear circuit
« Feedforward » compensation by the passive bouncer
Linear analysis:
LF compensator
HF compensator
Evaluation of a Hybrid Bouncer System for High Precision Klystron Modulators

## Slide 23: Performances
Simulation results
RMS error: 1500ppm
Losses: 0.9% of Wpulse
Evaluation of a Hybrid Bouncer System for High Precision Klystron Modulators

## Slide 24: Performances
Monte Carlo simulation results
Sensitivity analysis:
  500 runs
  Parameters are randomly chosen in a +/-10% range around the optimal solution (bouncer components only)
  Impact on precision and losses ?
Worst accuracy: 2600ppm
With only passive bouncer: 9700ppm
Highest losses: 1.3% of Wpulse
With only linear ballast: >5% of Wpulse
Evaluation of a Hybrid Bouncer System for High Precision Klystron Modulators

## Slide 25: Experimental set up
Evaluation of a Hybrid Bouncer System for High Precision Klystron Modulators

## Slide 26: Conclusion
Capacitor discharge based modulators need a compensation circuit (bouncer)
The presented topology aims at merging the advantages of a passive bouncer and an active linear stage
  Acceptable level of losses
  Fairly simple topology and control strategy
  High bandwidth (linear)
  Compensation of spread thank to a high bandwidth feedback control
Evaluation of a Hybrid Bouncer System for High Precision Klystron Modulators