## Slide 1: Detector/Receiver “Cold” Measurements
MadMax-Workshop MPP Munich
O. Reimann for the MADMAX-Group May 10, 2017

## Slide 2: Outline
Microwave radiometer (short reminder)
  Comparison between photon- and heterodyne detection
Current lab system
  Schematic
  First cold tests
Conclusion

## Slide 3: Photon Detection Setups
Two principle ways:
  Photon counting
  Measurement of mean photon flux
Photon counting
  Limited by photon energy (Needs „high energy“ photons)
  Energy (frequency) resolution is limited
Photon flux measurement
  Not limited by low energy photons
  Excellent frequency (energy) resolution (easily it can be better than 10-9), because of usually used “coherent” detection (normally heterodyne detection)

## Slide 4: Photon Detection Setups
Photon counting:
Photon flux measurement: direct heterodyne (“coherent”)
Mixer
Oscillator
Bandpass
Detector
Current meter
Detector
Current meter
Detector
Counter

## Slide 5: Choosing the Right Bandwidth
What is the detectable noise temperature for a given system noise temperature (Dicke-formula):
Detectable noise power (assuming no gain fluctuation)
Averaging time for a given signal/noise ratio:
with
and
with
DfF: Filter bandwidth
t: Averaging time
TSys: Total system noise temp.

## Slide 6: Choosing the Right Bandwidth
What is the best bandwidth for line detection
  Detectable background noise power increases with frequency (Square root)
  Signal noise increases with frequency (Linear, if rect. distribution)
  → Bandwidth should not be larger than line- width for best signal- noise ratio
Example
Receiver: TSys=5K
Signal: 10-23W (1photon/s @ 15GHz), linewidth 10kHz, equal distributed

## Slide 7: Receiver
Axion mass range: 40 µeV … 400 µeV Frequency range: 10 GHz … 100 GHz (l = 3 cm … 3 mm)
Detection of signal line in frequency domain with DnA = 10-6 nA
…

## Slide 8: Low-Noise Amplifiers
2 different devices (Low Noise Factory, Chalmer University)
Same characteristics @ RT but 1 is for cryo temperatures
6-20 GHz Cryogenic Low Noise Amplifier, 5K @ 8-10K
1-15 GHz Low Noise Amplifier, 75K @ RT
cannot significantly reduced
(Nature Materials Nov. 10, 2014
© Low Noise Factory

## Slide 9: Heterodyne Detection
Lab system:
Fake axion
Signal analyzer (4 samplers, 1.4% dead time)
LHe bath → 4K THe + 5.5K TAmp = 9.5K TSys
Her the reality is a little bit more complicated! (FT-analysis)
Front end mixers and amps

## Slide 10: Heterodyne Detection: First Cold Test
Inject fake axion signal with 1.2.10-22 W at LHe temp.
  Frequency: 18.85 GHz
  Frequency modulated with gaussian noise
  Signal bandwidth: 8 kHz, Lorentz-shaped

## Slide 11: Heterodyne Detection: First Cold Test
Inject fake axion signal with 1.2.10-22 W at LHe temp.
  Frequency: 18.85 GHz
  Frequency modulated with gaussian noise
  Signal bandwidth: 8 kHz, Lorentz-shaped
  Received signal after 28h measurement (averaged signal):

## Slide 12: Heterodyne Detection: First Cold Test
Inject fake axion signal with 1.2.10-22 W at LHe temp.
  Frequency: 18.85 GHz
  Frequency modulated with gaussian noise
  Signal bandwidth: 8 kHz, Lorentz-shaped
  Received signal after baseline subtraction and gain correction:

## Slide 13: Heterodyne Detection: First Cold Test
Inject fake axion signal with 1.2.10-22 W at LHe temp.
  Frequency: 18.85 GHz
  Frequency modulated with gaussian noise
  Signal bandwidth: 8 kHz, Lorentz-shaped
  X-Correlation signal with 8kHz width: s: Signal T: Testfunction (Lorentz, Gauss, …)
Highest peak

## Slide 14: Heterodyne Detection: First Cold Test
Inject fake axion signal with 1.2.10-22 W at LHe temp.
  Frequency: 18.85 GHz
  Frequency modulated with gaussian noise
  Signal bandwidth: 8 kHz, Lorentz-shaped
  X-Correlation signal with 8kHz width (Zoom):

## Slide 15: Heterodyne Detection: First Cold Test
Inject fake axion signal with 1.2.10-22 W at LHe temp.
  Frequency: 18.85 GHz
  Frequency modulated with gaussian noise
  Signal bandwidth: 8 kHz, Lorentz-shaped
  Why 8kHz Bandwidth? Algorithm is searching for best S/N-ratio:

## Slide 16: Heterodyne Detection: First Cold Test
Inject fake axion signal with 1.2.10-22 W at LHe temp.
  Frequency: 18.85 GHz
  Frequency modulated with gaussian noise
  Signal bandwidth: 8 kHz, Lorentz-shaped
  Why 8kHz Bandwidth? Algorithm is searching for best S/N-ratio:
Bin #
Peak Freq. in Hz
Best Filter in Hz
X-corr. S/N
Signal #

## Slide 17: Heterodyne Detection: First Cold Test
Inject fake axion signal with 1.2.10-22 W at LHe temp.
  Frequency: 18.85 GHz
  Frequency modulated with gaussian noise
  Signal bandwidth: 8 kHz, Lorentz-shaped
  Signal + Lorentz-fit (8kHz):

## Slide 18: Additional Facts:
Comparison with Allen’s run statistic algorithm showed good agreement
Cold tests are ongoing
  5.10-23 W in 10kHz linewidth already reached within one week in 10K Tsys (Physical limit)
  Different tests runs should give a clearer insight to possible problems (quantization noise, …)

## Slide 19: Conclusion
Receiver concept is OK
  Dead time 1,4%
  Sensitivity in warm and cold is OK
Next Tests:
  Systematic cold measurements
  Better Antenna measurements
  Cold background measurements in cryostat

## Slide 20: Appendix

## Slide 21: Spectral Power Density of (BB)-Noise
Contribution of a detector: (no phase preservation)
Contribution of an amplifier or mixer: (phase preservation)
Limit for low frequencies and/or high temperatures:
Noise temperature

## Slide 22: Spectral Power Density of (BB)-Noise
Example:
  Spectral power density for different temperatures
Frequency (Hz)
EN(W Hz-1)
400 K
100 K
10 K
1 K
100 K
Amplifier, Mixer
Detector
“Quantum limit”

## Slide 23: Noise Equivalent Power
System noise temperature TSys and bandwidth DfF are difficult to measure for broadband detectors
  Johnson noise
  Phonon-electron coupling
  Generation-recombination noise
  Background noise
  …
→ Using noise equivalent power (NEP):
Sometimes a little bit different NEP definitions are used, most of them have factor 2 or 2½ included (Because of 2 polarizations or time to bandwidth conversion)

## Slide 24: Broadband detectors
Types of broadband detectors
  Bolometers
  Microwave kinetic inductance detector (MKID)
  Double quantum well detectors
  Transition edge sensors (TES)
Usually they work good only at higher frequencies (> 50 … 100 GHz)
Often the devices are background limited
  Example: Background temperature 300 K, bandwidth 50 GHz → NEP = 9.2 10-16 W Hz-½
Temperature and bandwidth can be reduced, but then again the other noise sources start to dominate (see later)!

## Slide 25: Comparison: Heterodyne  Direct Det.
Noise equivalent power of a heterodyne system:
Non-existing graphene bolometer with 10 MHz coupling bandwidth and 20 mK temperature [1]. Unrealistic!!!
State-of-the-art bolometer
Frequency (Hz)
NEP (W Hz-½)
[1] K.C. Fong and K.C. Schwab, “Ultra-sensitive and Wide Bandwidth Thermal Measurements of Graphene at Low Temperatures“, 2012

## Slide 26: Heterodyne Detection: Real Devices
Noise temperature limit for InP devices:
  Mainly phonon self heating  Inner bulk black body radiator
Shi, et. al. A 100-GHz Fixed-Tuned Waveguide SIS Mixer Exhibiting Broad Bandwidth and Very Low Noise Temperature, 1997
InP-HFET,
Bryerton et. al. “Ultra Low Noise Cryogenic Amplifiers for Radio Astronomy”, 2013
InP-HEMT Our amplifier, LNF

## Slide 27: First Cold Measurement
First quick and dirty test:
  Very simple test in LHe-dewar
  Amplifier at LHe-temperature (4.1K)
Gain
Noise temperature
Room for improvement!

## Slide 28: Run Optimization
Measurement time vs. analysis threshold level and power boost factor:
  80 disks, LaAlO3, Tsys=8K, effectivity: 75%, 1day adjustment time
days/GHz

## Slide 29: Sensitivity in terms of Axions
no boost
Scenario II
> 104 boost needed!
QCD Axion DM prediction
  80 disks (LaAlO3)
  d=1m, B=10 T, t=200 h, DnA=10-6 nA
  8K amplifier temperature
  4s detection level

## Slide 30: Photon Noise Equivalent Power (NEPg)
Photon energy:
Noise equivalent power “of a photon”:
n: Mean photon flux (background + signal) in 1/s
Frequency n | Photon Energy Eg | 1 g/s = | NEPg for 1 g/s
10 GHz | 6.62 10-24 J (41.36 µeV) | 6.62 10-24 W | 9.4 10-24 W Hz-½
20 GHz | 1.33 10-23 J (82.71 µeV) | 1.33 10-23 W | 1.87 10-23 W Hz-½
50 GHz | 3.31 10-23 J (206.8 µeV) | 3.31 10-23 W | 4.69 10-23 W Hz-½
100 GHz | 6.62 10-23 J (413.6 µeV) | 6.62 10-23 W | 9.4 10-23 W Hz-½
n

## Slide 31: Double quantum dot
Function principle
  Absorption of photon with energy hn
  Electron in QD1 is excited to QD2 (tunneling)
  Electron can leave to drain lead and new electron enters from the source
  Then cycle can be repeated
  Current flow through the system
  d can be changed by electric field

## Slide 32: Microwave Kinetic Inductance Detector
Function principle:
  Breaking cooper pairs in a superconductor (inductor) by photons
  Stored energy (inner inductance) is changed
  Resonance frequency of the resonator shifts
Superconducting Gap Energy

## Slide 33: SIS-Mixer (Principle)
Cooper pairs break into quasi-particles and tunnel over the barrier
Using photon assistant tunneling for mixing
Slope of I-V curve has sharp discontinuity: efficient

## Slide 34: SIS-Mixer (Principle)
Mixer loss -> higher noise temperature
Double-sideband feature -> looking at two frequencies at the same time
J. Zmuidzinas, „COHERENT DETECTION AND SIS MIXERS”, 2002

## Slide 35: Heterodyne Detection: First Tests
Detection of a broadband noise signal
  Frequency: 15 GHz
  Linewidth: 200 kHz
  Detection bandwidth: 10 kHz
Modulated signal @ 15 GHz with 0.8 10-19 W in 600 s and 77 K

## Slide 36: Heterodyne Detection: First Tests
Detection of a line signal (Examples)
  Frequency: 15 GHz
  Detection bandwidth: 10 kHz
Signal line @ 15 GHz with -160 dBm (10-19 W or 104 g/s) @ RT
Signal line @ 15 GHz with -168,5 dBm (1.4 10-20 W or 1421 g/s) in 17h @ RT
Real signal: