## Slide 1: Development of Software Frameworks for LLRF Applications based on EPICS Zheqiao Geng June 05, 2019 EPICS Collaboration Meeting, ITER

## Slide 2
LLRF System and Software Challenges
Functions of LLRF application software:
RF system setup, calibration and optimization (e.g. set klystron working point, calibrate acc. voltage and beam phase, optimize RF for good stability)
RF control (e.g. feedback, adaptive feed forward)
Automation (e.g. high power RF conditioning, RF station startup, fault recovery, procedure to apply on beam)
Interlock Box
Power Supply
VME Crate
Down Converter
LO & Clock Generator
Expected Features of the Software Framework based on EPICS:
Allow developing EPICS software without knowing much about EPICS (e.g. record/device/driver supports)
Easily get or set values of multiple PVs in a function executed by a private thread
Possibly be able to automatically generate EPICS database and other configuration files (e.g. autosave request)
Implement a general architecture which should fit to different applications

## Slide 3
A General Software Architecture
The user codes can be grouped into modules. A module contains items:
EPICS records to configure the parameters of the module and display the results
Function blocks to process the data and perform logical controls
Maybe a thread to actively do its job
Interfaces with other modules
Interfaces for IOC shell to create, initialize or setup the module instances
Types of EPICS modules:
Control Device Module (module for control of instrument inserted by the control system designer)
Domain Device Module (module for control of physical device essential for the function of system )
Application Module (implements functions to handle data from domain device modules and perform other middle layer functions)
Typical architecture of EPICS modules

## Slide 4
Base Classes of the Framework
Yellow blocks are base classes

## Slide 5
Features of ooEpics:
EPICS database can be created by creating objects of LocalPV in user code.
Basic channel access functions (e.g. caget, caput, camonitor, w/o callbacks …) are wrapped by the RemotePV class. The remote channel names can be managed by a configuration file.
Provide base classes to implement finite state machines.
Provide general iocShell functions to create, initialize or setup a module instance.
Template for module skeleton code generation.
C++ Implementation: ooEpics

## Slide 6
Python Implementation: ooPye
Features of ooPye:
Fully Python based, no compilation against EPICS base needed. Use as much as possible the environment provided by the controls
Automatic generation of EPICS database and the soft IOC, hide details of EPICS for programming
A sort of pattern of software architecture that can be applied on many different systems

## Slide 7
Questions?