## Slide 1: Phoebus Alarm System Micro Services for Logging and Management.

## Slide 2: Alarm Philosophy
B. Hollifield, E. Habibi, "Alarm Management: Seven Effective Methods for Optimum Performance", ISA, 2007
A good alarm system is one which helps users take correct actions
ca
pva
Identify the problems
&
the corrective actions
  Manageable alarm rate <150/day
Help locating useful information
Notify subject matter expert
Alarm
System
Determine patterns & trends

## Slide 3: BEAST
Alarm Cfg & State
RDB
IOCs
Alarm Server
Current Alarms: Acknowledged? Transient? Annunciated?
LOG
Message RDB
JMS 2 Speech
JMS 2 RDB
Tomcat
Reports
CSS Applications
Alarm Client GUI
JMS
Alarm Updates
Ack’; Config Updates
Annunciations
Log Messages
TALK
ALARM_CLIENT
ALARM_SERVER
PV Updates (Channel Access, …)

## Slide 4
Alarm
Server
Alarm
Message
Logger
Alarm
Configuration
Server
Channel
Access
IOC
PVA
IOC
Alarm
Clients
Alarm micro services
Control
Systems
CS-Studio
…
…

## Slide 5: Alarm Logger Service

## Slide 6: Alarm Message Logger
Motivation
To create a archive of all alarm state changes and associated actions
Discover alarm patterns and trends
Generate Statistical reports on alarms
Debug the alarm system
Alarm
Message
Logger

## Slide 7: Alarm Message Logger
The alarm message logger subscribes to all
Configuration changes
  adding/removing or enabling/disabling
State changes
  e.g. alarm state changes from OK to MAJOR
Commands
  e.g. user actions to Acknowledge an alarm
All the above changes and commands are logged into a dedicated elastic index
Alarm
Message
Logger
Alarm Configuration
Alarm State
Alarm Command

## Slide 8: Architecture
Alarm
Message
Logger
Elasticsearch is a distributed, RESTful search and analytics engine.
An analytics and visualization platform called Kibana
Build and Run
git https://github.com/shroffk/phoebus.git
cd services/alarm-config-logger
mvn exec:java
Notes: Elasticsearch is a search engine based on the Lucene library.

## Slide 9: kibana client
A Timeseries view of phoebus alarm server messages.
Filtered:
pvname
node/system
alarm serverity
Notes: Machine learning and AI can help to systemize and identify alarm problems that is not so easily
detected by simple visualisation and statistics. Areas where machine learning can be particularly useful
are
1) identify false and missing alarms
2) root cause analysis of alarms.
Machine learning can be used to identify false alarms. Alarms can be classified in: A true event giving
a correct alarm or no event giving no alarm. This is the wanted behaviour of the alarm system. But the
alarm system can also give an alarm when there is no event and a true event can give no alarm. The
classification of an imaginary example with 21 alarms can be illustrated in the following confusion
matrix:
Figure 2: A confusion matrix showing number of positive and negative alarms paired with positive
and negative events.
Alarms can be classified from what type of alarm it is from the confusion matrix. Machine learning can
then be trained to recognize the different type of alarms and to build models that can be used to
identify new alarms in the different categories.
Root cause analysis of alarms can be complicated. A paper from (Abele, et al., 2013) [5] describes how
root cause analysis of alarms can be performed using machine learning and knowledge management.

## Slide 10: kibana client
Notes: Machine learning and AI can help to systemize and identify alarm problems that is not so easily
detected by simple visualisation and statistics. Areas where machine learning can be particularly useful
are
1) identify false and missing alarms
2) root cause analysis of alarms.
Machine learning can be used to identify false alarms. Alarms can be classified in: A true event giving
a correct alarm or no event giving no alarm. This is the wanted behaviour of the alarm system. But the
alarm system can also give an alarm when there is no event and a true event can give no alarm. The
classification of an imaginary example with 21 alarms can be illustrated in the following confusion
matrix:
Figure 2: A confusion matrix showing number of positive and negative alarms paired with positive
and negative events.
Alarms can be classified from what type of alarm it is from the confusion matrix. Machine learning can
then be trained to recognize the different type of alarms and to build models that can be used to
identify new alarms in the different categories.
Root cause analysis of alarms can be complicated. A paper from (Abele, et al., 2013) [5] describes how
root cause analysis of alarms can be performed using machine learning and knowledge management.

## Slide 11: kibana client
Notes: Machine learning and AI can help to systemize and identify alarm problems that is not so easily
detected by simple visualisation and statistics. Areas where machine learning can be particularly useful
are
1) identify false and missing alarms
2) root cause analysis of alarms.
Machine learning can be used to identify false alarms. Alarms can be classified in: A true event giving
a correct alarm or no event giving no alarm. This is the wanted behaviour of the alarm system. But the
alarm system can also give an alarm when there is no event and a true event can give no alarm. The
classification of an imaginary example with 21 alarms can be illustrated in the following confusion
matrix:
Figure 2: A confusion matrix showing number of positive and negative alarms paired with positive
and negative events.
Alarms can be classified from what type of alarm it is from the confusion matrix. Machine learning can
then be trained to recognize the different type of alarms and to build models that can be used to
identify new alarms in the different categories.
Root cause analysis of alarms can be complicated. A paper from (Abele, et al., 2013) [5] describes how
root cause analysis of alarms can be performed using machine learning and knowledge management.

## Slide 12: CS-Studio/Phoebus client
Notes: Machine learning and AI can help to systemize and identify alarm problems that is not so easily
detected by simple visualisation and statistics. Areas where machine learning can be particularly useful
are
1) identify false and missing alarms
2) root cause analysis of alarms.
Machine learning can be used to identify false alarms. Alarms can be classified in: A true event giving
a correct alarm or no event giving no alarm. This is the wanted behaviour of the alarm system. But the
alarm system can also give an alarm when there is no event and a true event can give no alarm. The
classification of an imaginary example with 21 alarms can be illustrated in the following confusion
matrix:
Figure 2: A confusion matrix showing number of positive and negative alarms paired with positive
and negative events.
Alarms can be classified from what type of alarm it is from the confusion matrix. Machine learning can
then be trained to recognize the different type of alarms and to build models that can be used to
identify new alarms in the different categories.
Root cause analysis of alarms can be complicated. A paper from (Abele, et al., 2013) [5] describes how
root cause analysis of alarms can be performed using machine learning and knowledge management.

## Slide 13: Alarm Data Management
The server can be configured to create a new index every day, week, month, or year
Searches can be performed across multiple indexes
Elastic Curator An Index Lifecycle Management tool which manages the cleanup and deletion of cold indices
# The units of the indices date span: Days (D), Weeks(W), Months(M), Years(Y).
date_span_units=M
# The value of the indices date span.
# An integer value to be combined with the units. For example, if months were selected and the value set to 2, each index would span 2 months.
date_span_value=1
http://localhost:9493/xf23id_opr_alarms_config_*/_search

## Slide 14: Alarm Configuration Service

## Slide 15: Alarm Configuration Service
Log all the configuration changes made to the alarm server configuration
Build and Run
git https://github.com/shroffk/phoebus.git
cd services/alarm-config-logger
mvn exec:java
Alarm
Configuration
Server
Subscribe,
Filter,
Timestamp,
Process
Alarm Configuration Messages

## Slide 16: Alarm Configuration Tree
Notes: Mapping of the alarm tree to the file structure

## Slide 17: Configuration History

## Slide 18: Configuration events

## Slide 19: Restore Scripts
Each alarm configuration change results in the creation or an update to the config.xml file.
The config.xml can be directly imported into the alarm server to restore it to the alarm configuration to that instant.

## Slide 20: Questions