## Slide 1: A Two-Tier PV Gateway for Channel Access from J-PARC Office Network to the Accelerator Control Network
Shuei Yamada
KEK/J-PARC Center Accelerator Control Group

## Slide 2: J-PARC
Japan Proton Accelerator Research Complex
Joint project of : KEK (High Energy Accelerator Research Organization) and JAEA (Japan Atomic Energy Agency)
©google
Hadron Experiment Facility
Materials and Life Science Facility
Neutrino Experiment Facility
LINAC 400 MeV/c @ 25Hz
RCS 3 GeV/c @ 25Hz
Main Ring 30 GeV/c @ 2.48 sec (FX to NU) @ 5.52 sec (SX to HD)
J-PARC
(in site of JAEA)
KEK
Tokyo

## Slide 3: Motivation : Network and Policy in J-PARC
Acc. Control LAN
Office LAN
DMZ
Acc. Equipment (EPICS IOCs)
⯰ Forbidden ⯰
⯲Allowed (routing)
⯲Allowed (NAT)
The Internet
I’d like to monitor our Acc. from my office
I wish I could use the same app. as control LAN

## Slide 4: Idea : 2-Tier Gateway
Requirements from J-PARC IT section: Operation of any devices in the control LAN shall be prohibited from the office LAN
Acc. Control LAN
Office LAN
DMZ
Acc. Equipment (EPICS IOCs)
⯰ Forbidden ⯰
CA
Gateway #1
CA
Gateway #2
⯲Allowed (routing)
⯲Allowed (NAT)

## Slide 5: Implementation
CA w/ TCP-only mode
Both gateways are configured to be read-only
Access control by iptables on both gateway
Acc. Control
LAN
Office LAN
DMZ
Acc. Equipment
(EPICS IOCs)
CA
Gateway #2
CA
Gateway #1
(NAT)

## Slide 6: Hardware
PiNON sabataro®
  Celeron J1900 (4 cores @ 2.4GHz) / 8GB
  SL6 + EPICS base R3.15.5 + Gateway R2.1.0

## Slide 7: Summary
An one-way gateway system was constructed, which allows Channel Access thru two-layer firewall
It has been in operation since Apr 2018