## Slide 1: What is going on with motion control at Diamond Motion Control Workshop
Ronaldo Mercado
Controls Group
Diamond

## Slide 2: Controllers in use
Mostly Delta Tau Geo Brick
  A few generations, VME based on some beamlines
  Packaged in a different enclosure for Diamond’s electrical standard
  Except for insertion devices
Legacy, in the accelerator
  OMS maxV
  OMS VME58

## Slide 3: Drivers in use
Mostly tpmac model 2
Also tpmac model 3
oms non-asyn
oms asyn (by Nick Rees/Austen Rose)
pmac driver – support for power pmac
  Needed for the mapping applications

## Slide 4: Motor record notes (1)
MRES – demands in integers
vs modern controller

## Slide 5: Motor record notes (2)
Logic in the motor record
  The motor record does not transmit demands if going beyond the limits
Biggest problem:
“New Target Monitoring” NTM
  Made worse when using jittery motors
  Demands from high level are not sent through
  Problematic in case of a diffractometer
  Current work-around: “Direct transfer” – demands sent to a separate record connected to the asyn port and driver, bypassing the motor record.