## Slide 1: IC@MS with EPICS Tango Bridge
EPICS Collaboration Meeting September 2022
S2Innovation (Poland, Cracow)
Presentation: Mateusz Nabywaniec

## Slide 2: EPICS vs Tango
Tango Controls:
Main unit are Device Servers
Each device server can have
some attrbiutes attributes
Popular support for thousends of devices
https://www.tango-controls.org/developers/dsc/
EPICS Controls:
Main unit - IOC
PV – piece of data associated with some device parameter

## Slide 3: Solution: EPICS TANGO Bridge
Tool to access Tango Classes via EPICS Channel Access
Server that provides mapping between Tango Attributes and Commands.
Implemented using pcaspy (https://pcaspy.readthedocs.io/en/latest/)
Documentation: https://epics-tango-bridge.readthedocs.io/en/latest/

## Slide 4: How to use it works? - read
To start IOC you need to provide pvdb.py file defining mapping Tango devices
epics-tango-bridge ./path/to/pvdb.py
Example Tango device
$ caget –c „tango:test/epics_tango_bridge/1:atrr:DoubleScalar” -> Return 40
Corresponding pvdb file

## Slide 5
Write eg. caput
Example Tango
Device Server
with different attributes
and commands
- manager
- Read and write threads
Pcaspy Driver
Reading and writing more detaied
Read e.g. caget
value
value
value
value

## Slide 6: Main advantages
Read and write suport using Channel Access
Support for scalar attributes (normal and polled)
Support for commands
Support for spectrum (one dimensional array), and images (two dimensional array)
Mapping alarms betwen Tango and EPICS

## Slide 7: IC@MS

## Slide 8: What is IC@MS?
Web application to manage alarms
Integrated
Cloud-ready
Alarm Management System
Aim: increase effectivity during working with unexpected situations
C@MS
IC@MS based on PANIC – Alarm System developed in ALBA Synchotron (Barcelona)
https://panic-training-materials.readthedocs.io/

## Slide 9: IC@MS is focused on daily operation
C@MS
Personel confirms start of solving the problem
Detection of unusual situation
Problem solved
No active (NORM)
Activated
(NACK)
Confirmed
(ACK)
Solved
(RTN)

## Slide 10: How does it work?
Input data (Tango/ EPICS)
Temperature sensor
IC@MS
Operated at IC@MS
Notification formula (PyAlarm)
If temperature is higher than
50  trigger alarm.
Processed by PANIC/PyAlarm
notifications
logging
Web API
MongoDB Cache
Speed up PANIC
Advanced logging
Backend

## Slide 11: Why IC@MS?
Better user interface for everyday use.
Access from anywhere through web browser.
No need to install on the client’s computer.
Web API.
Multiple access roles.
Integration with Active Directory, AD.
SMS, mobile or mail notifications.
Effective – tested with thousands of alarms.

## Slide 12: Main features
Alarms list
Modification of existing alarms
Multiple sources of data: EPICS PV, HTTP, MQTT, …
New alarm definition
Alarms history browser
Multiple searching and filtering options
Documented web API (Swagger)
C@MS

## Slide 13: Time for DEMO 

## Slide 14: Scenario
Composer DS
EPICS Tango Bridge
PyAlarm DS

## Slide 15: Log in

## Slide 16: Alarms list – all in one place

## Slide 17: Modification of existing alarm

## Slide 18: Monitoring values of PVs using EPICS Tango Bridge

## Slide 19: EPICS PV as a new data source

## Slide 20: Browsing history of one alarm…
Feature – remember all values for aggregating alarms

## Slide 21: … and history of all alarms

## Slide 22: Thank you!
https://s2innovation.com
contact@s2innovation.com
+48 795 794 667, +48 795 794 004