## Slide 1: PyDevice – New Features and Updates
Klemen Vodopivec
vodopiveck@ornl.gov
September 22th, 2022

## Slide 2: PyDevice Brief Introduction
# Keep running values in Python array
record(ao, "BeamPower:Cache") {
field(DTYP, "pydev")
field(DOL, "BeamPower CP")
field(OUT, "@beampower.append(VAL)")
field(FLNK, "BeamPower:Avg")
}
# Using Python built-in functions for average calc
record(ai, "BeamPower:Avg") {
field(DTYP, "pydev")
field(INP, "@sum(beampower)/len(beampower)")
field(FLNK, "BeamPower:Std")
}
# numpy one-liner for standard deviation
record(ai, "BeamPower:Std") {
field(DTYP, "pydev")
field(INP, "@numpy.std(beampower)")
}
Extend EPICS records functionality with the power of Python
Integrates into existing IOCs
  Leverage IOC core functionality
  Coexist with EPICS extensions
  Quick and robust adoption
Broad compatibility
  Python2 & Python3
  EPICS 3.14.12.x – EPICS 7.0.x
http://github.com/klemenv/PyDevice

## Slide 3
Python excels at processing arrays
Support for most element types
  (U)CHAR, (U)SHORT, (U)LONG, FLOAT, DOUBLE, STRING
Input and output arrays may differ in size but not type
Supporting More EPICS Base Records
waveform
EPICS 3.15 and later
String size inherited from EPICS base, default 65,535
Useful for file paths, URLs
lsi / lso

## Slide 4
Similar to aSub record but invokes Python for processing inputs
Passing multiple parameters to Python expressions:
  Functions
  Formulas
Selectable input and output field types and size
Python code unaware of record semantics
New pycalcRecord
record(pycalc, "Quadratic:X") {
field(INPA, "Quadratic:X:LowLimit")
field(INPB, "Quadratic:X:HighLimit")
field(CALC, "list(np.linspace(A,B,1000))")
field(MEVL, "1000")
}
record(pycalc, "Quadratic:Y") {
field(INPA, "2")
field(INPB, "-5.0")
field(INPC, "7")
field(INPH, "Quadratic:X CP")
field(CALC, "list(A*np.array(H)**2+B*np.array(A)+C)")
field(MEVL, "1000")
}
Generating 1000 samples of quadratic function

## Slide 5
Escaping Fields is Now Optional
pydev("VAL=834.2")
record(ao, "Number:Print") {
field(DTYP, "pydev")
field(VAL, "419.5")
field(OUT, "@print(%VAL%)")
}
pydev("VAL=834.2")
record(ao, "Number:Print") {
field(DTYP, "pydev")
field(VAL, "419.5")
field(OUT, "@print(VAL)")
}
Before
After
Does it print 834.2 or 419.5?
record(ao, "Equal") {
field(DTYP, "pydev")
field(VAL, "419.5")
field(OUT, "@VAL=%VAL%")
}
More pitfalls
record(ao, "Macros") {
field(DTYP, "pydev")
field(OUT, "@print($(HIGH))")
}
Escape with % whenever possible!

## Slide 6
Allow processing multiple records concurrently
  as long as CPython code releases GIL,
  or runs out of allocated time slice*
  Generally, it runs pretty well!
Configurable number of worker threads
  epicsEnvSet("PYDEV_NUM_THREADS","10")
  All worker threads busy => requests queued in FIFO
Concurrent Record Processing
David Beazley – Understanding GIL
* Python 2: sys.setcheckinterval()
Python 3: sys.setswitchinterval()
Queue
Records

## Slide 7
IOC folder
PyDevice folder
Add to IOC configure/RELEASE
PYDEVICE=/path/to/PyDevice
include $(PYDEVICE)/configure/CONFIG.PyDevice
ioc_DBD += pydev.dbd
ioc_LIB += pydev
Add to IOC iocApp/src/Makefile
Simpler Build Mechanism
Choose Python version in configure/CONFIG_SITE
PYTHON_CONFIG=python39-config

## Slide 8: Example – Fast Fourier Transform with scipy
record(waveform, ”Signal:X") {
field(DTYP, "pydev")
field(NELM, "600")
field(FTVL, "DOUBLE")
field(INP, "@np.linspace(0, 0.75, 600, endpoint=False)")
}
record(pycalc, ”Signal:Y") {
field(INPA, ”Signal:X")
field(CALC, "np.sin(100*np.pi*A)+.5*np.sin(160*np.pi*A)")
field(MEVL, "600")
field(FTVL, ”DOUBLE")
}
record(waveform, ”Signal:FFT:X") {
field(DTYP, "pydev")
field(NELM, "300")
field(FTVL, "DOUBLE")
field(INP, "@scipy.fft.fftfreq(600, 0.00125)[:600//2]")
}
record(pycalc, "Signal:FFT:Y") {
field(INPA, "Signal:Y")
field(MEA, "600")
field(CALC, "2.0/600 * np.abs(scipy.fft.fft(A)[0:600//2]")
field(MEVL, "300")
field(FTVL, ”DOUBLE")
}
FFT

## Slide 9: Example – Steerable Optics Evaluation
Builds a series of motor positions and submits the scan to ScanServer
Monitor motor related parameters for later analysis
Save parameters values to CSV file

## Slide 10: Example – Managing Remote Experiments
Controls Linux PAM authentication and disconnects active sessions when being disabled
Currently active users by executing remote SSH commands
Interface with experiment’s proposal database
Proposal ID is an instrument wide PV controlling data acquisition, sample activation calculation etc.

## Slide 11: Time for Questions? (and answers)