## Slide 1: Annual Meeting
JRA10:Cryogenic Polarized Target Application Hartmut Dutz Physikalisches Institut, Universität Bonn

## Slide 2: Plan of the presentation
Progress achieved by the WP during the last year
  Recommissioning of the Dubna-Mainz dilution refrigerator (CryPTA:ScM, CryPTA:APT)
  Design of a combined holding coil system (CryPTA:ScM)
  Improved light efficiency read out (CryPTA:APT)
Important highlights of the performed work
Plans and remaining tasks until the end of the project (31 July 2024)
  Tilted coil configuration for frozen spin mode (CryPTA:ScM)
Conclusions

## Slide 3: JRA10:CryPTA
Cooperation of four partners
Organization legal name | Short name | Activity leaders
Ruder Boskovic Institute Zagreb | RBI | M. Korolija
Ruhr-Universität Bochum | RUB | G. Reicherz
Rheinische Friedrich-Wilhelms-Universität Bonn | UBO | H. Dutz
Johannes Gutenberg Universität Mainz | UMainz | A. Thomas
M. Biroth, H. Dutz, St. Goertz, S. Heinz, A. Klotzbücher, M. Korolija,
O. Kostikov, V. Lagerquist, G. Reicherz, A. Thomas
 Develop new polarized target technologies for future polarization experiments

## Slide 4: JRA10:CryPTA
PT-Ingrediencies and responsibilities
Target material preparation and research
Magnet development
Slow Control
Cryogenic infrastructure
NMR
Target material preparation and research
Microwaves
Active target material preparation and research
Low temperature
Refrigerator design and operation

## Slide 5: Recommissioning of the Dubna-Mainz dilution refrigerator
Collaborative target group: Bonn/Dubna/Mainz/Bochum (2015 – 2021)
‘Mainz/Dubna frozen spin target’ + internal ‘holding’ coil(s)
Polarization history plot
p/d-run 2018
Operation of the polarized target (cold cryostat) at Crystal Barrel @ ELSA (CBELSA)
2017 (long. polarization) ~ 800h b.o.t.
pp = 63 %, (butanol, TEMPO), t ~ 1300h
2018 (transv. polarization) ~ 1000h b.o.t.
pp = 87 %, t ~ 500 h
2018 (transv. polarization) ~ 800h b.o.t.
pd = 76 %, t ~ 700 h
2019 (transv. polarization) ~ 500h b.o.t.
pp = 84 %, t ~ 800 h
2021 (transv. polarization) ~ 440h b.o.t.
pp = 78 %, t ~ 700 h
2021 (transv. polarization) ~ 500h b.o.t.
pd = 75 %, t ~ 500 h
Five years of successful operation on beam in Bonn and 8 years before at A2@MAMI
Polarization history plot
June 2021
Polarization history plot
November 2021,
d-butanol
CBELSA/TAPS horizontal frozen spin target
with internal transverse or longitudinal holding magnet
Dubna/Mainz dilution refrigerator is the
working horse for the PT projects

## Slide 6: Recommissioning of the Dubna-Mainz dilution refrigerator
Collaborative target group: Bonn/Dubna/Mainz/Bochum (2015 – 2021)
‘Mainz/Dubna frozen spin target’ + internal ‘holding’ coil(s)
Polarization history plot
p/d-run 2018
Polarization history plot
June 2021
Polarization history plot
November 2021,
d-butanol
Dubna/Mainz dilution refrigerator is the
working horse for the PT projects
CBELSA/TAPS horizontal frozen spin target
with internal transverse or longitudinal holding magnet
Operation of the polarized target (cold cryostat) at Crystal Barrel @ ELSA (CBELSA)
2017 (long. polarization) ~ 800h b.o.t.
pp = 63 %, (butanol, TEMPO), t ~ 1300h
2018 (transv. polarization) ~ 1000h b.o.t.
pp = 87 %, t ~ 500 h
2018 (transv. polarization) ~ 800h b.o.t.
pd = 76 %, t ~ 700 h
2019 (transv. polarization) ~ 500h b.o.t.
pp = 84 %, t ~ 800 h
2021 (transv. polarization) ~ 440h b.o.t.
pp = 78 %, t ~ 700 h
2021 (transv. polarization) ~ 500h b.o.t.
pd = 75 %, t ~ 500 h
Five years of successful operation on beam in Bonn and 8 years before at A2@MAMI
All activities stopped in March 2022, because of the Russian invasion of the Ukraine
No refrigerator for the CryPTA-project for CryPTA:ScM and CryPTA:APT
No working refrigerator for the experiment
No reliable planning was (is) possible
Since no one (all) of us has operated the refrigerator in the past
Nevertheless we decided to cool down the system

## Slide 7: Recommissioning of the Dubna-Mainz dilution refrigerator
After one year of learning to cool down to < 28mK and testing, we could reestablish:
Reliable cool down procedure
Stable and reproduceable parameters for DNP
Good polarization for Butanol (76% in 4h)
Sufficient low temperatures (< 28 mK) for long relaxation times in frozen spin mode (t ~ 2000h)
Next:
Being back in beam beginning next year
Combined internal coil project is now a high-priority work in progress
 Important highlight of the performed work in 2023 

## Slide 8: Design of a combined holding coil system (CryPTA:ScM)
New experimental approach in double polarized photo production experiments:
Longitudinal polarized electrons on a diamond radiator [F. Afzal et al., submitted to PRL. 2023]
Lets rotate the target polarization and measure them all

## Slide 9: Design of a combined holding coil system (CryPTA:ScM)
Combined longitudinal and transverse field
for a variable polarization direction in yz-plane or xz-plane
 Solenoid + ‘race-track’
Detailed studies and simulations are underway  V. Lagerquist
Initial approach:
combine solenoid + race track
minimize radiation length
minimize thickness of the package
reduced field strength
concept only works as holding field in frozen spin mode
0.4 T < BH to get reasonable relaxation times

## Slide 10: Design of a combined holding coil system (CryPTA:ScM)
Combined longitudinal and transverse field
for a variable polarization direction in yz-plane or xz-plane
 Solenoid + ‘race-track’
Design / simulation boundary condition for the compount:
field solenoid / race track B > 0.4 T
Inom £ 40A
D = 45 mm / length = 150 mm
Almost homogeneous mass distribution
Final goal:
Optimize the compound for minimum thickness
with an available wire for the race-track (first) and solenoid (easy task)
Maximum field, minimum thickness:
Cosine theta shape
Equal No. of windings per layer
Straight section angle ~ 24°
Victoria Lagerquist, UBO
PostDoc STRONG2020, WP24
Notes: Mantrel

## Slide 11: Design of a combined holding coil system (CryPTA:ScM)
Combined longitudinal and transverse field
for a variable polarization direction in yz-plane or xz-plane
 Solenoid + ‘race-track’
Maximum field, minimum thickness:
Cosine theta shape
Equal No. of windings per layer
Straight section angle ~ 24°
Price to pay:
Field variation in target area ~ 5%
Beam spot ~ 2%
Corresponding t variation has to be measured
Field variation in yz-, xz-plane in target area
Field variation on target surface
Victoria Lagerquist, UBO

## Slide 12: Design of a combined holding coil system (CryPTA:ScM)
Combined longitudinal and transverse field
for a variable polarization direction in yz-plane or xz-plane
 Solenoid + ‘race-track’
2 compound scenarios possible:
(wire: 0.203/0.229 mm, Cu-support: 0.3 mm + separating foils)
‘high current’ I = 40 A  B = 0.4 T
Solenoid: 2 layers, N = 1280  thickness: 0.45 mm
Race-track: 3 layers, N = 414  thickness: 0.69 mm
Compound thickness: ~ 1.6 mm
‘low current’ I = 35 A  B = 0.5 T
Solenoid: 3 layers, N = 1920  thickness: 0.63 mm
Race-track: 4 layers, N = 552  thickness: 0.92 mm
Compound thickness: ~ 2.2 mm
Next steps:
(Plans and remaining tasks until the end of the project (31 July 2024))
Measure more t(B)
Identify best scenario and winding procedure
Wind race-track and solenoid
Test the combined coil system
Or picking up an ‘old’ challenging idea: double helix configuration or canted cosine theta (cct) magnet
Victoria Lagerquist, UBO
Already strong interest in the technology by a SME for 3D-magnets

## Slide 13: Improved light efficiency read out (CryPTA:APT)
M. Biroth, A.Thomas
Students (2023/2024):
BSc A.Klotzbücher, BSc J.V.Patel
Focus on an improved light efficiency and readout under warm conditions:
Coupling of the scintillating fibers to the material and SiPMs
Geometry of the apparatus
Tests with 90Sr-source
Tests with photon beam planned
Light-tight test station with 90Sr-Source and 3d-positioning
Coincidence technique
to improve signal to noise ratio.
New Apparatus:

## Slide 14: Improved light efficiency read out (CryPTA:APT)
Spectra for different geometrical configurations to specify the optimum with respect to the small dimensions (target 2cm x 2cm diameter) and the way of the fibers to the SiPMs in the cryostat.
Readout via optical fiber
Next steps:
(Plans and remaining tasks until the end of the project (31 July 2024))
Repeat same measurements at low temperatures
Design of a propriate insert and fiber feed throught for the dilution refrigerator

## Slide 15: Tilted coil configuration for frozen spin mode (CryPTA:ScM)
15
C. L. Goodzeit et al., IEEE TRANSACTIONS ON APPLIED SUPERCONDUCTIVITY, VOL. 13, NO. 2, JUNE 2003
independent tilted coil (solenoid N) wound with a to z-axis
Tilted coil configuration (TCC) for the new dilution refrigerator for a variable polarization direction in plane
‘canted cosine theta (CCT) magnet’
For a = 45°, symmetric case, 2 independent coils
In between: any field direction possible

## Slide 16: Tilted coil configuration for frozen spin mode (CryPTA:ScM)
homogeneous long. or transv. magnetic field
adjustable field direction
homogeneous mass distribution around the target
R.B. Meinke et al.: SUPERCONDUCTING DOUBLE-HELIX ACCELERATOR MAGNETS,
IEEE TRANSACTIONS ON APPLIED SUPERCONDUCTIVITY, VOL. 13, NO. 2, JUNE 2003
TCC needs to be longer than a standard solenoid
TCC needs more windings/layers or current
For a required B in a polarized target:
TCC Perfect solution for polarized target experiments:
The real challenge:
Winding a 250 µm wire to a tilted coil
Our next task:
Full simulation needed (B, I, N, nL, s.c.)
Wind (etching) a demonstrator coil (one layer)
Coupled TCC
uncoupled / independent TCC
Tilted coil configuration (TCC) for the new dilution refrigerator for a variable polarization direction in plane
‘canted cosine theta (CCT) magnet’

## Slide 17: Conclusions
Despite the unfavorable circumstances in the last 3 years
 The complete target set-up is again available for experiments at ELSA, MAMI and the CryPTA project
CryPTA:ScM  the combined holding magnet for the dilution refrigerator and the near future data taking campaign is in progress.
CryPTA:APT  detailed design concepts for low temperature polarized active targets are defined.  the preparation of an improved target insert with optical fiber readout is on the way .
The extension gives us the opportunity to complete the project