## Slide 1: EP-DT-EO Detector Design Optimisation Tools
Diego Alvarez F., Mar Capeans, Andrea Catinaccio, Joao C. Batista L.
CERN EP-DT-EO
CERN, March 2016

## Slide 2: EP-DT Group
The mandate of the EP-DT group:
development, construction, operation and maintenance of particle detectors for the experiments at CERN
services and infrastructure for experiments and detector R&D
Services
For experiments:
Gas systems
Detector cooling systems
Instrumentation, controls, DAQ
For Detector R&D:
Thin film & glass Lab
Silicon facility
Wire-bonding & QART Lab
Micro-Pattern Technologies
Irradiation facilities
Specialized labs (optics, gluing…)
Scintillator production
Engineering office
R&D Projects
Rad-tolerant silicon detectors (RD-50)
Gaseous detectors (RD-51)
Micro-systems engineering
Joint Projects
M&O and Upgrades of the LHC experiments
AEgIS, CAST, CLOUD, NA62
R&D for Linear Collider Detectors

## Slide 3
Projects
Services
EP-DT Group

## Slide 4: Engineering Office (EO) Section
Mandate
To provide design & engineering expertise for the group’s projects
4
11 Staff members
1 Fellows
1 Tech Students
Staff and fellows profile:
8 engineers
4 designers
Averaging in between 11 and 20 engineers and designers per year.

## Slide 5: DT & EO in LHC Projects
Example CMS TOB, Tracker Outer Barrel

## Slide 6: DT & EO in LHC Projects
Example ATLAS TRT and full Inner Detector,

## Slide 7: DT in LHC Upgrades
LHCb
Up to LS2
Velo (mechanics)
ALICE
Up to LS2
LS3
ATLAS
Up to LS2
NSW Module0
UT (integration)
Integration aspects
Pixel (integration)
TK (modules, engineering
CMS
Up to LS2
Integration aspects
ALICE TPC (GEM prod.)
LS3
ITK Pixel
CO2 cooling
CO2 for Pixel
CO2 cooling
GE1/1 (GEM prod.)
RICH/TORCH
ATLAS AFP (controls)
SciFi (detector)
ITS
CO2 cooling
Detector Upgrades: EP-DT partners with CERN teams in the experiments (WP agreements)
On top, continuous M&O responsibility for magnet controls & safety, all gas systems, cooling coordination and since LS1 CO2 detector cooling M&O

## Slide 8: Section EP-DT-EO Competencies & Infrastructure
EO covers a wide range of disciplines in mechanical engineering, construction, and numerical simulation fields.
The core competencies of the section comprise:
  Design studies, 3D modelling and drafting
  Integration studies of detectors
  Simulation for structural and thermal analyses, composites, fluid-dynamics, multi-physics and structural verifications according to relevant standards and codes
The section covers as well activities of:
  Composite Material prototyping and manufacturing
  Project Engineering, manufacturing support and follow-up, relations with external suppliers, installation and first commissioning.
A range of tools available for CAD, Finite Element Analysis and analytical tools, rapid prototyping techniques (3D Printing)

## Slide 9: EP-DT-EO Infrastructure
Two open spaces and offices able to host 26 engineers and designers
Composite lab equipped with autoclave: provide capability to produce prototypes and final quality parts !
Testing equipment for R&D prototype characterisation
Additive Manufacturing 3D print (ABS)
Small test benches and equipment for project R&D (upgrades Atlas and CMS, Micromegas, LCD, etc.)

## Slide 10: Main Engineering Tools (EO)
ANSYS Classic and APDL programming
ANSYS Workbench
Scia Engineer Structures
Composites EsaComp
EXAGON assemblies
Analytical Mathcad library
Vibration SRS software

## Slide 11: Main Design Tools (EO)
Catalsyt for 3D printer Dimension Elite
CATIA V5 - 3D modeling and Smarteam
Autodesk Inventor - 3D modeling
Geomagic – laser scan reconstruction

## Slide 12: Integration design Tools (EO)
Leica HDS6200:
Ultra-high speed
scanning with > 1 million points/second. Reduces time needed for scanning
Romer Robotic measurement arm

## Slide 13: Web - EDMS and \dfs EO libraries
https://edms.cern.ch/nav/P:CERN-0000089058:V0/P:CERN-0000089058:V0/TAB3
Mathcad section library
ANSYS APDL scripts library
https://ph-dep-dt-eo.web.cern.ch/

## Slide 14: EP-DT-EO Current Projects
More than 30 projects / activities (non exhaustive list):
Atlas Upgrade ITk Pixel, Pixel structures R&D, Slim project nIDEP design (closing of ID) Micromegas design, FEA CMS : Upgrade TOB, TIB Upgrade High granularity Si Calorimeter Alice ITS upgrade ITS, TPC, installation LS2 TC, integration LHCb upgrade (SciFi tracker), UT detector TC integration, infrastructure design and calculations | NA62 Straw detector GTK integration and micro-cooling TC integration Neutrino LBNF: Structural engineering and design review 4.6 FTE’s period end March end May. Still ongoing. LCD: CLICdp Vertex, Integration studies HCAL, ILC collaboration AIDA FCAL Support to the Cooling Project (EP-DT-FS)

## Slide 15: EP-DT-EO Current Projects
More than 30 projects / activities (non exhaustive list):
Support (other projects) Micro-fabrication and micro-scint: Engineering support (for GTK, LHCb Velo, Alice), XY table FEA support: CMS HCAL, fracture mechanics, CMS tracker (student FEA), Alice ITS laser bonding, etc. Micro Cooling CFD Latch opto-links with ESE, design, creep studies X-ray generator Cubic GEM detector X-Ray bench x detector testing 3D printing, Catia user support | Composite lab Tools and infrastructures Prototype activities Thermal Testing Setup Engineering database Structure implementation Populating DB R&D Composite materials Thermal management materials Silicon fracture mechanics FEA methods: creep, CZM, fracture mechanics, XFEM, Ansys-Catia bi-directional associative connection, FEA model integration 3D printing technologies (Christophe)

## Slide 16: Some FEA examples for the ID BSS

## Slide 17
Virtual positioning and probing (envelope of the front IDEC-A re-constructed)
A. Catinaccio - CERN
17
Integration tools – Robotic arm

## Slide 18
A. Catinaccio - CERN
18
Integration tools – Laser scanner
Photo
Laser scan
Laser scan
Notes: 18

## Slide 19: Neutrino LBNF Detector: LAr Cryostats
4 x Steel Cryostats containing approximately 17kT of LAr
(http://www.gtt.fr)
Internal Dimensions:
L = 62m
W = 15.1m
H = 14m
Long Wall ~114MN
(11.6kT)
Short Wall ~27.7MN
(2.8kT)
ANSYS WB Beam and beam-shell models of ¼ cryostat:
  Offset beams to simulate the main frame and the grid
  Shells to represent the warm vessel (10mm thick)
  Joint (MPC184) to model imperfect connections
Notes: TCP= Time Projection Chamber
SURF: Sanford Underground Research Facility
DUNE: Deep Underground Neutrino Experiment
The DUNE collaboration will develop detectors for both sites:
A fine-grained near neutrino detector to be installed 600 m downstream of the Fermilab beamline.
A 40,000 metric ton cryogenic liquid argon detector deployed deep underground at Sanford Lab, located 800 miles (1,300 km) downstream in South Dakota.
Examples of the loads exerted by the LAr on the various walls:
Long Vertical Wall: approx. 114MN (equivalent to 11.6kT).
Short Vertical Wall: approx. 27.7MN (equivalent to 2.8kT).

## Slide 20: ANSYS WB: LBNF Cryostat Connections
Shell-to-Solid sub-modelling approach for structural connections:
  Bolts & Welds compliant with ASME Div2
Global Shell Model
Bottom Connection
Top Connection
Splice Connection

## Slide 21: SCIA software – FEA and EC3 compliance
Vertical beams – compliance with Eurocodes
Axial loads
Moments

## Slide 22: EC3 Mathacad – analytical calculations

## Slide 23: Atlas Tracker Upgrade phase II
The ITk global
engineering effort
Integrated model and envelopes
Overall ITk support structure
Pixel global support
Barrel strips global support
Endcap strips global support
Thermal enclosure design
Surface assembly and installation
Access scenarios
Failure management
Material for Simulation
Positioning Requirements
Common standards
Internal services
PP1 and TE feed-troughs
CATIA V5 model of the integrated Atlas ITk

## Slide 24: ANSYS ACP: CFRP Cylindrical Iso-grid
Feasibility study for ATLAS ITK Outer Cylinder
Edge-wise rosette to define fibre direction in the hoop, helicoidal reinforcements

## Slide 25: ANSYS WB & ACP: Global ATLAS ITK Model
Global, integrated FEA model to assess:
  Interaction between different sub-detectors for different design configurations
  Influence of support conditions during service life (e.g. transport, insertion, final position)

## Slide 26: ANSYS WB & ACP: ATLAS ITK CFRP Truss
ATLAS Pixel Barrel: Design and optimisation of CFRP truss (filament winding)
g
Angular section
Cross-member
Corner longitudinal reinforcement

## Slide 27: Fracture Mechanics Prediction Tool for ScSi
Development of prediction methodology for ScSi (experimental + numerical)
  Fracture testing of ScSi (SEVNB Test samples)
  J-integral approach in ANSYS
Validated with standardised pressure test samples (single channel)

## Slide 28: Alice Si micro-channel CFD simulations – manifold optimization (ANSYS CFX)

## Slide 29: Other examples of projects
ATLAS Micromegas
ALICE upgrade (ITS)
CMS Tracker upgrade
NA62 design and construction
ALICE Inner Tracker Silicon Upgrade
Mechanics and Cooling New design and prototype
Carbon Fibre reinforced structure
with embedded polyimide cooling pipes (OD=1mm)
Outer layer stave 1500mm length, 80 gram weight

## Slide 30: Material

## Slide 31: Skills and Capabilities (EO)
3D modeling and drafting
Advanced FEA: structural mechanics, thermal, fluid, coupled-analyses
  Static structural
  Modal analysis, pre-stressed modal (FEA & Experimental)
  Harmonic analysis (steady state response)
  Transient dynamic (implicit transient response)
  Vibrations & shocks: spectrum analysis, random vibration analysis, SRS.
  Buckling analysis: linear (eigen-buckling) and non-linear methods
  Non-linearities: changing status (ie contacts), plasticity,
  creep, large strain, stress stiffening …)
  Fracture mechanics
  Composite analysis (micromechanics, lamination properties, failure criteria …)
  APDL routines
Knowledge of materials metals, polymers, composites
Standards and calculations for: metallic frames, pressure equipment, lifting equipment …
Connections: bolted, welded, bonded
Analytical methods and Mathcad library
Testing, metrology integration tools (Laser Scanner, Romer Arm)
Production follow up, QA

## Slide 32
UNIT1
BENDOTTI Jerome
DIXON Neil
DUMPS Raphael
GONGALVES Antonio
KOTTELAT Luc-Joseph
KRISTIC Robert
LAHU Gregory
LOOS Robert
PIEDIGROSSI Didier
VERGAIN Maurice
VOGEL A (Fell)
UNIT2
ANSTETT Didier Henri
BOUVIER Philippe Jacques
IJZERMANS Pieter
LESENECHAL Yannick
VAN BEELEN Jacob Bastiaan
Detector Construction & Operations
(DT-CO)
Antti ONNELA
Deputy: F.PEREZ
EP-DT Detector Technologies
Group leader: Mar CAPEANS
Deputies: Andrea CATINACCIO & Michael MOLL
Secretariat: Veronique WEDLAKE
Safety Linkperson: Isabelle MARDIROSSIAN
Design room
BAULT Christophe (PL)
DEGRANGE Jordan
JAMET Olivier
LENOIR Philippe
Design and Analysis
ALVAREZ Diego
BATISTA Joao Carlos
DUARTE Fernando
GARGIULO Corrado
HATCH Mark
WERTELAERS Piet
MARTENSSON O (Tech)
Composite Lab
BOYER F (TRN VIA)
Engineering Office
(DT-EO)
Andrea CATINACCIO
Silicon det R&D
MAPELLI Alessandro
HONMA Alan
MCGILL Ian
MANOLESCU Florentina
BONNAUD J (Fell)
GALLRAPP C (Fell)
BRONUZZI I (Doct)
CURRAS E (Doct)
MATEU I (TRN FTEC)
NEUGEBAUER H (Doct)
OTERO Sofia (Doct)
PITAES C (TRN Pt)
Gas Det R&D
ROPELEWSKI Leszek (PL)
OLIVERI Eraldo
RESNATI F (Fell)
THUINER P (Doct)
Irradiation Facilities
RAVOTTI Federico (PL)
GLASER Maurice
FORTIN Richard G
GORINE G (Doct)
GOTKSE B (Doct)
Detector Development
(DT-DD)
Petra RIEDLER
GUIDA Roberto (Gas PL)
PETAGNA (Cooling PL)
CARRIE Patrick
DAGUIN Jerome
D'AURIA Andrea
DE MENEZES Louis-Philippe
MERLET Frederic
NOEL Jerome
PAVIS Steven
VERLAAT Bart
WASEM Albin
ZWALINSKI Lukasz
GIAKOUMI K (Fell EU)
MANDELLI B (Fell)
MOUSSY Y (Fell)
OSTREGA M (Fell)
PIMENTEL T (TRN Pt)
HELLENSCHMIDT A (Doct)
ROMAGNOLI G (Doct)
SPADAVECHIA N (Tech)
Fluidic Systems
(DT-FS)
Paola TROPEA
Engineering Facilities
(DT-EF)
Hans DANIELSSON
Deputy: PA.GIUDICI
Thin Film & Glass
SCHNEIDER Thomas (PL)
DAVID Claude
VAN STENIS Miranda
Micro-Pattern Tech
DE OLIVEIRA Rui (PL)
FERRY Serge
GRIS Alexandra
PIZZIRUSSO Olivier
RANCHIN David
RODRIGUES Alexis
TEIXEIRA Antonio
CHAMLEY C (Tech)
Machine Shops
BODE Alain
BRENDLEN Romain
BRUNEL Bernard
CANTIN Bernard
GARNIER Francois
Magnets support
BERGSMA Felix (PL)
DAVENPORT Martyn
GYS Thierry
HAHN Ferdinand
HAIDER Stefan
JORAM Christian
KLEMPT Wolfgang
MARTINENGO Paolo
SROKA S (Fell)
KOSTOGLOU S (Tech)
Technology & Physics
(DT-TP)
Burkhard SCHMIDT
PONS Xavier
BLANC Pascal
BOURGEOIS Nicolas
DERONT Laurent
MAIRE Gilles
RAVAT Sylvain
RIGAUT Y.A. (PA)
Detector Interface
(DT-DI)
Giovanna LEHMANN
Projects
Services
Contact Persons for Experiments and Projects
FSU PH40
FSU PH02

## Slide 33: Laser scan of ID services
Notes: 33