## Slide 1: Superconducting qubits for sensing applications
Danilo Labranca

## Slide 2
Qubits are two state quantum systems
They are the quantum mechanical analogous of the bit
More information is stored in a qubit
What is a qubit?
Classical bit
Quantum bit

## Slide 3
Built with Josephson Junctions or STJ (Superconducting Tunnel Junctions)
Cooper pairs in the SC can go through the insulator barrier thanks to quantum tunneling. The junction behaves as a non-linear inductor.
Superconducting Qubits
Cooper pairs tunneling
Junction critical current

## Slide 4
Transmon qubits are essentially LC oscillators with Josephson Junctions replacing the inductance.
It is a weakly anharmonic oscillator
It is the evolution of the Cooper pair Box with a ratio EJ / EC >> 1
Frequencies are usually between 4 GHz and 10 GHz
Transmon qubit

## Slide 5
Transmon coupled to a resonator
Dispersive readout  ωR ≠ ωQ
Resonator frequency depends on the qubit state
Frequencies are usually between 4 GHz and 10 GHz
Qubit readout
Resonator mode frequency is qubit-state dependent

## Slide 6
2 qubit chip fabricated @ NIST
One tunable and one fixed frequency qubit on the same line with two readout resonators
The tunable resonator qubit is controllable with a drive line
Qubit chip design for Qub-IT

## Slide 7
Superconducting Electronics Group
A. Sirois, M. Castellanos, D. Olaya, J. Bieseker, P. Hopkins, S. Benz

## Slide 8
Qubit measurements @NIST
Cavity Spectroscopy
The first measurement to characterize a superconducting qubit is to find the resonator frequency
The high/low power measurement (or punch-out) show the bare (high-power) and “dressed” frequencies of the resonator
Qubit
Resonator
VNA

## Slide 9
Qubit measurements @NIST
Qubit Spectroscopy
We can now fix the readout frequency at and scan the qubit control tone frequency to find
Readout tone transmission plotted as a function of the control frequency
Both phase and amplitude bring information on the qubit state, but at the phase response is greater
Qubit
Resonator
VNA

## Slide 10
Qubit measurements @NIST
Qubit AC Stark Shift
Scanning the power of the VNA tone we can populate the cavity with more and more photons
By doing qubit spectroscopy at each power, we can observe the qubit Stark shift that depends on the number of photons in the cavity
Qubit
Resonator
VNA

## Slide 11
Qubit measurements @NIST
Chevron Plot
Chevron plot is built by scanning and
It is equivalent to Rabi flopping at detuned frequency from
The oscillation dumping is dependent on the coherence times of the qubit
A better estimate of can be obtained by fitting the frequency profile of this plot  calibrate again the π-pulse

## Slide 12
Qubit measurements @NIST
Rabi Flopping
We switch to time domain measurement
We pulse both tones:
Qubit: gaussian pulse at
Cavity: square pulse at
Observation of power and time Rabi flopping by scanning the power and duration of the qubit pulse
Note: qubit gaussian pulse is digitally truncated at
@ 50ns

## Slide 13
Qubit measurements @NIST
Chevron Plot
Chevron plot is built by scanning and
It is equivalent to Rabi flopping at detuned frequency from
The oscillation dumping is dependent on the coherence times of the qubit
A better estimate of can be obtained by fitting the frequency profile of this plot  calibrate again the π-pulse

## Slide 14
Qubit measurements @NIST
T1 measurement
π-pulse followed by a cavity measurement after a time interval Δt repeated N times and averaged
Exponential decay of the excited population of the qubit

## Slide 15
Qubit measurements @NIST
T1 measurement
π-pulse followed by a cavity measurement after a time interval Δt repeated N times and averaged
Exponential decay of the excited population of the qubit

## Slide 16
Qubit measurements @NIST
T2* measurement - Ramsey
π/2-pulses separated by time interval Δt
π/2-pulse  half the amplitude of the π-pulses
We are mapping the qubit in a superposition state and monitoring the phase information lifetime
The oscillation frequency is equal to the detuning and gives the best estimate of
The exponential decay is T2* measurement

## Slide 17
Qubit measurements @NIST
T2* measurement - Ramsey
π/2-pulses separated by time interval Δt
π/2-pulse  half the amplitude of the π-pulses
We are mapping the qubit in a superposition state and monitoring the phase information lifetime
The oscillation frequency is equal to the detuning and gives the best estimate of
The exponential decay is T2* measurement

## Slide 18
Qubit measurements @NIST
T2E measurement – Spin Echo
Same as Ramsey pulse sequence with an additional π-pulses at Δt/2
This additional π-pulse has the goal to eliminate the impact of low frequency phase noise by refocusing the state
The exponential decay time is a measure closer to the actual T2 of the qubit

## Slide 19
Sensing protocol

## Slide 20
Photon in cavity - Ramsey mapping
Detection cavity
Readout cavity
R. Lescanne et al., Phys. Rev. X (2020)

## Slide 21
Photon in cavity - Ramsey mapping
No photon
1 photon
State preparation

## Slide 22
Photon in cavity - Ramsey mapping
No photon
1 photon
State preparation
Interaction time

## Slide 23
Photon in cavity - Ramsey mapping
No photon
1 photon
State preparation
Interaction time
Projection measurement

## Slide 24
Itinerant photon
Same Ramsey Mapping, but the single photon reflecting on the cavity-qubit system causes a phase flip in the qubit state

## Slide 25
Itinerant photon
Same Ramsey Mapping, but the single photon reflecting on the cavity-qubit system causes a phase flip in the qubit state

## Slide 26
Itinerant photon
Same Ramsey Mapping, but the single photon reflecting on the cavity-qubit system causes a phase flip in the qubit state

## Slide 27
Other interesting applications

## Slide 28
Transmon as a power-meter
300 μm
Transmon qubit strongly coupled to a transmission line
Applications:
            Power measurement on chip
            Tunable single microwave photon source

## Slide 29
How it works
Coherent drive along a transmission line
            Incident photon rate (𝞶) depends on the drive power
            2-level system → absorbs photons with rate Ω
            Rabi frequency → Ω
            Qubit relaxation rate → г1
Incident power at the qubit
Incident photon rate
Qubit
Transmission line
Ω

## Slide 30
Transmission measurement
Varying input power with VNA
Higher power = Higher Ω
Depth of the resonance depends on the power at the qubit

## Slide 31
Power curve

## Slide 32
Power curve

## Slide 33
Transmon as a single-photon source
Reflection
Transmon is a TLS
Only single photons can be reflected
We can build a tunable single-microwave photon source
Source coherence measurements → Hanbury-Brown-Twiss (HBT) experiment

## Slide 34
Beam-splitter
JPA 2
Reflection
Hanbury-Brown-Twiss (HBT) experiment

## Slide 35
Beam-splitter - 90° hybrid
Superconducting CPW 50/50 beam-splitter
Four 𝛌/𝟒 sections with impedances 𝟓𝟎𝛀 and 𝟓𝟎𝛀/√𝟐
Input “b” - resistor
Input “a”
Output “c”
Output “d”
-
Input modes
Output modes

## Slide 36
Beam-splitter - 90° hybrid
Superconducting CPW 50/50 beam-splitter
Four 𝛌/𝟒 sections with impedances 𝟓𝟎𝛀 and 𝟓𝟎𝛀/√𝟐
-
Input modes
Output modes

## Slide 37
Delay unit
Superconducting CPW resonator shunted by a DC-squid
Tunable resonator to introduce a tunable time delay
The edge of the resonance permits fine tuning of the time delay

## Slide 38
Delay unit
Superconducting CPW resonator shunted by a DC-squid
Tunable resonator to introduce a tunable time delay
The edge of the resonance permits fine tuning of the time delay

## Slide 39
HBT expected result
Measuring g(2)(τ) > g(2)(0) values will prove the quantum nature of the traveling state
Measured Γ1≈16.8 MHz → T1≈9.5 ns → Improve efficiency
New design with higher T1

## Slide 40
New design
Direct drive control line
Unidirectional output line
Expected T1≈500 ns
Drive line
Output line
Flux line

## Slide 41
Conferences and courses
Conferences:
APS March Meeting 2023 | March 5-10, 2023 | Las Vegas, NV
16th European Conference on Applied Superconductivity | September 3-7, 2023 | Bologna, Italy
Courses
Quantum Optics, Adam Kaufman and James Thompson | Covers quantum optical and atomic systems including topics such as: coherent and squeezed states, theory of optical coherence, atom-radiation interaction, optical Bloch equations, open quantum systems, dynamics on the Bloch sphere, resonance fluorescence, beam-splitters and interferometry, entanglement and quantum information.
IBM QGSS 2023 – Theory to Implementation

## Slide 42
Backup slides

## Slide 44
Lab frame
Qubit frame
RWA