## Slide 1: Impact of divertor X-points on axisymmetric modes in tokamaks
Franco Porcelli
Polytechnic University of Turin, Italy
In collaboration with:
A. Yolbarsop, U. of Science and Technology of China, Hefei
R. Fitzpatrick, IFS, U. of Texas at Austin
19th European Fusion Theory Conference, October 2021

## Slide 2: OUTLINE
INTRODUCTION: X-point resonance, why it matters
The math of the X-point singularity, and (perhaps) a surprising result
CONCLUSIONS and DEVELOPMENTS – A new line of research, what to expect

## Slide 3: INTRODUCTION: X-point resonance
B∙∇ξ = i(n/R)BT ξ + i BP(ψ, ϑ) Σm (m/r) ξm = 0
Resonance condition at the X-point
satisfied for n=0 and any m
because BP(ψ, ϑ)=0 on the X-point.
The toroidal field line going through the magnetic X-point is resonant to n=0 perturbations!
Schematic diagram of a divertor (single null configuration)

## Slide 4
Axisymmetric (n=0) modes in shaped toroidal plasmas are global plasma modes, normally associated with VDEs.
Because of the X-point resonance, current sheets localized along the magnetic separatrix are likely to form. This may have an important impact on plasma edge activity.
Ref.: A. Yolbarsop, F. Porcelli, R. Fitzpatrick, Nuclear Fusion Letters 2021.
Furthermore, a stable n=0 mode tends to acquire an Alfvénic oscillation frequency. As a result, a “resonant” interaction with energetic particles can lead to a new type of fast ion instability (but this is another talk, see Tommaso Barberis, this conference, Thursday afternoon, poster session).
Axisymmetric Modes and X-point resonance: Why it matters

## Slide 5: Let us review the philosophy behind passive and active feedback stabilization of vertical plasma displacements.
A heuristic model:
three parallel current wires.
Lister et al, NF 1990;
Lazarus et al, NF 1990.

## Slide 6
Three-current-wires model

## Slide 7: Cubic dispersion relation
where
; (Laval et al, PF1974)
for passive feedback stabilization
Three roots:
stable, oscillatory
unstable (requires active feedback)
Note: only two oscillatory roots for : (ideal wall limit)

## Slide 8: Comments
Only the weakly growing, zero frequency mode is considered for active feedback stabilization.

## Slide 9: Comments
Only the weakly growing, zero frequency mode is considered for active feedback stabilization.
No X-point resonance effects.

## Slide 10: Comments
Only the weakly growing, zero frequency mode is considered for active feedback stabilization.
No X-point resonance effects.
Hey! What about the weakly damped, high frequency solutions?

## Slide 11
The math of X-point singularity, and (perhaps) a surprising result.
For details, see:

## Slide 13
Equilibrium magnetic structure
Plasma occupies and regions

## Slide 14: Perturbations: The ideal-MHD constraint at the magnetic X-point rigid-shift analytic solution.

## Slide 15
Rigid-vertical-shift stream function
Elliptical coordinates
X- point coordinates
and
Stream function in elliptical coordinates:
Use flux-freezing condition to obtain perturbed flux
Note:
single m=1
harmonic in
elliptical angle;
perturbed flux
vanishes at
X-points.
EXACT ANALYTIC SOLUTION

## Slide 16
Vacuum solution (no wall)
However, the separatrix is not a const magnetic surface, and so analytic determination of
coefficients is an inherently intractable problem.
Analytic progress is possible if flux coordinates (u, v) are used:
orthogonal coordinates!

## Slide 17
Since
. We can use this to determine
the coefficients.
After straightforward algebra, we obtain

## Slide 18: Mathematics of X-point singularity – in essence: (1) non-analiticity
Consider magnetic flux on separatrix
Fourier spectrum al large
 NOT an analytic function of
Indeed:
as
for small

## Slide 19: Continuity along the separatrix determines the perturbed flux in the vacuum region. This involves a parameter q. Along the separatrix:
+
even: q = p/2
odd: q = - p/2
for small

## Slide 20: Current sheet along the separatrix:
where
as
Growth rate:
Two classes of modes:
even: q=p/2 - stable oscillatory roots - current sheet on separatrix
odd: q=-p/2 - neutrally stable with - no current sheet
for small

## Slide 21: Conclusions – 2 The mathematics of the X-point singularity is established!
n=0 current sheets form along the magnetic separatrix, with as the X-point (at ) is approached.
The surprising result is that, because of these current sheets, the ideal-MHD vertical displacement is stable even in the absence of a passive feedback stabilization wall.
Conclusions

## Slide 22: Conclusions
The stabilization mechanism is a direct consequence of the ideal-MHD flux-freezing constraint on the X-points, which generates current sheets localized along the magnetic separatrix, exerting a force capable of pushing back the plasma in its vertical motion.

## Slide 23: Have these axisymmetric X-point current sheets been observed?
Perhaps yes…
JET experiments:
- J. Lingertat et al., J. Nucl. Mat. 241, 402 (1997);
- E. R. Solano et al., Nucl. Fusion 57, 022021 (2016).
Numerical simulations (M3D-C1; NIMROD; JOREK):
- I. Krebs, F. G. Artola, C. R. Sovinec, S. C. Jardin, K. J. Bunkers, M. Hoelzl, and N. M. Ferraro, Phys. Plasmas 10, 930 (2020).

## Slide 24: CONCLUDING REMARKS
Have we forgotten anything?

## Slide 25: Check-list for n=0 developing theory
Ideal-MHD
Resistive-MHD
Extended-MHD
Hybrid Kinetic-MHD
SOL Physics, field-line-tying, special boundary conditions
other…

## Slide 26: Check-list for n=0 developing theory
Ideal-MHD (Yolbarsop, Porcelli, Fitzpatrick, NF Letter 2021)
Resistive-MHD
Extended-MHD
Hybrid Kinetic-MHD (Barberis, Porcelli, Yolbarsop, 2021 EFTC, to submitted)
SOL Physics, field-line-tying, special boundary conditions
other…
V
V

## Slide 27: Thank you for your attention!

## Slide 28: Additional material

## Slide 29: Mathematics of X-point singularity – in essence: (2) non-periodic in vacuum region

## Slide 30
In the vacuum regions, , is no longer a periodic variable. Suitable solutions of that
decay (no wall!) to zero at infinity are
Continuity of flux at the separatrix provides a relationship between and

## Slide 31: Consistent behavior requires
and
+
even: q = p/2
odd: q = - p/2
for small