## Slide 1
Dimuon Measurement in CBM Experiment
Anand Kumar Dubey
VECC, Kolkata

## Slide 2
Outline
Dilepton measurements
CBM experiment at FAIR
Schematic of dimuon measurements in different expt.
Muon Chamber (MUCH) system of CBM
-- Simulation results
-- Detailed R&D
Summary

## Slide 3
Facility for Antiproton & Ion Research
SIS100/300
SIS18
HESR
CR
Compressed Baryonic Matter
Super Fragment-Separator:
Nuclear Structure and Astrophysics
Anti-Proton Physics
p-Linac
1012/s; 1.5 GeV/u; 238U28+
1010/s 238U92+ up to 11 (35) GeV/u
3x1013/s 30 (90) GeV protons
radioactive beams
1011 antiprotons 1.5 - 15 GeV/c,
stored and cooled
radioactive beams up to 1.5 - 2 GeV/u; up to factor 10000 higher in intensity than presently
antiprotons 3 - 30 GeV
Primary Beams
Secondary Beams
Storage and Cooler Rings
Technical Challenges
cooled beams
rapid cycling superconducting magnets
dynamical vacuum
100 m
FAIR phase 1
FAIR phase 2

## Slide 4
The Compressed Baryonic Matter Experiment (CBM)@FAIR
2021

## Slide 5
Dilepton pairs emitted in energetic heavy-ion collisions provide valuable information on the evolution and on the properties of the hot and dense fireball.
Comparison of charmonium yields measured in proton-nucleus and nucleus-nucleus collisions has led to the observation of an anomalous dissociation of charmonium in central collisions of heavy nuclei which was explained by color screening in the quark-gluon phase.
Till today, this observation still has remained one of the most convincing experimental facts hinting towards the existence of partonic degrees of freedom in the fireball at top SPS energies.
The dilepton measurements at the CERN-SPS have been performed mainly at 158 A GeV, except for one spectrum taken in Pb+ Au at 40 A GeV by the CERES collaboration where even an increased excess yield has been observed
The Dileptons

## Slide 6
B. Alessandro et al., EPJC39 (2005) 335
R. Arnaldi et al., Nucl. Phys. A830 (2009) 345
R.Arnaldi, P. Cortese, E. Scomparin Phys. Rev. C 81 (2009), 014903
Using the previously defined reference:
Central Pb-Pb:
 still anomalously suppressed
In-In:
almost no anomalous
suppression
In-In 158 GeV (NA60)
Pb-Pb 158 GeV (NA50)
Anomalous suppression

## Slide 7
A systematic beam energy scan in order to search for the onset of in-medium mass modifications of vector mesons or for partonic contributions to the dilepton yield has not been performed yet.
With the dilepton measurements in heavy-ion collisions at FAIR energies the CBM collaboration will open a new era of dilepton experiments in the energy range between 2 and 40 A GeV where the highest net- baryon densities can be created in the laboratory,
no dileptons have been measured in heavy ion collisions at these energies.
The CBM collaboration will systematically measure both dielectrons and dimuons in p+p, p+A and A+A collisions as function of beam energy and size of the collision system.
The dielectron and dimuon high-precision data will complement each other, and will provide a complete picture on dilepton radiation off dense baryonic matter. Also gamma conversion contamination is largely suppressed in case of dimuons.
.

## Slide 8: The CBM experiment
HADES
MVD + STS
RICH
TRD
PSD
EMC (park. pos.)
Muon detector
(parking position)
dipole magnet
Tracking, momentum, V0: MVD+STS+dipole magnet
Event characterization: PSD
Hadron id: TOF
Lepton id: RICH+TRD or MUCH
g, p0: EMC
High speed DAQ & trigger
TOF
SIS 100 setup

## Slide 9
CBM Experiment @ FAIR
PSD
Dipole Magnet
MuCh
TRD
RPC (TOF)
STS
Muon Chamber (MUCH) system
Aim: to detect dimuon signals from low mass vector mesons and J/y
(13.5 λI)
Novel subsystem of segmented absorbers
-- design goal being to simultaneously identify low and high momentum muons over full phase space
SIS100 : 2-4 GeV/u  4 chambers + 4 absorbers
SIS300 : upto 45 GeV/u 5 det.stations + 6 absorbers

## Slide 10: CBM @ SIS-100 & SIS-300
Beam | plab, max | √sNN, max
heavy ions (Au) | 11A GeV | 4.7 GeV
light ions (Z/A = 0.5) | 14A GeV | 5.3 GeV
protons | 29 GeV | 7.5 GeV
The first years of CBM operation will be at SIS-100 with a start setup
Beam | plab, max | √sNN, max
heavy ions (Au) | 35A GeV | 8.2 GeV
medium ions (In) (Cu) | 38A GeV 41A GeV | 8.5 GeV 8.9 GeV
light ions (Z/A = 0.5) | 45A GeV | 9.3 GeV
protons | 90 GeV | 13 GeV
CBM at SIS-300
…. at interaction rates up to 10 MHz (J/y)

## Slide 11
What is the typical configuration for dimuon detection in particle physics ?

## Slide 14
d
Au
μ
μ
Semi-leptonic decays of HF hadrons:
Electrons: |y| <0.35
-Tracked with DC,PC
-ID with RICH, EmCal
Muons: 1.2 < |y| < 2.2
~10λ hadron absorbers
-Tracked with wire chambers
-Further muon ID with layers of steel and streamer tubes

## Slide 15
ALICE Detector
(Muon Arm)

## Slide 16
ALICE MUON ARM
The optimized design provides
--- a good shielding capability and
--- a limited multiple scattering (…mass resolution).
 Using low-Z material in the absorber layers close to the vertex, and a high-Z shielding materials at the other end. => Pb + Boronated polyethylene & Pb + tungsten
The ALICE forward muon spectrometer will study the complete spectrum of heavy quarkonia (J/Ψ, Ψ′, ϒ, ϒ′, ϒ′′) via their decay in the μ+μ– channel.

## Slide 17: Muon detection system: MUCH
LMVM @ SIS100 + ToF
LMVM @ SIS300 + ToF
ID after hadron absorber with intermediate tracking layers
major combinatorical background from p,K decays into mn, punch through of hadrons and track mismatches
→ use excellent tracking to reject p,K decays in the STS
60 C + 20 Fe + 20 Fe + 30 Fe + 35 Fe + 100 Fe (cm)
30 cm gap between 2 absorbers
Notes: Layout optimization!

## Slide 18
Total number of particles as a function of the traversed length in iron. The particle momenta have been taken from the simulation of central Au+Au collisions at 25 A GeV, their numbers have been normalized.
Optimizing Absorber thicknesses

## Slide 19
Track reconstruction efficiency for primary muon tracks from J/psi as a function of
momentum for two tracking algorithms: nearest neighbor (red) and branching (blue). Left plot
shows MUCH tracking efficiency, right plot shows STS-MUCH tracking efficiency. Horizontal
lines represent numbers integrated over momentum.
25 AGeV

## Slide 20
3 layout options for SIS100 and SIS300
Basic SIS100
Extended SIS100
SIS300
Lengths:
6.4m (SIS100)
7.3m (SIS300)
TOF wall

## Slide 22
Detector options
One or two slides to show the
options and status
Occupancy (25 AGeV central collisions)
Geant3 + segmentation + GEM profile implemented

## Slide 23
Hit density on 1st station (Carbon as first absorber)
FLUKA calculations
(min-bias collisions)
25 AGeV
10 AGeV
400 KHz/cm^2

## Slide 24
FLUKA calculations
Neutron Flux on 1st station
35 AGeV
10 AGeV

## Slide 25
Neutron-equivalent dose
35 AGeV
10 AGeV

## Slide 26
TID: Total Ionizing Dose
at the outer edge of the
detector is around 10krad
Ref : http://cbm-wiki.gsi.de/cgi-bin/viewauth/Radiationstudies/WebHome?CGISESSID=2bce338388a71f099de8d3ca43e0f2b7
26

## Slide 27: Cocktail/ Background distribution for LMVM
For both setups Cocktail/Background ratios of about 100 are reached in central Au+Au collisions at 25 AGeV for minv ~ 0.5 – 0.6 GeV/c2
Cocktail/Background
muons
electrons

## Slide 28
Acceptance plots for J/psi mesons simulated for Au + Au collisions at 10 A GeV
for the PLUTO input (left) and after reconstruction (right).

## Slide 29: Invariant mass spectra – muons
Shown: central (b=0fm) Au+Au collisions at 25 AGeV
Mass resolution: 12 MeV (w) and 29 MeV (J/y) only due to momentum determination in STS
LMVM spectra for SIS100 show similar quality
J/y in central pAu at 30GeV with superb S/B ratio
S/B2s = 1.68
J/y
r
f
w
h

## Slide 30: Muons in CBM at SIS100
Running scenario:
Au+Au at 4 energies (4, 6, 8, 10 A GeV) up to 1 MHz
central Au+Au at 4 A GeV
2106  in 2 weeks
central Au+Au at 8 A GeV
η
ρ
ω
φ
2105  in 2 weeks
(approx. NA60 statistics)
ω
φ
η
ρ
Simulation: Signal yields from HSD, Background from UrQMD

## Slide 31
Challenges in Muon detection
Main issues:
High collision rates ~ 10 MHz
The first plane(s) have a high density of tracks
High granularity ~ average hit rate is about 0.4 hit/cm2
Should be radiation resistant –
high neutron dose  ~1013 n.eq./sq.cm/year
Large area detector – with modular arrangement
Data to be readout in a self triggered mode
-- a must for all CBM detectors.
-- and event reconstructed offline by grouping
the timestamps of the detector hits.

## Slide 32
Particle Density at Different MUCH stations
Hits/sq.cm\event
Radius (cm)
Different detector technologies for different stations
-- For the first two stations, which demand a high rate capability, Gas Electron Multiplier technology (GEM) would be used.
-- Straw tube and TRD for the other layers.
A. Senger, GSI

## Slide 33
Straw Tube R&D by Dubna Group
The straws with inner diameters of 4 and 9.53 mm have been tested in the SPS test beam at
CERN, with the same gas mixture of Ar/CO2 (80/20) and the gas gain 7 104 in both cases.
The efficiency was about 98% and 99% for the 4 mm and 9.53 mm straws, respectively.

## Slide 35
Spatial resolution as a function of the scaled distance to the anode for the straws with 4 mm (circles) and 9.53 mm (diamonds) inner diameter.
gas mixture Ar/CO2 (80/20), and the gas gain was about 70K in both cases.
The signal processing requirements of the straw tube have led to the design of a full-custom, analogue, bipolar ASIC. It provides eight channels of amplifier, shaper, discriminator and base line restorer.

## Slide 36
Triple GEM module for the first Two stations

## Slide 37
Gas Electron Multiplier (GEM) and its working principle
Active medium is a gas mixture.
electron multiplication takes place in holes
of two copper foils separated by kapton
Amplification may use 2 or 3 stages.
  Maximum size ~100 cm x ~50 cm
70m
140um
140m
a 50 micron polyimide foil with a 5 micron Cu layer deposited
on both sides of polyimide
Basic elements of a GEM chamber:
1. Drift plane
2. Amplifying element – GEM
3. Readout Plane
Cascaded GEMs can give higher gains and have lesser spark proability
70um

## Slide 38
Prototype fabrication at VECC
Readout plane
256 Pads
8 mm x 3.5 mm
10 ohm Resistors for protection
Outer side view
GEMS
1 2 3
CERN made framed
GEMs 10 cm x 10 cm
Gas - Ar/CO2 – 70/30
inner side
512 pads 3 mm x 4 mm
Outer side view
Multilayered
Readout PCB
Thermal stretching and framing of 31 cm x 31 cm
large size GEMs at VECC

## Slide 39
Beam test of GEM prototype chambers
Aim :
-- to test the response of the detector to charged particles. mainly in
terms of efficiency, cluster size, gain uniformity, rate handling capability
-- testing with actual electronics for CBM : nXYTER
nXYTER is a 32 MHz, 128 channel self triggered ASIC first developed by
DETNEE collaboration for neutron measurements.
– coupled to ROC(ReadOut Controller)
and then fed to the DAQ.
-- testing with the actual CBM DAQ
The nXYTER ADC spectra is inverted as compared to conventional picture,
this has to be subtracted from a baseline value channel by channel

## Slide 40
40
Test setup at Jessica beamline at COSY (Julich)
GEM chambers
STS station

## Slide 41: Beam spot (for high intensity runs), 2.3 GeV/c protons
GEM 2(10 cm x 10 cm)
GEM 3 (31cm x 31 cm)
Beam profiles as seen by 10 cm x 10 cm prototype and 31 cm x 31 cm prototype (right)

## Slide 42
Time difference between trigger (AUX) and detector hits
Test Results
gain
self triggered mode
Published in NIMA
Time correlation
Efficiency
Cluster size vs. voltage
Pulse height
spectra
Cluster size

## Slide 43
Rate test
using high intensity Cu X-ray
source in RD51 lab at CERN, with conventional
electronics
Gain remains almost stable with rate
Highest Rate in this picture ~ 1.4 MHz/cm2
95 kHz/sq.cm
1.38 MHz/sq.cm
HV = 3200 V,
Vgem~358 V,
gas- Ar/CO2(70/30)
Published in JINST-2014

## Slide 44
Test with absorbers – MiniMUCH
at CERN SPS, H4 beamline. Pion beams of GeV/c(with some muons and electrons)

## Slide 45
Gem1
Gem2
Gem3
Residuals for GEM2
beam
Reconstructing the track using GEM1 and GEM3 and Projecting the
hits at plane_GEM2 and finding the distribution of residuals

## Slide 46
Building a Real size MUCH sector prototype

## Slide 47: Layout --one layer of MUCH on a Drive

## Slide 48
Station # for SIS100 | Layer # | Total no of pads | R1 (cm) | Pad size (min) | R2 (cm) | Pad size (max) | Area (sq.mt) | No of 128 channel FEB/layer (round off) | No of Sector per layer
1 | 1 | 28800 | 25 | 4.36mm | 100.25 | 17.48mm | 2.95 | 240 | 16
 | 2 | 28800 | 25 | 4.36mm | 100.25 | 17.48mm | 2.95 | 240 | 16
 | 3 | 28800 | 25 | 4.36mm | 100.25 | 17.48mm | 2.95 | 240 | 16
2 | 1 | 30600 | 34.5 | 5.9mm | 146.9 | 25.4mm | 6.4 | 240 | 24
 | 2 | 30600 | 34.5 | 5.9mm | 146.9 | 25.4mm | 6.4 | 240 | 24
 | 3 | 30600 | 34.5 | 5.9mm | 146.9 | 25.4mm | 6.4 | 240 | 24
Station # for SIS300 | Layer # | Total no of pads | R1 (cm) | Pad size (min) | R2 (cm) | Pad size (max) | Area (sq.mt) | No of 128 channel FEB/layer (round off) | No of Sector per layer
1 | 1 | 28800 | 25 | 4.36mm | 100.25 | 17.48mm | 2.95 | 240 | 16
 | 2 | 28800 | 25 | 4.36mm | 100.25 | 17.48mm | 2.95 | 240 | 16
 | 3 | 28800 | 25 | 4.36mm | 100.25 | 17.48mm | 2.95 | 240 | 16
2 | 1 | 30240 | 29.5 | 5mm | 123.5 | 21.3mm | 4.5 | 240 | 20
 | 2 | 30240 | 29.5 | 5mm | 123.5 | 21.3mm | 4.5 | 240 | 20
 | 3 | 30240 | 29.5 | 5mm | 123.5 | 21.3mm | 4.5 | 240 | 20
# of sectors, FEB, area, etc.

## Slide 49
MUCH station layout

## Slide 50
Sector Chamber elements – (old design)
Top Honey comb
plate
Enclosure frame with ‘O’ ring seal
Drift plane PCB
HV divider
Pad plane PCB With clamping frame
GEM3
GEM1
GEM2
GEM spacer frame -1
GEM spacer frame -2
GEM spacer frame -3

## Slide 51: Real size readout PCB designed at VECC
471mm
797.2mm
708mm
J. Saini
797mm

## Slide 52
Readout PCB
inner side
Readout PCB
outer side with FEB connectors

## Slide 53
Real size GEM foil
31 cm x 31 cm GEM foil 12 HV seg.
~ Sector based readout.
1200 pads with progressive
increasing size
-- 9 FEBs placed at the three
sides of the board
-- coupled to 5 ROC’s
For CBM MUCH -- GEM foils having 24 HV Segmentation.

## Slide 54
Now all the three layers of each clamp segment are fastened together with screws at select places. While designing the layout of the GEM foil some circular copper patterns are generated at the edges to enhance the grip of the edge clamp segments.
The clamp segments are provided with an internal groove to accommodate a stainless steel nut. Thus after assembly of the segment a screw can be inserted sideways through the segment which mates with the embedded nut Fig.xx
The outer chamber frame has provision to insert screws from side walls through a small gas tight O-ring seal and the screw can be coupled to the embedded nut in the corresponding clamp segment.
After clamping all the foils the screws on the sides of the chamber frame can be tightened to stretch the foils in-situ .The screws are tightened until optimum tension is reached in all the three GEM foils.
HV contacts are brought out of the foils through spring contacts. This needs further improvement.
For large scale production it may be possible to mould the clamp segments with some engineering plastic like PEEK.
This method completely eliminates the slow gluing procedure and suitable for large volume production of chambers. Also since the grid-spacers are absent in the active zone, sparking probability due to glass filaments on the grid edges is eliminated. The chamber is opened for GEM replacement.
Stretching of GEM foils – glue-less approach – “ns2”

## Slide 55
Drift Plane
12-14 segments on either side
GEM Foil segmentation and HV connection
Total 24-28 HV segments per foil

## Slide 56
GE 1/1 for CMS
GE 1/1 for CMS

## Slide 58
Module Assembly schematic
Drift Plane
Spacers
GEM foils
Readout Plane
39 mm
Drift board
Readout board
6mm slotted Al or grid
for cooling
8 mm Aluminum Base – support structures
FEBs
6 mm Aluminum frame or grid with
water cooling
HV chain

## Slide 59: GEM foils for Real-size prototype

## Slide 60
Response of the real size prototype to Fe55 X-rays

## Slide 61
Beamtest of real size prototype at JESSICA@COSY, Juelich

## Slide 62
Beam spots at different positions of the prototype
Run91
X,Y=(19,16)
Pad size=5.76 mm
Run100
X,Y=(21,18)
Pad size= 5.97mm
RUN169
X,Y=(32,7)
Pad size = 7.26 mm
Run133
X,Y=(16,10)
Pad size=5.46mm

## Slide 63: Test Results of Real Size Prototype
-- a gain uniformity of < 15 % observed

## Slide 64
Technical Design Report
Submission for internal review: 21/10/13
Review: 7-8 Nov 2013
Submitted to FAIR: December 2013
Approved – December 2014
( VECC + 12 Indian Institutes, PNPI Gatchina, JINR Dubna )

## Slide 65
Summary
Dimuon measurement is at the core of the CBM physics program
Feasibility studies performed for a layout with
segmented absorber and detector triplets
Different detector technologies will be implemented at different stations
SIS100 layout R&D completed, can be extended to SIS300 chambers
First Real size Prototype using “ns2” stretching assembled and tested successfully with proton beams and using self triggered nXYTER electronics. New radiation hard chip for actual experiment would be
available soon.
Mechanical design underway for superstructure and detector chambers.
GEM module production may start early next year.

## Slide 66
Thank You

## Slide 67
BACKUPS

## Slide 68
Experiment | Energy sNN (Au/Pb beams) | Observables | Reaction rates Hz
STAR@RHIC BNL | 7 – 200 GeV | hadrons, electrons, muons | 1 – 800 (limitation by luminosity)
NA61@SPS CERN | 6.4 – 17.4 GeV | hadrons | 80 (limitation by detector)
HADES@SIS18 GSI | < 2.4 GeV | electrons, hadrons | 2·104 (limitation by detector)
Future/planned Experiments: |  |  | 
CBM@SIS FAIR | 2.7 – 4.9 GeV 2.7 – 8.3 GeV | hadrons, electrons, muons | 105 – 107 (limitation by detector)
MPD@NICA Dubna | 4.0 – 11.0 GeV | hadrons | 100 - 1000 (limitation by luminosity)
Experiments exploring dense nuclear matter

## Slide 69: MUCH-XYter: specifications
Input signal range of 1.5-100 fC
Charge polarity – negative
ENC – less than 0.3 fC
Detector capacitance up to 100 pF
maximum hit rate/channel – 2 MHz
Power consumption – 2 mW/ch

## Slide 70
Cooled plate for FEB cooling
8mm thick Alluminum plate with internal channel for water flow
Chilled water In/Out connections

## Slide 71: Background - muons
Particles identified as muons = reconstructed after MUCH (25 AGeV central Au+Au)
Total number allows for a trigger also for LMVM
min. 14 MuCh hits
LMVM setup (no TOF)
J/y setup (no TOF)
min. 17 MuCh hits
(70%)

## Slide 72
What is the typical configuration for dimuon detection in particle physics ?
Magnet
Absorber
Muon trigger and tracking detectors

## Slide 74
Comparison between
Carbon and iron absorber
Carbon as first absorber,
Rest iron
10 AGeV
25 AGeV
Peak particle densities for two
cases are similar
Carbon has advantages for
installation inside magnet

## Slide 75: ALICE Dimuon Detector

## Slide 76
Preliminary
158 GeV cross sections constrained by the relative normalization
Systematic error on (absolute) luminosity estimation quite high
Relative luminosity estimate between 158 and 400 GeV
much better known (~2-3% systematic error)
Normalize NA60 400 GeV cross section ratios to NA50 results
J/ production cross sections for pA data
New result: J/y cross section in pA

## Slide 77: From aliceinfo.cern.ch/public/…chapter2….ALICE dimoun spectrometer
Hard, penetrating probes, such as heavy quarkonium states, provide an essential tool to study the early and hot stage of heavy-ion collisions. In particular they are expected to be sensitive to Quark-Gluon Plasma formation. In the presence of a deconfined medium (i.e. QGP) with high enough energy density, quarkonium states are dissociated because of colour screening. This leads to a suppression of their production rates. At the high LHC collision energy, both the charmonium states (J/Ψ and Ψ′) as well as the bottomonium states (ϒ, ϒ′ and ϒ′′) can be studied. The Dimuon spectrometer is optimized for the detection of these heavy quark resonances.
The ALICE forward muon spectrometer will study the complete spectrum of heavy quarkonia (J/Ψ, Ψ′, ϒ, ϒ′, ϒ′′) via their decay in the μ+μ– channel. The spectrometer acceptance covers the pseudorapidity interval 2.5 ≤ η ≤ 4 and the resonances can be detected down to zero transverse momentum. The invariant mass resolution is of the order of 70 MeV in the J/Ψ region and about 100 MeV close to the ϒ. These values allow to resolve and measure individually all five resonance states.
The main components of the spectrometer are shown on the following sketch.
Basic principle of the Dimuon spectrometer: an absorber to filter the background, a set of tracking chambers before, inside and after the magnet and a set of trigger chambers.
The front absorber suppresses all particles except muons coming from the interaction vertex. It is made of carbon and concrete in order to limit the multiple scattering and the energy loss of the muons. The inner beam shield protects the chambers from background originating from particles at small angles. It is made of tungsten, lead and stainless steel to minimize the background arising from primary particles emitted in the collision and from their showers produced in the beam pipe and in the shield itself.
The tracking system is made of 10 cathode pad/strip chambers arranged in 5 stations of 2 chambers each. The spatial resolution should be better than 100 mm and all the chambers are made of composite material (< 3% X0 per chamber) to minimize the scattering of the muons in order to obtain the required resolution. To limit the occupation rate to a maximum of 5% the full set of chambers has more than 1 million channels.

## Slide 78: Dileptons at FAIR - the aim
no ρ,ω,φ → e+e- (m+m-) measurement between 2 and 40 AGeV
no J/ψ → e+e- (μ+μ-) measurement below 158 AGeV
Study EM radiation (+ heavy flavor) in baryon dominated matter at moderate temperature as accessible by FAIR!
Photons: access to early temperatures
Low-mass vector mesons: in-medium properties of r
Intermediate range: acces to fireball radiation
J/y: charm as a probe for dense baryonic matter
[A. Drees]

## Slide 79: Decay muons
Background dominated by decay muons
Vertex-z distribution of reconstructed m tracks in STS/ MUCH:
Successful reduction of decay muons by tracking cuts!
m-ID in STS
m-ID in MUCH

## Slide 80: Acceptance – r-meson
muons
Central (b=0fm) Au+Au collisions at 25 AGeV
Midrapidity at 2
electrons

## Slide 81: Muons in CBM at SIS100
Commissioning of high rate data taking (10 MHz)
Exploratory measurement: Charmonium production
central Au+Au at 10 A GeV
30 GeV p + Au
J/ψ  µ+µ-
1000 J/ψ in 1013 events (10 days)
(multiplicity from HSD)
1000 J/ψ in 1012 events (1 day)
(multiplicity from HSD)
J/ψ  µ+µ-

## Slide 82: Picture of the triple GEM prototype chambers
built at VECC
built by GSI Colleagues
(GEMS stretched and framed at GSI)
Parameter | GEM chamber (VECC) | GEM chamber (GSI)
Drift gap | 3 mm | 3 mm
Transfer gap-1 | 1 mm | 2 mm
Transfer gap-2 | 1 mm | 2 mm
Induction gap | 1.5 mm | 2 mm
Segmentation | 3 mm x 3 mm | 6 mm x 6 mm
Number of pads | 512 | 256