## Slide 1
The INO project
V.M. Datar
INO Cell, Tata Institute of Fundamental Research
Mumbai-400005
EILH-2016, AMU, Nov 2-6, 2016

## Slide 2
INO at Pottipuram (Theni)
Underground complex
51 kton ICAL Neutrino Detector
IICHEP, Madurai (Area: 12.6 ha)
Area: 27 ha
1270m
317 kton ICAL modules
22m228800 glass RPCs
3.7M electronic channels

## Slide 3
25 institutions (national labs, Universities, IITs) participating

## Slide 4
An underground lab to study neutrinos, dark matter…
Measure neutrino mass ordering, will help us understand how universe evolved (matter-antimatter asymmetry)
Help us go beyond Standard Model of Particle Physics
Development of biggest electromagnet, state of art technologies for particle detectors, electronics …
Will involve students to participate in building, testing detector components. Will spread experimental culture in area of HEP in particular, science in general
Pottipuram best place to do it – for TN and India
Why INO?

## Slide 5
Outline
1. Iron Calorimeter (ICAL) detector
2. Current status of ICAL and INO
3. Other experiments at INO

## Slide 6
1. Iron Calorimeter (ICAL) detector
Atmospheric neutrinos – provide a range
of energies (E1-10 GeV) and matter
propagation lengths  1 – 13000 kms
(free!)
Measurements hitherto did not distinguish between neutrinos (  ) and anti-neutrinos (  )
 ,  identified via charged current interaction
 + n   + p ,  + p   + n

## Slide 7
Why does one need a huge magnet?
Neutrinos cannot be detected directly but only via charged particles produced in -matter weak interaction
Muon neutrinos interact (CC) with Fe of magnet producing  with opposite curvature in B-field
Range of 1 GeV muon in Fe/H2O : 0.6 m/5m
Radius (bending) of muon in B=1 Tesla: 1 m
Up/Down direction using timing information

## Slide 8
Muon flux as a function of depth
Muon intensity (m-2 sr-1 yr-1)
Depth (metres water equivalent)
How deep underground ?
Low  event rates  3/day Cosmic muons most important background, reduced by 106 if detector depth = 1 km, deeper, the better 
mines or tunnels
Pottipuram

## Slide 9
Access tunnel and caverns
2 km long tunnel , D-shape 7.5 m wide, down-slope at 1 in 13.5
1270 m vertical rock cover, 1 km on all sides
~3 yrs for making tunnel, caverns
ICAL cavern

## Slide 10
Choice of detector
Possible detectors:
liq. Argon (“modern” cloud chamber based on
ionization chamber) - magnetic field difficult
sampling calorimeter with Iron - magnetic field easy
Iron + plastic scintillator (MINOS)
Iron + Resistive Plate Chamber (ICAL@INO)

## Slide 11
Choice of configuration
Magnet for target material and B-field
Iron based electromagnet is natural choice
Permanent magnet too expensive, reversing field too time consuming! High Tc SC based magnet complicated.
Two possibilities:
Toroidal field with axial conductor (MINOS, Soudan)
Layered magnet with rectangular coil (as in
MONOLITH @ Gran Sasso)

## Slide 12
MINOS Far detector
(5.4 kton)
Schematic of ICAL modules (317 kton)

## Slide 13
Schematic of Iron Calorimetric detector
B-field for 60 kA-turns, typical low C steel
Glass RPC for detecting charged particles
Signal pickup
X
Y
3 modules × 17 kton
Each with 150 layers Fe+RPC
B-field > 1 Tesla (90%)

## Slide 14
Different from normal gap magnets with field between pole pieces – here field is essentially within the Fe plates
Each module  17 kton (will be largest Fe based electromagnet in world!)
150 layers of soft iron (low carbon steel) of dimensions 16m  16m tiled with 4m  2m  56mm
Gap between successive layers of soft iron : 40mm
for glass Resistive Plate Chambers  35mm thick
Magnetic field > 1 Tesla, 1.5 Tesla desirable
Features of 17 kton ICAL magnet

## Slide 15
Challenges and Issues
Large size (3 nos of 16m16m14m)
Large copper coils (8m15m, 80 kA turns, 150 tons)
Large mass (largest electromagnet) 3  17 kton
Assembly minimizing gaps, preserving planarity
Piece-wise uniformity of B-field (> 1 T over 90% area)
Measurement of interior B-field (open problem)
Stability – mechanical, B-field (1%)
Large no. of RPCs  30,000 (World total  10K)
Electronics 4 M channels, fast (nsec), P/ch < 50mW

## Slide 16
Electromagnetic simulation study of ICAL magnet
B-field simulation using 3D finite element commercial software
B-field uniformity studied for various plate thicknesses, tiling configurations, air gaps, slots (for Cu coils), coil configurations. NI, 2 low carbon steels
Muon momentum response (from reconstructed trajectory) studied for a few coil currents, plate thicknesses

## Slide 17
B-field uniformity for
NI=20 kA.turns
C2 for different gaps
Fractional area with B > 1 T
S.P. Behera et al., IEEE Magnetics 51, 7000409 (2015)

## Slide 18
Muon response of ICAL for various B-field strengths

## Slide 19
Physics with Iron Calorimeter detector
ICAL will measure atmospheric muon neutrinos and muon-antineutrinos
Energy range: 1 GeV  E  20 GeV
Zenith angles: 0     70, 110     180
Neutrino mass hierarchy – normal or inverted
Neutrino mixing parameters (m232 , 23)
Non-standard interactions
Ultra high energy cosmic muons
White paper on “Physics Potential of the ICAL detector at INO”
under review in Pramana (2016); arXiv:1505.07380

## Slide 20
R. Gandhi et al., PRL 94, 051801 (2005)
Matter effect on oscillation probabilities vs. E

## Slide 21
Mass hierarchy of neutrinos – sensitivity of ICAL
m1 < m2 < m3 (NH) or m3 < m1 < m2 (IH) ?
ICAL can identify MH using matter effect on atmospheric  , 
(at 3 level with ICAL alone:  9 years, +acc. Expts: 6 years)
With accelerator based expts. can probe CP violation in -sector
ICAL only
ICAL + T2K + NovA

## Slide 22
Long range forces with Le  L gauge: limits of . 10 52 may be obtained (IOP group)
Sterile neutrinos: ICAL can probe very low m142
(IOP, TIFR)
Other physics possibilities

## Slide 23
Searching magnetic monopoles at ICAL@INO
MM
MM

## Slide 24
Energy loss of MM in 2mm RPC gas
KE (=103) for mMM=1015 GeV/c2
109 GeV !
E (10m Fe)  102 GeV
E (2RE)  108 GeV

## Slide 25
Upper bound on MM flux for 10 yrs of ICAL
(1015 cm2 sr 1 s1 )
Upper bound on MM flux for 0 observed events
N. Dash et al., Astroparticle Physics 70, 33 (2015)

## Slide 26
Searching for anomalous KGF events at ICAL
About 7 anomalous events found during 25 years of running the proton decay experiment – multiple tracks leading back to an origin not in detector or rock but in air
If KGF events are genuine, we should see many more with ICAL as cavern & detector  10 times larger
With additional detectors on 4 sides, should be able to provide data for/against KGF events in 2-3 years of running time

## Slide 27
2. Current status of ICAL and INO
Magnet: 35 ton 1st prototype ICAL detector
@ VECC, Kolkata with Bmax  1.5 Tesla.
8m8m20 layers prototype ICAL design ready for
IICHEP, on hold. 600T steel, OFHC Cu procured.
Building 70 ton mini-ICAL (4m4m11 layers)
RPCs: 2m 2m (12 nos) industry made glass RPCs
working @ Madurai lab. ~60/400 nos. delivered
Electronics: FE boards with ASIC, DAQ boards,
DC-DC HV units, Trigger system, DAQ software: testing or under fabrication.

## Slide 28
IICHEP site @ Madurai: 12.6 ha plot fenced
Awaiting reclassification.
INO underground lab site @ Pottipuram:
27 ha plot fenced. Water storage tank completed.
Pre-project infrastructure work
(road, water, electric power) partly done. Work
halted due to PIL in Madurai bench of Madras HC.
Financial approval for INO project in Dec 2014 given by Union Cabinet ( Rs. 1583 crores)
30 PhD students (BARC@HBNI)
have been part of INO-GTP
1st batch 2008-2009

## Slide 29: Soft Iron Plates for IICHEP, Madurai
168 (for 21 layers) soft iron plates, OFHC Cu coil procured
Soft iron plate
Soft iron plates at M/S Essar
8 plates in 32 ton trailer/trip
OFHC Cu coil
Notes: Packed soft iron plate

## Slide 30: RPC handling trolley for engg. module
Parameters | Prototype
Weight | 19 ton
Size | 6.5 m x 3m x 12.5 m
Rail | A75
Horizontal travel | 13.5 m
Vertical travel | 8 m
Vertical speed | 4 m/min max
Horizontal speed | 4 m/min max
RPC shelf (Elec. operated) | Stroke length 750 mm
Shelf speed | 92 mm/min max
Modular type lift support structure | 
RPC handling trolley delivered at IICHEP Madurai in April 2016

## Slide 31
mini-ICAL at IICHEP (rented premises)
Plate B
Pedestals
PA
PB
PC
PD
Target date: 31 March 2017

## Slide 32
Making the Cu coil
Straighten
Bend
In-situ silver brazing
Induction brazing tool

## Slide 33
RPCs, Electronics & Trigger, DAQ

## Slide 35
RPC-DAQ corner board + NINO FE
On board DC-DC HV module

## Slide 36
3. Other experimental possibilities at INO
Neutrinoless Double Beta Decay in 124Sn using a cryogenic bolometric detector (R&D ongoing for TINTIN)
Dark Matter search using a cryogenic CsI detector for low mass WIMPs (5-30 GeV/c2) (R&D ongoing for DINO)
Low energy accelerator for nuclear reaction cross sections ~ Gamow energy of astrophysical interest (Univ. groups working on proposal)

## Slide 37
ZA  Z2A + 2 + 2e Normal lepton#-conserving DBD
ZA  Z2A + 2 Lepton#-violating DBD
Neutrinoless double beta decay – is  =  ?
Maria Goeppart Mayer, Phys. Rev. 48, 512 (1935)
Why measure NDBD?
Majorana or Dirac ?
Absolute mass scale of 
NDBD m =  Uei2 mi ei(i) 
-decay m = { Uei2 mi 2 }1/2
20  [Q0]5  [NME]2   m  2
Large Q-value preferred
48Ca, 150Nd, 100Mo, 116Cd, 124Te

## Slide 38
Cryogen free dilution refrigerator @ TIFR
Base Temp. ~7 mK
Refrig power 1.4 mW @ 120mK
Cryogenic bolometer for NDBD
Insulators at low T, specific heat C  T3
Trise = E/(mC)  1/T3
In SC at T<Tc, Ce drops, so lattice C  T3
Goal: 1 kg natSn bolometer with NTD Ge sensor

## Slide 39
Rise time ~ 50 ms
Fall time ~ 2 s
Preliminary results with improved electronics (Oct. 2015)
V. Nanal, INO Collab meeting 25th Oct 2016

## Slide 40
Dark Matter search at INO – DINO (SINP)
Dark Matter believed to consist of Weakly Interacting Massive Particles (WIMPs) of mass 5-100 GeV/c2

## Slide 41
from Pijushpani Bhattacharjee (INO Collab meeting 25 Oct 2016)

## Slide 42
Future Possibilities
Low energy ion accelerator for Nuclear Astrophysics for measuring reactions going on in core of stars

## Slide 43
A cryogenic Indium detector for solar e ?
100 Ton 8% In-loaded liquid scintillator for solar e proposed by Raghavan (1976, 2007) to measure Tcore directly via shift + broadening of pp, 7Be energy spectrum (Bahcall 1993)
Cryogenic detector (qp current): Compact (1m3), High resolution (few keV), segmented.
Single Ee (MeV)
Events/(20 keV.5yr.10T In)

## Slide 44
India based Neutrino Observatory (INO) in Nature (13 Aug 2015)

## Slide 45
Acknowledgements
INO Collaboration
TINTIN, DINO collaborations
ICAL Magnet: Shiba Behera, M.S. Bhatia, D. Badodkar, S.P. Prabhakar, N. Dalal and DRHR colleagues
MM, DMP decay sensitivity of ICAL: Nitali Dash, Gobinda Majumder

## Slide 46
Thank you!