## Slide 1: Development of the PiGreCo simulation code for material analysis using the PIGE technique
Konstantinos Preketes-Sigalas
Department of Physics
School of Applied Mathematical
and Physical Sciences
National Technical University of Athens, Greece
Tandem Accelerator Laboratory
Institute of Nuclear and
Particle Physics
NCSR – “Demokritos”

## Slide 2: Introduction
PIGE (Particle Induced Gamma-ray Emission)
  Light-element (Li, B, F, Mg etc.) analysis of thick target
  Resonant-PIGE: depth profiling
Relative measurements: Need of several standards (stopping power)
 Absolute (standard-less) measurements
 Differential cross sections (IBANDL)
+ Simulation Code (integration of c.s.)

## Slide 3: PiGreCo (Particle Induced Gamma-Ray Emission COde)
Open-source code (Available in the scientific community via http://tandem.inp.demokritos.gr/pigreco/)
Programmed in C++ / Qt-5 libraries for GUI
Distributions for Windows/Linux/MacOS
Homogenous monolayer target
Stopping power:
  ZBL/SRIM compilations (elemental targets)
  Bragg’s rule (compound targets)
Straggling: Gaussian distribution – Bohr’s approximation
Cross sections: R33 format files  Compatibility with the IBANDL database

## Slide 4: Yield calculation
Using standards:
Standard-less measurements:
Eb
dE
dE
Eb-dE
Eb-2dE
≤dE
…
Einit≥Emin
Target
Beam

## Slide 5: The algorithm
Initial composition - Target division
Stopping power calculation (Ssam)
Yield calculation (Ym)
Comparison with experimental yield (Yuser)
Reconstruction of the matrix

## Slide 6: Stopping power
Elemental target
,
  ZBL compilation (default) [1]
  SRIM 2013 compilation [2]
Compound target
  Bragg’s rule
[1] J.F. Ziegler et al., NIMB 35 (1988) 215
[2] J.F. Ziegler et al., Lulu Press (2015)
Straggling
Vavilov’s theory (Computational-time consuming)
 Lorentzian distribution
 Gaussian distribution (current version)
 , [3]
(beam energy ripple)
[4,5]
[3] E. Szilágyi et al., NIMB 100 (1995) 103
[4] N. Bohr, Mat. Fys. Medd. Dan. Vid. Selsk. 18.8 (1948)
[5] J.W. Mayer et al., New York, San Francisco, London: Academic Press (1977)

## Slide 7: Layout

## Slide 8: Fitting
Target division in dE layers (dE=5 keV by default)
Cross-section linear interpolation
Stopping-power calculation for each layer
Yield calculation for the 1st “Fit” element
Comparison with the respective experimental yield
Element concentration is changed accordingly
(Concentration of linked element)
Excess/lack concentration is equally distributed to the “Free” elements
Steps 3-8 for all “Fit” elements
Program stops:
  1% convergence for all “Fit” elements
  50 iterations for each “Fit” element

## Slide 9: Code validation
Tandem Accelerator 5.5 MV Laboratory,
INPP, NCSR – “Demokritos”
2 standard samples
  Phosphate rock (NIST, SRM 120b)
  Multicomponent glass (NIST, SRM 1412)
Ep=1.5 – 4.0 MeV (variable steps)
θlab=55° and 90°

## Slide 10: Validation results
Element | Reaction | Eγ (keV) | Cross section | Difference
Fluorine | 19F(p,p’γ1-0)19F | 110 | Chiari et al. [1] | 2.3%
Sodium | 23Na(p,p’γ1-0)23Na | 440 | Chiari et al. [1] | 4%
Element | Reaction | Eγ (keV) | Cross section | Difference
Sodium | 23Na(p,p’γ1-0)23Na | 440 | Chiari et al. [1] | 2.8%
Boron | 10B(p,p’γ1-0)10B | 718 | Lagoyannis et al. [2] | 0.3%
Magnesium | 25Mg(p,p’γ2-1)25Mg | 390 | Preketes et al. [3] | 1.9%
 | 25Mg(p,p’γ1-0)25Mg | 585 | Preketes et al. [3] | 3%
 | 25Mg(p,p’γ2-0)25Mg | 975 | Preketes et al. [3] | 4%
Phosphate rock (“NIST 120b”) @ Ep = 4000 keV and θlab = 55°
Multicomponent glass (“NIST 1412”) @ Ep = 3500 keV and θlab = 90°
[1] M. Chiari et al., to be published, data retrieved from the IBANDL database
[2] A. Lagoyannis et al., NIMB 342 (2015) 271
[3] K. Preketes-Sigalas et al., NIMB 386 (2016) 4

## Slide 11: Summary and Plans
PiGreCo (http://tandem.inp.demokritos.gr/pigreco/)
  Homogenous monolayer targets
  Compatibility with R33 format files from the IBANDL database
  User-friendly – Distributions for Windows/Linux/MacOS
Improvements
  User-supplied stopping powers
  Weight percentage Atomic percentage (current version)
  Depending on feedback (e-mail: preketes@inp.demokritos.gr)
Future plans:
  Cross-section errors
  Straggling: Lorentzian distribution
  Breit-Wigner formula for narrow-isolated resonances
  Multilayer targets (resonant PIGE) / ill-posed problem

## Slide 12: Thank you for your attention!

## Slide 13: Layout…

## Slide 14: Target window
Homogenous monolayer target
  # of elements
  Composition (elements + initial concentrations)
    Total concentration equal to 1
    For the last element concentration press “F” (Fill)
  Element “behavior”:
    Fit (at least 1 and up to 5)
    Free (at least 1): excess/lack concentration
    Fixed: NO change
          ONLY for stopping power
  Link a “Fit” with a “Free” element
    (e.g., B:O is 1:2  O at least twice of B)
Extras: Load/Save

## Slide 15: Reaction window
Cross sections: in subdirectory “R33Data”
One cross section for each “Fit” element (tabs)

## Slide 16: Main window

## Slide 17: Validation results
Element | Reaction | Eγ (keV) | Initial yield (#/sr/μC) | Cross section | Difference
Fluorine | 19F(p,p’γ1-0)19F | 110 | 5.1x106 @ 2500 keV | Chiari et al. | 2.3%
Sodium | 23Na(p,p’γ1-0)23Na | 440 | 6.01x106 @ 2498 keV | Chiari et al. | 4%
Element | Reaction | Eγ (keV) | Initial yield (#/sr/μC) | Cross section | Difference
Sodium | 23Na(p,p’γ1-0)23Na | 440 | 6.01x106 @ 2498 keV | Chiari et al. | 2.8%
Boron | 10B(p,p’γ1-0)10B | 718 | 2.4x104 @ 2002 keV | Lagoyannis et al. | 0.3%
Magnesium | 25Mg(p,p’γ2-1)25Mg | 390 | 2.4x104 @ 2400 keV | Preketes et al. | 1.9%
 | 25Mg(p,p’γ1-0)25Mg | 585 | 8.5x104 @ 2416.2 keV | Preketes et al. | 3%
 | 25Mg(p,p’γ2-0)25Mg | 975 | 2.2x104 @ 2400 keV | Preketes et al. | 4%
Phosphate rock (“NIST 120b”) @ Ep = 4000 keV
Multicomponent glass (“NIST 1412”) @ Ep = 3500 keV