## Slide 1
Institute of
Nuclear & Particle Physics
fast Micromegas and dense Neutrinos
George Fanourakis
Institute of Nuclear & Particle Physics
N.C.S.R. “Demokritos”

## Slide 2
Fast detectors: Motivation
High Luminosity Upgrade of LHC:
To resolve pile-up.
ATLAS/CMS simulations: ~140 vertices per crossing (σt~170ps).
PID techniques: Alternatives to RICH methods, J. Va’vra,
https://dx.doi.org/10.1016/j.nima.2017.02.075
Extra detector requirements:
20 ps timing + tracking info.
Large surface coverage.
Multi-pads for tracking.
Resistance to aging effects.

## Slide 3
The standard Micromegas Detector
Drift Conversion region
Radiation creates electrons, which drift to the mesh plane.
Amplification region
Electrons go through the mesh and are amplified. The charge movement induces signals on the anode strips/pads.
Timing limitations
Conversion region too long: The electrons are created at different places
Diffusion effects: for a 3mm drift length  ~6 ns !
Lukas Sohl
(master thesis)
Anode - Read out
Mesh
Cathode
HV1
HV2
Ground

## Slide 4
The Picosec detector
A particle produces Cerenkov radiation.
Photons produce electrons in the photocathode.
Electrons are amplified by a two stage Micromegas detector.
We observe a signal with two components:
  Fast: electron peak (~1 ns).  good timing
  Slow: ion tail (~100 ns).
F.J. Iguaz (Saclay)
MCP signal

## Slide 5
Photocathode:
1) CsI and different:
- producer (CERN, Saclay)
- thicknesses (11, 18, 25, 36nm)
- metallic interface (Al, Cr) &
thicknesses (Cr 3, 5.5nm)
2) Pure metallic
- Al(8nm), Cr (10,15,20nm)
- Diamond, B-doped Diamond, DLC
Micromegas:
- standard bulk
- bulk with 6 pillars
- thin mesh bulk
Resistive (different values)
microbulk
Gas Mixture:
- Compass gas
- CF4 + 10% C2H6
- Ne + 20% C2H6
Amplification field
Drift field
Operation voltages
Crystal:
- Different Thicknesses of MgF2 (2,3,5mm)
- Different Materials
E. Oliveri (CERN)
Many parameters to optimize

## Slide 6
Single pad PICOSEC, active area: 1 cm diameter
Best result: 24 ps (bulk MM + Cr/CsI photocathode).
Optimum operation point: Anode +275V / Drift – 475V.
Nphe = 10.1 ± 0.7
Result repeated in two different beam campaigns.
σTOF = 24.3 ps
Reaching time resolution 24 ps !!!

## Slide 7
Nucl.Instrum.Meth. A903 (2018) 317-325

## Slide 8
Testing resistive PICOSECs
Values not far from the bulk PICOSEC detector
Worked fine for hours of pion beam

## Slide 9
Expanding the active area: Multipad PICOSEC
19 hexagonal pads
36 mm diameter active area
tested successfully October 2018 (again!)

## Slide 10
a Design Study
ESSνSB (ESSnuSB)
Study CP Violation in leptonic sector
(INPP) G. Fanourakis, Th. Geralis, G. Stavropoulos

## Slide 11: Design Study ESSνSB (2018-2021)
Kick-off meeting in January 2018, Lund.
ESSνSB has already started engaging postdocs.
partners: IHEP, BNL, SCK•CEN, SNS, PSI, RAL
More information on:
http://essnusb.eu/

## Slide 12: ESSnuSB web site

## Slide 13
Objectives

## Slide 14
INPP
Introduce Micromegas tracking detectors
Investigate the ESSnuSB potential for studying NSI
Some details
2 GeV protons

## Slide 15
European Spallation Source
May 2018

## Slide 16
more sensitivity at 2nd oscillation max.
for "large" θ13 1st oscillation maximum is dominated by atmospheric term
CP interference
solar
atmospheric
θ13=8.8º
(arXiv:1110.4583)
L/E
1st oscillation max.: A=0.3sinδCP
2nd oscillation max.: A=0.75sinδCP
(see arXiv:1310.5992 and arXiv:0710.0554)
P(νμ→νe)
2nd oscillation maximum
θ13=8.8º
("large" θ13)
dCP=-90
dCP=0
dCP=+90
L/E
very intense neutrino beam needed
Non-CP terms
CP violating
atmospheric
solar
interference
+…
Going for the 2nd Oscillation Maximum

## Slide 17
Yes, if we place our far detector at around 500 km from the neutrino source.
MEMPHYS like Cherenkov detector
(MEgaton Mass PHYSics studied by LAGUNA)
Neutrino Oscillations
Proton decay
Astroparticles
Understand the gravitational collapsing: galactic SN ν
  Supernovae "relics"
Solar Neutrinos
Atmospheric Neutrinos
500 kt fiducial volume (~20xSuperK)
Readout: ~240k 8” PMTs
30% optical coverage
(arXiv: hep-ex/0607026)
New 20" PMTs with higher QE and cheaper (see JUNO), the detection efficiency will improve the detector performance keeping the price constant, not yet taken into account.
Can we obtain the 2nd Oscillation Maximum?

## Slide 18
Physics Performance
little dependence on mass hierarchy,
δCP coverage at 5 σ C.L. up to 60%,
δCP accuracy down to 6° at 0° and 180° (absence of CPV for these two values),
not yet optimized facility,
5/10% systematic errors on signal/background.
540 km

## Slide 19
In combination with the other experiments
ESSνSB + DUNE can resolve CP with a minimum 10σ sensitivity in 4-5 years !
ESSνSB + 2THK can resolve CP in 3 years !
ESSνSB + 2THK can resolve the Hierarchy by breaking the hierarchy-δCP degeneracies
Apart from the fact that ESSνSB has the highest sensitivity for resolving CP among all the coming experiments (DUNE, T2HK and variations)
Nuclear Physics B 937 (2018) 303–332