## Slide 1: Deuteron induced reactions on Lithium and Fluorine
E. Taimpiri1,2, M. Axiotis2, K. Bosbotinis1, M. Kokkoris1, A. Lagoyannis2, A. Ziagkova1
1 Department of Physics, National Technical University of Athens, Zografou campus, 15780 Athens, Greece
2 Tandem Accelerator Laboratory, Institute of Nuclear and Particle Physics, N.C.S.R. “Demokritos”, Aghia Paraskevi, 15310 Athens, Greece

## Slide 2: Motivation
Lithium (natural abundance: 92.5% 7Li, 7.5% 6Li)
Fluorine (monoisotopic: 100% 19F)
widely used in industry
Need for detection and quantification via d-PIGE technique
Deuteron beams : necessary for the case of 6Li
Reliable differential cross sections needed (without the use of standards)
Complete lack of data for 7Li
One published work for 6Li & 19F (by G.A. Sziki (2006) for Εd= 0.8 – 2 MeV and θ=60°)
Existing literature:
Aim: Differential cross section data for the
6Li(d,n’γ1-0)7Be, 6Li(d,p’γ1-0)7Li, 7Li(d,d’γ1-0)7Li & 19F(d,p’γ1-0)20F

## Slide 3: Experimental setup
Deutron energy range: 1 – 2.2 MeV
20 keV step
5.5 MV Tandem Van de Graaff Accelerator of N.C.S.R. “Demokritos”
Beam current 20 nA
Faraday cup
Targets
Thin layer of natLiF (92.5% 7Li, 7.5% 6Li) evaporated on a thick natTa layer
Thin 6LiF (5% 7Li, 95%6Li) layer was evaporated on top of a natC substrate, with a top layer of 197Au
Detection systems
3 HPGe detectors (80% relative efficiency) placed at 0, 55 and 90, with respect to the beam axis
20 cm from the targets
Angular uncertainty: 11
Standard NIM (Nuclear Module Instrumentation) electronics

## Slide 4: Data Analysis
Absolute measurement
[barn/sr]
where,
: experimental yield, determined by integrating each peak of interest
: the number of incident deuterons
: the target thickness
: absolute efficiency of the detector

## Slide 5: Data Analysis :
6LiF target: via EBS (Elastic Backscattering Spectroscopy) technique
Proton beam: 1.3 MeV,
Surface Silicon Barrier detector placed at 170
Use of the 19F(p,p0)19F reaction (evaluated data from IBANDL)
natLiF target: via EBS, RBS & NRA techniques
Ratio 1:1 for lithium and fluorine
Uncertainty: 7%, for both measurements
Target |  |  | 
6LiF |  |  | 
natLiF |  |  | 
Target |  |  | 
6LiF |  |  | 
natLiF |  |  | 

## Slide 6: Data Analysis :
152Eu calibrated point source of R0=(2173) kBq
: yield of incident gamma rays
: the duration of the measurement
: the activity of the source the time of the measurement
: the intensity of each gamma ray
where,
Uncertainty: 5.4%
εabs of HPGe (80%) detector at 90
Fitting function :

## Slide 7: Data Analysis : &
Number of incident deuterons Nd
Beam charge collected with the Faraday cup setup
Experimental yield Y(E,θ)
Peaks of interest integrated via the Tv code
Statistical uncertainty: < 3%, for all spectrums
Typical spectrum of 6LiF target at Ed=2 MeV, θ=0
Uncertainty: 3.5%

## Slide 8: Results: Differential cross sections
19F(d,p’γ1-0)20F Εγ=656 keV
6Li(d,n’γ1-0)7Be Eγ=429 keV
Uncertainties :
Energy : ~ 4.5%
Statistical : ~ 3%, for all spectrums
Total systematic: ~ 9.5% (due to Nd , Nt & εabs)

## Slide 9: Results : Differential cross sections
6Li(d,p’γ1-0)7Li & 7Li(d,d’γ1-0)7Li Εγ=478 keV
The 478 keV case
Via the absolute measurement formula :
6LiF target (5% 7Li, 95%6Li)
natLiF target (92.5% 7Li, 7.5% 6Li)
2 equations 2 unknown terms
6Li(d,p’γ1-0)7Be
7Li(d,d’γ1-0)7Li

## Slide 10: Results: Comparison with literature
Comparison between present work’s results for the 7Li(d,d’γ1-0)7Li reaction at 55and modified data by Sziki at 60, shows a really good agreement
19F(d,p’γ1-0)20F
G.A. Sziki’s data for the 7Li(d,d’γ1-0)7Li have been modified
Existing data in IBANDL correspond to the 6Li(d,p’γ1-0)7Li reaction, by Sziki at 60
Looking back in the publication it is clear that the contribution of the 7Li(d,d’γ1-0)7Li reaction, at the 478 keV peak, has been totally ignored
7Li(d,d’γ1-0)7Li
Satisfying agreement for the 19F(d,p’γ1-0)20F reaction between present work at 55 and Sziki at 60

## Slide 11: Conclusions and Future perspectives
Differential cross section measurements of the 6Li(d,n’γ1-0)7Be, 6Li(d,p’γ1-0)7Li, 7Li(d,d’γ1-0)7Li & 19F(d,p’γ1-0)20F reactions
Deuteron energy range : 1 MeV – 2.2 MeV, θ=0°, 55°, 90°
Good agreement with existing data for the differential cross sections of the 7Li(d,d’γ1-0)7Li & 19F(d,p’γ1-0)20F reactions
Clarification of the 478 keV case
Benchmarking experiment for the validation of the obtained differential cross sections

## Slide 12
Thank you for your attention!