## Slide 1: A Windowless Window to the Universe
Ophir Ruimi, Physics Ph.D. Student
HUJI Fundamental Interactions Group, Prof. Guy Ron
JGU Mainz & HIM, MAM Section, Prof. Dmitry Budker
IBER 2023 – University of Coimbra, September 6th, 2023
Vacuum Separation by a Plasma Window for Nuclear Astrophysics Research (and Various Applications)

## Slide 2: Talk Outline
Why Plasma Windows
Operation principles, applications, Sci-Fi
Motivation: electron, ion and photon beam transmission from vacuum to atmosphere
Example: Stellar nucleosynthesis
Nuclear Astrophysics at SARAF: Liquid Lithium and enriched water targets
Results, conclusions and future work
Answer questions
The Plasma Window is a novel apparatus that utilizes a stabilized plasma arc as an interface between vacuum and atmosphere or pressurized targets without solid material. It’s useful in non-vacuum electron-beam welding, as well as in some Physics experiments.
What is a Plasma Window?
Star Trek: The Next Generation (1987)

## Slide 3: Plasma is ionized gas comprising of ions and electrons. Just like any other gas, plasma exerts pressure. Electric and magnetic fields exert forces on plasmas, which can confine plasmas in vacuum whose pressure can block, curb or confine other fluids. In a Plasma Window, electric and/or magnetic fields confine plasmas, whose pressure is large enough to balance atmospheric pressure (or even higher).
The states of matter and the idea behind a Plasma Window
A plasma is much less dense than a gas when both are at the same pressure. Plasmas have a much larger resistance to flow (viscosity) than gases. A plasma “plug” or “window” can slow down the flow of gases with little effect of fast particles passing through it.

## Slide 4
Simulation of a cube in empty space filled with air having a hole plugged by a Plasma Window; Courtesy of Jeffery Mitchell (BNL)

## Slide 5: Operation Principles
Ideal Gas: p = nkT
Where p is the partial pressure, n is the density and T is the temperature of the gas or the plasma, k is the Boltzmann constant.
Viscosity:
Poiseuille equation for the gas flow rate Q, where d and ℓ are the tube radius and length, η is the gas viscosity, and pa is the arithmetic mean of p1 and p2.
A critical assumption, gas is incompressible. Compressibility can be neglected if the Mack number M satisfies 0.5 M2 << 1. Some of the assumptions are no longer valid once a discharge is initiated, since the flow becomes compressible and nonisothermal. Therefore, a thorough analysis of such a gas and plasma flow requires solution of Naviar-Stokes equation for the gas. For electrons and ions, the relevant transport equations are the continuity, momentum transfer and viscosity equations:
Where m is the particle mass and q its charge. R is the species total momentum transfer, p its partial pressure and P is the stress tensor, ; η is the viscosity, λ is the Coulomb logarithm. The Naviar-Stokes equation is basically the momentum equation without the electric and magnetic field terms. Note viscosity dependence on temperature x>1 for gases.

## Slide 6: The Sky is not the Limit – When Sci-Fi Meets Reality: Plasma Window Has Captured People’s Imagination Featured in popular science magazines, newspapers, Michio Kaku‘s book Physics of the Impossible and in an accompanying syndicated article 10 Impossibilities Conquered by Science @#8 PW is listed under Creating force fields.
Star Trek Shuttle’s Bay Door
A Plasma Window at BNL
Star Trek: The Next Generation (1987)

## Slide 7: Force fields
Dome in the battle of Wakanda
The shield around the USS Enterprise
The Gungan handheld shields
Star Wars: A New Hope (Episode IV), George Lucas 1977
Avengers: Infinity wars (2018)

## Slide 8: Down to Earth
Schematic diagram of a Plasma Window
The stabilized plug of plasma seals the vacuum chamber to air but allows particle beams to pass through

## Slide 9: Producing a 3D CAD model from hand-written drawings

## Slide 10: Producing a 3D CAD model from hand-written drawings

## Slide 11: Plasma Window components’ terminology
(OFHC Cu)

## Slide 12
(2% Th)

## Slide 13
9.5 mm, insulators: 1.4 mm
119.9 mm
66.8 mm
Central aperture: 5 mm
(OFHC Cu)

## Slide 14: Plasma Lens (Focuses charged particles similar to light focusing by an optical lens)
Current
Electron beam
entering plasma
window
Electron beam
exiting plasma
window
Vz
Fr
Bθ

## Slide 15: RIKEN (RIBF) Plasma Window (Wako Center)
empty hole becomes window when filled with plasma

## Slide 16
BNL Gas Stripper R&D for FRIB (MSU)

## Slide 17
Ady Hershcovitch (BNL, SUNY)

## Slide 18: The challenge: Particle beams and electromagnetic radiation are usually generated in vacuum. For some applications it is desirable to bring beams in air or pass the beams through internal gas targets. Such applications include Nuclear Physics experiment, as well as electron beams for welding, X-ray, VUV, EUV for use in microscopy, lithography, etc.
Motivation
Electron-beam welding is the highest quality welding that can be performed. But, it’s done in vacuum, resulting in low production rates and limits on object size. Double hull ship can’t fit in a vacuum system. Past in-air EBW: lower quality.

## Slide 19
Workpiece
1 m
Motivation
(East Granby, CT, USA)
Electron Beam Through Plasma Window for the NRL

## Slide 20: Photons transmission via a Plasma Window
Thin solid windows are used for a whole spectra of high energy gammas; But, in some of these cases, these solid foils limit gamma outputs; i.e., machines are capable of generating higher intensities, the beam degrades, and the foil is damaged (two-fold problem).
Plasmas, including those in a PW, have a dual personality: electromagnetic radiation of frequency below the plasma frequency is severely attenuated, while the PW is completely transparent for electromagnetic radiation with frequency above the plasma frequency (unless there is a gas/plasma resonance).
The plasma frequency is the frequency at which electrons in a plasma oscillate:
A PW opened to atmosphere has a plasma density of about 1.5x1017 cm-3, for which the plasma frequency is = 3.5x1012 Hz; i.e., electromagnetic radiation with wavelength above 86000 nm are attenuated, while the PW is completely transparent for shorter wavelengths. There is no limit on radiation power that can pass through a PW. Furthermore, the bigger the radiation flux, the better
the PW works (creating more ionization).
Experimental data, e.g.: Light from a HeNe 632.8 nm laser and UV radiation from NSLS (BNL), as well as X- and gamma-
rays were passed through a PW open to atmosphere without any attenuation.
Cross sections for interaction of radiation from ultraviolet out into the hard x-ray regime, with individual particles is
usually minuscule, e.g., for Thompson scattering σ = 2/3 b (1 b = 10-24 cm2), i.e. mfp ~ 107 cm.
At resonance, however, some photo-absorption and -ionization cross sections can reach the 10-19–10-18 cm2 level.
The typical target thickness of a PW ~ 1.5x1017 cm-2 is about four orders of magnitude lower than that of a
conventional 250 µm beryllium window with ~ 2.5x1021 cm-2. Electromagnetic radiation of an energy far
from the absorption resonances of the working gas should have negligible interaction with a PW due to
small target thickness coupled with low interaction cross sections.

## Slide 21: Further applications: Commercial & Scientific
Several different types of accelerator systems can benefit from the utilization of the PW system.
Commercial Applications:
Non-vacuum electron beam welding: With PWs, higher production rates, no limit on the size of target objects, and high quality electron beams in atmosphere.
Non-vacuum material modifications by ion implantation, and dry etching, or micro-fabrication: Presently performed only in vacuum, since ion beams at energies used in these applications are completely attenuated by foils and by long differentially pumped sections.
Electron beam melting: for manufacturing alloys is performed at a pressure of about Torr. A major drawback of operating at this pressure range is the loss of elements with low vapor pressure. Consequently, it is desirable to raise the operating pressure to a higher level.
Electron beam generation of photo-neutrons for the production of medical isotopes (e.g., Tc-99): A 40 MeV electron beam strikes a W target. Resultant radiation can dislodge a neutron (via a giant resonance) to create a new element. With a plasma window, the target can be in the air, sufficiently cooled to absorb an intense electron beam to generate photo-neutrons.
Windowless gas targets for fast neutron radiography to detect nitrogen (weapons) and carbon (diamonds), as well as for other forms of neutron tomography and therapy (BNCT).
Windows for high power lasers (especially high-pressure gas lasers) and LBW.
Scientific Applications:
Windowless beamlines for transmission of synchrotron radiation: Plasma windows offer many advantages over presently used beryllium windows: radiation passes through the window unaffected. A plasma window cannot be damaged by radiation. UV filter for rejection of ‘high-order’ light is of significant benefit to experiments like threshold photoionization spectroscopy, where contamination even at the harmonic content can obscure the features of the spectrum of interest. X-ray microscopies, since it is free from the attenuation and spatial structure that attend the use of conventional window materials (e.g. beryllium or SiN), i.e., no scratches.
Windowless gas targets for fast (fusion) neutron generation (neutron sources).
Radioactive waste transmutation (ATW): protons are accelerated to 2 GeV unto a heavy metal target in air. Resultant spallation neutrons reduce radioactive waste. Presently, windows limit proton output.
APT – tritium production by accelerator: Solid windows limit beam and tritium output.
Spallation Neutron Source (SNS): To replace various solid windows with cooling problem.
Windows for high power x-ray source (DARHT).
Internal (gas or plasma) targets, strippers, lenses in storage rings: A plasma stripper/lens or an internal gas target "sandwiched" between two PWs. Examples: BNCT based on recirculating proton beams and various internal targets (including spin-polarized).
Fast acting valves in UHV beamlines. In case of vacuum breach, plasmas can be ignited faster than mechanical valves without damage to beamline (unlike, presently used, msec spring loaded shutters).

## Slide 22: The Soreq Applied Research Accelerator Facility - SARAF
A multi-user and versatile particle accelerator. It is based on a proton/deuteron RF superconducting linear accelerator, with variable energy (up to 40 MeV) and a continuous wave (CW) high ion current (0.04-5 mA), located at the Soreq Nuclear Research Center.
Motivation
2024

## Slide 23
Characterization of neutron-induced reaction rates on unstable isotopes is essential for understanding the nucleosynthesis occurring in astrophysical events involving massive stars (s-processes - e.g., the s-process acting in the range from Ag to Sb):
Motivation
An enriched water () target is under consideration at SARAF, for using the (p,n) reaction at an accelerated proton energy of 2.6 MeV in order to produce a 5 keV Quasi-Maxwellian neutron spectrum. So far, this reaction has been operated on solid targets, with corresponding low proton current and neutron flux. We aim to make use of the very high current available at SARAF-II to produce orders of magnitude more neutrons, and thus require a high-density target that is able to withstand high currents, which leads us to select a liquid based target. The only relevant liquid is .
Image courtesy of EMMI, GSI/Different Arts.

## Slide 24
Endgoal – The better understanding of processes occuring in:
Asymptotic giant branch stars
Pulsars, binary mergers
Active galactic nuclei
Supernova explosions
Motivation
Data will be used in state-of-the-art nucleosynthesis codes simulating the interior of stars during different burning stages, in collaboration w/ Rene Reifarth’s gp. @GUF

## Slide 25
Conservation of the expensive entails the use of a circulating target, containing a
reservoir, a heat exchanger and a cooling loop, which controls the liquid's temperature and
flow rate.
The high vapor pressure of is incompatible with accelerator vacuum.
We opt to solve this by using a Plasma Window.
Simulation of energy and heat deposition in target – preliminary results
Energy loss and heat deposition probe of 2600-keV proton beam in . The volume power density plotted is the power deposited within one radial standard deviation.
Energy loss vs. depth in the target
Heat deposition
Energy loss rate vs. initial beam energy
Required stream velocity on impact:

## Slide 26
Experiment overview
SARAF’s phase II is under construction, beamtime planned for mid-end 2024
s-process activation of gaseous targets: Kr, Xe, 99Tc.

## Slide 27
Summary
Plasma is the fourth fundamental state of matter. It contains a significant portion of charged particles – ions and electrons. The presence of these charged particles is what primarily sets plasma apart from the other fundamental states of matter. It is the most abundant form of ordinary matter in the universe, being mostly associated with stars. Plasma can be artificially generated by heating a neutral gas or subjecting it to a strong electromagnetic field.
Plasma is much less dense and much more viscous than a gas when both are at the same pressure.
A Plasma Window (PW) is an apparatus that separates between vacuum and atmosphere without any solid walls, and can hinder the flow of gases with little effect of fast particles passing through it.
PWs have many applications in medicine (e.g. BNCT), industry (e.g. EBW, LBW) & science (e.g. in particle accelerators).
PWs are used for scientific research in the fields of experimental particle physics, nuclear astrophysics, plasma chemistry, high-energy physics, accelerator physics and more.
PWs have been used for the transmission of electrons, protons, photons and heavy ions at various energies.
A particle beam passing via a PW can improve both the beam’s and the PW’s characteristics.
Photon transmission through a PW is possible above the plasma frequency, typically ~10 THz (or at a wavelength below ~100 µm).
What seemed to be science fiction (“force fields”) 40 years ago is today’s reality.
PWs actively contribute to the noble cause of our better understanding of the universe we live in.

## Slide 28: Questions?
Thank You for your attention

## Slide 29
Magnetic Resonance Spectroscopy and Imaging in the CASPEr Dark Matter Experiment
Poster #42/P12 – Ophir Ruimi (HUJI & JGU)
for the CASPEr collaboration
ophir.ruimi@mail.huji.ac.il
How to detect axions?
Hyperpolarization by SEOP
Xe transport and sample preparation
Achieved and projected results