## Slide 1: SPS ongoing studies: towards reinforcement learning for electrostatic septum alignment
EPFL Activities Meeting 05. July 2019
M. Schenkꝉ, M. Fraser*, B. Goddard*, S. Hirlaender*Ꝉ, V. Kain*, T. Pieloniꝉ
*CERN & ꝉEPFL, Switzerland
Ꝉalso at University of Malta

## Slide 2: Overview
Introduction
  SPS slow-extraction scheme
  Electrostatic septum: an optimisation problem
Motivation: reinforcement learning
Data-driven model
  Overview
  Results: training and validation
Final remarks

## Slide 3
x
x’
Septum wires
B. Goddard (TE-ABT)
SPS slow-extraction scheme
SPS delivers protons to Fixed Target experiments (FT)
FT request constant particle flux for several seconds (= spill)
Solution: multi-turn resonant extraction scheme
  Excite third-order resonance
  Extract beamlets by means of electrostatic septum (ZS)
Challenge: inherently a lossy process Optimisation problem: align ZS anode wires to reduce particle losses
Why important: need to reduce losses / activation (SLA Working Group), particularly in view of Physics Beyond Collider projects (BDF: SHiP)
Slow extraction
Losses on wires
M. Fraser (TE-ABT)
field-free region
Extracted beam
Introduction

## Slide 4
M. Fraser (TE-ABT)
SPS ZS composed of 5 tanks
System with 12 degrees of freedom (dof)
  10 dof: adjustable anode wire positions up- and downstream for every tank
  2 dof: girder positions up- and downstream
Loss monitoring: > 20 beam loss monitors (BLMs)
Entangled dynamics & ‘many’ parameters: modeling and optimisation not straightforward
anode wires
circulating beam
cathode
extracted beam
M. Fraser (TE-ABT)
to FT experiments
The SPS ZS
Introduction

## Slide 5
Until 2018:
  Manual, anode-by-anode optimisation
  Time-consuming (≈ 8 h) and tedious
  Required several times per year
Test in Nov. 2018:
  Automatic alignment: proof-of-principle with modified numerical optimiser (Powell’s method)
  Does first line search along every direction, then simultaneous parameter adjustment
  Big impact: time for full adjustment reduced to 40’ with same improvement on total loss
BLMs near ZS
Norm. beam loss (Gy/charge)
Controls (features)
Output (observables)
s
x
M. Fraser (TE-ABT)
Iterations
0
20
40
60
80
100
120
Anode pos. (cm)
-1
1
0
Norm. loss (%)
1.0
1.4
1.2
S. Hirlaender, V. Kain (BE-OP) & TE-ABT
SPS ZS alignment procedures
Introduction

## Slide 6
Can we do even better?
  Numerical optimiser has no memory: alignment from scratch every time
  Reinforcement learning (RL)
    Agent interacts with environment and learns dynamics of the system
    State not restricted to action space
    Agent strategy / knowledge typically represented by neural network (Deep RL)
    => once trained, agent remembers and finds optimum in a few steps
agent
Environment (e.g. accelerator)
action
state (observation) reward
Reinforcement learning
Reinforcement learning
Motivation

## Slide 7
RL defines state-of-the-art performance in robotics, playing games (e.g. Atari, AlphaGo), … and artificial intelligence problems in general
Applied to particle accelerator domain
  Proof-of-principle at CERN Low Energy Ion Ring (LEIR)
  1 control parameter: optimise injected intensity by tuning dipole magnet strength (BHN10)
  Solved as discrete control problem
  Model-free RL agent successfully learned the dynamics of the system
Implemented and tried out various continuous control algorithms using OpenAI gym environment templates
Experience shows: sample efficiency is of major importance for our problems
Reinforcement learning
Motivation
S. Hirlaender, V. Kain, M. Schenk
action
state
reward

## Slide 8
Can we do even better?
  Numerical optimiser has no memory: alignment from scratch every time
  Reinforcement learning (RL)
    Agent interacts with environment and learns dynamics of the system
    State not restricted to action space
    Agent strategy / knowledge typically represented by neural network (Deep RL)
    => once trained, agent remembers and finds optimum in a few steps
Reinforcement learning
  Sample efficiency is key as machine time is expensive
  Idea: Pre-train agent offline for ‘warm start’ in accelerator
Offline training requires a model F(x) of the system
  Tracking simulation, data-driven model, …
  Fast, cheap evaluation needed: Pre-training may require a few thousand iterations
agent
Environment (e.g. accelerator)
action
state (observation) reward
Reinforcement learning
Reinforcement learning
Motivation
BLMs
Beam loss (Gy/charge)
Features
Observables
F(x)
data-driven model

## Slide 9
Start with simple model
9 features All anode positions (except ZS1 UP), no girders
5 observables BLMs ZS1, ZS2, .., ZS5
Neural network Feed-forward, dense, 1 hidden layer, 7 - 15 nodes, leaky ReLU activation
Adam optimizer
Missing features: girders, orbit, cathode voltage, ...
Training and test sets from existing data
  Training on data from Powell scan 01.11.18, 467 samples => Predict manual scan 27.03.19 (independent test set, 7 months) => Fake scans for all anode positions
  Training on data from Powell scan and manual scan 27.03.19, 1308 samples => Predict manual scan 30.03.19 (test set) => Perform anode scans as above
BLMs
Beam loss (Gy/charge)
Features
Observables
F(x)
Overview
ZS data-driven model

## Slide 10
Overfitting?
Accuracy relatively low due to small number of samples
Case I: Training data and evolution (7-node neural network)
ZS data-driven model
Features
Observables

## Slide 11
Zoomed view of total loss
Good quantitative agreement, given simplicity of model and low number of samples
Training and test set separated by 7 months
Offset in ‘baseline’ & some peaks only qualitative agreement
  Missing feature (girder, orbit)?
  See individual loss on BLM ZS5 (backup)
Another source of discrepancy is range in anode positions
  Training set: ≈ ± 0.5 - 1 mm
  Test set: up to ≈ ± 2 mm
Case I: Test set predictions (total loss)
ZS data-driven model

## Slide 12
Good quantitative agreement, given simplicity of model and low number of samples
Training and test set separated by 7 months
Offset in ‘baseline’ & some peaks only qualitative agreement
  Missing feature (girder, orbit)?
  See individual loss on BLM ZS5 (backup)
Another source of discrepancy is range in anode positions
  Training set: ≈ ± 0.5 - 1 mm
  Test set: up to ≈ ± 2 mm
Case I: Test set predictions (total loss)
ZS data-driven model
Peak not predicted
Moving ZS1 UP
Not trained for that
Moving in range [-2, 2] mm
Not trained for that (extrapolation)
But: ZS5 no big impact on total loss, hence prediction still OK

## Slide 13
Case I: Trained on Powell data (7-node NN)
Case II: Trained on Powell and manual scan data (15-node NN)
Good news: both models predict similar loss response
Loss response is convex – as expected
Small impact on total loss from ZS4 and ZS5 – as observed in the machine
‘Piecewise linear’ functions due to simplicity of network
Case II: A second ZS NN model with 15 nodes trained on Powell and manual scan data performs even better on a test set (backup)
Scan individual anode positions and predict total loss
Validation: orthogonal anode scans
ZS data-driven model

## Slide 14
Measurement
Model
Validation: Powell optimisation on SPS machine and trained model
ZS data-driven model

## Slide 15
Measurement
Model
Validation: Powell optimisation on SPS machine and trained model
ZS data-driven model
Measurement and model show similar evolution
Model behaves well
Powell algorithm probes feature space better, not just along orthogonal directions
Similar test with COBYLA (Constrained Optimisation BY Linear Approximation) algorithm: converges even faster than Powell (see backup)

## Slide 16
Even with little training data: ZS model performs well and passes validation tests
It is not yet complete and hence improved further: adding more features / observables
Trained ZS model is now embedded in OpenAI gym environment and used for RL benchmarks
Excellent testbed for multidimensional RL optimisation problems to study various algorithms for continuous control
Sample efficiency is key (for accelerator domain)
Data-driven or surrogate models can be game changers
Final remarks

## Slide 17
Backup

## Slide 18
Offsets on BLM ZS5
Possibly due to changed settings on features that are not included in the model (orbit, girder, cathode voltage, etc.)
Overfitting artefacts?
Case I: Test set predictions (individual BLMs)
ZS data-driven model

## Slide 19
Orthogonal scans reasonable: convex shapes
No strong impact on total loss from ZS4 and ZS5, as observed in the machine
Piecewise linear functions due to simplicity of network
Case I: Tests with ‘fake’ anode scans
ZS data-driven model

## Slide 20
Start with simple model
9 features All anode positions (except ZS1 UP), no girders
5 observables BLMs ZS1, ZS2, .., ZS5
Neural network Feed-forward, dense, 1 hidden layer, 7 - 15 nodes, leaky ReLU activation
Adam optimizer
Missing features: girders, orbit, cathode voltage, ...
Training and test sets from existing data
  Training on data from Powell scan 01.11.18, 467 samples => Predict manual scan 27.03.19 (independent test set, 7 months) => Fake scans for all anode positions
  Training on data from Powell scan and manual scan 27.03.19, 1308 samples => Predict manual scan 30.03.19 (test set) => Perform anode scans as above
BLMs
Beam loss (Gy/charge)
Features
Observables
F(x)
Overview
ZS data-driven model

## Slide 21
Case II: Training data (15-node neural network)
ZS data-driven model

## Slide 22
Other scans / settings (miniscans)
Case II: Test set predictions (on ‘independent’ data set)
ZS data-driven model

## Slide 23
Other scans / settings (miniscans)
Less surprising that performance of the model is good
It ‘has seen the test set’ already (sets not independent …)
Even when overfitting would likely still perform well on test set
Difficult to find solid, independent test from available data in that case
Case II: Test set predictions (on ‘independent’ data set)
ZS data-driven model

## Slide 24
COBYLA with constraints on anode positions to ± 2 mm: Optimisation on NN model to check if it produces sensible output
Not clear yet how NN model behaves outside ‘trained range’ …
COBYLA or Powell algorithms probe feature space better, not just along orthogonal directions
Reward = total loss x 1014
Optimum expected at 8 x 10-14 Gy/charge (from data and NN model)
Even faster convergence than Powell – looks promising
Validation: COBYLA performance on trained model (7-node NN)
ZS data-driven model