## Slide 1: Status of SixTrack loss rate simulations
04. May 2020
M. Schenk for the EPFL team EPFL & CERN, Switzerland
Acknowledgements
R. Bruce, R. De Maria, M. Giovannozzi, A. Mereghetti, D. Mirarchi, T. Persson, S. Redaelli

## Slide 2: Objectives and overview
What we would like to learn
  Loss rate dependency and sensitivity to machine knobs: How do chromaticity, octupoles, tunes, etc. affect long-term (~106 turns) particle loss?
  How are losses distributed with respect to H / V?
Type of studies
  Similar to dynamic aperture (DA) studies
  Instead of 1 m amplitude threshold: use H, V, S primary collimators near IR7 (w/o. scattering)
  Results likely of qualitative nature
Framework
  PySixDesk & SixTrack
  Using HTCondor for now
  Move to BOINC soon
Complement LHC beam loss model based on experimental data with SixTrack simulations

## Slide 3: Contents
Aperture model
Particle initialization
Post-processing / analysis
Some test results for discussion
Questions & feedback

## Slide 4: Aperture model
Primary collimators only
Discussion with collimation and SixTrack experts (21.02.20)
  Consider black absorber model: expect losses only on primaries (TCP) since no scattering
  Full aperture model not required for our purposes
Created very simple model consisting only of TCPs near IR7 (betatron cleaning)
A. Mereghetti: calculate collimator gaps from N. Fuster-Martinez, Evian 2019 (Tab. 1: TCP IR7 at injection: 5.7σ for εnorm = 3.5 μm rad)
Half gaps set in our model depend on beta functions at elements
Loic’s 3D aperture / loss visualizer 

## Slide 5: Aperture model
Track square beam through machine to verify gaps and skew collimator angles
TCP S
half gap: 5.057 mm
angle: 127.5°
TCP V
half gap: 4.308 mm
angle: 90°
TCP H
half gap: 5.973 mm
angle: 0°
Validation
Gaps correctly applied and tilt angle correctly propagated to SixTrack

## Slide 6: Contents
Aperture model
Particle initialization
Post-processing / analysis
Some test results for discussion
Questions & feedback

## Slide 7: Particle initialization
Work with DA-style initial conditions and weights, i.e. uniform polar or rectangular grid in (Jx, Jy) space (Actual Gaussian distributions would require tracking too many “irrelevant” core particles)
So far
  (Py)SixDesk runs SixTrack one-turn jobs first to obtain Twiss parameters for given lattice and machine parameters
  Cannot initialize matched distribution otherwise
With DIST block
  DISTlib takes care of the matching, no need for one-turn jobs for our studies
  Simplifies particle initialization and job management
SixTrack DIST block

## Slide 8: Particle initialization
SixTrack DIST block
Node runs init_dist.py: generates distribution on rectangular grid for given amplitudes (twin particle also initialized – “close” to original one)
DIST block in fort.3: read distribution from file
All momenta initialized to 0 here for now OK for transverse planes: fast phase mixing similarly to DA studies
Longitudinal coordinate also set to 0 (OK ?)
Included in PySixDesk, but in a “hacky manner”

## Slide 9: Particle initialization
SixTrack DIST block
Example: steps of 0.25 in normalised amplitude with εnorm = 3.5 µm rad at 450 GeV, i.e. εnorm / βγ ≈ 7.3 nm, and 2Jx,y = εgeo
Validation: and data from singletrackfile at turn 0 (IP3)
  MAD-X: /
  Looking good
Coord. space
Action space
0.45 mm
0.33 mm

## Slide 10: Contents
Aperture model
Particle initialization
Post-processing / analysis
Some test results for discussion
Questions & feedback

## Slide 11: Post-processing: loss calculation
Gaussian weights
(Jx, Jy) space divided into square cells, s.t. every cell contains 1 particle (pair) = 1 initial condition
ci,j (t) : flag particle in cell (i, j) dead (= 1) or alive (= 0) after t turns
Calculate weights wi,j in action space for beam distribution we would like to mimic
Weights are illustrated by orange color
=
- ] [ - ]
= wi,j
Example: round Gaussian beam

## Slide 12: Post-processing: loss calculation
Gaussian weights: validation
S. Y. Lee, Accelerator Physics, 4th edition, pg. 59
Validation: compare calculated Gaussian weights to literature
All in good agreement

## Slide 13: Contents
Aperture model
Particle initialization
Post-processing / analysis
Some test results for discussion
Questions & feedback

## Slide 14: Some test results
Goal: verify that “collimators” work
Machine parameters
  LHC @ 450 GeV
  Qx = 62.28 / Qy = 60.31, Q’x,y = 15
  εnorm = 3.5 µm rad
  Three cases: Ioct = {-40 A, -20 A, 0 A}
Initialize particles on rectangular grid
  Up to 2Jx,y = 36 εrms, i.e. 6σ (beyond collimator limits) (”missing beam”: = 3.1 x 10-8)
  Amplitude steps of 0.25
  Total of 2 x (36 / 0.25)2 = 41’472 particles (incl. twin)
  Longitudinal position = 0 for all particles
5000 turns
Just one error seed
Running on HTCondor
Short runs (5000 turns): setup

## Slide 15: Some test results
Example 1: Ioct = -40 A
Losses on collimators within first few hundred turns (discussed with Daniele)

## Slide 16: Some test results
Example 1: Ioct = -40 A
Losses on collimators within first few hundred turns (discussed with Daniele)

## Slide 17: Some test results
Example 2: Ioct = -20 A

## Slide 18: Some test results
Example 3: Ioct = 0 A

## Slide 19: Some test results
Goal: we are interested in “slow” losses, driven by non-linearities
Same machine parameters
  LHC @ 450 GeV
  Qx = 62.28 / Qy = 60.31, Q’x,y = 15
  εnorm = 3.5 µm rad
  Three cases: Ioct = {-40 A, -20 A, 0 A}
Initialize particles on rectangular grid
  Up to 2Jx,y = 16 εrms, i.e. ”missing beam”: = 6.7 x 10-4
  Amplitude steps of 0.25
  Total of 2 x (16 / 0.25)2 = 8’192 particles (incl. twin)
  Longitudinal position = 0 for all particles
106 turns
Just one error seed
Running on HTCondor
Long runs (106 turns)

## Slide 20: Some more test results
Example 1: Ioct = -40 A
Do observe losses until up to 106 turns
Encouraging, but Ioct = -40 A for 3.5 µm rad beam at injection energy is very high
Why is everything lost on skew collimator? Expected?

## Slide 21: Some more test results
Example 2: Ioct = -20 A
Losses are reduced – that’s OK
Main loss in beginning – not much else happening till end
”Sensitivity issue”? More turns required?
Again everything lost on skew collimator

## Slide 22: Some more test results
Example 3: Ioct = 0 A
Slightly higher loss rate (unexpectedly), but all lost in first few thousand turns
Again everything on skew collimator

## Slide 23: Some more test results
Example 4: Ioct = -100 A …
Very unrealistic scenario …
Just to see what happens

## Slide 24: Contents
Aperture model
Particle initialization
Post-processing / analysis
Some test results for discussion
Questions & feedback

## Slide 25: Questions & feedback
Generally: are we on the right track? Better approaches / suggestions?
First tests show that it may be challenging to reach sensitivity for actual (close-to) operational machine parameters
However, some things still left for testing
  Longitudinal coordinate z = 0?
  Only looked at Ioct. What about tunes, Q’, other error seeds, etc.?
  Yet more turns, larger phase space area?
  Consider twin particle
  Other ideas?
Grid and beam distribution
  Rectangular or polar?
  Grid density: our loss is upper estimate since we assume whole area is lost if our cell-particle is lost. Should be good estimate if cells are small enough
  Mimic beam distribution with weights: way to go?
  Gaussian beam? (especially important at high amplitudes where we see losses)
Using Python script to generate initial distribution on each computing node: would that work with BOINC?
Papers / references on the subject?