## Slide 1: Realistic Optics & Single-Particle Tracking Models for the FCC-ee
R. De Maria, F. Schmidt, F. Zimmerman (CERN)
A. Faus-Golfe, G. Simon (Uni. Paris Saclay)

## Slide 2: PhD Description: Realistic Optics & Single-Particle Tracking Models for the FCC-ee
The 2020 Update of the European Strategy for Particle Physics requests Europe, together with its international partners, to investigate an electron-positron Higgs and electroweak factory as a possible first stage of a future large circular collider infrastructure. Preparing for such a post-LHC accelerator complex and demonstrating its feasibility requires appropriate simulation tools that this PhD project will help develop in a single coherent framework.
The thesis will address several tasks:
Treating fully symplectic 6D particle beam dynamics with the addition of deterministic synchrotron radiation and quantum fluctuations;
enabling a realistic interaction-region model, including solenoid systems;
allowing for a flexible representation of “tapering” in the collider arcs.
The new tool will support emittance tuning studies, dynamic aperture optimization, machine tuning and optics corrections studies.
The code development should be based on a modular approach.
In particular, the tool must feature an interface with strong-strong and weak-strong beam-beam simulation codes.
The new code should allow for a later addition or inclusion of spin motion (e.g. 8D spin formalism of D. Barber et al., or as in SITROS by J. Kewisch), which could optionally, time permitting, already be integrated as part of this PhD.
The work will be carried out in the framework of a FCC-EPFL collaboration on simulation tools.

## Slide 3: Detailed PhD Goals:
Machine modeling:
  Interaction region: detailed description of solenoid, fringe field and large crossing angle,
  Lattice with magnetic field imperfection, alignment imperfection
  Tapering: ideal and realistic
  Detailed apertures of IR and arcs
  Circuit and knobs definitions
Physics models:
  Tracking: 6D symplectic with radiation damping and quantum excitation (compare per element excitation vs lumped)
  Optics linear and non-linear: TRANSPORT and TPSA based
  6D Beam-beam: inject crab waist on top of SixTrack-like [1] beam-beam that has already large crossing angle and hourglass effect.
  Add beam-strahlung in tracking and optics
  Equilibrium emittances with imperfection and realistic interaction region: compare different methods (moments vs integrals vs tracking and Hirata-Ohmi-Oide vs Chao vs Sands)
  Momentum acceptance via tracking and optics.
  Tracking debris and photons should be allowed: coupling with debris/photons generators
  Dynamic aperture (DA) with realistic IR model and imperfections. Sufficiently fast to enable DA based optimization and lifetime.
  Spin: compute de-polarization
[1] G. Iadarola et al. 6D beam-beam interaction step-by-step, CERN-ACC-NOTE-0023

## Slide 4: Team Roadmap: main stages
1) Preparing a repository of scripts in collaboration Felix and Xavier using existing codes [1] and expertise [2] that:
  Compute Twiss parameters: on and off momentum
  Compute equilibrium emittances
  Compute dynamic aperture
  Provide an interface for the weak-strong and strong-strong codes
by using one recent version of the FCC lattice, properly adapted to for each code to achieve the most accurate results within the limit of the codes. This allows to gain experience and establish benchmarks.
2) With this experience and the using the benchmark:
identify an existing code as base and plan a set of updates needed to reach the desired goals
coordinate implementation efforts with the teams involved
3) Study how to integrate spin
[1] One or more among MAD8, SAD, MAD-X, PTC, PYAT, BMAD
[2] H. Burkhardt, J. Jowett, K. Oide, D. Sagan, L. Van Reisen-Haupt, …

## Slide 5: Next steps
For Guillaume: reading literature, gain experience with the codes
Starting collaboration with Felix for building the example library: this is synergetic with the work of the general framework.
Clarify current limitations of the existing codes and identify potential improvements
Expected timelines:
  Guillaume ready to start as trainee
  PhD planned to start in September