## Slide 1: Electron Cloud Studies for FCC-ee
Sabato Luca1, Mether Lotta2
Acknowledgement: Pieloni Tatiana1, Iadarola Giovanni2, Paraschou Konstantinos2
1 2
ABP-CEI Section Meeting
1st June 2023
This work was performed under the auspices and with support from the Swiss Accelerator Research and Technology (CHART) program (www.chart.ch).

## Slide 2: Outline
Introduction
E-Cloud Formation Process
Build-up Simulation Results
Stability Simulations
Conclusions and Outlook
ABP-CEI Section Meeting 01/06/2023

## Slide 3: Outline
Introduction
  Scientific Goal
  FCC
  New Parameters
E-Cloud Formation Process
Build-up Simulation Results
Stability Simulations
Conclusions and Outlook
ABP-CEI Section Meeting 01/06/2023

## Slide 4: Introduction: Scientific Goal
The scientific goal of the research activity is to check the stability limits by means of self-consistent beam stability simulations for the different arc elements with realistic electron cloud (e-cloud) distributions obtained from build-up simulations
Comparison between the analytical central electron density threshold for single bunch instability and the simulation results
The beam stability simulations are heavy from the computational point of view
For this reason, a preliminary study to identify the parameters, in the range of the values of FCC-ee case, which play a significant role in the e-cloud formation has been performed
[ ] K. Ohmi et al., “Study of Electron Cloud Instabilities in FCC-hh”, Proc. of IPAC2015
ABP-CEI Section Meeting 01/06/2023

## Slide 5: Introduction: FCC-ee
FCC-ee is a circular electron-positron collider, the first stage towards a 100 TeV proton-proton collider FCC-hh
[ ] FCC week 2022, “Accelerator overview”, Frank Zimmermann, Tor Raubenheimer
The Z configuration has been investigated, because the strongest e-cloud effects are foreseen for this configuration due to the highest number of bunches (smallest bunch spacing)
ABP-CEI Section Meeting 01/06/2023

## Slide 6: Introduction
New machine and beam parameters
  More bunches -> less bunch spacing (max 18.9 ns)
  Smaller bunch intensity
  Bunch length
[ ] K. Oide 16th March 2023, “Impact of beamstrahlung on crab sextupole compensation”, 163rd FCC-ee Optics Design Meeting & 34th FCCIS WP2.2 Meeting
ABP-CEI Section Meeting 01/06/2023

## Slide 7: Introduction
ABP-CEI Section Meeting 01/06/2023
15/05/2023
Design in PyECLOUD
Design in PyECLOUD
New vacuum chamber
Courtesy of R. Kersevan and F. Santangelo

## Slide 8: Outline
Introduction
E-Cloud Formation Process
Build-up Simulation Results
Stability Simulations
Conclusions and Outlook
ABP-CEI Section Meeting 01/06/2023

## Slide 9: E-Cloud Formation Process
Trailing bunches of the train are in a dense electron-cloud
Transverse instabilities
Transverse emittance blow-up
Particle losses
    Secondary Electron Emission can drive an avalanche multiplication effect filling the beam chamber with an electron cloud
    Proton bunch
    e- is emitted (photoelectric effect)
    Secondary Electron Emission
Courtesy of
G. Iadarola
e-cloud induces other unwanted effects like:
Heat load on the beam chambers
Vacuum degradation
Affects mainly machine operating with positively charged particles (p+, e+, positive ions…)
ABP-CEI Section Meeting 01/06/2023

## Slide 10: E-Cloud Formation Process
  it depends on the history of the surface, in particular on accumulated electron dose -> to a certain extent the e-cloud cures itself (beam induced scrubbing)
The chamber geometry influences e- acceleration and time of flight
Surface properties have a primary role in the e- multiplication process
  The main quantity involved is the Secondary Electron Yield (SEY):
  The SEY is the ratio between emitted and impacting electron current as a function of the energy of the impinging electrons
  It depends on surface chemical properties
Courtesy of
G. Iadarola
ABP-CEI Section Meeting 01/06/2023

## Slide 11: E-Cloud Formation Process
A key ingredient is the bunch spacing:
  It determines how many electrons survive between consecutive bunch passages
  Significant impact on multipacting threshold, i.e. SEY above which avalanche multiplication (multipacting) is triggered
Bunch intensity and bunch length also have an important effect as they affect the acceleration received by the electrons
PyECLOUD simulations – LHC arc dipole
Maximum Secondary Electron Yield (dmax)
Accumulation of primary e-
Multipacting
Accumulation of primary e-
Multipact.
Courtesy of
G. Iadarola
ABP-CEI Section Meeting 01/06/2023

## Slide 12: E-Cloud Formation Process
Electron trajectories are strongly influenced by externally applied magnetic fields (Electrons spin around the field lines)
e-cloud distribution in the LHC arc magnets
Courtesy of
P. Dijkstal
ABP-CEI Section Meeting 01/06/2023

## Slide 13: Outline
Introduction
E-Cloud Formation Process
Build-up Simulation Results
  Parameter Overview
  Summary Previous Results
  Results for New Parameters
Stability Simulations
Conclusions and Outlook
ABP-CEI Section Meeting 01/06/2023

## Slide 14: Simulation Results: Parameter Overview
ABP-CEI Section Meeting 01/06/2023
Element:
  Drift space
  Quadrupole (5.65 T/m)
    focusing
    defocusing
  Dipole (1.415 mT)
    close to focusing quadrupole
    close to defocusing quadrupole
The version V22.2 has been used
[] https://acc-models.web.cern.ch/acc-models/fcc/fccee/V22.2/z/
βx
βy
Focusing
quadrupole
Defocusing
quadrupole
Dipole
Dipole
Dipole
Dipole
Drift space
Drift space
Defocusing
quadrupole

## Slide 15: Simulation Results: Parameter Overview
Element:
  Drift space
  Quadrupole (5.65 T/m)
    focusing
    defocusing
  Dipole (1.415 mT)
    close to focusing quadrupole
    close to defocusing quadrupole
  εg,x = 0.71 nm
  εg,y = 1.42 pm
Drift space
Dipole close to foc quad
Dipole close to defoc quad
Focusing quadrupole
Defocusing quadrupole
ABP-CEI Section Meeting 01/06/2023

## Slide 16: Simulation Results: Parameter Overview
For the summary plots
The parameter is divided by the transverse surface of the vacuum chamber in order to do the comparison with different vacuum chambers
Parameter
ABP-CEI Section Meeting 01/06/2023

## Slide 17: Simulation Results: Summary Previous Results
Focusing
Defocusing
No dependence on beta functions found in quadrupoles and dipoles
  positrons, beam chamber 9 mm, bunch spacing 10 ns
ABP-CEI Section Meeting 01/06/2023
For more details: L. Sabato, 20th November 2022, “E-cloud studies in the FCC-ee”, 159th FCC-ee Optics Design Meeting & 30th FCCIS WP2.2 Meeting

## Slide 18: Simulation Results: Summary Previous Results
Beam chamber winglet geometry
  a = 9 mm
  a = 10 mm
  a = 11 mm
Courtesy of
R. Kersevan
Design in PyECLOUD
a
ABP-CEI Section Meeting 01/06/2023

## Slide 19: Simulation Results: Summary Previous Results
No dependence on the beam chamber winglet height
  positrons, dipole, bunch spacing 10 ns
9 mm
10 mm
11 mm
ABP-CEI Section Meeting 01/06/2023
For more details: L. Sabato, 20th November 2022, “E-cloud studies in the FCC-ee”, 159th FCC-ee Optics Design Meeting & 30th FCCIS WP2.2 Meeting

## Slide 20: Simulation Results
ABP-CEI Section Meeting 01/06/2023
No dependence on the beam chamber winglet height
Recently confirmed also for the sextupoles (from the studies of H. Maury and K. Cantún, Universidad Autónoma de Yucatán)
9 mm 10 mm 11 mm
Courtesy of H. Maury and K. Cantún

## Slide 21: Simulation Results: Summary Previous Results
Particles: positron, electron
ABP-CEI Section Meeting 01/06/2023

## Slide 22: Simulation Results: Summary Previous Results
Dependence on the bunch charge
  Drift space, bunch spacing 10 ns
Positron Bunches
Electron Bunches
In the case of electron bunches, the e-cloud density is smaller
Multipacting occurs in a few cases
Central density?
ABP-CEI Section Meeting 01/06/2023
For more details: L. Sabato, 20th November 2022, “E-cloud studies in the FCC-ee”, 159th FCC-ee Optics Design Meeting & 30th FCCIS WP2.2 Meeting

## Slide 23
Dependence on the bunch charge:
  (Drift space, bunch spacing 10 ns, bunch intensity 2.0e11 ppb, SEY 1.6)
  Positron Bunches Electron Bunches
In the case of electron bunches, the electrons are mainly located far from the beam chamber centre
Simulation Results: Summary Previous Results
ABP-CEI Section Meeting 01/06/2023
For more details: L. Sabato, 20th November 2022, “E-cloud studies in the FCC-ee”, 159th FCC-ee Optics Design Meeting & 30th FCCIS WP2.2 Meeting

## Slide 24: Simulation Results: Summary Previous Results
Drift space
Dipole
Quadrupole
Dependence on the bunch intensity
  positrons, bunch spacing 10 ns
In the drift space and dipole, the electron density has a similar behaviour with respect to the bunch intensity
  less bunch intensity more electron density
In the quadrupole,
  the bunch intensity has a negligible effect on the electron density
ABP-CEI Section Meeting 01/06/2023
For more details: L. Sabato, 20th November 2022, “E-cloud studies in the FCC-ee”, 159th FCC-ee Optics Design Meeting & 30th FCCIS WP2.2 Meeting

## Slide 25: Simulation Results: New Parameters
Element: Drift space, Dipole, Quadrupole
Bunch spacing: 15 – 25 ns (step 5 ns)
Bunch intensity: 0.8 – 2.0e11 (step 0.2e11)
SEY: 1.0 – 1.6 (step 0.1)
Bunch Length: 11.8 mm
Total: 441 simulations
ABP-CEI Section Meeting 01/06/2023

## Slide 26: Simulation Results: New Parameters
bunch spacing 15 ns, longer bunch length
In the drift space and dipole, the electron density has a similar behaviour with respect to the bunch intensity
  the dependence on the bunch is not monotonic
In the quadrupole,
  the bunch intensity has a non-negligible effect on the electron density
  less bunch intensity less electron density
Drift space
Dipole
Quadrupole
ABP-CEI Section Meeting 01/06/2023

## Slide 27: Simulation Results: New Parameters
Drift space
Dipole
Quadrupole
Bunch spacing 15 ns, longer bunch length
Drift space
Dipole
NEW
OLD
Quadrupole

## Slide 28: Simulation Results: New Parameters
Drift space
Dipole
Quadrupole
Bunch spacing 20 ns, longer bunch length
Drift space
Dipole
NEW
OLD
Quadrupole

## Slide 29: Simulation Results: New Parameters
Drift space
Dipole
Quadrupole
Bunch spacing 25 ns, longer bunch length
Drift space
Dipole
NEW
OLD
Quadrupole

## Slide 30: Simulation Results: New Parameters
For a fixed bunch spacing
  The e-cloud density has the same order of magnitude for the new parameters and the old ones
  The new configuration of beam chamber / bunch length / bunch intensity does not significantly alter the e-cloud density
New parameters, max bunch spacing reachable 18.9 ns (16,000 bunches)
Old parameters, max bunch spacing reachable 32.9 ns (9,200 bunches)
ABP-CEI Section Meeting 01/06/2023

## Slide 31: Simulation Results: New vs OLD
Drift space
Dipole
Quadrupole
Drift space
Dipole
NEW
15 ns
OLD
30 ns
Quadrupole

## Slide 32: Outline
Introduction
E-Cloud Formation Process
Build-up Simulation Results
Stability Simulations
Conclusions and Outlook
ABP-CEI Section Meeting 01/06/2023

## Slide 33: Stability Simulations
A complex problem involving two sets of particles mutually interacting
ABP-CEI Section Meeting 01/06/2023
Beam charge distribution
E.M.
forces
Maxwell’s equations
e- equations of motion
Vacuum chamber
Shape, PEC boundary conditions
Maxwell’s equations
E.M.
forces
e- production mechanisms
(e.g. secondary emission)
Electron cloud effects
Beam equations of motion
External forces from
Magnets & RF
External B field
Courtesy of
G. Rumolo

## Slide 34: Stability Simulations
Beam dynamics simulations  Model the interaction of the beam (typically a single bunch) with a given initial electron distribution
ABP-CEI Section Meeting 01/06/2023
Beam charge distribution
E.M.
forces
Maxwell’s equations
e- equations of motion
Vacuum chamber
Shape, PEC boundary conditions
Maxwell’s equations
E.M.
forces
e- production mechanisms
(e.g. secondary emission)
Electron cloud effects
Beam equations of motion
External forces from
Magnets & RF
Pre-calculated initial electron distribution
External B field
Courtesy of
G. Rumolo

## Slide 35: Stability Simulations
E-cloud build-up  Solely focuses on electron dynamics with an unperturbed beam distribution to determine how the e-cloud forms and where it saturates
ABP-CEI Section Meeting 01/06/2023
Courtesy of
G. Rumolo
Beam charge distribution
E.M.
forces
Maxwell’s equations
e- equations of motion
Vacuum chamber
Shape, PEC boundary conditions
Maxwell’s equations
E.M.
forces
e- production mechanisms
(e.g. secondary emission)
Electron cloud effects
Beam equations of motion
External forces from
Magnets & RF
Pre-calculated forces from unperturbed beam distribution
External EM fields in RF cavity
External B field

## Slide 36: Stability Simulations
The beam stability simulations are heavy from the computational point of view
HPC cluster at INFN-CNAF (Bologna, Italy) allowing for Message Passing Interface (MPI) applications across multiple nodes
  The cluster presently features a total of about 800 CPU-cores
ABP-CEI Section Meeting 01/06/2023

## Slide 37: Stability Simulations
Bunch length
10
9
8
7
6
5
4
3
2
1
MP1
MP2
MP3
MPN
…
Convergence studies on the numerical parameters are needed:
  the number of longitudinal slices along the bunch
  the average number of MPs/slice used to model the proton bunch
  the number of e-cloud interactions (kicks) along the ring
  the number of MPs used to model the e-cloud at each interaction
  the configuration of the transverse grids used to compute the fields generated by the beam and by the electrons through the PIC method [ ] )
ABP-CEI Section Meeting 01/06/2023
[ ] E. Belli, “PyPIC: the multigrid solver”, EC Meeting #32 – September 2, 2016

## Slide 38: Stability Simulations
For the first results, see the presentation of Fatih Yaman on Thursday 8th June at 14:30
ABP-CEI Section Meeting 01/06/2023

## Slide 39: Outline
Introduction
E-Cloud Formation Process
Build-up Simulation Results
Stability Simulations
Conclusions and Outlook
ABP-CEI Section Meeting 01/06/2023

## Slide 40: Conclusions and Outlook
The FCC-ee in the Z configuration has been investigated, because the strongest electron cloud effects are foreseen for this configuration, due to the highest number of bunches (smallest bunch spacing)
Some parameters, in the range of considered values, give a negligible contribution to the e-cloud formation
  Beta functions (focusing-defocusing) in quadrupoles and dipoles
  Beam chamber winglet geometry
In some cases multipacting can occur even with electron bunches
  The e-cloud density is smaller compared with the positron bunches
  The electrons are mainly located far from the beam chamber centre
The dependence on the bunch intensity is not monotonic:
  It is dependent on the considered value range
  it is related to the different elements
ABP-CEI Section Meeting 01/06/2023

## Slide 41: Conclusions and Outlook
  Increasing the bunch spacing, the e-cloud density decreases in all elements (for more cases there is no multipacting)
For a fixed bunch spacing
  the e-cloud density has the same order of magnitude for the new parameters and the old ones
  the new configuration of beam chamber / bunch length / bunch intensity does not significantly alter the e-cloud density
The max bunch spacing reachable
  new parameters, 18.9 ns (16,000 bunches)
  old parameters, 32.9 ns (9,200 bunches)
Comparing the new configuration and the old configuration with the max bunch spacing reachable
  e-cloud density is higher in all the elements
ABP-CEI Section Meeting 01/06/2023

## Slide 42: Conclusions and Outlook
One of the main concerns is the e-cloud effect on the beam stability
Further studies will be performed in order to check the stability limits by means of self-consistent beam stability simulations for the different arc elements with realistic e-cloud distributions obtained from build-up simulations
ABP-CEI Section Meeting 01/06/2023

## Slide 43: Thank you for your attention
ABP-CEI Section Meeting 01/06/2023

## Slide 46: Introduction: FCC
The research project is in the framework of long term coherent stability for the Future Circular Collider (FCC)
FCC study is developing designs for a new research infrastructure to host the next generation of higher performance particle colliders to extend the research currently being conducted at CERN
The goal of the FCC is to push the energy and intensity frontiers of particle colliders, with the aim of reaching collision energies of 100 TeV, in the search for new physics
ABP-CEI Section Meeting 01/06/2023

## Slide 47: Simulation Results: Summary Previous Results
Particle
Beam chamber winglet geometry
Element
Bunch spacing: 10 – 30 ns (step 5 ns)
Bunch intensity: 2.0 – 2.8e11 (step 0.1e11)
SEY: 1.0 – 1.6 (step 0.1)
Total: 9,450 simulations
ABP-CEI Section Meeting 01/06/2023

## Slide 48: Background: Case Study
(3)
(2)
(2)
(3)
E0 and R0: shape parameters.
For the LHC beam chambers:
  E0 = 150 eV
  R0 = 0.7
ABP-CEI Section Meeting 01/06/2023

## Slide 49: Background: Case Study
(2)
(3)
(4)
𝛿𝑚𝑎x
(2)
(4)
s: shape parameter;
: maximum of the SEY curve dependent on the surface material, roughness and history
Emax: electron energy, where the SEY reach the maximum 𝛿𝑚𝑎x:
For the LHC beam chambers:
  s = 1.35
  Emax = 332 eV
ABP-CEI Section Meeting 01/06/2023

## Slide 50: Background: Case Study
Parameter Overview
Secondary emission model:
LHC beam chambers:
  = 1.0828
  = 1.6636
[eV]
[] B. Henrist et al., “Secondary Electron Emission Data for the Simulation of Electron Cloud”, cds 2002.
ABP-CEI Section Meeting 01/06/2023

## Slide 51: Project Goals
  The goal is to go below the SEY threshold for instabilities driven by e-cloud
Comparison between the analytical central electron density threshold for single bunch instability and the simulation results
Single-bunch stability simulations in dipoles
Analytical equation
[] K. Ohmi et al., “Study of Electron Cloud Instabilities in FCC-hh”, Proc. of IPAC2015
Courtesy of
L. Mether
ABP-CEI Section Meeting 01/06/2023

## Slide 52
ABP-CEI Section Meeting 01/06/2023