## Slide 1
Overview of FCC-ee specific hardware activities
Paolo Giacomelli
INFN Bologna
Fostering Swiss collaboration towards a future circular collider - Part 2
Zurich, 25-26 August 2022

## Slide 2: Detector concepts fast overview
France, Switzerland, USA, ...
------
campaigns

## Slide 3: Vertex detector: IDEA
Inspired by ALICE ITS based on MAPS technology, using the ARCADIA R&D program
  Pixels 20 × 20 mm2
Light
  Inner layers: 0.3% of X0 / layer
  Outer layers: 1% of X0 / layer
Performance:
  Point resolution of ~3 mm
  Efficiency of ∼100%
  Extremely low fake rate hit rate
5 MAPS layers:
R = 1.7 - 2.3 - 3.1 cm
Pixel size: 20 x 20 mm2
R = 32 - 34 cm
Pixel size: 50 x 100 mm2

## Slide 4: Momentum measurement
ZH (Hmm)
Muon pt
ZH (Hmm)
Muon pt
90 degree
MS only
ZH (Zmm)
Muon pt
Z or H decay muons in ZH events have rather low pt
  Transparency more important than asymptotic resolution

## Slide 5: Central tracker
Two solutions under study
CLD: All silicon pixel (innermost) + strips
  Inner: 3 (7) barrel (fwd) layers (1% X0 each)
  Outer: 3 (4) barrel (fwd) layers (1% X0 each)
  Separated by support tube (2.5% X0)
IDEA DC
IDEA: Extremely transparent Drift Chamber
  GAS: 90% He – 10% iC4H10
  Radius 0.35 – 2.00 m
  Total thickness: 1.6% of X0 at 90o
    Tungsten wires dominant contribution
  Full system includes Si VXT and Si “wrapper”

## Slide 6: Drift chamber
IDEA DC
IDEA: Extremely transparent Drift Chamber
  Gas: 90% He – 10% iC4H10
  Radius 0.35 – 2.00 m
  Total thickness: 1.6% of X0 at 90o
    Tungsten wires dominant contribution
  112 layers for each 15o azimuthal sector
  max drift time: 350 ns

## Slide 7: Drift chamber
In general, tracks have rather low momenta (pT ≲ 50 GeV)
  Transparency more relevant than asymptotic resolution
Drift chamber (gaseous tracker) advantages:
  Continuous tracking: reconstruction of far-detached vertices (K0S , L, BSM, LLPs)
  Outstanding particle separation via cluster counting (dN/dx) or dE/dx
    >3s K/p separation up to ~35 GeV
dN/dx from Garfield++

## Slide 8: Dual Readout Calorimetry
Measure simultaneously:
  Scintillation signal (S)
  Cherenkov signal (Q)
Calibrate both signals with e-
Unfold event by event fem to obtain corrected energy
Alternate
Cherenkov fibers
Scintillating fibers
with:
Newer DR calorimeter
( bucatini calorimeter)
~2m long capillaries

## Slide 9: Dual Readout Calorimeter
Full GEANT4 implementation of the DR calorimeter
EM
HAD

## Slide 10: Crystal option
ECAL layer:
  PbWO crystals
  front segment 5 cm (~5.4 X0)
  rear segment for core shower
  (15 cm ~16.3 X0)
  10x10x200 mm³ of crystal
  5x5 mm² SiPMs (10-15 um)
1x1x5 cm3
PbWO
1x1x15 cm3
PbWO
~20 cm PbWO4
sEM ≈ 3%/
DR w. filters
Timing layer
  LYSO 20-30 ps
PF for jets

## Slide 11: Ongoing R&D Click here for more R&D information

## Slide 12: Si Tracker R&D
M. Dam

## Slide 13: ARCADIA MD1 test
s
Few events (zoom)
90Sr
Few events (zoom)
Preliminary results: on-line QA-plots
110 nm CMOS CIS technology, high-resistivity bulk, operated in full depletion mode
Pixel size = 25x25 2
Matrix = 512 x 512
Thickness = 200
Few cosmic tracks
(Tilted sensor)

## Slide 14: R&D on new LGADs
R&D on new type of LGAD - RSD detectors (AIDAinnova) for FCC-ee
Excellent space resolution at low occupancy
Excellent time resolution
Very thin
Possible use in secondary trackers or time of flight detectors
INFN Genova

## Slide 15: Wire chamber: Cern test beam 11-2021
HV cable
inlet gas
manifold
outlet gas
manifold
HV distr.
box
DRS
signal
box
signal cables
(40 cm)
upstream
trigger tile
downstream
trigger tile
The experimental setup
at CERN H8 beam
November 2021
1 cm
3 cm
2 cm
Drift tubes pack
Event display

## Slide 16: IDEA: Wire chamber
Ionization clusters ( ) and
single electron pulses ( )
1 cm tube
2 cm tube
3 cm tube
Typical pulse spectra
90%He - 60° - 2cm
90%He - 0° - 2cm
80%He - 60° - 2cm
90%He - 60° - 1cm
90%He - 45° - 1cm
80%He - 60° - 1cm
Electron peak finding

## Slide 17: Future activities
Beam test scheduled for next June at CERN H8 aimed at:
  measuring the cluster density as a function of bg at different muon beam momenta
  defining the relativistic rise and the Fermi plateau of dE/dx and dN/dx in He based gas mixtures (lack of experimental data and discrepancies among different simulation models)
Checking the particle identification performance with cluster counting and with dE/dx using as a benchmark the CP violating process:
Bs  Ds K
Plenty of scope for new collaborators!
Investigate relativistic rise region

## Slide 18: CALICE calorimetry

## Slide 19: IDEA: 2020 Dual Readout prototype
Electromagnetic dimensions of 10x10x100 cm3
9 towers containing 16x20 capillaries (160 C and 160 S)
Capillary tube with outer diameter of 2 mm and inner diameter of 1.1 mm 1-mm-thick fibers
Full prototype - 9 towers
Single tower
Fiber guiding system
Hamamatsu SiPM: S14160-1315
PS Cell size: 15 μm
Front end board
housing 64 SiPM
Readout Boards CAEN A5202
“Bucatini calorimeter”

## Slide 20: IDEA: 2020 Dual Readout prototype
Two test beams in 2021: DESY and CERN
Preliminary - no filters used
DESY with e- 1-6 GeV
SPS with e+ 10-125 GeV
Preliminary
yellow filters used over scintillating fibers,
neutral filters used over clear fibers
Front end board
housing 64 SiPM

## Slide 21: IDEA: DR future prototypes
1 Mini-Module (MM):
32 x 16 channel ( 512 ch )
1 Module:
2 x 5 MMs
→ 10 FEE boards
(8-channel grouping)
~ 13 x13 x 200 cm3
17 modules, ~ 65 x 65 x 200 cm3
HiDRa2
- 2 central modules with SiPMs
→ ~ 10 k SiPMs, ~ 20 FEE boards
- all others with PMTs
→ ~ 150 PMTs
Full hadronic shower containment calorimeter

## Slide 22: IDEA: Plate based + 3D printing calo (Korea)
“Short-term plan”
“Mid-term plan”
Building more and
more modules
2022-2025
Strong collaboration on DR calorimetry between INFN, Korea and USA
Copper (3D printed)

## Slide 23: IDEA: Crystal ECAL with DR calorimeter
M. Lucchini

## Slide 24: IDEA: Crystal ECAL with DR calorimeter
Sensible improvement in jet resolution using dual-readout information combined
with a particle flow approach → 3-4% for jet energies above 50 GeV
crystals + IDEA w/o DRO
crystals + IDEA w/ DRO
crystals + IDEA w/ DRO + pPFA
Event display
M. Lucchini

## Slide 25: IDEA: m-RWELL Test beam 2021
New μ-RWELL prototypes with 40 cm long strips
strips
beam
7 m-RWELL prototypes with resistivity varying between
10 and 80 MOhm/£
will allow to define best resistivity for final 50x50 cm2 detector
H8 Test beam 11/2021
a) Design optimization:
- different HV filter applied
b) Detector characterization
- HV scan at 0°
- HV scan at different angles and drift field
1- Signal shape
(cluster charge, cluster size)
2 - Detector performance
(efficiency, space resolution)
LNF
BOLOGNA
FERRARA
TORINO

## Slide 26: Results from test beam data

## Slide 27: IDEA: 2D m-RWELL ideas
m-RWELL with 2D anode readout
Good performance
but need higher gain wrt. to 1D
m-RWELL
More complex PCB construction
2 stacked 1D m-RWELL
1 view per m-RWELL
easy PCB construction
2D performance to be measured
m-RWELL with strips
on top and anode
HV on DLC,
TOP to ground
2D performance to be measured
x strip
y strip
y strip
x strip
y strip
x strip

## Slide 28: IDEA: Test with TIGER electronics
Test with TIGER ASIC
Developed for BESIII CGEM-IT
Prepare new readout card based on System On Modules (SOM)
Aim
Develop dedicated ASIC for m-RWELL (AIDAinnova task 11.3)

## Slide 29: R&D projects and funding
AIDAinnova (01/04-2021-30/03/2025)
    CMOS pixel sensors
    High granularity calorimetry, Dual Readout calorimetry
    Large drift chamber
    m-RWELL detectors
EURO-LABS (01/09/2022-31/08/2026)
  Will provide funds for Transnational Access
CERN EP R&D
  CMOS sensors, LAr calorimetry, etc.
ECFA has defined a detector roadmap in which FCC-ee is clearly documented
Some National funding schemes have started (Italy, France, etc.)

## Slide 30: Conclusions
FCC-ee will be a fascinating machine, allowing to achieve unprecedented precision on EW measurements and Higgs couplings
  Up to 4 detector concepts should be proposed for the 4 IPs
    For the time being 3 detector concepts have been proposed
      CLD, IDEA and a LAr-based detector
Need for significant R&D in the next 4-5 years
  For the time being IDEA is the most active on hardware studies and developments
    A lot of ongoing activities on all IDEA sub-detectors
  Profiting from several national funding schemes, EU projects (AIDAinnova, EURO-LABS), etc.
  Now several international colleagues have joined these efforts, but there is still HUGE space for collaboration on basically every aspect of these detector concepts
Lots of possibilities for International colleagues to join IDEA and help on all these developments!!

## Slide 31: Backup

## Slide 32: DR calorimeter
Scintillation
Čerenkov
Front
Rear
Copper (3D printed)

## Slide 33: m-RWELL-based detectors
Ø Define the best resistivity of the DLC for both µRWELL fundamental tiles and build the 50×50 cm2 prototypes for the pre-shower and muon systems.
Ø Optimize the engineering mass construction process together with the ELTOS industry.
Ø Develop a custom-made ASIC for the µRWELL with the experience obtained from the TIGER chip and to test the µRWELL prototypes.
Ø Develop a new reconstruction algorithm, ML-based, to improve the resolution of µRWELL.
Ø Simulation of the CEPC decay channels of interest to optimize the detector design with special emphasis on Long Lived Particles to show the impact of a performing tracked in the muon system instead of a tagger.
Strip length
~22.5 cm
Ø Two large microRWell chambers M4 in Bologna;
Ø Ferrara has procured the Tiger electronics;
Ø Plan to start equipping the M4s with the TIGER next spring;
Ø Use a cosmic telescope to characterize the detector and the electronics and later to expose the chamber with the TIGER electronics to a test beam;
Ø Funding received to develop a new ASIC starting from the experience of the TIGER.
2022-2024 R&D program
Development of a new ASIC

## Slide 34: The IDEA detector concept
New, innovative, possibly more cost-effective concept
  Silicon vertex detector
  Short-drift, ultra-light wire chamber
  Dual-readout calorimeter
  Thin and light solenoid coil inside calorimeter system
    Small magnet ⇒ small yoke
  Muon system made of 3 layers of m-RWELL detectors in the return yoke
https://pos.sissa.it/390/
IDEA concept (proposed in FCC CDR)
Innovative Detector for e+e- Accelerator
Acknowledgments
I need to thank many colleagues, in particular:
P. Azzi, F. Bedeschi, and R. Santoro

## Slide 35: IDEA detector layout
Beam pipe: R∼1.5 cm
Vertex:
5 MAPS layers
R = 1.7-34 cm
Drift Chamber: 112 layers
4 m long, R = 35-200 cm
Outer Silicon wrapper:
Si strips
Superconducting solenoid coil:
2 T, R ∼ 2.1-2.4 m
0.74 X0, 0.16 l @ 90°
Preshower: ∼1 X0
Dual-Readout Calorimeter:
2m / 7 lint
Yoke + Muon chambers

## Slide 36: m-RWELL technology
The m-RWELL is composed of only two elements:
m-RWELL_PCB
drift/cathode PCB defining the gas gap
m-RWELL_PCB = amplification-stage ⊕ resistive stage ⊕ readout PCB
m-RWELL operation:
  A charged particle ionises the gas between the two detector elements
  Primary electrons drift towards the m-RWELL_PCB (anode) where they are multiplied, while ions drift to the cathode
  The signal is induced capacitively, through the DLC layer, to the readout PCB
  HV is applied between the Anode and Cathode PCB electrodes
  HV is also applied to the copper layer on the top of the kapton foil, providing the amplification field
(*) G. Bencivenni et al., “The micro-Resistive WELL detector: a compact spark-protected single amplification-stage MPGD”, 2015_JINST_10_P02008)
LNF
BOLOGNA
FERRARA
TORINO

## Slide 37: Preshower and muon detector
Preshower Detector
High resolution before the magnet
to improve cluster reconstruction
Efficiency > 98%
Space Resolution < 100 mm
Mass production
Optimization of FEE channels/cost
Muon Detector
Identify muons and search for LLPs
Efficiency > 98%
Space Resolution < 400 mm
Mass production
Optimization of FEE channels/cost
Preshower
pitch = 0.4 mm
FEE capacitance = 70 pF
1.5 million channels
Muon
pitch = 1.5 mm
FEE capacitance = 270 pF
5 million channels
Barrel Preshower
Similar design for the Muon detector
Endcap Preshower
Similar design for the Muon detector
50x50 cm2 2D tiles to cover more than 4330 m2
Detector technology: µ-RWELL

## Slide 38: Status of Simulation of IDEA concept
FASTSIM Delphes IDEA card used for performance studies FCCSW
Very sophisticated compared to default.
Latest additions: Vertexing, LLP, PID, dN/dx, dE/dx
FULLSIM: standalone GEANT4 description
Fully integrated geometry
Output hits and reco tracks converted to EDM4HEP
Ready for PFlow development and other reconstruction frameworks/algorithms (ACTS, Pandora etc) in FCCSW