## Slide 1: CERN-ISOLDE’s new high-resolution laser ion source PI-LIST: Results, characteristics, and developments
Reinhard Heinke
for the PI-LIST collaboration

## Slide 2: ISOLDE at CERN

## Slide 3: The ISOLDE facility at CERN
GPS
General Purpose Separator
HRS
High Resolution Separator
Target area
MEDICIS
Radioactive laboratory
Low energy RIB
High energy RIB

## Slide 4: ISOLDE frontend and target/ion source unit
Target container
Ion source

## Slide 5: ISOLDE’s resonance ionization laser ion source RILIS
Ionization
lasers
Production / Reservoir
p+
Energy
Ground state
Ion
Ion
+
Excited states
Atom
Effusion of reaction products provided as hot atomic vapor ( > 2000°C )
Highly efficient laser ionization of element of choice as function of laser wavelength  in-source spectroscopy (<< 1pps)
Extraction and mass separation as ion beam

## Slide 6: The RILIS laser setup
10kHz rep-rate wavelength-tunable systems (commercial + development)
4ω Ti:Sa
210-230 nm
Ti:Sa
700-950 nm
dye
550-700 nm
2ω Ti:Sa
350-475 nm
2ω dye
300-350 nm
3ω Ti:Sa
230-300 nm
UV pumped dye
475-550 nm
385-545 nm
Raman shift
+ 2ω
Sum mixing
532nm
Difference mixing 1064nm
300-340 nm
520-860 nm
Solid state laser development:
Mixing (poster J. Wessolek), Raman shifting (poster C. Bernerd)

## Slide 7: A new community-driven laser scheme database
Poster R. Trappitsch
https://rims-code.github.io
From community for community: Feedback, feature requests, extension to tool hub, …

## Slide 8: RILIS @ ISOLDE: The workhorse ion source
22 elements: Pm, Er, Yb, Gd, In, Dy, Tl, Cd, Hg, Al, Cr, Ac, Ca, Mg, Tm, Zn, Mn, Pb, Sb, Be, Ag, Pr
28 out of 33 weeks (including weekends) + development
RIB delivery and nuclear structure experiments
2023 ISOLDE operation schedule

## Slide 9: ISOLDE’s resonance ionization laser ion source RILIS
Ionization
lasers
Production / Reservoir
Energy
Ground state
Ion
Ion
+
Excited states
Atom
Effusion of reaction products provided as hot atomic vapor ( > 2000°C )
Highly efficient laser ionization of element of choice as function of laser wavelength  in-source spectroscopy (<< 1pps)
Extraction and mass separation as ion beam
Beam purity influenced by competing ionization mechanisms
p+

## Slide 10: The Laser Ion Source and Trap LIST
e-/
experiment
/
Spatial separation: hot cavity ↔ laser ionization volume
Suppression of surface ionized species
Pure laser ionization inside RF quadrupole structure
Factor up to 106 in suppression ↔ Factor 20-100 reduction in beam intensity
Versatility: Mimic standard RILIS by extracting and guiding ions from hot cavity
Energy
Ground state
Ion
Ion
+
Excited states
Atom
90 mm
p+

## Slide 11: Nuclear structure laser spectroscopy
Ac laser ionization scheme
(used at LISOL, TRIUMF, ISOLDE, JGU, …)
x 105
Hyperfine structure spectroscopy:
Interaction of nucleus with electron shell
Nuclear spin, deformation
Changes in charge radii
Changes in mean square charge radii
Spectroscopy on Tl with LIST: Z. Yue, next talk!

## Slide 12: A laser spectroscopist’s playground
https://www.ikp.tu­darmstadt.de/gruppen_ikp/ag_noertershaeuser/research_wn/exotic_nuclei_wn/ uebersicht_2/laserspectroscopy_survey.de.jsp
Nuclides investigated by laser spectroscopy
B. Marsh et al, Nature Physics 14, 1163–1167 (2018)
Collective effects of protons and neutrons
 How to derive from first principles / strong force?

## Slide 13: “Sub-Doppler” hot cavity in-source spectroscopy
Atomic beam cone
vthermal
Crossed atom beam / laser geometry in LIST structure:
The Perpendicularly Illuminated PI-LIST
Selection of reduced Doppler ensemble in laser intersection volume
Suitable narrow-band laser
  Resolution improvement by >1 order of magnitude
Narrow bandwidth spectroscopy laser
≙ 400 nm
≙ 800 nm

## Slide 14: Off-line results from PI-LIST
97-99Tc T. Kron et al, PRC
100 – 120 MHz
Lateral laser incoupling through window in vacuum vessel
Nuclear structure investigations on long-lived radioisotopes
Standard tool for high resolution spectroscopy
143-147Pm D. Studer et al, Eur. Phys. J. A.
100 – 250 MHz
249-253Cf F. Weber et al, PRC
50 – 200 MHz
More from Mainz!
Es, Fm, … (Tuesday talks)
Window not possible at ISOLDE frontend!

## Slide 15: ISOLDE adaption of PI-LIST
No windows possible in ISOLDE frontend
Reflection by metallic mirror surfaces
Off-axis guiding of laser through ion beam line
Robust metallic mirrors
Adapted extraction electrode
Beam shape comparison
Emittance simulations
PI-LIST ready for on-line experiment!

## Slide 16: Holmium – a showcase
Internal reflection PI-LIST mode
FWHM = 160 MHz
Standard in-source /1000
165Ho fit
166mHo fit
Cumulative fit
J = 15/2
J = 15/2
43 HFS components
+ 23 from leaking 165Ho
Hyperfine structure studies on long-lived 163,166mHo for the ECHo project

## Slide 17: Nuclear shape effects in the heavy-element region
Gaffney et al., Nature 497, 199–204 (2013)
Pear shaped intrinsic nuclear configurations
Breaking of reflection symmetry
Prominent around 222Ra (Z ≈ 88, N ≈ 134)
Inverted odd-even staggering of charge radii? (Po, At, Fr, Rn, Ra)
Within EU ITN LISA: Laser Ionization and Spectroscopy of Actinides
Lynch et al., Phys. Rev. C 97, 024309 (2018)
Project closure conference 1 - 4 September @ CERN

## Slide 18: Octupole deformation in Ac isotopes
E. Verstraelen et al, PHYSICAL REVIEW C 100, 044321 (2019)
Significant isobaric contamination  LIST suppression
Low sensitivity to QS  PI-LIST high resolution
Recent investigations and EDF theory on Ac:
Available data matched only with octupole asymmetry
Distinct kink as benchmark case
Nuclear moments as supporting data
Notes: Less repetition, make physics plot bigger, show IOES

## Slide 19: IS664: Experimental setup
Joined NB laser infrastructure
CRIS Matisse cw Ti:Sa
RILIS injection-locked pulsed ring cavity
Cross-hall fiber
Separator launch
PI mode referencing
Detector and DAQ
MagneTOF single ion counter at GLM/LA1 beam lines
Highly sensitive
Laser-synchronized 10kHz DAQ (CRIS time tagger)
Laser ions
Background
Ion travel time (μs)
Ions in time window (arb.u.)

## Slide 20: Preliminary results: Radii kink confirmed?
Preliminary
In-situ analysis by Michael Heines
Preliminary
Lower yield  Compromise on resolution

## Slide 21: Complementary data: Collinear laser spectroscopy at TRIUMF
Slide content: Courtesy of Ruohong Li
226Ac+ (~107 ions/s)
342nm
Deceleration
electrodes
Fluorescence monitor
COLLAPS principle: Fluorescence detection after exciting ionic transition
Ac-225
Ac-226
Ac-228
Ac-229
 Complementary high-resolution data; Systematic check of nuclear structure results
~ 40 MHz
Scanned transition
PI-LIST best case: 220MHz

## Slide 22: PI-LIST for isomer-pure RIB production
Example case for inspiration
I = 3- / 6-
HFS known from collinear spectroscopy
I = 6-
I = 3-
200 MHz
2800 MHz
Capabilities greatly expanded
Relative frequency (MHz)
Relative signal
B. Cheal et al., Phys. Rev. C 82, 051302(R) (2010)
Isomer-pure RIB’s
Direct spectroscopy in clean samples
(Spin-)Controlled feeding
Switch ID ↔ efficiency
Notes: Skip?

## Slide 23: PI-LIST in the landscape of laser spectroscopy
PI-LIST
PI-LIST still “young”
“Simple” unit instead of beamline
Versatile operation modes
Isomer-selective RIB production

## Slide 24: Resolution meta-analysis
# |  | Mass (amu) | WL (nm) | Temp. (C) | LIST type | FWHM (MHz) | Opt? | Doppler (MHz) | Fraction
1 | Tc | 99 | 430 | 1700 | JGU | 98 | yes | 2230 | 4%
2 | Ho | 165 | 410 | 1000 | JGU | 104 | yes | 1455 | 7%
3 | Ho | 165 | 410 | 1000 | JGU mirror | 114 | yes | 1455 | 8%
4 | U | 238 | 830 | 1700 | JGU | 60 | yes | 745 | 8%
5 | Rb | 87 | 780 | 300 | JGU mirror | 62 | yes | 707 | 9%
6 | Ac | 225 | 418 | 1500 | JGU | 200 |  | 1442 | 14%
7 | Pm | 145 | 452 | 1500 | JGU | 150 |  | 1661 | 9%
8 | Cf | 250 | 417 | 800 | JGU | 55 | yes | 1067 | 5%
9 | Ac | 227 | 439 | 2000 | ISOLDE | 200 | yes | 1548 | 13%
No benchmark
ISOLDE

## Slide 25: Efficiency considerations
RILIS  LIST
LIST  PI-LIST
PI-LIST opt.
~ 30
~ 2
~ 10
Total:
Loss factors
~ 500 - 1000
Efficiency extrapolation with 225Ac:
~10-4 (Standard RILIS: 10%)
Geometric atom beam losses: Opening angle
Shape atom cone
Move potential
ridge closer

## Slide 26: Optimization pathways
Relative atom density
Distance from atomizer (mm)
Simulation data
3mm
1.5mm
Improve active volume: Shape electric potential
DC offset of LIST corpus
Improve repeller geometry
Also facilitates ion guiding
Shape effusing atom cone
Laser duty cycle
Multiple chances in tube vs. ~1 in atom cone
Standard
DC -5V
DC -10V
Multi-tube
Orifice design
RF phase synchronization
Trapping efficiency, investigated at TRIUMF
Dedicated off-line development infrastructure highly beneficial

## Slide 27: Atom beam collimation – experimental investigation
Test atomizer cross sections
Standard
Multi-capillary
Thin
Data analysis and feedback into simulation infrastructure ongoing
-
Experimental alternatives:
Planar laser induced fluorescence /
Deposition on catcher foils
A. Zadvornaya et al., Phys. Rev. X 8, 041008

## Slide 28: Future plans: Lanthanide campaign (LoI246)
Lanthanide elements as fitting case for (PI-)LIST:
Surface-ionizable  suppression needed
Extensive laser scheme groundwork done
PI-LIST off-line spectroscopy successful
Release behavior studied (MEDICIS)
High atomic level density (open shells) disadvantage for charge exchange
Interest in various nuclear structure phenomena, including p+ emitters beyond dripline
Change of deformation
OES,
Vanishing in isomers?
Strong
deformation?
 Ta target + LIST: lanthanide yield measurement campaign up to CERN LS3
Charge radii around N = 82

## Slide 29: Summary
RILIS @ ISOLDE: The workhorse RIB source and its evolution
PI-LIST: “Sub-Doppler” resolution enhancement
  High resolution spectroscopy: Ac octupole deformation
  Isomer-selective ionization
  Ongoing developments (FI-LIST  K. Wendt later)

## Slide 30
Thanks to you for LISTening…
… and to all the collaborators!

## Slide 31
https://rims-code.github.io
Contribute to sharing!

## Slide 32: IS664: Experimental setup
Joined NB laser infrastructure
CRIS Matisse cw Ti:Sa
RILIS injection-locked pulsed ring cavity
Cross-hall fiber
Separator launch
PI mode referencing
Detector and DAQ
MagneTOF single ion counter at GLM/LA1 beam lines
Highly sensitive
Laser-synchronized 10kHz DAQ (CRIS time tagger)
Laser ions
Background
Ion travel time (μs)
Ions in time window (arb.u.)
Radioactive noble gases from target on p+ impact
Group protons, measure later (slow release of Ac)
Detector moved to CB0
IDS/ASET on standby / parallel experiments

## Slide 33
PI-LIST at ISOLDE
90mm
Hot cavity
Spectroscopy laser
Metal mirror
Effusing atoms
Ion extraction electrode
PI-LIST structure
4x new orifices Ø = 6mm
Ionization laser
Heinke et al., NIMB 541, 8–12 (2023)
On-line applicable adaption
Alternative for external laser access through window
Robustness
Technical implementation
Confirmation of operation transparency of changes
Control and feedback systems (LabVIEW)
Notes: Mass separator is workhorse.
Laser system development -> design changes
Ever-growing portion of landscape